DECmate II  Specification
        - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -





	    REV.    DATE 	    MAJOR CHANGES	    # OF PAGES
	  ------------------------------------------------------------
	 |	 |	    |				   |	      |
	 |   0	 |16-Nov-81 | Originate                    |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------
	 |	 |	    |				   |	      |
	 |   1   |17-Nov-81 |Added CPU instruction list	   |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------
	 |	 |	    |Changed instruction timings to|	      |
	 |   2	 |30-Dec-81 |reflect 8/4 MHz. operation.   |	      |
	 |	 |	    |Added Z80 softcard to options.|   33     |
	 |	 |	    |Added Index, changed name.    |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------
	 |	 |	    |				   |	      |
	 |   3	 |10-Apr-82 |Added details of communication|	      |
	 |	 |	    |and user writeable characters |	      |
	 |	 |	    |Re-arranged sections.	   |	      |
	 |	 |	    |				   |	      |
 	  ------------------------------------------------------------
	 |	 |	    |				   |	      |
	 |	 |08-Aug-82 |Added environmental specns.,  |	      |
	 |	 |	    |dimensions and electrical	   |	      |
	 |	 |	    |requirements. Added example of|	      |
	 |	 |	    |programming the communications|   59     |
	 |	 |	    |port. Added to list of ESCape |	      |
	 |	 |	    |sequences supported.	   |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------
	 |	 |	    |				   |	      |
	 |   4	 |18-Jan-83 |Added ROM useage data, disk   |	      |
	 |	 |	    |useage for TRK 0 and 78, 79   |   71     |
	 |	 |	    |Updated ESCape sequence list  |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------
 	 |	 |	    |				   |	      |
	 |	 |	    |				   |	      |
	 |	 |	    |				   |	      |
	 |	 |	    |				   |	      |
	  ------------------------------------------------------------







							JOHN KIRK




   			    DECmate II  Specification
        - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -


	INDEX.

	Section		   Contents				   Page

	1.		Physical				    2

	   1.1		   Mechanical				    2
	   1.2		   Electrical				    2
	   1.3		   Environmental			    2

	2.		System Components

	   2.1		   CPU					    3
	   2.2		   Memory				    3
	   2.3		   Disk					    4
	   2.4		   Display				    4
	   2.5		   Keyboard				    5
	   2.6		   Printer Controller			    5
	   2.7		   Clock				    5
	   2.8		   Communications Port			    6

	3.		Options

	   3.1		   Graphics				    6
	   3.2		   5.25" Winchester Disk Sub-system	    6
	   3.3		   Z80 Softcard				    6
	   3.4		   RX01/02 Adaptor			    6

	4.		Detailed Description - Basic Machine

	   4.1		   CPU					    7

	   4.2		   Display				    7
	   4.2.1	      Screen Format and Modes		    8
	   4.2.2	      Character Attributes		    8
	   4.2.3	      Character Types			    9
	   4.2.4	      Scrolling				   10
	   4.2.4.1	         Types of Scrolling		   10
	   4.2.4.2	         Scrolling Regions		   10
	   4.2.5	      Display Control - ANSI Mode	   10
	   4.2.5.1	         CPR				   10
	   4.2.5.2	         CUU				   10
	   4.2.5.3	         CUD				   11
	   4.2.5.4	         CUF				   11
	   4.2.5.5	         CUB				   11
	   4.2.5.6	         CUP				   12
	   4.2.5.7	         HVP				   12
	   4.2.5.8	         DSR				   12
	   4.2.5.9	         IND				   12
	   4.2.5.10	         NEL				   12
	   4.2.5.11	         RI				   12
	   4.2.5.12	         DA				   13
	   4.2.5.13	         ED				   13

   			    DECmate II  Specification
        - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	   4.2.5.14	         EL				   14
	   4.2.5.15	         DECKPNM			   14
	   4.2.5.16	         DECPAM				   14
	   4.2.5.17	         SM				   15
	   4.2.5.18	         RM				   15
	   4.2.5.19	         ANSI Specified SM/RM Parameters   15
	   4.2.5.20	         DEC Private SM/RM Parameters	   16
	   4.2.5.21	         SCS				   17
 	   4.2.5.22	         SGR				   20
	   4.2.5.23	         DECDWL				   20
	   4.2.5.24	         DECDHL				   21
	   4.2.5.25	         DECSWL				   21
	   4.2.5.26	         DECSTBM			   21
	   4.2.5.27	         HTS				   22
	   4.2.5.28	         TBC				   22
	   4.2.5.29	         DECSC				   22
	   4.2.5.30	         DECRC				   22
	   4.2.5.31	         DECPRS				   22
	   4.2.5.32	         DECLL				   22
	   4.2.5.33	         DECALN				   22
	   4.2.5.34	         IL				   23
	   4.2.5.35	         DL				   23
	   4.2.5.36	         DCH				   23

	   4.2.6	      Display Control - VT52 Mode

	   4.2.6.1	         Cursor Up			   23
	   4.2.6.2	         Cursor Down			   24
	   4.2.6.3	         Cursor Right			   24
	   4.2.6.4	         Cursor Left			   24
	   4.2.6.5	         Enter Graphics Mode		   24
	   4.2.6.6	         Exit Graphics Mode		   24
	   4.2.6.7	         Cursor Home			   24
	   4.2.6.8	         Reverse Linefeed		   24
	   4.2.6.9	         Erase to End of Screen		   24
	   4.2.6.10	         Erase to End of Line		   24
	   4.2.6.11	         Direct Cursor Address		   25
	   4.2.6.12	         Identify 			   25
	   4.2.6.13	         Enter Alternate Keypad Mode	   25
	   4.2.6.14	         Exit Alternate Keypad Mode	   25
	   4.2.6.15	         Enter ANSI Mode		   25

	   4.3		   Keyboard				   25

	   4.3.1	      Instruction List			   26

	   4.4		   RX50 Disk Controller			   26

	   4.5		   Printer Port				   29
	   
	   4.6		   Communications Port			   30
	   4.6.1	      Instruction List			   30
	   4.6.2	      Internal Registers		   32
	   4.6.2.1		 Control Register - R0		   32

   			    DECmate II  Specification
        - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	   4.6.2.2		 Control Register - R1		   33
	   4.6.2.3		 Control Register - R2		   33
	   4.6.2.4		 Control Register - R3		   33
	   4.6.2.5		 Control Register - R4		   34
	   4.6.2.6		 Control Register - R5		   34
	   4.6.2.7		 Control Register - R6		   35
	   4.6.2.8		 Control Register - R7		   35
	   4.6.2.9		 Status Register 0		   36
	   4.6.2.10		 Status Register 1		   36
	   4.6.3	      Data Transfer
	   4.6.3.1		 Input				   37
	   4.6.3.2		 Output				   37

	   4.7		   Clock				   37

	5.		Detailed Description - Options

	   5.1		   Identification			   38
	   5.1.1	   Z80 APU				   38
	   5.2		   Graphics				   39
	   5.3		   Micro Winchester Disk Adaptor	   39
	   5.4		   RX01/02 Adaptor			   39

	6.		Firmware Details			   39

	   6.1		   CRT Controller and Associated Logic	   40
	   6.1.1	      80/132 Column Mode		   41
	   6.1.2	      Video Enable			   41
	   6.1.3	      Screen Mode			   41
	   6.1.4	      Cursor Mode			   41
	   6.1.5	      Erase Control			   41
	   6.6.6	      Extended Character Mode		   42
	   6.1.7	      User Character Set Mode		   42
	   6.1.8	      CRT Controller Registers		   44
	   6.1.9	      Cursor Visibility			   46

	   6.2		   Panel Requests			   47
	   6.2.1	      PR0				   47
	   6.2.2	      PRO 				   47
	   6.2.3	      PR2				   47
	   6.2.4	      PR3				   47

	   6.3		   Terminal Input Output		   50

	Appendix A.	Standard ROM Character Definitions	   51
	Appendix B.	CPU Instruction Set			   52
	Appendix C.	Example of Communications-Port Use	   56
	Appendix D.	Memory Allocation			   62
	Appendix E.	ROM Contents				   63
	Appendix F.	Disk Format Track 0, Tracks 78 and 79	   68
	Appendix G.	Boot Block Standard			   71

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
















     General

	This document describes a single board computer system  having  a
	single RX50 drive as the basic mass storage device. A second RX50
	is optional.

	Together with the LK201 keyboard  and  the  VR201  monitor,  this
	forms a lower cost replacement for the existing DECmate I system.
	Features of this new system are compared and contrasted to  those
	of DECmate I.

	Options include Z80 auxiliary processing  unit,  bitmap  graphics
	card  and  interfaces  to  RX02(RX01)  disk drives and to a 5.25"
	Winchester disk.

	One stated goal is that existing software,  now  running  on  the
	DECmate  I,  will  run  unaltered with the exceptions relating to
	disk capacity differences and  the  programming  notes  given  in
	Sections  4.6  and  4.7.  The new machine has additional features
	over and above those of DECmate I which may be used  as  software
	 is  developed, these will not, however, cause improper operation
	for those programs unaware of the new features.

	This specification describes what the combination of hardware and
	firmware   currently   do   (Firmware   Revision   0224).  Future
	enhancements to the firmware may add to what is described here.












	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 1      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     1. Physical

	The single board computer system  module, the  RX50  floppy  disk
	drive(s)  (RD50/51  Disk Drive) and  a power supply to supply the
	module, disk(s), monitor and keyboard are housed in  a small  box
	that  connects  to  the  AC  power  line  and to the monitor. The
	keyboard connects to the  monitor.  Provision  is  made  for  the
	addition  of one or more daughter boards to allow optional bitmap
	graphics, Z80 APU, RX01/02 adaptor and an interface  to  a  5.25"
	Winchester disk drive.

     1.1 Mechanical

     1.1.1 System Box

		Dimensions		  6.5" (H) x 14.3" (D) x 19" (W)
	 	Weight (single RX50)	  30 lbs.
		       (Dual RX50)	  32 lbs.

     1.1.2 Monitor

		Dimensions		  11.5" x13.75" x12.25"
		Weight			  14 lbs.

     1.1.3 Keyboard

		Dimensions		  2" x6.75" x21"
	        Weight			  4.5 lbs.

     1.2 Electrical

		Input voltage		  95 - 128 VAC 1 phase or
					  190 - 256 VAC 1 phase

		Frequency		  47 - 63 Hz.

		Power Consumption	  218 watts (max.)
					  3A @ 120 VAC.
					  1.5A @ 240 VAC.

	The AC input voltage selection is made by a switch at the rear of
	the  system  box.  A  detachable linecord allows the system to be
	configured easily for operation in most countries of the world.

     1.3 Environmental

	Operating :

		 temperature range	  59 - 90 F

		  humidity		  20 - 80 % non condensing with a
					  maximum  wet bulb of 77 F and a
					  minimum dewpoint of 6 F.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 2      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	(Recommended operating range   65 - 75 F, 40 - 60% RH)

		Altitude 		  0 - 10,000 feet.

     2.0 System Components

	The basic DECmate II configuration is as follows :

	.	CPU  -  6120 High Speed CMOS Processor
	.	32K words of user memory
	.	32K words of control memory used for
			Internal diagnostics
			Floppy disk bootstrap
			Character display level 1 terminal emulation
			Display buffer memory
			Space available to user for fast overlays etc.
	.	Dual/quad 5.25" floppy disk controller
	.	Video display controller
	.	Keyboard controller
	.	Serial printer controller
	.	100 Hz. crystal controlled clock
	.	Multi-protocol communications line controller

      2.1 CPU

				DECmate II	DECmate I

	CPU chip		6120		6120
	Speed			8/4 MHz.	5 MHz.
	Interrupt Latency	< 250 usec.	< 1 msec.
	DMA overhead		~10%		2.5%

     2.2 Memory

				DECmate II	DECmate I

	User memory		32K words	32K words
	Control memory		32K words	4K words
	Startup & self-test	4K words	Included in control
						memory number.

	The startup ROM is loaded into control memory RAM  at  power  on.
	This   code   performs   self-test,  initialization  of  the  I/O
	controllers  and  CRT  controller.  When  this  is   successfully
	completed  the  disk bootstrap code is executed. The main part of
	control panel memory which defines the  terminal  characteristics
	is  then  loaded from the disk. Additional or replacement control
	memory code may be loaded from the disk as required to extend the
	function of the machine, e.g. support for multiple display pages,
	high speed overlays etc.



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 3      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     2.3 Disk

	The DECmate II has as standard a single RX50 disk  drive  with  a
	second  drive  optional.  Capacity differences from DECmate I are
	given below. All numbers are in decimal.
 
     2.3.1 		DECmate II		DECmate I

			RX50 drive(s)	RX02
	Basic	

	# of drives 	1 - 5.25"		2 - 8"
	# of surfaces   2			2
 	Capacity/drive  408K 12-bit words	256K 12-bit words
			816K bytes		512K bytes
	Basic capacity  408K 12-bit words	512K 12-bit words
			816K bytes		1.024M bytes
	Expansion	Second drive within	Second RX02, requires
			same system box.	additional box
	Total capacity  816K 12-bit words	1.024M 12-bit words
			1.632M bytes		2.048M bytes

     2.3.2 Format

	# tracks	 80			 77
	# sectors/track  10			 26
	Bytes/sector    512			256
	Words/sector	256			128
	Recording       MFM			MFM with FM headers

	All the current  operating  systems  use  12-bit  mode  for  disk
	storage,  thus  capacity numbers are given for both this mode and 
	for 8-bit mode (byte).

     2.4 Display
			DECmate II 		DECmate I

 	CRT		   12" diagonal, P4 phosphor
 	Format, normal  24 x 80 		24 x 80

	Format, wide    24 x 132 		14 x 132

	Character	7 x 9 matrix 	7 x 9 matrix
			(within a 10 x 10 character cell)
	Character set   DEC Multi-national	94 ASCII subset plus
			set plus Katakana	special graphics
			and DECmate I foreign.
			128 user defined	128 fixed (ROM) option
						for foreign language.
	Character	Bold 			Bold
	attributes	Blink 			Blink
			Underline 		Underline
			Reverse 		Reverse
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 4      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Character type  Normal			Normal
			Double Height		  -
			Double Width		  -

	Screen		Normal 			Normal
	attributes	Reverse			  -

	Scrolling	Jump or variable rate*  Jump only
			smooth scrolling.

	Scroll region   Selectable scroll 	Full page scroll region.
						only

	Windows		Multiple display pages  Single page only
			horizontal scroll.**
	Performance	Full screen update      Full screen update
			< 0.1 seconds. 		< 2 seconds.

	*  Current firmware implements fixed rate smooth scroll only.
	**  Current  firmware  implements  single  page  only  with   no
	   horizontal scrolling.

	The  CRT  controller  uses  a  buffer  area  in  control  memory,
	accessing  data by DMA using a single row buffer. Sequential list
	screen addressing is used, allowing all the features of the VT100
	to  be  implemented.  In  addition, multiple display pages may be
	used in some future revison of the  firmware,  giving  fast  page
	swaps  or  horizontal  scrolling  for those applications programs
	that  can  take  advantage  of  these  features.  (not  currently
	implemented).

     2.5 Keyboard

	This is a version of the LK201 keyboard with keycaps  appropriate
	for  the Word Processing Software. Initially only a subset of the
	keyboard capabilities will be supported, enough  to  perform  the
	functions  of  the  VT100/DECmate  I  keyboard.  The interface to 
	DECMate  II  is  by  a  full  duplex,  serial  asynchronous  line
	operating at 4800 baud.

     2.6 Printer controller

	A full duplex serial asynchronous line with EIA signalling levels
	and programmable speed, DECmate I compatible.

     2.7 Clock

	A 100  Hz.  clock,  crystal  controlled  as  on  DECmate  I,  the
	instruction set is, however, different - see Section 4.7




	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 5      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	
     2.8 Communications

			DECmate II		DECmate I

	Standard	Single line, async/	None
			sync., byte and bit
			protocols
	Optional	None			Two lines, async/sync.
						byte and bit protocols

	I/O levels	EIA only		EIA only

	The communications line  that  is  standard  on  the  DECmate  II
	supports  both  bit  and byte oriented synchronous communications
	protocols in addition to asynchronous operation.

     3.0 Options

     3.1 Graphics

	An optional daughter board provides bitmap graphics capabilities.
	Refer to the appropriate option description for full details:

	Resolution	768 (H) x 240 (V)

	# of planes	3 with a fourth optional

	Grey scale      8 levels

	Colour		R-G-B outputs  to  external  colour  monitor  via
			colour  map,  16  colours  (with  optional fourth
			plane).

	Performance	Medium, programmed I/O device

     3.2 Micro Winchester Disk System 

	A second option board allows connection  of  a  5.25"  Winchester
	disk  drive, capacity either 5 or 10 MBytes. This drive is housed
	in the system box, occupying the space normally reserved for  the
	second RX50 floppy disk drive.

     3.3 Z80 Auxiliary Processing Unit (APU)

	A third option module allows a Z80 processor and memory system to
	be  added  to  the DECmate II. Control code, executed by the 6120
	processor, allows the Z80 to be selected as the active  processor
	with the 6120 performing all the I/O operations for it.

     3.4 RX01/02 Adaptor

	Another option allows one or two RX01  or  RX02  8"  floppy  disk
	drives  to be attached to DECmate II. This allows for simple file
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 6      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	interchange between existing 8"  diskettes  and  5.25"  diskettes.
	This  option  card  and  the Micro Winchester Option are mutually
	exclusive.

     4.0 Detailed Description

     4.1 CPU

	The 6120 is a high speed, CMOS  processor  that  executes,  as  a
	subset,   the   instruction   set  of  the  PDP  8/A.  Additional
	instructions implement stack operations and provide  a  mechanism
	for  using  the dual address space feature of the processor. Each
	address space has  its  own  interrupt  mechanism,  allowing  the
	single  CPU  to  be  used  to  execute  a  user program and, in a
	completely  transparent  mode,  to  emulate  certain   peripheral
	devices  -  the keyboard and display portions of the machine - to
	allow program compatibility with older PDP 8 machines  where  the
	terminal was a separate device connected via a serial line.

	The emulation process is similar to that used with the DECmate  I
	and  although  the  hardware is significantly different, software
	compatibility is maintained.

     4.2 Display

	The DECmate I used a display buffer that could be switched to  be
	a part of the CPU control memory address space when an update was
	required. When the  CRT  controller  was  accessing  the  display
	buffer  it  was  no longer a part of the CPU memory and there was
	therefore no contention between the CRT controller and  the  CPU,
	nor  any  CPU  bus overhead. In this way all the bandwidth of the
	display buffer memory was available during the active portion  of
	the  display.  The  limitation of this scheme is that the display
	buffer is only available to the CPU for about 1.5 msec. per frame
	(16.67  msec.).  This meant that display buffer updates had to be
	performed  as  a  burst  operation,  during  this  1.5  msec.  In
	addition, as this was a control memory operation, user interrupts
	were locked out for the total duration of the update interval. It
	was thus necessary to limit the update time to less-than  l-msec.
	to  avoid  losing  data  coming in on the communications line, or
	limit the communications line speed to something less  than  9600
	baud.  The  result of these constraints was that the screen could
	not be  changed  faster  than  an  effective  rate  of  9K  baud.
	(effective  rate  compares  the  change to that of a conventional
	terminal connected over a serial asynchronous line)

	The DECmate II uses a  portion  of  the  control  memory  as  the
	display  buffer memory together with a single row buffer which is
	filled from control memory by DMA. The DMA filling process  is  a
	burst operation and locks out the CPU for one line time, 64usec.,
	every 640 usec. This is an overhead of about 10%, but distributed
	over  the  entire frame rather than lumped as is the 1 msec. with
	DECmate I. As the display buffer is available to the CPU  at  all
	times  other  than  during the DMA cycles, the screen data may be
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 7      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	changed very quickly.

	More memory space is available for the display  buffer  than  was
	possible  with DECmate I, giving the ability to maintain multiple
	display pages and switch between them very quickly or to use this
	additional  space  to  implement  horizontal scrolling. The space
	allocated for the display buffer allows for up to  three  display
	pages  in 80 column mode and, subject to certain constraints, two
	pages in 132 column mode.  An  added  advantage  of  the  display
	buffer  structure  adopted  is  that  the  screen contents may be
	preserved when changing from 80 column to  132  column  mode  and
	vice versa.

     4.2.1 Screen Format and Modes

	The display has 24 rows of characters, selectable for 80  or  132
	characters per row on a screen basis.

	Characters may be  displayed  as  white  on  a  black  background
	(Normal Mode) or black on a white background (Reverse Mode).

     4.2.2 Character Attributes

	For both formats and modes the following  attributes,  selectable
	on a character basis are allowed :

	Normal Screen Mode

		BLINK - the selected character is  displayed  alternating
		between two intensities, normal (as modified by attribute
		BOLD) and lower than normal.

		BOLD - the selected character is displayed  at  a  higher
		than normal intensity.

		UNDERLINE - the selected character has a continuous  line
		added  below  the  lowest  character element for an upper
		case character  or  through  the  first  element  of  the
		descender for characters with descenders.

		REVERSE -  the  selected  character  is  displayed  as  a
		reverse  image,  i.e.  the  cell background is white, the
		character information is black. This  attribute  modifies
		the  action  of  attributes BLINK and BOLD such that they
		operate  on  the  cell  background  rather  than  on  the
		character  data,  e.g. REVERSE and BOLD results in a cell
		background that is brighter than  normal,  the  character
		itself remains black.

	Reverse Screen Mode

		BLINK - the cell background of the selected character  is
		displayed alternating between two intensities, normal (as
		modified by attribute BOLD) and lower than normal.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 8      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

		BOLD - the cell background of the selected  character  is
		displayed at a higher than normal intensity.

		UNDERLINE -  the  selected  character  has  a  continuous
		(black) line added below the lowest character element for
		an upper case character or through the first  element  of
		the descender for characters with descenders.

		REVERSE -  the  selected  character  is  displayed  as  a
		reverse  image,  i.e.  the  cell background is black, the
		character information is white.  This attribute  modifies
		the action of attributes BLINK and BOLD in Reverse SCreen
		Mode such that they operate on the character data  rather
		than on the cell background e.g. REVERSE and BOLD results
		in a character that is white and  brighter  than  normal,
		the cell background being black.

     4.2.3 Character Types

		Character type may be selected on a row basis to be :

		Normal - the character row is 80 or 132  characters  each
		defined within a 10 dot x 10 dot cell as shown in Fig. 1

		Double Width - the character row is 40 or  66  characters
		each defined within a double width cell.

		Double Height - the character row is 40 or 66  characters
		each  defined  within  a  double  height and double width
	 	cell, thus a double height  character  row  occupies  two
		normal row positions.

				Dot Position

		(9)0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0
	L 0      . . . . . . . . . . . . . . . . . . . . . .
	i 1	 . * * * * * * * . . . * * * * * * * . . . *
	n 2	 . * * * * * * * . . . * * * * * * * . . . *
	e 3	 . * * * * * * * . . . * * * * * * * . . . *
	  4	 . * * * * * * * . . . * * * * * * * . . . *
	N 5	 . * * * * * * * . . . * * * * * * * . . . *
	u 6	 . * * * * * * * . . . * * * * * * * . . . *
	m 7	 . * * * * * * * . . . * * * * * * * . . . *
    	b 8      # = = = = = = = # # # = = = = = = = # # # =
	e 9	 . + + + + + + + . . . + + + + + + + . . . +
	r 0	| |		    | |
		| |<---Character----->|
		| |       Cell      | |
		|<-----Attribute--->|
		|         Cell      |



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 9      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
			
	* Upper case, lower case or Special Graphics
	= Lower case, Underline or Special Graphics
	+ Lower case or Special Graphics 
	. Special Graphics

		FIGURE 1 - Character Cell Dot Placement

     4.2.4 Scrolling

     4.2.4.1 Types

	Scrolling may be set to be Jump or Smooth.  In  Jump  scroll  the
	display advances by a complete character row at a time, in Smooth
	scroll it advances by one or more lines of a row at a time,  with
	the default of two lines at a time. (every 16 msec.)

     4.2.4.2 Regions

	The normal mode of operation of the display is for the entire  24
	rows  to be considered as a scrolling region. The display control
	also allows the scroll region to be set to be only a part of  the
	screen,  e.g.  rows 5 to 12 may be set to scroll with rows 1 to 4
	and 13 to 24 remaining fixed.

     4.2.5 Display Control

	To control the features of the display portion  of  the  machine,
	the following ESCAPE sequences are defined as the user interface.
	The convention in the descriptions that follow is that the ESCAPE
	sequence,  when  issued by the user, causes the effect indicated.
	ESCAPE sequences generated  by  the  display  emulation  code  in
	response  to  an  ESCAPE  sequence  received  from  the  user are
	explicity noted.

     4.2.5.1 CPR - Cursor Position Report

	     ESC [ Pv ; Ph R	033 133 ** 073 *** 122

				Generated  by   the   display   emulation
				firmware as a reply to the user generated
				sequence  "DSR"  asking  for  a  position
				report.	
			Pv	the  current  cursor  vertical  position,
				expressed as a decimal string.
			Ph	the current cursor  horizontal  position,
				expressed as a decimal string.

	A response with no parameters, or parameters  of  0;0,  indicates
	that the cursor is at the HOME position.

     4.2.5.2 CUU - Cursor Up


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 10     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	     ESC [ Pn A 	033 133 ** 101

				Moves the cursor up by the number of rows
				specified by the parameter Pn, given as a
				decimal  string.  No   parameter   or   a
				parameter of 0 or 1 indicate a single row
				move. If  an  attempt  is  made  to  move
				cursor  above  the top margin, the cursor
				is positioned  at  the  top  margin.  The
				cursor   horizontal   position  does  not
				change.

     4.2.5.3 CUD - Cursor Down

	     ESC [ Pn B 	033 133 ** 102

				Moves the cursor down by  the  number  of
				rows specified by the parameter Pn, given
			 	as a decimal string. No  parameter  or  a
				parameter  of  0  or 1 indicates a single
				row move. If an attempt is made  to  move
				the  cursor  below the bottom margin, the
				cursor  is  positioned  at   the   bottom
				margin.  The  cursor  horizontal does not
				change.

     4.2.5.4 CUF - Cursor Forward

	     ESC [ Pn C 	033 133 ** 103

				Moves the cursor right by the  number  of
				columns  specified  by  the parameter Pn,
				given as a decimal string.  No  parameter
				or  a  parameter  of  0  or 1 indicates a
				single column move. If an attempt is made
				to  move  the  cursor  beyond  the  right
				margin, the cursor is positioned  at  the
				right   margin.   The   cursor   vertical 
				position does not change.

     4.2.5.5 CUB - Cursor Backwards

	     ESC [ Pn D   	033 133 ** 104 

				Moves the cursor left by  the  number  of
				columns  specified  by  the parameter Pn,
				given as a decimal string.  No  parameter
				or  a  parameter  of  0  or 1 indicates a
				single column move. If an attempt is made
				to   move  the  cursor  beyond  the  left
				margin, the cursor is positioned  at  the
				left margin. The cursor vertical position
				does not change.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 11     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     4.2.5.6 CUP - Cursor Position

	     ESC [ Pv ; Ph H	033 133 ** 073 *** 110

				Moves  the   cursor   to   the   position
				specified  by  the  parameters Pv and Ph.
				Out of range parameters cause the  cursor
				to be positioned at the respective screen 
				extremity. See "Origin Mode", 4.2.5.20

				Pv - cursor vertical position,  expressed
				as a decimal string.

				Ph  -   cursor    horizontal    position,
				expressed as a decimal string.

     4.2.5.7 HVP - Horizontal and Vertical Position	

	     ESC [ Pv ; Ph f	033 133 ** 073 *** 146

				Same effect as CUP - see 4.2.5.6

     4.2.5.8 DSR - Device Status Report

	     ESC [ 6 n 		033 133 66 156

				A  request  to  the   display   emulation
				firmware   to  report  back  the  current
				cursor position using a CPR sequence, see 
				Section 4.2.5.1

     4.2.5.9 IND - Index

	     ESC D 		033 104

				Moves the cursor position down  one  row,
				scrolling   if   necessary.   The  cursor
				horizontal position is unchanged.

     4.2.5.10 NEL - New Line 

	     ESC E 		033 105

				Moves the cursor to the first  column  of
				the   next   row   down,   scrolling   if
				necessary.

     4.2.5.11 RI - Reverse Index

	     ESC M 		033 115

				Moves the  cursor  up  one  row,  reverse
				scrolling   if   necessary.   The  cursor
				horizontal position is unchanged.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 12     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     4.2.5.12 DA - Device Attributes

	     ESC [ Pn c		033 133 * 143

				Pn - 0  or  not  present  is  used  as  a
				sequence generated by the user program to
				request  that   the   display   emulation
				firmware    report    back   the   device
				characteristics, using a DA  sequence  as
				defined below.

	     ESC [ ? 61;1 c	033 133 077 066 061 073 061 143

				Defines the  DECmate  II  as  a  Level  1
				Terminal   with   132  column  extension.
				Having been identified as such, the  user
				program  may  request more information by
			 	use of  the  Secondary  Device  Attribute
				Request.

	     ESC [ > Pn c	033 133 076 * 143

				Pn - 0 or not present is a  request  from
				the user program for transmission back of
				the Secondary Device Attribute  Response.
				The  resposnse for a DECmate II operating
				with its own internal  terminal  Firmware
				is:

	     ESC [ > 3 c	033 133 076 63 143

     4.2.5.13 ED - Erase in Display

	     ESC [ Pn J 	033 133 * 112

				Pn  -  a  parameter  defining  the  erase
				function.

	     Pn 		Erase Function

	     0 (060) or none    Erase from the current cursor position to 
				the end of the screen, inclusive.

	     1 (061) 		Erase from the start of the screen to the
				current cursor position, inclusive.

	     2 (062) 		Erase the entire screen.

	In all cases  the  cursor  position  is  unchanged  when  the  ED
	function has been completed.



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 13     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     4.2.5.14 EL - Erase in Line

	     ESC [ Pn K		033 133 * 113

				Pn  -  a  parameter  defining  the  erase
				function.

	     Pn			Erase Function

	      0 (060) or none   Erase from the current cursor position to
				the end of the current row, inclusive.

	      1 (061) 		Erase from the start of the  current  row
				to the cursor, inclusive.

	      2 (062) 		Erase the entire current row.

	"Current row" refers to that row on which the cursor is displayed
	when the EL command is given. In all cases the cursor position is
	unchanged when the EL function has been completed.

     4.2.5.15 DECKPNM - Keypad Numeric Mode

	     ESC > 		033 076

				In this mode  of  operation,  the  keypad
				keys  transmit  codes  that correspond to
				the symbols shown on the keys,  with  the
				exception   of  PF1-4.  The  cursor  keys
				transmit  ANSI  cursor  movement   ESCAPE
				sequences - see 4.2.5.20

     4.2.5.16 DECPAM - Keypad Application Mode

	     ESC = 		033 075

				In this mode the codes transmitted by the
				keypad keys change to the sequences shown
				below.

	Key		Keypad Numeric		Keypad Application
			Mode			Mode

	0		0	(060)		ESC O p (033 117 160)
	1		1	(061)		ESC O q (033 117 161)
	2		2	(062) 		ESC O r (033 117 162)
	3		3	(063)		ESC O s (033 117 163)
	4		4	(064)		ESC O t (033 117 164)
	5		5	(065)		ESC O u (033 117 165)
	6		6	(066)		ESC O v (033 117 166)
	7		7 	(067)		ESC O w (033 117 167)
	8		8	(070)		ESC O x (033 117 170)
	9		9	(071)		ESC O y (033 117 171)
	-		-	(055)		ESC O m (033-117 155)
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 14     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	,		,       (054)		ESC O 1 (033 117 154)
	ENTER		RET     (015)		ESC O M (033 117 115)
	PF1		ESC O P (033 117 120)   ESC O P (033 117 120)
	PF2		ESC O Q (033 117 121)   ESC O Q (033 117 121)
	PF3		ESC O R (033 117 122)   ESC O R (033 117 122)
	PF4		ESC O S (033 117 123)   ESC O S (033 117 123)

     4.2.5.17 SM - Set Mode

	ESC [ PS ; Ps ; ..... h        033 133 * 073 * ..... 154

	Set one or more operating parameters, specified by the  parameter
	string  Ps....,  as  defined  in  Section  4.2.5.19.  DEC Private
	parameters are specified by adding the character "?"  immediately
	after the CSI introducer (ESC [).

	i.e. the SM sequence for a DEC Private parameter is :

	ESC [ ? ;Ps ; Ps ; ...... l


     4.2.5.18 RM - Reset Mode

	ESC [ Pr ; Pr ; ...... l       033 133 * 073 * 073 ... 150

	Reset  one  or  more  operating  parameters,  specified  by   the
	parameter  string  Pr....,  as  defined  in Section 4.2.5.19. DEC
	Private parameters are specified  by  adding  the  character  "?"
	immediately after the CSI introducer (ESC [).

	i.e. the RM sequence for a DEC private parameter is :

	ESC [ ? Pr ; Pr ; ..... l

     4.2.5.19 ANSI Specified Parameters Applicable to SM and RM

	Parameter		Function 		Mnemonic

	   2 (062)	SET - turns OFF the keyboard    KAM	
			RESET - enables the keyboard	

	   4 (064)	SET-- selects insertion mode    IRM
			RESET - selects replacment mode	

	  12 (061 062)  SET - turns OFF local echo	SRM
			RESET - turns ON local echo

	  20 (062 060)  SET - enables Newline mode	LNM
			RESET - disable Newline mode

	  IRM		When  Insertion  Mode  is  set  to  Insert  (SM),
			characters  sent  to  the  screen for display are
			inserted  at  the  current  cursor  position  and
			characters to the right of the cursor position
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 15     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
			are pushed towards the  right  hand  end  of  the
			current  row.  As  characters moved right in this
			fashion move beyond the right  margin,  they  are
			lost.  When  Insertion  Mode is set to Replace, a
			character sent to the screen for display replaces
			any character at the current cursor position.

	SRM		When local echo is turned ON, characters typed on
			the  keyboard  are  displayed  on  the screen and
			transmitted to the application program. When this
			mode  is  turned  OFF  (normal),  the application
			program is responsible for echoing characters.

	LNM		When this mode is  enabled  (SET),  pressing  the
			RETURN  key  causes  both CR (015) and a LF (012)
	  		codes to be passed to  the  application  program.
			When  this mode is disabled (RESET), pressing the
			RETURN  key  causes  a  CR  code   only   to   be
			transmitted.

     4.2.5.20 DEC Private Parameters Applicable to SM and RM

	Parameter		Function 		Mnemonic

	   1 (061)	SET - enables Cursor Key Mode   DECCKM
			RESET - disables "    "   "

	   2 (062)	SET - enables ANSI mode		DECANM
			RESET - enables VT52 mode

	   3 (063)	SET - enables 132 column mode   DECCOLM
			RESET - enables 80 column mode

	   4 (064)	SET - enables smooth scroll	DECSCLM
			RESET - enables jump scroll

	   5 (065)	SET - gives white background	DECSCNM
			RESET - gives black background

	   6 (066)	SET - enables Origin Mode	DECOM
			RESET - disables Origin Mode

	   7 (067)      SET - enables auto-wrap 	DECAWM
		 	RESET - disables auto-wrap

	   8 (070)	SET - keyboard keys auto-repeat DECARM
			RESET - no auto-repeat

	  25 (062 065)  SET - the cursor is visible     DECCUR
			RESET - the cursor is invisible

	 Cursor key mode - the  four  cursor  keys  may  be  selected  to
			transmit  either  ANSI cursor key movement ESCAPE
			sequences or Application ESCAPE sequences by this
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 16     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			SM/RM parameter if Keypad Application Mode is SET
			-  see  4.2.5.16.  If  Keypad Application Mode is
			SET, the  alternative  code  sequences  that  the
			cursor keys can transmit are as follows :

	Cursor Key 	Cursor Key Mode		Cursor Key Mode
			RESET			SET

	 UP arrow	ESC [ A (033 133 101)   ESC O A (033 117 101)
	 DOWN arrow 	ESC [ B (033 133 102)   ESC O B (033 117 102)
	 RIGHT arrow	ESC [ C (033 133 103)   ESC O C (033 117 103)
	 LEFT arrow	ESC [ D (022 133 104)   ESC O D (033 117 104)

	ANSI/VT52 Mode -If  ANSI  Mode  is  SET,  the  display  interface
			responds  to  the  ANSI  set  of ESCAPE sequences
			defined in Section 6.6

			If ANSI  Mode  is  RESET,  i.e.  VT52  Mode,  the
			display  interface  responds  to  the VT52 set of
			ESCAPE sequences defined in Section 7.

	Origin Mode -  	If this mode  is  RESET,  the  screen  origin  is
			always  located  at  the upper left corner of the
			screen and cursor addressing is absolute  wrt  to
			screen  physical location. If Origin Mode is SET,
			the screen origin is relative to the start of the
			current scrolling region and the cursor cannot be
		  	positioned outside of the scrolling region.  When
			the  Mode  is changed, the cursor is repositioned
			at the new origin.

	Autowrap -	If this Mode is RESET,  characters  sent  to  the
			display  when  the  cursor  is  positioned at the
			rightmost column  of  a  row  overwrite  previous
			data,  if  any, at that location. If this Mode is
			SET, sending new characters at  this  point  will
			cause an automatic NEWLINE to occur.

     4.2.5.21 SCS - Select Character Set

	The DECmate II  is  able  to  display  characters  and  character
	graphics from data stored in a character generator ROM or in RAM.
	The ROM provides the bit patterns for the  standard USASCII,  UK,
	DEC  Multinational, Special Graphics and Katakana character sets.
	The RAM may be loaded by the user to provide a  wide  variety  of
	other  Foreign  Language  characters  or extensions to the normal
	display capabilities, e.g. scientific symbols.

	DECmate II can support both 7-bit and 8-bit codes for display. In
	its  normal  mode  of  operation,  codes received for display are
	assumed to be 7-bit and are masked to 7-bit prior to any  display
	translation  occurring.  If  DEC 8-bit mode is selected, the full 
	8-bits of an input code have significance *.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 17     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	In interpreting input codes  for  display,  there  are  two  code
	groups  defined:-  GL, codes in the range 041 - 176 and GR, codes
	in the range 241 - 376. At any time GL may be invoked to  be  any
	one  of four sets G0, G1, G2 or G3 and GR to any one of G1, G2 or
	G3. In turn G0 - G3 may be  designated  to  be  any  one  of  the
	possible  character  reportoires. Character reportoires supported
	by DECmate II at present are :

	* Current firmware implements ONLY Terminal Level 1, any  attempt
	to change to 8-bit display mode is ignored.

		USACSII
		LINE DRAWING (SPECIAL GRAPHICS)
		DEC MULTINATIONAL SUPPLEMENTAL

	These are the reportoires recommended for future use. UK  is  now
	considered a part of DEC Multinational Supplemental.

		UK
		FRENCH
		FRENCH-CANADIAN
		DUTCH
		GERMAN

	These are included (together with  any  other  Foreign  Languages
	that may be added) for compatibility with DECmate I and any other
	software that uses the obsolete language mapping of the VTl00W.

		JIS ROMAN
		KATAKANA

	These are extensions to the  DEC  8-bit  Multinational  character
	representation (see DEC Std. 169)

		ALTERNATE ROM A
		ALTERNATE ROM SPECIAL GRAPHICS
		USER DEFINED (RAM)

	The  first  two  of  these  are  again  included  for   backwards
	compatibility,  the  User  defined RAM is a new feature whose use 
	and designation is TBD.

	For further details on the future use of character sets and those
	to be supported in future DEC products, refer to DEC Std. 169.

	Following self test, G0, G1 and G3 are set to USASCII and  G2  is
	set  to  DEC  Multinational  Supplemental. The loadable character
	generator RAM is cleared.

	The G0 - G3 sets  may  be  designated  by  the  following  ESCape
	sequences :


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 18     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	ESC ( Fx	033 050 Fx	Designate the G0 set

	ESC ) Fx	033 051 Fx	Designate the G1 set

	ESC * Fx	033 052 Fx	Designate the G2 set

	ESC + Fx	033 053 Fx	Designate the G3 set

	Where Fx is a parameter defining one of the  available  character
	reportoires as follows :

		Fx		Character reportoire

		A (101)	  	UK set
		B (102)		USASCII
		I (111)		JIS KATAKANA
		J (112)		JIS Roman Graphic
		K (113)		German
		R (122)		French
		0 (060)		Special graphics
		1 (061)		Alternate character ROM
		2 (062)		Alternate character ROM, special graphics
		3 (063)		French-Canadian 
		4 (064)		Dutch
		< (074)		DEC 8-bit Multinational Supplemental

	GL and GR may be invoked as G0 - G3 in  either  Single  Shift  or
	Locking  Shift.  In  Single  Shift,  the  next  graphic character
	received following the receipt of the Single Shift Code  will  be
	displayed  using  the  newly  selected  character  reportoire, in
	Locking Shift, all graphic characters received following  receipt
	of  the  Locking  Shift code will be displayed using the selected
	character reportoire.

	Single Shift Invokation

	SS2  -  ESC N   (033 116)       Invoke GL to G2 
	SS3  -  ESC O   (033 117)	Invoke GL to G3

	There are no Single Shift invokation ESCape sequences for GR, nor
	for  GL  to G0 or G1. In 8-bit mode GL may be invoked as a single
	shift to G2 or G3 on receipt of the following :-

	SS2		(216)		Invoke GL to G2
	SS3 		(217)		Invoke GL to G3

	Locking Shift Invokation

	LS2  - ESC n    (033 156)	Invoke GL to G2
	LS3  - ESC o    (033 157)	Invoke GL to G3

	LS1R - ESC ~    (033 176)	Invoke GR to Gl
	LS2R - ESC }    (033 175)	Invoke GR to G2	
	LS3R - ESC |    (033 174)	Invoke GR to G3
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 19     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	There is no ESCape sequence to Invoke GL to  G0  or  G1,  instead
	this function is performed by Control Codes :

	LS0  -  SI      (017) 		Invoke GL to G0 
	LS1  -  SO 	(016) 		Invoke GL to G1

	Appendix A defines the standard character patterns.

     4.2.5.22 SGR - Select Graphic Rendition

	ESC [ Pn ; Pn ;..... m 	 	033 133 * 073 * 073 ... 155

	Establishes  the  attributes  to  be   appended   to   subsequent
	characters according to the parameter string Pn .., as follows :

		Pn	Action

		0 (060) All attributes OFF, normal character display
		1 (061) Display at increased intensity
		4 (064) Display with underline
		5 (065) Display blinking
		7 (067) Display as a negative (reverse) image

	There are four display intensity levels for  a  given  brightness
	setting,  these  are  0  or  no  display  and  1,  2,  3  - being
	sequentially increasing  levels  of  intensity.  Combinations  of
	attributes result in displays as defined below :

		Pn	Character/Underscore	Background

		0	Level 2			Level 0
		1	Level 3			Level 0
		4	Level 2	 * 		Level 0
		5	Level 2/level 1		Level 0
		1;4	Level 3	 * 		Level 0
		1;5	Level 3/level 2  *	Level 0
		4;5	Level 2/level 1  *	Level 0
		1;4;5   Level 3/level 2		Level 0
		7 	Level 0			Level 2 
		1;7 	Level 0			Level 3
		4;7	Level 0			Level 2	 *
		5;7	Level 0			Level 2/level 1
		1;4;7   Level 0			Level 3	 *
		1;5;7   Level 0			Level 3/level 2  *
		4;5;7   Level 0			Level 2/level 1  *
		1;4;5;7 Level 0			Level 3/level 2

	* these display levels alternate at the character BLINK rate.

     4.2.5.23 DECWDL - Double Width Row

	ESC $ 6		033 043 066

			This causes the  row  containing  the  cursor  to
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 20     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
			become  a  double  width   character   row.   All
			characters  to  the  right  of  the centre of the
			screen are lost, the display becomes either 40 or
			66 columns wide. The cursor position is unchanged
			unless it was previously  to  the  right  of  the
			screen  centre, in which case it is positioned at
			the new right margin.

     4.2.5.24 DECDHL - Double Height Row

	ESC # 3		033 043 063

			This causes the  row  containing  the  cursor  to
			become  the  top  half of a double height, double
			width character row.

	ESC # 4		033 043 064

			This causes the  row  containing  the  cursor  to
			become the bottom half of a double height, double
			width row.

			These sequences must be used  in  pairs  and  the
			same  character  data  must be placed in the same
			positions on each of the  rows  to  form  correct
			double height characters. An attempt to display a
			standalone top half or bottom half  of  a  double
			height   row  will  result  in  an  unpredictable
			display. If the row was previously single  width,
			all  characters to the right of the centre of the
			screen are lost. The cursor position is unchanged
			unless  it  was  previously  to  the right of the
			screen centre, in which case it is positioned  at
			the new right margin.

     4.2.5.25 DECSWL - Single Width Row

	ESC # 5		033 043 065

			This causes the  row  containing  the  cursor  to
			become  single  width,  single height. The cursor
			position is unchanged, i.e.  it  remains  at  the
			same column number.

     4.2.5.26 DECSTBM - Set Top and Bottom Margins

	ESC [ Pn ; Pm r 033 133 ** 073 ** 162

			This sets the top and bottom  screen  margins  to
			define   the  scrolling  region.  Parameters  are
			expressed as decimal strings.

			Pn - the number of the top row in  the  scrolling
			     region.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 21     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			Pm  -  the  number  of  the  bottom  row  in  the
			       scrolling region.

	The minimum scrolling region is two rows, the top row number must
	be lower than the bottom, see Origin Mode - 4.2.5.20

     4.2.5.27 HTS - Horizontal Tab Set

	ESC H 		033 110

	Set one horizontal stop at the current cursor position.

     4.2.5.28 TBC - Tab Clear

	ESC [ Pc g 	033 133 *** 147

	Clear horizontal tab stop(s), defined by parameter Pc.

		Pn	Action

		0 (060) Clear  horizontal  tab  at  the  current   cursor
			position, the default case with no parameter.

		3 (063) Clear all horizontal tabs.

     4.2.5.29 DECSC - Save Cursor (DEC Private)

	ESC 7 		033 067

			This sequence causes the current cursor position,
			graphic  rendition and active character set to be
			saved.

     4.2.5.30 DECRC - Restore Cursor (DEC Private)

	ESC 8 		033 070

			This sequence causes the previously saved  cursor
			position,  graphic rendition and character set to
			be restored.

     4.2.5.31 DECPRS - Print Screen (DEC Private)

	ESC [ i 	033 133 151

			This sequence is ignored.

     4.2.5.32 DECLL - Load LEDS (DEC Private)

	ESC [ Ps q 	This sequence has no effect on DECmate II.

     4.2.5.33 DECALN - Screen Alignment Display (DEC Private)

	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 22     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	ESC g 8 	033 043 070

			This sequence fills the entire  screen  with  the
			screen alignment pattern.

     4.2.5.34 IL - Insert Line

	ESC [ Pn L	033 133 *** 114

			This sequence causes Pn (expressed as  a  decimal
			string)  lines of blanks to be inserted below the
			current line. Lines below the  current  line  are
			scrolled down. This sequence has no effect if the
			cursor is positioned outside the scrolling region.

     4.2.5.35 DL - Delete Line

	ESC [ Pn M 	033 133 *** 115

			This sequence causes Pn (expressed as  a  decimal
			string)  lines  to  be  deleted below the current
			line. As lines are deleted, blank lines scroll in
	 		from  the  botton. This sequence has no effect if
			the cursor is  positioned  outside  the  scroiing
			region.

     4.2.5.36 DCH - Delete Character

	ESC [ Pn P	033 133 *** 120

			This sequence causes P characters  (expressed  as
			a  decimal  string)  to te deleted, starting with
			the character at the cursor position and deleting
			towards  the right hand margin. As characters are
			deleted, characters to the right  of  the  cursor
			move to the left to fill the space created by the
			 deletion.   See  Set/Reset  Mode  for  Character
			Insertion. 

     4.2.6 VT52 Mode ESCAPE sequences

	When the DECmate II is placed into VT52 Mode - see  4.2.5.20  for
	details  of  this  SM  parameter,  the  following  set  of ESCAPE
	sequences become recognised, replacing those  listed  in  Section
	4.2.5.*

     4.2.6.1 Cursor Up

	ESC A		The cursor is move up by one row. If  an  attempt
			is  made  to move the cusor above the top margin,
			it is positioned at the top  margin.  The  cursor
			horizontal position does not change.

	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 23      Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     4.2.6.2 Cursor Down

	ESC B 		The cursor is move down by one row. If an attempt 
			is  made  to  move  the  cursor  below the bottom
			margin, it is positioned at  the  bottom  margin.
			The cursor horizontal position does not change.

     4.2.6.3 Cursor Right

	ESC C		The cursor is moved one column to the  right.  If
			an  attempt is made to move the cursor beyond the
			right margin,  it  is  positioned  at  the  right
			margin.  The  cursor  vertical  position does not
			change.

     4.2.6.4 Cursor Left

	ESC D 		The cursor is moved one column to the left. If an
			attempt is made to move the cursor byond the left
			margin, it is positioned at the left margin.  The
			cursor vertical position does not change.

     4.2.6.5 Enter Graphics Mode

	ESC F 		The  special  graphics  character  set   of   the
			standard  character  ROM  are  selected - see the
			ANSI SCS sequence ESC ( 0 - Section 4.2.5.20

     4.2.6.6 Exit Graphics Mode

	ESC G 		The character set reverts to the standard USASCII
			-  see  ANSI  SCS  sequence  ESC  (  B  - Section
			4.2.5.20

     4.2.6.7 Cursor to Home

	ESC H 		The cursor is positioned at HOME,  the  top  left
			corner of the screen.

     4.2.6.8 Reverse Line Feed

	ESC I 		Moves the cursor up one row without changing  the
			horizontal    position,   reverse   scrolling  if
			necessary.

     4.2.6.9 Erase to End of Screen

	ESC J 		Erases all character positions from  the  current
			cursor  position  to the end of screen inclusive.
			The cursor position remains unchanged.

     4.2.6.10 Erase to End of Line

	ESC K 		Erases all character positions from  the  current
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 24     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
			cursor position to the end of  the  current  row.
			The cursor position remains unchanged.

     4.2.6.11 Direct Cursor Address

	ESC Y Pr Pc	The cursor is moved to the screen location  given
			by  the  two  ASCII character codes following the
			Direct  Cursor  Addressing   delimiter   (Y)   as
			follows:

			the row  and  column  parameters  are  formed  by
			adding  037 to the actual row and column numbers,
			and sending that  pair  of  ASCII  characters  so
			formed  as  the next two characters following the
			upper case Y, e.g.  to  position  the  cursor  at
			screen  position  2;5  the sequence sent would be 

			ESC Y     !     $
				(041=2 044=5)

     4.2.6.12 Identify

	ESC Z		This causes the  display  emulation  firmware  to
			return  the  following identification sequence to
			the user program :

			ESC / Z

			indicating  that  it  is  a  VT100  type   device
			emulating a VT52.

     4.2.6.13 Enter Alternate Keypad Mode

	ESC = 		This causes the auxiliary keypad keys to transmit 
			ESCAPE   sequences   for   Application  Dependent 
			Purposes.

     4.2.6.14 Exit Alternate Keypad Mode

	ESC > 		This causes the auxiliary keypad to transmit  the
			ASCII  codes  for  the  functions  or  characters 
			engraved on the keys.

     4.2.6.15 Enter ANSI Mode

	ESC < 		This causes the display emulation firmware to  go
			into  ANSI  mode  and  interpret ESCAPE sequences 
			defined in Section 4.2.5.* (VT100 Mode).

     4.3 Keyboard

	The LK2XX keyboard implements the functions of keyboard scanning,
	debouncing,  autorepeat  etc.  and  transmits  key  codes  to the
	DECmate II to indicate keydown conditions. Following decoding  in
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 25     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Control Panel Memory, the resulting keyboard  character  code  is
	passed  to the user program. Data transmission to the keyboard is
	provided to allow certain keyboard parameters to be set up,  e.g.
	keyclick  loudness. The following list of instructions is for use
	by the keyboard handling code in Panel Memory  and  not  for  the
	user.  The  characteristics  of this interface are fixed with the
	following parameters :

	Speed 		4800 baud 	Character	8 data bits

     4.3.1 Instruction List

	Instruction	Description

	6050		Set keyboard input flag.
	6051	  	Skip on keyboard input flag, clear it if set.	
	6052		Clear the AC.
	6053		NOP
	6054		Inclusive OR keyboard input data  with  AC<4:11>,
			result to AC<4:11>, AC<0:3> undefined.
	6055		Set/clear keyboard input  interrupt  enable  with
			AC<ll>. AC unchanged following this instruction.
	6056	 	Clear  AC,  then  read  keyboard  input  data  to
			AC<4:11>, AC<0:3> undefined.
	6057		NOP
	6110		Set keyboard output flag.
	6111		Skip on keyboard output flag, clear it if set.
	6112		NOP
	6113		NOP
	6114		AC<4:11> to the keyboard, AC unchanged.
	6115		Set/clear keyboard output flag  interrupt  enable
			with   AC<ll>.   AC   unchanged   following  this
			instruction.
	6116		AC<4:11> to the keyboard, AC cleared.
	6117		NOP

     4.4 Disk Interface

	The disk storage integral to the DECmate  II  is  a  single  RX50
	floppy  disk  drive  with a second RX50 optional, see Section 2.3
	for capacity details.

	The disk may be used in either 8 or 12 bit modes. In  both  modes
	the  disk  format  is  the  same,  the  differences  are  in  the
	utilization of the available capacity  and  the  format  of  data
	transfer  between  the  user  program and the disk controller. In
	8-bit mode the transfers are as 8-bit bytes to/from AC<4:ll>  and
 	the full disk capacity is available. In 12-bit mode the transfers
	are full word transfers with an  effective  sector  size  of  256
	12-bit words, the disk controller still reads and writes 512 byte
	sectors, reformatting the 12-bit data as it is received from  the
	user and creating 12-bit words prior to transferring read data to
	the user. The unused bits in each sector are discarded.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 26     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Instruction     Function

	SEL - 6750 	Select a disk pair.

		If the RX02 Adaptor is not present (see section 5.4)

			AC 11
			    0   Select RX50 drive pair A
	 		    1   Select RX50 drive pair B

	 	If the RX02 Adaptor is present (see section 5.4)

	 		AC 00   11
			    0   0/1	Select RX50 drive pair A/B
			    1    0	Select RX02 drive pair A/B
					(See RX02 adaptor description for
					details)

	 		The  first  pair  of  RX50  drives  (pair  A)  is
	 		selected  by  CAF and following self test. The AC
	 		is unchanged by this IOT.

	LCD - 6751	Load the Command Register.

			This instruction must only be issued when DONE is
			true.  The  contents of the AC are transferred to
			the disk controller to be used as a command.  The
			AC is cleared following this instruction.

			AC(5)=0 selects 12-bit mode of operation.
			AC (5)=1 selects 8-bit mode of operation.
			12-bit  mode  is  selected  by  CAF,  RXINIT  and
			following self test.

			AC(7)=0 selects the left drive (drive 0 - RX50).

			AC(7)=1 selects the right drive (drive 1 - RX50).

			AC<8:10> define the command to be executed by the
			disk controller as follows :

			Command	        	AC 8  9  10	

			Read Sector		   0  1   1
			Write Sector		   0  1   0
			Fill Buffer		   0  0   0
			Empty Buffer		   0  0   1
			Read Status		   1  0   1
			Read Error Code		   1  1   1
			Write Sector with
			Deleted Data mark	   1  1   0
			No Operation 		   1  0   0
			AC<O:4, 6, 11> have no effect.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 27     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	XDR - 6752	Transfer Data.

			This IOT performs data interchange between the AC
			and  the  disk controller, the transfer direction
			is controlled by the disk controller depending on
			the  command  being  executed  which controls the
			data direction line OUT, and  the  state  of  the
			DONE interface signal.

			1. DONE false and OUT Low (data from disk)

			   12-bit  Mode  :  the  next  word  of  data  is
			   transferred   from   the  disk  controller  to
			   AC<0:11>, the  AC  is  cleared  prior  to  the
			   transfer.
			   8-bit  Mode  :  the  next  byte  of  data   is
			   transferred   from  the  disk  controller,  an
			   inclusive OR is performed  with  AC<4:11>  and
			   the  result  placed  in  AC<4:11>. AC<0:3> are
			   unchanged.

			2. DONE false and OUT High (transfer to disk)

			   12-bit Mode : AC<0:11> are transferred to  the
			   disk   controller.   The   AC   is  unchanged.
			   8-bit Mode : AC<4:11> are transferred  to  the
			   disk controller. The AC is unchanged.

			3. DONE true

			   This IOT now performs a  transfer  to  the  AC
			   from   the   disk  controller.  8/12-bit  Mode
			   determines whether an 8  or  12  bit  transfer
			   occurs.

	STR - 6753	Skip on Transfer Request transition.

			If  the  Transfer  Request  interface  line   has
			changed  from  false  to  true since this IOT was
			last issued, the next sequential instruction will
			be skipped. If the skip does occur the transition
			detector will be reset. The AC  is  unchanged  by
			this IOT.

	SER - 6754	Skip on Error transition.

			If the Error  interface  line  has  changed  from
			false to true since this IOT was last issued, the
			next sequential instruction will be  skipped.  If
			the skip does occur, the transition detector will
			be reset. The AC is unchanged by this IOT.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 28     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	SDN - 6755	Skip on Done transition.

			If the Done interface line has changed from false
			to  true since this IOT was last issued, the next
			sequential instruction will be  skipped.  If  the
			skip  does occur, the transition detector will be
			reset. The AC is unchanged by this IOT.

	INTR - 6756	Set/clear Interrupt Enable.

			If AC(11)=0, the Interrupt Enable  for  the  DONE
			transition detector to cause an interrupt will be
			cleared. If AC(ll)=l, it will be set. The  AC  is
			unchanged by this IOT.

			Power-on and CAF clear the Interrupt Enable.

	RXINIT - 6757   Initialize.

			The following are cleared :

				Done transition flag
				Transfer Request transition flag 
				Error transition flag
				Done Interrupt Enable

			Drive pair select is set to Unit A.
			All drives are caused  to  initialize,  the  disk
			controller is reset.
			At the end  of  drive  initialization,  the  Done
			transition   flag   will   be   set  to  indicate
			completion.

     4.5 Printer

	The  printer  interface  is  a  standard,  full  duplex,   serial
	asynchronous  port. The receive capability is provided to support
	printers that use an XON-XOFF protocol to signal  when  they  are
	able/unable to accept new data from the DECmate II.

	Instruction	Description
	6320		Set printer port input flag
	6321		Skip on printer port input flag, clear it if set
	6322		Clear the AC 
	6323		NOP
	6324		Inclusive OR the printer  input  port  data  with
			AC<4:11>,  place  the result in AC<4:11>. AC<0:3>
			are unchanged. 
	6325		Set/clear printer  port  input  interrupt  enable
			with AC(ll).
	6326		Clear the AC then transfer the printer port input
			data to AC<4:11>.
	6327		NOP
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 29     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	6330		Set printer port output flag
	6331		Skip on printer port output  flag,  clear  it  if
			set.
	6332		NOP
	6333		Set the printer port baud rate for both input and 
			output as follows:

	AC<8:11>	Baud Rate       AC<8:11>	Baud Rate

	   0 	    	    50	  	  10		  1800
	   1		    75	  	  11	 	  2000
	   2		   110		  12		  2400
	   3		   134.5	  13		  3600
	   4		   150		  14		  4800
	   5		   300		  15		  7200
	   6		   600		  16		  9600
	   7		  1200		  17		 19200

	6334		Transfer AC<4:11> to the printer, leaving the  AC
			unchanged.
	6335		Set/clear interrupt enable for the  printer  port
			output with AC(11). The AC is unchanged.
	6336		Transfer AC<4:11> to the printer, then clear  the
			AC.
	6337		NOP

     4.6 Communications

	The communications controller  provides  a  single,  full  duplex
	serial port  for either asynchronous or synchronous operation. In
	the synchronous mode of operation either  bit  or  byte  oriented
	protocols may be selected. Full modem control is provided.

     4.6.1 Instruction List

	Three device codes are used to control the  communications  port,
	30,  31  and  36. 30 is associated with transferring receive data
	from the communications controller chip to the AC, 31 with moving
	data   from   the   AC   to  the  communications  controller  for
	transmission and 36 for modem control functions.

	The communications controller chip has several internal registers
	which  must be initialised prior to using the communications port
	in a particular mode. Following self-test, the  port  is  set  to
	asynchronous mode, with parameters as shown below:

	        Baud Rate       -	1200
		Data elemenets  -	8
		Stop bit(s)     -	1
		Parity	   	-	None



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 30     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Instruction     Description

	6360 	Set Modem Change Flag. 		Note 1. 
	6361 	Skip on Modem Change Flag, clear it if set. 
	6362 	Load Modem Control Register from AC<4,7:11>

	AC Bit  Function 			Circuit #	Note 2

	  04	Enable Terminal Timing		103/116
	  05	Select Internal/External Timing 		Note 3
	  07	Set Request to Send		105
	  08	Set Data Terminal Ready		108.2
	  09	SR				111
	  10	Enable Local Loopback		141
	  11	Enable Remote Loopback

	6363		Set Baud Rate from AC<4:11> as shown  in  4.5  in
			the printer description (6333 definition)

	6364		Read Modem Status to AC<7:11>

		AC Bit  Modem Line			Circuit #. Note 2
		  07
		  08 					125
		  09 					109
		  10 					107
		  11 					106

	6365		Set/clear Modem Change Flag Interrupt Enable with
			AC<ll>. The AC is unchanged by this instruction.
	6366		Access   Communications    Controller    Internal
			Register

	Following power-on or after a RESET,  this  instruction  is  used
	together  with  the  Data Field to write the communicatiions chip
	Control Register R0 and in so doing may specify another  internal
	register  for  access,  Control  Registers <0:7>, which are write
	only and Status Registers <0:1> which are  read  only.  Whichever
	register is specified will be the register accessed the next time
	that  this  instruction  is  issued,  following  access  to   the
	specified register, access reverts to Control Register R0.

     Note 1. This flag is set if any one of the following signals changes
		state :
			Signal		Circuit #

			Carrier 	109
			Ring 		125
			Data Set Ready  107
			Clear to Send   106

	  2. Circuit numbers refer to CCITT circuits.
	  3. Internal timing must always be selected for asynchronous
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 31     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	operation, send and receive baud rates are controlled by the  IOT
	6363, as described above.

     4.6.2 Internal Registers

     4.6.2.1 Control Register R0

	This register has three fields, used as follows :

	Field A - Register Pointer.

	AC<9:11>  specify  the  register  to  be  accessed  on  the  next
	execution  of  this  instruction.  If the register specified is a
	WRITE register, AC<00> must be set to 0 for this instruction.  If
	the register is a READ register, AC<00> must be set to 1 for this
	instruction.

	Field B - Command

	AC<6:8> specify one of a set of  commonly  used  commands  to  be
	executed :

	AC<6:8>		Command
	   000		No operation
	   001	  	Send ABORT - used when operating  in  SDLC  mode,
			causes  the  SDLC  ABORT  code to be transmitted,
			destroying any data  currently  in  the  transmit
			buffer.  Following transmission of the ABORT, the
			transmitter reverts to the IDLE phase.
	   010	 	Unused 
	   011		Communications  Port  Reset.  The  communications
			controller and Modem control lines are set to the
			same initial state as following power-on.
	   100		Enable  Interrupt   on   next   character.   When
			operating   in   Interrupt   on   First  Received
			Character Mode,  this  command  may  be  used  to
			re-enable  the  interrupt  for  the next received
			character (generally at the end of amessage)
	   101		Reset Pending Transmitter Interrupt.  Clears  the
			interrupt  condition  caused  by  the transmitter
			buffer becoming empty.
	   110		Error Reset, used to reset an interrupt caused by
			detection of a parity error or overrun error.
	   111		End  of  Interrupt,  resets  the   communications
			controller  chip  internal  priority  network  to
			allow for a lower priority interrupt.

	Field C - CRC control commands

	AC<4:5> specify the operating mode of the CRC generator/checker.



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 32     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
	AC<4:5>		CRC Mode
	   0 0		No operation
	   0 1		Reset CRC receiver check logic
	   1 0		Reset CRC transmitter generator logic
	   1 1		Reset Idle/CRC latch, allows transmission of  the
			CRC   field   when  transmitter  underrun  occurs,
			followed by idle characters.

     4.6.2.2 Control Register R1

	This register is loaded from the AC as follows :

	AC <4:6>	0
	   <7:8>
	    0 0		Disable Receive Data interrupts
	    0 1		Interrupt  only  on  the  first   data  character
			received following this instruction
	    1 0		Interrupt on all data characters received and  on
			errors
	    1 1		Interrupt on received data characters

	AC <9>		0
	AC <10>		Enable interrupts on  transmit  buffer  empty  or
			when the transmitter enters the Idle phase.
	AC <11>		Enable interrupts on the following :
			SDLC ABORT detection or termination
			Idle/CRC latch ebcoming set (CRC being sent)
			Entering or leaving synchronous Hunt Phase break
			detection or termination

     4.6.2.3 Control Register 2

			This register has no relevant bits for DECmate II
			operation  of the communications controller chip,
			if it is ever written, it must  be  written  with
			all zeroes.

     4.6.2.4 Control Register 3

	Loaded from AC<4:11> as follows :

	AC <4:5>	Select data bits per character for receive data

	    0 0		5 bits
	    0 1		7 bits
	    1 0		6 bits	
	    1 1		8 bits
	AC <6>		0
	AC <7>		Enter Sync Hunt Phase
	AC <8>		Enable receiver CRC. Used in  character  oriented
			protocols    to   selectively   exclude   certain
			characters from the CRC calculation.  There is  a
			one  character  delay between a receive character
			becoming available  for  reading  and  its  being
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 33     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			presented to  the  CRC  logic,  allowing  a  full
			character time to decide whether to exclude it or
			not.
	AC <9>		Enable Address Search Mode. In SDLC Mode, setting
			this  bit  inhibits  character assembly until the
			8-bit   character   (secondary   address   field)
			following  the starting flag of a message matches
			either  the  address  programmed   into   Control
		 	Register R6 or the global address 11111111.
	AC <10>		Sync Character Load Inhibit. In synchronous mode,
			setting  this  bit  prevents sync characters from
			being loaded into the receiver buffer.
	AC <11>		Receiver Enable, starts  the  receiver  following
			all initialization.

     4.6.2.5 Control Register 4

	Loaded from AC<4:11> as follows :

        AC <4>		0
	AC <5>		1
	AC <6:7>	Select operating mode for synchronous operation

	    0 0		8-bit    internal    synchronisation    character
			(MONOSYNC)
	    0 1		16-bit   internal    synchronisation    character
			(BISYNC)
	    1 0		SDLC
	    1 1		Illegal

	AC <8:9>	Select synchronous/asynchronous mode

	    0 0		Synchronous mode, see AC <6:7>
	    0 1		Asynchronous mode, 1 stop bit
	    1 0		Asynchronous mode, 1.5 stop bits
	    1 1		Asynchronous mode, 2 stop bits
			Note: the  above  stop  selections  are  for  the
			transmitter  only, the receiver always checks for
			a single stop bit.

	AC <10:11>	Parity select

	    0 0		No parity check or generate.
	    O 1	 	 "    "     "    "    "
	    1 0		Check/generate odd parity
	    1 1		Check/generate even parity

     4.6.2.6 Control Register 5

	loaded from AC <4:11> as follows :

	AC <4>		0

	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 34     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	AC <5:6>	Select transmit data bits/character
	    0 0		5 bits or less - see Table II
	    0 1		7 bits
	    1 0		6 bits
	    1 1		8 bits
			For 5 bits per character or less, the  format  of
			the  data  loaded into the transmitter determines
			the actual data word length as below :

	AC 4 5 6 7 8 9 10 11	Data bits/character

	   1 1 1 1 0 0  0  D		1
	   1 1 1 0 0 0  D  D		2
	   1 1 0 0 0 D  D  D 		3
	   1 0 0 0 D D  D  D		4
	   0 0 0 D D D  D  D 		5

	AC <7>		Set the transmit data line to the spacing  state,
			used to send the BREAK condition.
	AC <8>		Enable   the   transmitter,   set    after    all
			initialization has been completed.
	AC <9>		Select CRC polynomial
				    16    12    5
	    0		CRC-CCITT (x   + x   + x  + 1)
				 16    15    2
	    1		CRC-16 (X   + x   + x  + 1)
	AC <10>		0
	AC <11>		Enable/disable CRC  generation  on  the  transmit
			data stream.

     4.6.2.7 Control Register 6

	loaded from AC <4:11> with SYNC byte 1, used as follows :

	MONOSYNC	the 8-bit SYNC character that is  transmitted  in
			the Idle phase 
	BISYNC		the least  significant  (first)  8  bits  of  the
			16-bit   receive   and  transmit  synchronisation
			field.
	SDLC		the  secondary  address  value  matched  to   the
			Secondary Address Field of the SDLC frame when in
			Addresss Search Mode.

     4.6.2.8 Control register 7

	loaded from AC <4:11> with SYNC byte 2, used as follows :

	MONOSYNC	8-bit SYNC character matched by the-receiver
	BISYNC		the most  significant  (second)  8  bits  of  the
			16-bit   receive   and  transmit  synchronisation
			field.
	SDLC		the AC value must be set to 01111110.

	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 35     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     4.6.2.9 Status Register 0

	The following information is loaded to AC <4:11> :

	AC <4>		If operating in asynchronous mode, indicates that
			a  BREAK  has  been  received.  If  operating  in
			synchronous SDLC mode, that an ABORT sequence has
		 	been received.
	AC <5>		Indicates the state of the Idle/CRC latch used in
			synchronous modes.
	AC <6)		0
	AC <7>		If operating in asynchronous mode - 0
			If operating in synchronous mode a zero indiactes
			that the receiver is in the receive data phase, a
			one indicates the sync hunt phase.
	AC <8>		0	
	AC <9>		Transmit buffer empty
	AC <10>		Interrupt pending
	AC <11>		Received character avalilable
	AC <0:3 >	Undefined

     4.6.2.10 Status Register 1

	the following information is loaded into AC <4:11> :

	AC <4> 		End of  SDLC  Frame;  when  in  SDLC  Mode,  this
			indicates  that  the  End  OF Frame flag has been
			received and that the CRC error flag and  residue
			code  are  valid, This flag is reset on the first
			character of the next message frame.
	AC <5> 		In  asynchronous  mode,  this  flag  is  set   to
			indicate  that  a framing error has been detected
			on the received data. In synchronous modes,  this
			bit indicates the current result of comparsion of
			the computed CRC value and the appropriate  check
			value. It is usually set to a one. 
	AC <6>		A receive overrun has occurred.
	AC <7>		Parity check is  enabled  and  a  receive  parity
			error has been detected.
	AC <8:10> 	SDLC Residue Code. The data portion  of  an  SDLC
			message   is   terminated  by  an  End  of  Frame
			character. It may consist of any number  of  bits,
			not  necessarily an integral number of characters,
			thus  when  the  End  of   Frame   condition   is
			indicated,  these  three  bits indicate where the
			data field terminated.
	AC <11> 	When operating in  asynchronous  mode,  this  bit
			indicates  when  the  transmitter  buffer and the
			output  shift  register  are   both   empty.   In
			synchronous mode, it is always set to a one.
	AC <0:3> 	Undefined


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 36     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     4.6.3 Data Transfer

     4.6.3.1 Input

	6300		Set this device code flag
	6301		Skip on any  communications  flag  condition  and
			clear the flag, if set. Flag conditions are :
			Transmit buffer empty
			Receive character available
			Errors; parity, overrun, framing
			Special synchronous conditions, if enabled
	6302		NOP
	6303		NOP
	6304		Transfer the contents of the receive buffer to AC
			<4:11>
	6305		Enable interrupts for this device code, using  AC
			<11>
	6306		Transfer the contents of the receive buffer to AC
			<4:11>
	6307		NOP

     4.6.3.2 Output

	6310		Set this (dummy) flag
	6311		Skip on dummy flag
	6312		NOP
	6313		NOP
	6314		Transfer AC <4:11> to the transmit buffer
	6315		Enable interrupts for this device code, using  AC
			<11>
	6316		Transfer AC <4:11> to the transmit buffer
	6317		NOP

	As can be seen from the set of  instructions  given  above,  this
	communications   controller  has  a  quite  different  method  of
	operation from that of the DP278. An example of how to initialize
	and service this device for the asynchronous mode of operation is
	given in Appendix C. For more details, refer to the DEC  Purchase
	Specification for the controller chip (7201).

     4.7 Clock

	The clock provides a periodic interrupt at a 100  Hz.  rate.  The
	clock  frequency  source  is  crystal controlled, thus cumulative
	errors should be expected. As the basic accuracy of  the  crystal
	is  0.01%,  these  errors  should not account to greater than +-3 
	seconds in an 8 hour period.






	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 37     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Instruction	Description

	6130		Set clock flag.
	6131		Skip on clock flag, clear it if set.
	6132		NOP
	6133		NOP
	6134		NOP
	6135		Set/clear clock interrupt enable with AC(ll).
	6136		NOP
	6137		NOP

	The clock interrupt enable is cleared following self test.

	Note that the clock instruction set is different from that of the
	DECmate I and the VT78.

     5. Detailed Description - Options

     5.1 Identification

	The LAS instruction allows a user to determine which options  are
	present on DECmate II :

		AC

		08	0	-	APU present
			1	-	No APU present

		09	0	-	RX78 or RD51 controller present*
			1	-	No additional storage adaptor
					present

		10	0	-	Graphics Controller present
			1	-	No graphics Controller present

		AC<00:07>, <11> -	undefined

	* Which of these is present may be tested  by  issuing  the  RD51
	controller instruction 6707 with the AC set non-zero. If the RD51
	controller is present, the AC will be cleared.

     5.1.1 Z80 Softcard

	A daughter module may be added to the basic single board computer
	module  to  allow the execution of applications written for a Z80
	microprocessor. This added module has a Z80  processor  with  its
	own 64 K bytes of memory and an interface to the 6120 CPU system.
	The 6120  performs  all  the  actual  I/0  operations  for  disk,
	keyboard, screen, printer and communications.

	A sequence  (TBD)  will  allow  operation  to  be  switched  from
	executing  applications programs using the PDP-8 CPU to using the
	Z80 CPU, supporting CP/M(TM) file structure.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 38     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	For more details refer  to  the  Z80  Auxiliary  Processing  Unit
	Specification.

     5.2 Graphics

	Refer to the Option Engineering Specification.

     5.3 Micro Winchester Disk Adaptor

	Refer to the Option Engineering Specification.

     5.4 RX01/RX02 Adaptor

	This daughter module may be added to the base machine in place of
	the  Micro Winchester Adaptor to allow one or two RX01 or RX02 8"
	floppy disk units to be attached to the DECmate II. An  extension
	to  the  SEL IOT allows the external 8" disk(s) to be selected in
	place of the internal 5.25" disk(s) - see Section  4.4.  In  this
	way  the  same IOTs may be used to control either the internal or
	external disk unit(s).

	The adaptor has a 37-pin subminiature D  connector  allowing  the
	same  cable  to  be  used  to  connect to one or two RX01/02 disk
	drives as is used with DECmate I.

	The selection of the external adaptor using the SEL IOT has  some
	limitations  in  the selection of the subsequently active pair of
	RX01/02 drives.  As  the  external  adaptor  cannot  perform  any
	operations  until  after  it  has been selected, the SEL IOT that
	changes disk selection from one  of  the  internal  units  to  an
	external unit cannot also change which pair of external drives is
	active. Drive pair  "A"  of  the  external  drive  controller  is
	selected  on  power-on  or  following  a  CAF/RXINIT instruction.
	Subsequently issuing a SEL  IOT  with  AC=400X  will  select  the
	external  drive  pair  "A"  regardless of AC<ll>. To select drive
	pair "B",  a  second  SEL  must  be  issued  with  AC=4001.  When
	switching back to the internal drives, the setting of AC<ll> will
	determine  which  of  the  external  drive  pairs  will  be  left
	"selected". This "selected" drive pair will be the pair activated
	when the next SEL with AC=400X is issued.

     6. Firmware Details

	In general, the information given in this section, relates to how
	Control  Panel Code, invisible to the user, accesses the hardware
	to perform some function requested by  a  user  generated  Escape
	Sequence.

	The section on the User Defined Character Set which  is  included
	gives  information on how a user may directly modify the contents
	of the User Defined Character Generator Memory.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 39     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     6.1 CRTC and Associated Logic Programming

	The CRT Controller for the VT 278 (DECmate  I)  occupied  control
	panel  memory  address space. As all control panel memory is used
	with DECmate II, the CRT registers are now programmed by IOTs. It
	is  necessary to set a register number with one IOT and then read
	or write this register with another IOT. Note that registers  are
	pre-defined  as  READ  or WRITE, thus two IOTs are needed, one to
	Read a specified register and the other to Write. Issuing a  Read
	IOT  to a WRITE register will give unpredictable results, issuing
	a Write IOT to a READ register will result in  a  bus  contention
	situation, again with unpredictable results.

	It is also necessary  to  be  able  to  establish  the  following
	parameters :

	80/132 column mode 	        - Section 6.1.1
	Video Enable 	        	- Section 6.1.2
	Screen mode, normal or reverse  - Section 6.1.3
	Cursor mode, block or underline - Section 6.1.4
	Erase control bits 0 and 1 	- Section 6.1.5
	Extended Character Set Mode     - Section 6.1.6
	User Character Set Mode 	- Section 6.1.7

     IOT list - Device Code 12

	6121	Skip on End of Frame Interrupt, clear the flag if set and
		the skip occurs.
	6122	Load the CRT Controller register  number  from  AC<6:11>.
		Load  the  cursor visibility enable with AC<01>, load the
		cursor visibility disable with AC<00>. - Section
	6123	If the DF is odd:
		Load   User   Character   RAM   Character   number   from
		AC<1:7>, Line number from AC<8:11>.
		If the DF is even:
		Load User Character RAM Data from AC<4:11> - Section
	6124	Write selected CRT controller  register  from  AC<4:11> -	
		Section
	6126	Load control register
		AC  00  - Erase bit 0
		    01  - Erase bit 1
		    04  - 80/132 column mode (0 = 80 column)
		    05  - Video Enable (0 = disable)
		    08  - Extended Character Set Mode
		    09  - User Character Set Mode
		    10  - Cursor mode:  0 = block
					1 = underline
		    11 - Screen Mode:   0 = white on black
					1 = black on white
	6127	Read selected CRT controller register, used to clear  End
		of Frame Interrupt.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 40     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     6.1.1 80/132 Column Mode

	This bit is changed when the DEC Private ESCape Sequence  ESC [ 3
	l/h is received, the SM final character (Lower Case "H") sets 132
	column mode, the RM final character  (Lower  Case  "L")  sets  80
	column  mode.  Changing  column  mode  leaves  the display in the
	following condition :

	Screen cleared - all memory locations in the visible  region  set
	to contain 0000.
	All display rows-set to single-width, single height.
	Origin Mode cleared.
	Scroll region set to 24 rows (default).
	Scroll mode unchanged.
	Cursor placed at the HOME position.
	Cursor Mode unchanged.
	Screen Mode unchanged.
	Character sets for GO and G1 unchanged.
	Character attributes cleared.

     6.1.2 Video Enable

	This bit is used to blank the  display  and  to  allow  the  User
	Character Set RAM to be altered - see Section 6.1.7

     6.1.3 Screen Mode

	Changing Screen Mode (white characters on a black ground  =  mode
	cleared,  black  characters on a white ground = mode set), alters
	no other display parameters.

     6.1.4 Cursor Mode

	Changing cursor mode (block  cursor  =  mode  cleared,  underline
	cursor = mode set), alters no other display parameters.

     6.1.5 Erase Control

	To minimize CPU overhead,  certain  long  duration  screen  erase
	functions are executed by hardware, these are listed below :

	  EL0 - Erase in Line from current cursor position to end of line
	  EL1 - Erase in Line, entire line
	  ES0 - Erase in Screen from current cursor position  to  end  of
		screen
	  ES1 - Erase in Screen, entire screen

	The  particular  erase  function  is  initiated  by   loading   a
	combination of Erase Bits 0 and 1 :

			ERBIT 0		ERBIT 1
	EL0, ES1 *	  1		  0
	ES0, ES1 * 	  1		  1
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 41     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     *  for these functions, the  display  firmware  is  responsible  for
	setting  the  cursor  to the left margin before issuing the erase
	function request and then restoring the cursor when  the  display
	hardware indicates that the erase is complete.

	Erase functions are synchronised with the display timing  by  the
	Control  Panel  code waiting for an End of Frame interrupt before
	initiating an erase function and then waiting for the next End of
	Erame interrupt to indicate that the erase has been completed.

     6.1.6 Extended Character Set Mode

	DECmate I has two 2K x 8 character generator ROMs each  of  which
	allows  for  the display of up to 128 characters/symbols. One has
	the US/UK character set plus the  special  graphics  set  of  the
	VT100,  the  other  all  the  characters for the Foreign Language
	DECmate  I  variations  plus  some  additional  special  graphics
	symbols.  These  two  ROMs  together  provide the basic DEC 8-bit
	multinational character set. (See DEC Std. 138). DECmate II  adds
	to   this  the  ability  to  display  the  Katakana  set  of  the
	multinational character set and a  User  Defined  Character  Set.
	These  additional  characters/symbols  are accessed using a ninth
	character code bit.

	To be able to display  more  than  256  characters,  an  Extended
	Character  Set  Mode is provided for DECmate II. In this mode the
	internal representation of characters in the  display  buffer  is
	nine  bits,  rather  than  the  eight  bits  of  DECmate  I.  The
	additional bit is obtained by deleting  the  character  attribute
	"BLINK".  Section  6.1.7  gives details of this mode and the User 
	Character Set Mode.

     6.1.7 User Character Set Mode

	To provide even greater flexibilty for displaying characters  and 
	symbols  that  may be needed by a particular user program, a User
	Defined Character Generator is provided  with  DECmate  II.  This
	allows  a  further  128  characters,  defined  by the user, to be
	displayed. Display is controlled by the User Character  Set  Mode
	Enable bit, set on a page basis.

     6.1.7.1 Loading the User Defined Character Generator (UDCG)

	To enable writing the UDCG the Video Enable Bit must  be  cleared
	in  the  display  control word (AC<5>). This is done by issuing a
	PR3 Panel Call with the AC zero, the UDCG may  then  be  changed.
	The  entire  UDCG  may be altered or only specific locations, the
	order of changing the UDCG does not  matter.  Programming  is  as
	follows:

     A. Clear the AC, issue PR3 with the  following  location  containing
	(TBD)  -  the  function  number  of  the  Panel memory routine to
	disable the display and enable changing the UDCG.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 42     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     B. Load AC<1:7> with the 7-bit character code for the  character  to
	be  altered  and AC<8:11> with the first line number (000). (Line 
	numbers run from 0000 to 1001 : 0 - 9 decimal).

     C. Set the Data Field to an odd value (1, 3, 5, 7) 
	Issue the IOT 6123 (this does not clear the AC)

     D. Set the Data Field to an even value (0, 2, 4, 6).
	Load AC<4:11> with the character dot pattern  for  the  specified
	line.  The  character  dot  pattern is entered as it will appear,
	e.g. AC<4> is the leftmost dot of the character cell, see  Figure
	1,  Section  4.2.3,  note  that  if  a  character is defined with
	CD<7>=1, it will be a right filled character, i.e. dot  positions
	8 and 9 in Figure 1. will also be present.
	Issue the IOT 6123 (the AC is not cleared)

	Repeat steps B, C, D for each line of the character definition.

	Set the AC=7777, issue PRQ as in A. to re-enable the video.

     6.1.7.2 Accessing the Extended Character Set and the User Defined 
	Character Set.

	As noted earlier, the Extended Character Set and the User Defined 
	Character  Set are accessed by an Extended Character Set Mode bit
	(ECSM) and a User Character Set Mode Enable (UCSME) bit. The  way
	the  user  program  controls  these  bits is not yet defined. The
	combination of these bits results  in  access  to  the  character
	generators as shown below :

	ECSM = 1          Character Code |  Character Code
			    Bit 9 = 0    |    Bit 9 = 1
		  ------------------------------------------------
		 |	    |    	 |	     |		  |
		 |UCSME = 0 | UCSME = 1	 | UCSME = 0 |	UCSME = 1 |
		 |          |            |           |		  |
	----------------------------------------------------------
	Internal |          |		 |	     |		  |
	Char.Code|  US/UK   | US/UK	 |   US/UK   |User defined|
	Bit 8=0  | 	    |		 |   with    | Characters |
		 |	    |		 | Yen mark  |		  |
	----------------------------------------------------------
	Internal |	    |		 |	     |		  |
	Character| Alternate| Alternate  |Katakana   |User defined|
	Code Bit | (Foreign)| (Foreign)  |	     | Characters |
	Bit 8=1  |	    |		 |	     |		  |
	----------------------------------------------------------
		 |<-These are the only-->|
		 |possibilities when not |
		 | in Extended Mode 	 |

	In this way arbitrary character substitutions may  be  made  from
	the user defined character set when displaying US/UK, any Foreign
	Language or Katakana.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 43     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
    6.1.8 Loading and Reading the CRT Controller Registers

	The CRT Controller has one group of internal registers  that  are
	generally   only   changed   when  it  is  initially  programmed,
	parameters which affect the display format  and  a  second  group
	that must be modified continually, cursor position etc.

     6.1.8.1 R0 - Characters per horizontal period

	This register is  loaded  from  AC  <4:11>  with  the  number  of
	characters that make up one row of the display. This includes the
	visible area, non-visible areas and retrace time.

     6.1.8.2 R1 - Characters per data row

	This register is loaded  from  AC  <4:11>  with  the  (number  of
	displayed characters per row - 1).

     6.1.8.3 R2 - Horizontal delay

	This register is  loaded  from  AC  <6:11>  with  the  number  of
	character  times  which represents the time from the leading edge
	of horizontal sync to the trailing edge of horizontal blank.

     6.1.8.4 R3 - Horizontal sync width

	This register is  loaded  from  AC  <5:11>  with  the  number  of
	character  times  representing  the  width of the horizontal sync
	pulse.

     6.1.8.5 R4 - Vertical sync width

	This register is  loaded  from  AC  <5:11>  with  the  number  of
	horizontal  periods  representing  the width of the vertical sync
	pulse.

     6.1.8.6 R5 - Vertical delay

	This register is  loaded  from  AC  <4:11>  with  the  number  of
	horizontal periods representing the time between the leading edge
	of vertical sync and the trailing  edge  of  the  vertical  blank
	signal.

     6.1.8.7 R6 - Skew bits

	This register is loaded from AC <6:11> with a number of character
	times  that  define a skew between cursor and blank and the video
	signal going to the monitor.

     6.1.8.8 R7 - Visible data rows per frame

	This register is loaded from AC <4:11> with the (number  of  data
	rows  to  be  displayed - 1). For DECmate II this means 23(8) for 
	both 80 and 132 column modes of operation.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 44     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
   6.1.8.9 R8 - Scan sines per data row/Scan lines per frame (MSB)

	This register is loaded from AC <7:11> with the (number  of  scan
	lines  that  make  up one data row -1), for DECmate II this means 
	11(octal). AC <4:6> define the most significant three bits of the 
	number of scan lines per frame.

     6.1.8.10 R9 - Scan lines per frame

	This register is loaded from AC <4:11> with the least significant
	8 bits that define the total number of scan lines per frame - see
	R8.

     6.1.8.11 ROA - DMA control register

	This  register  is  loaded  from  AC  <4:11>  with  DMA   control
	information as follows :

	AC <4>		DMA disable,  disables  all  CRT  controller  DMA
			accesses.  As the CRT controller on DECmate II is
			also the source of  memory  refreshes,  this  bit
			must  never  be set to zero unless loss of memory
			data can be tolerated.
	AC <5:7>	Define the delay between DMA bursts when the  CRT
			controller  is  operating  in burst DMA mode. For
			DECmate II DMA cycles for a given row occur as  a
			single burst, so these three bits are set to 111.
	AC <8:11>	Define the number of DMA cycles in any one burst,
			when  the  CRT  controller  is  operating  in the
			burst DMA mode. The  number  loaded  here  is  N,
			where the number of DMA cycles in a burst is then
			4*(N+1).  This  mode is not applicable to DECmate
			II.

     6.1.8.12 ROB - Control Register

	This register is loaded from AC <4:11> with the following :

	AC <4>		Unused
	AC <5>		0 - smooth scroll. This causes the smooth  scroll
			offset  register  (R17)  to  define the number of
			lines that will be scrolled per  frame.  This  is
			the  only  mode  used  for  DECmate II, thus this
			bit must be set to 0. 
	AC <6:7>	These two bits define interlace mode. DECmate  II
			uses no interlace. These two bits are both set to
			0.
	AC <8:10>	These three bits define the buffer  configuration
			being  used  with  the CRT controller. DECmate II
			uses a single row buffer, thus these  three  bits
			must be set to 100.
	AC <11>	0

	Thus the programming word for ROB is X0 001 000 010(8).
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 45     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     6.1.8.13 ROC - Table start register, low byte

     6.1.9 Cursor Visibility

	The DECmate I attempted to "make the cursor do the correct thing"
	by  suppressing  the  cursor  whenever new data was output to the
	screen  at  greater  than  a  given  rate.  This  was   partially
	successful  in  that the cursor was not visible when updating the
	screen using Direct Cursor  Addressing  sequences,  unfortunately
	the  cursor was also not visible when doing things like moving it
	across a line when editing. DECmate II attempts  to  treat  these
	two  events separately, when the firmware detects that the cursor
	is being re-positioned by means of  a  Direct  Cursor  Addressing
	Sequence, it will clear the cursor visibility bit when it updates
	the cursor address register within the CRT controller. The effect
	of  this  is  to suppress the cursor (make it invisible) for half
	the cursor blink rate period (130 milliseconds), timed  from  the
	update, regardless of the previous state of the cursor visiblity.
	Then if another Direct Cursor Address command occurs within  this
	period, the cursor will remain invisible.

	If the cursor address register is being  updated  for  any  other
	reason,  the  firmware  will  set the cursor visibility bit, this
	causes the cursor to be visible for half the  cursor  blink  rate
	period   (130   milliseconds),   timed  from  the  update,  again
	regardless of the previous state of cursor visibility.  Thus,  in
	the  cases  of  normal  output  to the screen by echoing keyboard
	input and advancing through a piece  of  text,  the  cursor  will
	remain visible.

	Setting and clearing the cursor is done by loading one of two  AC
	bits  when  a  CRT  controller  register  is selected. AC<00> = 1
	clears the cursor visibility enable bit  and  would  be  selected
	prior  to  updating  the  cursor as the result of a direct cursor
	addressing sequence, AC<01> = 1 sets the  visibility  enable  and
	would  be  selected prior to updating the cursor position for any
	other reason. The effect of setting either of these bits (but not
	both)  is  that  when the selected CRT register is later written,
	the cursor will be set ON or OFF for the  time  specified  above.
	Care  must be taken to ensure that both AC<0:1> are set to 0 when
	no effect is intended on the normal alternating cursor display.

     6.2 Panel Requests

	There are four instructions which, when issued  in  user  memory,
	cause  some action to be performed by the control memory code. To
	maintain compatibility with DECmate I, the first three  of  these
	operate in the same way as with DECmate I. The fourth is modified
	and although the types of operations that may be performed  using
	this  fourth  instruction  are  similar  there  is  no  backwards
	compatibility.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 46     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     6.2.1 PR0 - Panel Request 0

	This instruction may be used to read the contents of a  specified
	screen location. Its use is as follows :

			PR1	
			Row Address	/ Absolute, 0 - 27
			Column Address  / Absolute, 0 - 117 (0 - 203)
			XXXX		/ Return made here with contents
					/ of specified screen location in
	 				/ the AC

     6.2.2 PR1 - Panel Request 1

	This instruction was used with DECmate I  to  allow  the  display
	buffer  memory  to  be  updated  quickly.  It  is not needed with
	DECmate II as the same screen update restrictions do not apply to
	this  new machine, it is retained for compatibility reasons only.
	To move data to  the  display  buffer  portion  of  memory,  this
	instruction is used in the following way :

			PR1
			Row Address	/ Absolute, 0 - 27
			Column Address  / Absolute, 0 - 117 (0 - 203)
			Data		/ 12 bits, includes attributes
			...		/ group of three entries
			...		/ repeated for as many screen
			...		/ locations as to be changed
			7777		/ terminator
	Attributes :

		AC	00	-	Blink
			01	-	Underline
			02	-	Bold
			03	-	Reverse

    6.2.3 PR2 - Panel Request 2

	For DECmate I this was equivalent to  entering  SET-UP  mode  and
	depressing a key, specified as :

			PR2 
			N 		/ The ASCII code for the  key  to
					/ be "pressed"

	This Panel Request has no action on DECmate II. If it  is  issued,
	return will be made to CALL+2 for compatibility.

     6.2.4 PR3 - Panel Request 3

	This is a general call to execute a routine  in  control  memory.
	With  DECmate I  the absolute address in control memory had to be
	specified in the location following the PR3  instruction  and  no
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 47     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	validity checking was performed, calls to some arbitrary  address
	could,  therefore,  cause unpredictable results. The operation of
	this instruction for  DECmate  II  has  been  modified,  now  the
	routine  to  be  executed  in  control  memory  is specified by a
	function number in the location following the request. The format
	is as follows :

			PR3 
			FUNCT   /Function 
			ARG1    /First argument (optional) 
			ARG2    /Second argument (optional)
			..
			..
			7777    /Terminator

	If a return is to be made, it is made to the  location  following
	the 7777 terminator.

	The following functions are implemented in the  current  firmware
	(Revision 216 or 224)

	Function	Action				Argument(s)

	0000		Print the character		None
			in the accumulator.

	0001		Select video enable		None
			with AC<ll>.
			0 = disable, 1 = enable

	0002		Select extended character
			Mode with AC<ll>.
			0 = disable, 1 = enable

	0003		Select User Charaacter Set	None
			with AC<ll>.
			0 = disable, 1 = enable

	0004 		Select Cursor Style with AC<ll> None
			0 = Block, 1 = Underline

	0005		Execute Power-on Clear 		None
			There is no return as self-test
			is run.

	0006		Execute SET-UP Menu 		None

	0007		Request Display Status 		None
			On return, AC = 0000 means the
			display is not busy, AC =7777
			it is busy.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 48     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Function	Action 				Argument(s)

	0010		Select Function Key Mode with   None
			AC<ll>. 0 = transmit ESC/BS/LF
			1 = transmit ESCape sequences
			for these three keys.

	0011		Select Keyboard Case with	none
			AC<11>. 0 = lower-case,
			1 = upper-case.

	4000+10*N+M	Load data from user memory to
			panel memory.
			N - CP memory destination field
			M - user memory source field

					Argument 1	User memory SA
					Argument 2	CP memory SA
					Argument 3	2's complement of
							#   of  words  to
							move

	5000+10*N+M	Load data from panel memory to
			user memory.
			N - user memory destination field
			M - control panel source field

					Argument 1	CP memory SA
					Argument 2	User memory SA
					Argument 3	2's complement of
							#   of  words  to
							move

	6000+10*N	Transfer control to CP memory
			field N.
					Argument 1	CP memory SA

	7000		Send data to the keyboard

					Argument(s)	data in bits
							<4:11>. Bits
							<0:3> must be
							zero.
			N.B. No check is made on the
			data sent.

	7100+10*N	Transfer Screen Control Data
			to a user buffer in Field N.

					Argument l	User Buffer SA



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 49     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

		29  (decimal)  words   are   moved   to   the   specified
		user buffer. They are :

		Word 1 - Column Mode: 0 = 80, 7777 = 132
		Word 2 - Origin Mode: 0 = absolute, 7777 = relative
		Word 3 - The  number  of  the  top  row  of  the  current
			 scrolling region.
		Word 4 - The number of the  bottom  row  of  the  current
			 scrolling region.
		Word 5 - The control word for  the  CRT  Controller  Chip
			 (See Section 6.asdasdas)
		Word 6 - High Word of the Row Address Table for Row 1
		Word 7 -
		....	  -
		....   -
		Word 29- High Word of the Row Address Table for Row 24.


     6.3 Terminal Input Output

	DECmate I had a physical register (TTI), through  which  keyboard
	input  data  was  transmitted  from the keyboard scan routines in
	Control Panel memory for the user  program  to  be  able  to  use
	normal  keyboard  instrcutions,  KRB,  KRS KCC. DECmate II has no
	such register, all keyboard data transfer  instructions  cause  a
	single  Control Panel Interrupt, control panel code then inspects
	the interrupting instruction and  modifies  the  AC  as  required
	prior to returning control to the user program.

	For output, TLS and other such instructions also cause a  Control
	Panel  interrupt  in  the same way as with DECmate I, the data in
	the AC is taken and interpreted by Control Panel Memory code.

	Instructions that cause Control Panel Interrupts are :

		6030, 6032, 6034, 6036
		6040, 6042, 6044, 6046

	Interrupts  from  any  of  these  user  issued  instructions  are
	identified by the single instruction 6071.

	The Skip and Interrupt Enable instructions,  (6031,  6035,  6041,
	6045) do not cause Control Panel Memory interrupts.










	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 50     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Appendix A - Standard ROM Character Definitions

				 TBS


















































	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 51     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Appendix B - CPU Instruction Set

	All times are for operation at 8 MHz. (I/O at 4 MHz.)

     B1. Basic Instructions

     Mnemonic   Octal   Description	        Execution Time
					      Direct  Indirect  Autoindex
	AND	0XXX	Logical AND to AC	1.75	2.5	 3.25
	TAD	lXXX	Two's complement ADD	1.75	2.5	 3.25
	ISZ	2XXX	Increment & Skip if 0   2.26	3.00	 3.76
	ISZ	2XXX	(When SKIP occurs)	2.76	3.51	 4.26
	DCA	3XXX	Deposit & clear AC	1.75	2.5	 3.25
	JMS	4XXX	Jump to subroutine	1.75	2.5	 3.25
	JMP	5XXX	Jump 			1.00    1.75	 2.47

     B2. Group 1 Operate Micro-instructions

	1.5 uSec if no BSW or double rotate, 1.9 uSec otherwise.(#)
							  	  *
     Mnemonic   Octal   Description 			  Sequence

	NOP	7000	No operation 				-
	CLA	7200	Clear AC 				1
	CLL	7100    Clear Link 				1
	CMA	7040	Complement AC 				2
	CML	7020	Complement Link 			2
	RAR	7010	Rotate AC & Link right 			4
	RAL	7004	Rotate AC & Link left 			4
	RTR#	7012	Rotate AC & Link two right 		4
	RTL#	7006    Rotate AC & Link two left 		4
	BSW#	7002	Swap AC<0:5> & AC<6:11> 		4
	R3L	7014	Rotate AC ONLY three left 		4
	IAC	7001	Increment AC, carry to Link 		3

     B3. Group 2 Operate Micro-instructions - 1.75 uSec.
								  *
     Mnemonic   Octal   Description 			  Sequence

	SMA	7500	Skip on minus AC 			1
	SZA	7440	Skip on zero AC 			1
	SPA	7510	Skip on positive AC 			1
	SNA	7450	Skip on non-zero AC 			1
	SNL	7420	Skip on non-zero Link 			1
	SZL	7430	Skip on zero Link 			1
	SKP	7410	Unconditional Skip 			1
	OSR+	7404	Inclusive OR status bits to AC 		3
	HLT$	7402	Halt program in main memory 		3
	CLA	7600	Clear AC 				2

	+ Add 0.25 uSec. 		$ NOP in Panel Memory.
	* Sequence indicates at which point in the instruction execution
	the operation occurs. 1 is before 2, 2 before 3, etc.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 52     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     B4. Group 3 Operate Micro-instructions - 1.5 uSec

     Mnemonic   Octal   Description

	NOP	7401    NO operation
	CLA	7601    CLear AC
	MQL	7421    Load AC to MQ then clear AC
	MQA	7501    Inclusive  OR  MQ  with  AC,  result  to  AC,  MQ
			unchanged
	CAM	7621    Clear both AC and MQ
	SWP	7521    Swap AC and MQ
	ACL	7701    Load MQ to AC, MQ unchanged
	CLA SWP 7721    Load MQ to AC then clear MQ

     B5. Internal Control Instructions ( Panel Memory )

     Mnemonic   Octal   Description		    Execution Time, uSec.

	PRS	6000	Read Panel Status Word*			  2.01
	ION	6001	Enable Interrupt System			  1.5
	IOF	6002	Disable Interrupt System		  1.5
	PGO	6003	Reset HLTFLG				  1.5
	PEX	6004	Exit to main Memory after next
			JMP or JMS				  1.5
	RTF	6005	Restore fields and flags from AC	  2.01
	SGT	6006	Skip on GT flag				  1.75
	CAF	6007	Clear all flags				  1.75
	WSR	6246	I/O write			 	  1.72
	GCF	6256	Get current fields and flags		  2.26
	CPD	6266	Clear Panel Data Flag			  1.5
	SPD	6276	Set Panel Data Flag			  1.5

     B6. Internal Control Instructions ( Main Memory )

     Mnemonic   Octal   Description                 Execution Time, uSec.

	SKON	6000	Skip if Interrupt System ON,
			turn it OFF				  1.75
	ION	6001	Turn ON Interrupt System		  1.5
	IOF	6002	Turn OFF Interrupt System		  1.5
	SRQ	6003	Skip on Interrupt Request		  1.75
	GTF	6004	Get Interrupt Flags 			  2.26
	RTF	6005	Restore Flags and Fields from AC	  2.00
	SGT	6006	Skip on GT flag				  1.75
	CAF	6007	Clear all flags				  1.75
	WSR	6246	I/O write				  1.72
	GCF	6256	Get current fields and flags		  2.26
	PR0	6206	Make Panel Request			  1.5
	PR1	6216	Make Panel Request			  1.5
	PR2	6226	Make Panel Request			  1.5
	PR3	6236	Make Panel request			  1.5


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 53     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     B7. Memory Extension Instructions 

     Mnemonic   Octal   Description                 Execution Time, uSec.

	CDF     62N1	Change to Data Field N			  1.5
	CIF     62N2	Change to Instruction Field N		  1.5
	CDF CIF 62N3	Change both DF and IF to N		  1.5
	RDF     6214	Read Data Field to AC<6:8>		  1.5
	RIF     6224	Read Instruction Field to AC<6:8>	  1.5
	RIB     6234	Read Interrupt Buffer to AC<6:11>	  2.25
	RMF     6244	Restore Memory Fields		  	  1.5

     B8. Stack Instructions

     Mnemonic   Octal   Description                 Execution Time, uSec.

	PPC1	6205	Push (PC+1) to stack 1			 2.25
	PPC2	6245	Push (PC+1) to stack 2		  	 2.25
	PAC1	6215	Push AC to stack 1			 2.25
	PAC2	6255	Push AC to stack 2			 2.25
	RTN1	6225	Pop top of stack 1 to PC		 2.25
	RTN2	6265	Pop top of stack 2 to PC		 2.25
	POP1	6235	Pop top of stack 1 to AC		 2.25
	POP2	6275	Pop top of stack 2 to AC		 2.25
	RSP1	6207	Read stack 1 pointer to AC		 1.25
	RSP2	6227	Read stack 2 pointer to AC		 1.25
	LSP1	6217	Load stack 1 pointer from AC		 1.25
	LSP2	6237	Load stack 2 pointer from AC		 1.25

     B9. IOT instructions - External

	Of the form "6XYZ" where XY is not 00 nor in the range 20  -  27.
	They  require 4.0 uSec for Write only, 4.5 for Write followed by
	Read.

	Terminal I/O Instructions

	Input

     Mnemonic   Octal   Description                 Execution Time, uSec.

	KCF	6030    Set Keyboard Flag. *			  4.0
	KSF	6031	Skip on keyboard flag, clear
			it if set. * 			  	  4.0
	KCC	6032    Clear the AC. *			  	  4.0
	KRS	6034    "OR" keyboard buffer to AC.		  4.5
	KIE	6035    Set/clear Keyboard Interrupt
			Enable with ACll. * 			  4.0
	KRB	6036    Load Keyboard buffer to AC.		  4.5




	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 54     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Output

     Mnemonic   Octal   Description                 Execution Time, uSec.

	SPF	6040	Set output flag.			  4.0
	TSF	6041	Skip on output flag, clear
			it if set. *				  4.0
	TCF	6042	Clear the AC. *				  4.0
	TIE	6045	Set/clear Output Interrupt
			Enable with AC 11. *			  4.0
	TLS	6046	Load AC<4:11> to the screen.		  4.0

	* These instructions execute differently from the PDP 8/A or VT78.








































	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 55     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Appendix C.

	Communications Controller Programming

	This example is  in  two  parts,  channel  initialization  and  a
	suggested way to handle interrupt service.

     C1. Communications Port Initialization

     Cl.l Defaults 

	Following the completion of Self-test,  the  communications  port
	will be left in the following state :

	Mode			:	Asynchronous
	Baud rate		:	1200
	Character		:	8 data bits
	Parity			:	NONE
	Stop Bit(s)		:	1

	Modem Lines
	Data Terminal Ready	:	ON
	Request To Send		:	OFF
	Local loopback		:	OFF
	Remote Loopback		:	OFF
	Clock Mode		:	Internal

     C1.2 Setting Communications Controller Chip Parameters

	The communications controller chip has two sets of internal 8-bit
	registers,  A  and B. Mostly the registers of set A are used, but
	to identify the cause of interrupt a register from the B set must
	be  read.  The  A set and B set are addressed using the same IOT,
	the Data Field determines which will be accessed. With  the  Data
	Field  set to an Even number (0, 2, 4, 6), register set A will be
	accessed, with the Data Field set to an ODD number, register  set
	B.  The  following shows how they must be set up for asynchronous
	mode operation.

	The general method of addressing a communications  chip  register
	is  to  define a register number in AC<9:11> and whether it is to
	be read or written, specified by AC<00>, issue the IOT 6366, then
	read or write the selected register with this same IOT, i.e. this
	IOT  sequentially  selects  a  register  then accesses it. If the
	register selected is Control Register 0,  which  is  Write  Only,
	then  this  sequence can be shortened to a single IOT with the AC
	specifying  the  register  number  (0)  in  AC<9:11>   and   also
	containing the data to be written into CR0 in AC<4:8>.





	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 56     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			 DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	e.g. Write Control Register 4A

		CDF	00	/or 20, 40, 60
		TAD	(4	/select CR4 for a write
		6366
		CLA
		TAD	(VAL	/data to be written into CR4
		6366		/Load CR4
		(CLA)
		CDF	XX	/back to user required value

	     Read Status register 2B

		CDF	10      /or 30, 50, 70
		TAD	(4002   /select Status register 2 for
				/READ, AC<00>=1 specifies READ
		6366		/select register
		CLA
		6366		/Status Register 2 -> AC
		AND	(177    /High order bits undefined
		CDF	XX	/back to user required value

	     Write Control Register OA

		CDF	00
		TAD	(0XX0
		6366		/load CR0 from AC<4:8>
		(CLA)
		CDF	XX	/user value

     C1.3 Values to be used

	The chip must be initialized in the following sequence any  time;
	that any parameter involved is modified.

     C1.3.1 Issue chip reset	6367
     C1.3.2 Reset Channel
				CDF	00
				TAD	(30
				6366		/Select CR0A, load with
				CLA		/30 = RESET
     C1.3.3 Initialize CR2A
				CDF	00
				TAD     (2	/select register CR2A
				6366
				CLA
				TAD     (20	/Fixed number
				6366 	/load into CR2A
				CLA




	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 57     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     C1.3.4 Initialize CR2B
				CDF	10
				TAD	(2	/Select CR2B
				6366
				CLA
				6366		/load CR2B with 000
     C1.3.5 Initialize CR4A
				CDF	00
				TAD	(4
				6366		/select CR4A
				CLA
				TAD	CR4VAL
				6366
				CLA ....

	   CR4VAL is loaded with the following:

		AC <4:5>	01 (Must not be-changed)
		   <6:7>	00 (Must not be changed)	
		   <8:9>	Define number of STOP bits
				00 - Illegal
				01 - 1 STOP bit
				10 - 1.5 STOP bits
				11 - 2 STOP bits
		    <10>	Parity - ignored if AC<ll> = 0
				0 - ODD parity
				1 - EVEN parity
		    <11>	Parity Enable
				0 - no parity generated or checked
				1 - generate and check parity, sense set
				by AC<10>.

	e.g. 1 STOP bit, no parity, value loaded is 104

     C1.3.6 Initialize CR1A
				CDF	00
				TAD	(1
				6366		/select CR1A
				CLA
				TAD	(26	/fixed, must not change
				6366
				CLA ...

     C1.3.7 Initialize CR2A
				CDF     00
				TAD	(2
				6366
				CLA
				TAD	(26
				CLA ....



	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 58     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     C1.3.8 Initialize CR3A
				CDF	00
				TAD	(3
				6366
				CLA
				TAD	CR3VAL
				6366
				CLA 

		CR3VAL is loaded with the following :

		AC <4:5>	Number of data bits for receive
				00 - 5 bits
				01 - 7 bits
				10 - 6 bits
				11 - 8 bits
		AC <6:10>	00000
		AC <11>		1 - Enables Receiver

	e.g. 8 data bits for receive, receiver enabled, value  loaded  is
	     301.

     C1.3.9 Initialize CR5A
				CDF	00
				TAD	(5
				6366
				CLA
				TAD CR5VAL
				6366
				CLA 

		CR5VAL is loaded with the following ;

		AC <4>		0
		AC <5:6>	Number of data bits for transmit
				00 - 5 bits (or less)
				01 - 7 bits
				10 - 6 bits
				11 - 8 bits
		AC <7>		Send a BREAK
		AC <8>		1 - enables transmitter
		AC <9:11>	000

	The chip is now ready for transmit and receive.

     C1.3.10 Set Modem Status and clock mode

	For the simplest case, the only Modem line to be  asserted  would
	be  DTR.  In  all cases for asynchonous operation, internal clock
	must be selected, thus  the  Modem  Control  Register  should  be
	loaded with the value 0010 using IOT 6362.


	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 59     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     C2. Interrupt Service

     C2.1 Data Transfers

	As there is only one flag for Send, Receive  and  Errors,  it  is
	necessary  to  interrogate  the communications controller chip to
	identify the cause of a communications interrupt. There are three
	possible  interrupt  conditions,  Transmit  Buffer Empty, Receive 
	Data Available and Error (Overrun, Framing, Parity - if enabled).

			6301		/Skip on Comm. port flag
			JMP 	NOTCOM
		IDENT,  CDF	10	/ODD to read Status Reg. 2B
			TAD	(4002
			6366
			CLA
			6366		/Perform read
			AND	(7	/mask to three LS bits

	the AC now contains the following :

	AC	9	10	11	Condition

		0	0	0	Hardware malfunction
		0	0	1	Hardware malfunction
		0	1	0	Hardware malfunction
		0	1	1	Hardware malfunction
		1	0	0	Transmitter Buffer Empty
		1	0	1	Hardware malfunction
		1	1	0	Receive Data Available
		1	1	1	Parity, overrun or framing error
					OR Hardware malfunction

	To determine what caused the 111  result,  one  further  register
	must be read, Status register 1A

			CDF	00
			TAD	(4001   /select SRlA for reading
			6366
			CLA
			6366		/read selected register
			AND	(377

	the AC now contains the following :

		AC <0:4>	Undefined
		   <5>  	Framing Error
		   <6> 		Overrun Error
		   <7> 		Parity Error
		   <8:11>	Undefined

	In addition status register  1A  should  be  read  following  any
	Receive Data interrupt to check for Errors.
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 60     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	When the cause of the  interrupt  has  been  determined  and  the
	appropriate  action taken, Read Receiver, transmit next character
	etc., the interrupt condition must be cleared. For a READ this is
	done by writing to Control Register 0A with a data pattern of 70.
	For a Transmit Buffer condition, the transmit done condition must 
	first  be  cleared by issuing a write to CR0A with a data pattern
	of 50.

	   e.g. to dismiss the transmitter

		  	   CDF     00
			   TAD     (50	   /select CR0A
			   6366		   /and write 50 to it (dismisses
					   /transmitter)

	   and common exit for any interrupt condition

			   CDF	   00
			   TAD	   (70
			   6366 	   /select CR0A and write 70 to it
					   /(common End Of Interrupt Exit)

     C2.2 Modem Interrupts

	The second interrupt associated with the communications  port  is
	the  Modem  Change  Flag. This may be identified by a normal flag
	test,

			   6361    /Skip on Modem Change Flag, clear flag
				   /if found set

	   The Modem status may then be read by the Read Modem Status IOT

			   6364	   /Read Modem Status to AC<7:11>

		   AC <0:6>	   Undefined
			<7>	   State of Analog Loopback
			<8>	   State of Calling Indicator (Ring)
			<9>	   State of Signal Detect
			<10>	   State of Data Set Ready
			<11>	   State of Clear to Send












	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 61     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Appendix D.

	Memory Allocation

	Of the 64K words of memory available with  DECmate  II,  32KW  is
	allocated  to the Application Program at all times - Main Memory. 
	The second 32KW - Control Panel Memory, is used as follows :

	Fields <P0:1>   Firmware,  loaded  from  disk   controlling   the
			terminal emulation, keyboard handling etc.

	Fields <P2:3>   Display Buffer

	Fields <P4:7>   Not allocated, may be used  by  the  Applications
			Program with certain limitations.

	Additionally, at power-on time, Field 0 of Control  Panel  Memory
	is  overlayed  by  ROM with program execution starting at address
	P07777. ROM or RAM  may  be  selected  as  being  the  source  of
	instructions  and indirect addresses or the source/destination of
	operands in way similar to that in which the  IF  and  DF  fields
	operate  with  the  normal memory extension. The ROM-RAM accesses
	are controlled by the WSR (6246) instruction as follows :

		    Instruction Fetch (Defer)	Operand Access

	AC<11>=0    Next cycle from ROM		No change
	AC<ll>=l    Next cycle from RAM		No change

	AC<00>=0 	No change		ROM
	AC<00>=1	No change 		RAM






















	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 62     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     Appendix E.

	ROM Useage.

	DECmate II has, as noted in Appendix D, 4K of ROM which  overlays
	Field  0  of  Control  Panel  Memory  at  power-on time. This ROM
	performs several functions:

     E1. Processor Initialization

	Dynamic RAM memory is initialized. 
	The I/O Controller chips are initialized 
	The CRT Controller Chip is initialized 
	The Communications Controller Channel is initialized

     E2. Self Test

	A very basic RAM memory test is performed. The machine will  loop
	forever if this test fails.
	A simple loader is then moved from  ROM  to  RAM,  Control  Panel
	Field  P0  and  executed  to  move  the  remainder of ROM to RAM,
	Control Panel Field P7.
	Execution of the loaded code begins  at  RAM  address  P70200  in
	Control Panel Memory.
	Fields P2 and P3 of Control Panel Memory are cleared.
	The CRT Controller chip is checked to ensure that it  is  causing
	interrupts.
	Fields <MO:7> of Main Memory and Fields <P2:6> of  Control  Panel
	Memory are then tested.
	Code is moved to Main Memory to allow the normal interrupt system
	to  be  checked  for the Real Time Clock and Printer Port. Checks
	are also made to ensure that the HLT instruction, Panel  Requests
	and Keyboard instructions cause Control Panel Interrupts.
	The Keyboard serial data path is then checked in  local  loopback
	mode.
	If there is an RD51 present on the system, a delay of 15  seconds
	is  initiated  to allow time for the RD51 motor current demand on
	the power supply to drop to its normal operating level. When this
	delay  is  over,  or  if  it  is determined that there is no RD51
	present, the RX50 controller is allowed to start  by  issuing  an
	initial LCD IOT. Data transfer to/from the RX50 controller buffer
	is then checked.

	Any errors detected during the self-test result in the display of
	an error number at the completion of the test.

     E3. Bootstrap Procedure

	At the end of self-test,a further check is made for the  presence
	of the RD51 disk.

	. RD51 Present:

	If the controller is found to be present,  a  further  10  second
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 63     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	delay is initiated to allow the disk to come fully up  to  speed. 
	During  this 10 second period, the RD Ready bit is tested. If the
	bit does not come true before the 10 second period is  over,  the
	timer  is  reset  and  the flag test made again. Once the flag is
	found to be set, the disk error flag is checked. If there  is  an
	error  condition  indicated by the RD51 controller, bootstrapping
	continues using the RX50. If no  error  is  indicated,  the  RD51
	Startup  Block is read into Control Panel Memory Field P7. At the
	completion of the read, the block is checked  for  validity.  The
	first 6 bytes must be as follows :

			001	/Start of identifier sequence
			122	/R
			104	/D
			065	/5
			061	/1
			002	/End of identifier sequence

	If the Startup Block verifies good, it is then executed. Refer to
	the  appropriate  RD51 controller specification(s) for details of
	the Startup Block format.  If  the  block  is  invalid  (by  this
	check), bootstrapping continues from the RX50.

	. RD51 Not present:

	A Read Status command is issued to the RX50 controller  and  a  4
	second timer established. If the RX50 controller does not set the
	Done flag within this period, the sequence is repeated. When  the
	Done  flag  is finally found, the drive status is read. If Unit 0
	(Drive A) is not ready, the DECMATE II logo  is  displayed  as  a
	double height , double width image, centred on the screen. If the
	drive is ready or when it does become ready (when a  diskette  is
	inserted in drive 0), the screen is cleared and Track 1 Sector 0,
	the Bootstrap Block for  all  operating  systems,  is  read  into
	memory  in  8-bit  mode. If a disk error is indicated during this
	read operation, a picture  of  a  diskette  is  displayed  as  an
	indication  to  try another system disk. If no error is indicated
	by the disk  controller,  the  data  read  is  then  checked  for
	validity.  A  valid  Boot  block  must  conform to the Boot Block
	Standard (See Appendix G).  If  the  validity  check  fails,  the
	diskette picture is displayed and the read operation repeated. If
	the Boot Block passes this check it is assumed good.

	The next area of  the  diskette  to  be  validated  is  the  Main
	Keyboard  Translation  Table. This is stored in sector 3 of Track
	0. This area of the diskette  is  read  in,  in  8-bit  mode,  to
	Control  Panel  Memory,  starting  at  address 15350. (The actual
	keyboard translation table data begins at 15360, the first  eight
	characters  read  which  are  used for validation are read into a
	buffer area). If a disk controller error is indicated during this
	read  operation,  the  diskette picture is displayed and the read
	repeated. If no controller error is indicated, the data read  can
	then be validated. The first bytes read must be :
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 64     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
			001	/Start of identifier sequence
			113	/K
			102	/B
			104	/D
			102	/B
			122	/R
			104	/D
			002	/End of identifier sequence

	If the data does not pass this check,  it  is  assumed  that  the
	keyboard  translation  table  is invalid, the diskette picture is
	displayed and the read operation repeated. If the validity  check
	is  passed, system initialization continues with reading the User
	Character Generator RAM data from the diskette, Track 0,  Sectors
	7  -  10,  into  memory. If no controller error is indicated, the
	data read in is  validated  in  the  same  way  as  the  Keyboard
	Translation Table. In this case the first words of data read must 
	be :

			001	/Start of identifier sequence
			125	/U
			103	/C
			107	/G
			122	/R
			101	/A
			115	/M
			002	/End of identifier sequence

	If the validity check fails, or if there was  a  disk  controller
	error  indicated  after  the  read  operation, the User Character
	Generator RAM is loaded with zero (all blank characters). If  the
	validity  check  is  passed,  the  data read from the diskette is
	loaded into the UCG RAM.

	This completes the loading of language  specific  data  from  the
	diskette,  the actual firmware is now loaded. All Track 78 is now
	read in 12-bit  mode  into  Control  Panel  Memory,  starting  at
	address  P00000.  If  a  controller  error  is  indicated  at the
	completion of the read, the diskette picture is displayed and the
	entire  diskette  readin  operation  restarted.  If no controller
	error is indicated, the remainder of Control Panel  Memory  Field
	P0  is  loaded  from Track 79, Sectors 1 - 6, with the same check
	made for controller error as with Track 78. Following  this,  the
	remainder of Track 79 is read into Control Panel Memory Field P1,
	starting at address P10000 with the same error check  made.  When
	all  the  firmware  has been read in, it is checked for validity,
	memory locations P00001 - P00003 must be :

			P00001/6201
			P00002/0033
			P00003/0077

	(memory location P00000 contains the current  firmware  revision)
	If   the  validity  check  fails,  the  entire  diskette  read-in 
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 65     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	operation is restarted.  If  the  check  is  good,  execution  of
	firmware begins at Address P00200 in Control Panel Memory.



















































	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 66     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
     E4. SETUP

	Code in ROM supports the "SETUP" feature of  the  DECmate  II  to
	allow  certain  screen  features  such  as  column mode (80/132),
	cursor style etc. to be changed by a user and  optionally  stored
	in  the  firmware  area  of the system diskette to be used as new
	defaults. SETUP is invoked by a  user  program  issuing  a  Panel
	Request  to the firmware which in turn loads a section of the ROM
	into Control Panel Memory Field P7 and then transfers control  to
	the  loaded code at address P00177, by means of a subroutine call
	to address P000176 with the AC = 0000. (See HLT processing)

	The ROM code then reads Track 0, Sectors 1 and 2 in  8-bit  mode.
	These two sectors contain the text file that results in the SETUP
	Menu being displayed. The text  file  is  validated  after  being
	read.  If there is an error on reading in these two sectors or if
	the validation check fails, return is  made  immediately  to  the
	firmware  and  hence  to the user program. The first bytes of the
	text file must be:

			001	/Start of identifier sequence
			123	/S
			105	/E
			124	/T
			125	/U
			120	/P
			002	/End of identifier sequence

	The remainder of the file can contain any text  with  a  page  of
	text  starting  with  a  control  code  002 (^B), using any 8-bit
	character codes, but must refer in  sequence  to  the  selectable
	parameters  as listed below. The end of a text field and start of
	a parameter field is  defined  by  the  control  code  036  (^^),
	sub-fields  within a parameter field are separated by the control
	code 037 (^_). The end of the entire screen of text is defined by
	the  control  code  003  (^C). Subsequent pages are prefixed with
	another control code 002 (^B). See the  example  of  the  English
	Language  SETUP  file below, in particular refer to the operating
	instructions given below the row of "====".

	In  this  example,  the  following  representations  of   control
	characters are used:

		. 	Space
		^A 	001
		^B 	002
		^C 	003
		^^ 	036
		^_ 	037

	All other codes are actual displayed characters.

	The second "page" of text "Are you sure etc..." is  displayed  in 
	response  to  the  user  pressing  the  "Do"  key to save the new 
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 67     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	Selections on the  firmware  area  of  the  system  diskette.  It
	replaces  the  text  displayed below the row of "====". The third
	"page" of text is displayed in response to the user pressing  the
	"Re-move"  key  to  mount  a new system diskette. It replaces the
	entire page.

	English Language SETUP Text File Version 1.

	^ASETUP^B......USER.SELECTIONS.MENU

	Screen.Width..........^^80......^_132
	Cursor.Style..........^^Block...^_Underline
	Cursor.Visibility.....^^Visible.^_Invisible
	Scrolling.............^^Fast....^_Slow
	Screen.Mode...........^^Normal..^_Reverse

	Keyboard.keyclick.....^^ON......^_OFF

	Terminal.Mode.........^^VT100...^_VT52

	Baud.rates

	.....Printer..........^^300^_600^_1200^_2400^_4800^_9600
	.....Communications...^^300^_600^_1200^_2400^_4800^_9600

	=======================================================================
	....Press.:
	...........'->'.to.Advance '<-'.to.Backup,.'Select'.to.fix.new.selection
	...........'Do'.to.fix.new.selections.and.leave.Selections.Menu
	...........'Return'.to.use.new.selections.and.leave.Selections.Menu
	...........'Remove'.to.load.new.System.Disk
	^C^BAre.you.sure.?..Press.'Do'.to.confirm
	^C^BInsert.new.System.Disk.and.press.'Do'

	Any.other.key.will.return.to.User.Selections.Menu
	^C

















	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 68     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

     Appendix F.

	RX50 Disk Format/Useage.

	There are three tracks on a DECmate II floppy diskette  that  are
	reserved  and  may not be used by any operating system, tracks 0, 
	78 and 79.

	Track 0 :

	Sectors 1 and 2 contain the text file  that  supports  the  SETUP
	handler  part  of  ROM.  These  sectors are written (and read) in 
	8-bit mode.

	Sector 3 contains the main keyboard translation table, (the  main
	keyboard  comprises  all keys of the main array, but excludes the
	cursor pad, the application pad  and  the  function  keys).  This
	sector  is  written  (and  read in) in 8-bit mode and consists of
	four bytes per key location on the main key array, defining  what
	each key shall generate in the four possible modes :

	Normal, Shifted, Caps (or Shift) Lock and Control.

	The value stored in each location of  the  table  is  the  actual
	8-bit  value  to  be  generated  for  that combination of key and
	modifier. For any key and modifier that generates no  code,  that
	table entry is set to contain a zero.

	Example : Key address 194 is  the  key  labelled  "A",  the  four
	entries for this key address are :

		Normal  Shift   Caps Lock	Control

		141 	101 	101		001
		(a)     (A)     (A)		(Control code SOH)

	The key sequence is as follows :

		Key Address	Key definition for USASCII - WPS

		188		DELETE
		189		RETURN
		190		TAB
		191		GRAVE ACCENT- TILDE
		192		1 !
		193		Q
		194		A
		195		Z
		196		NO KEY AT THIS POSITION
		197		2 @
		198		W
		199		S
		200		X
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 69     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
		201		< >
		202		NO KEY AT THIS POSITION
		203		3 #
		204		E
		205		D
		206		C
		207		NO KEY AT THIS POSITION
		208		4 $
		209		R
		210		F
		211		V
		212		"SPACE"
		213		"SPACE"
		214		5 %
		215		T
		216		G
		217		B
		218		NO KEY AT THIS POSITION
		219		6 ^
		220		Y
		221		H
		222		N
		223		NO KEY AT THIS POSITION
		224		7 &
		225		U
		226		J
		227		M
		228		NO KEY AT THIS POSITION
		229		8 *
		230		I
		231		K
		232		, ,
		233		NO KEY AT THIS POSITION
		234		9 (
		235		O
		236		L
		237		. .
		238		NO KEY AT THIS POSITION
		239		0 )
		240		P
		241		NO KEY AT THIS POSITION
		242		; :
		243		/ ?
		244		NO KEY AT THIS POSITION
		245		= +
		246		] }
		247	 	\ |
		248		NO KEY AT THIS POSITION
		249		- _
		250		[ {
		251		' "
		252		NO KEY AT TH IS POSITION
		253 		NO KEY AT THIS POSITION
		254		NO KEY AT THIS POSITION
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 70     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

		255 		NO KEY AT THIS POSITION

	For keys required to generate a NULL (000) code, the  appropriate
	table  location  is  setup  to contain 377. (For the USASCII- WPS
	keyboard, there are three entries of this kind, the  two  "SPACE"
	key  addresses  and  the "2" key address, all three generate NULL
	for the CNTRL condition). The ROM loading program then performs a
	further  translation  on  this code to load a 4000 value into the
	actual keyboard translation table.

	Refer  to  LK201  Keyboard  Specification  for  Foreign  Language
	Variations.

	Sector 4 contains the text file that supports the HLT instruction
	part  of the ROM code. This file is specified in a similar way to
	the SETUP text file. When a HLT instruction is executed  in  user
	memory,  the  HLT  processor  present  in  panel memory moves the
	contents of ROM into control panel memory Field  7,  starting  at
	location  70100  and then transfers control to the loaded code by
	executing a JMS to location 70176. The HLT processing  code  then
	reads  Track 0 Sector 4 and performs a validity check on the text
	data. The first eight words read must be :

				001	/Header
				110	/H
				114	/L
				124	/T
				106	/F
				114	/L
				107	/G
				002	/Terminator

	If an error is made on reading the  sector  or  if  the  validity
	check  fails,  return  is made immediately to the firmware, which
	will in turn return to the user program at the location following
	the  HLT  instruction. If there is no read error and the validity
	check is passed, the CRT controller Row Address Table is reset so
	that  the  current  screen data may be preserved for the possible
	return from the HLT processing and the text file displayed.  This
	is  formatted  in  the same way as the SETUP text file but allows
	only the options of "Do" to continue from the HLT and "SETUP"  to
	enter  SETUP.  If the "Do" option is selected, the CRT Controller
	RAT is reset to restore the original screen data.

	Sectors 5 and 6 are currently unused.

	Sectors 7 - 10 contain the  data  to  be  loaded  into  the  User
	Defined  character  Generator RAM. This data is read in as a part
	of the Bootstrap process. If a disk read error occurs or the disk
	data  fails  a  validity  check, the User Charatcer RAM is filled
	with nulls. If there is no read error and the validity  check  is
	passed,  the  data read is loaded into the RAM. The data consists
	of 16 bytes  per  character,  one  byte  for  each  possible  RAM
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						      16-January-1983
						      Page 71     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

			    DECmate II  Specification
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -

	location allocated for a character. As only 10 lines are actually
	used  to  display a character, only the first 10 bytes of each 16
	have significance, the last 6 of a group of 16  should  be  zero.
	The validation check for this data is :

			001	/Header
			125	/U
			103	/C
			107	/G
			122	/R
			101	/A
			115	/M
			002	/Terminator

     Appendix G.

	The section of the RX50 Bootstrap Block Standard that applies  to
	DECmate  II  requires  that  The  Boot  Block (Track 1, Sector 1)
	contain the following at its beginning :

		Byte #		Contents

		0		0
		1		0
		2		N - an   offset    to    additional    ID
				    information
		3		1 - System Disk (A non-system disk  would
				    contain 0 here)
		4		0
		5		0

	Additional ID words begin here

		2*N+2		010 - PDP 8 Code on this diskette
		2*N+3		010 - RX278 Controller
		2*N+4		010 - WPS8 Diskette Structure
				011 - OS8 Diskette Structure
				012 - COS310 Diskette Structure
				100 - CP/M Diskette Structure
		2*N+5		347 - WPS8  )
				346 - OS8   ) computed check value
				345 - COS310) for above data
				257 - CP/M  )
		2*N+6		0   - always
		2*N+7		1   - Revision of this standard +  single
				      sided diskette

	For greater detail refer to the actual standard.





	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -
						   16-January-1983
						   Page 72     Rev 4
	- - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - - -