-----------------------------------------------------------------
	------------------------------
	|    |   |   |   |   |   |   |			 ENGINEERING
	|  D | I | G | I | T | A | L |			SPECIFICATION
	|    |   |   |   |   |   |   |
	------------------------------
	-----------------------------------------------------------------











			 LK200 FUNCTIONAL SPECIFICATIONS

















	Copyright (c) May, 1982 	    Digital Equipment Corporation
	Author L. Huntington




	These designs and specifications are the sole property of Digital
	Equipment Corporation and shall not be reproduced, copied or used
	in whole or in part as a basis for the manufacture or sale of any
	equipment  described  herein  without  written  permission of the
	owner.





				Table of Contents				_________________
			

	  Section 						   Page

	1.0     INTRODUCTION 					     1
	1.1       Scanning					     2
	1.1.1       Timing Requirements				     2
	1.1.2       Sneak Path Detection			     2
	1.1.3       Rollover					     2
	1.2       Transmission					     2
	1.2.1       Transmission Buffer and speed		     2
	1.2.2       Transmission Encoding			     2
	1.3       Receive					     3
	1.3.1       Receive Buffer and Speed			     3
	1.3.2       Receive Encoding				     3

	2.0     KEYBOARD FUNCTIONAL DIVISIONS 			     3

	3.0     MODES 						     3
	3.1       Down Only					     4
	3.2       Down, Autorepeat				     4
	3.3       Down/up				 	     4
	3.4       Special Considerations Regarding Autorepeat	     4
	3.5       Special Considerations Regarding Down/up mode	     6
	3.6       Autorepeat Rates				     6

	4.0     KEYBOARD PERIPHERALS 				     6
	4.1       Audio						     6
	4.2       LED's						     7

	5.0     KEYBOARD-TO-TERMINAL PROTOCOL 			     7
	5.1       Keycode Transmission				     7
	5.2       Special Code Transmission			     7
	5.3       Powerup Transmission				     9

	6.0     TERMINAL-TO-KEYBOARD PROTOCOL 			     9
	6.1       Commands					    10
	6.2       Parameters					    10
	6.3       Peripheral Commands				    11
	6.3.1	    Flow control				    12
	6.3.2	    LED's					    13
	6.3.3	    Audio					    13
	6.3.4	    Autorepeat					    13
	6.3.5	    Other					    13
	6.4       Mode Set Commands				    14
	6.4.1       Division Mode Settings			    14
	6.4.2       Autorepeat Rate Buffer Association		    15
	6.4.3       Autorepeat Rate Buffer Values		    15

	7.0     SPECIAL CONSIDERATIONS 				    16
	7.1       Error Handling				    16
	7.2       Keyboard Locked Condition			    17
	7.3       Reserved code					    17
	7.4       Test mode					    17
	7.5       Future Expansion				    17

								  Page ii



				Table of Contents				_________________


	  Section 						   Page

	8.0     APPENDIX I    KEYCODE TRANSLATION TABLE 	    19
	9.0     APPENDIX II   DEFAULTS 				    24
	10.0    APPENDIX III  KEYBOARD MATRIX  			    25
	11.0    APPENDIX IV   KEYSWITCH LAYOUT       		    27


 								   Page 1

    1.0 INTRODUCTION

	This document is a specification of  the  firmware  functionality
	available  in  the  LK200 keyboard.  Products using the LK200 may
	use only a subset of the functionality available in the keyboard.

	The firmware inside the keyboard  is  responsible  for  executing
	three concurrent tasks.

	The first task consists of detecting any changes in the state  of
	the  keyboard  matrix, referred to as the process of scanning the
	keyboard.

	The second task consists  of  transmitting  the  results  of  the
	keyboard scan to the terminal.

	The  third  task  consists  of  receiving  information  from  the
	terminal.  This  information  may  control  either the peripheral
	hardware or the transmission parameters on the LK200.

 								   Page 2

    1.1 SCANNING

    1.1.1 Timing Requirements

	The LK200  firmware  is  responsible  for  handling  a  Keystroke
	depressed  for  as little as 20 ms., during which time the switch
	closure may be expected to bounce for 5 ms. Multiple keys will be
	detected  in  correct  order  when interkeying times are not less
	than 8.33 ms.

	Given the susceptibility to high frequency noise, each  key  must
	be verified as a legitimate event.

	Scan rate is 120 hertz, or 8.33 ms.


    1.1.2  Sneak Path Detection

	A sneak path, or "ghost" key may occur  only  when  3  out  of  4
	corners  of a rectangle in the keyboard matrix are closed.  Sneak
	paths will be prevented by  carefully  laying  out  the  keyboard
	matrix positions, so that the keys belonging to a  single fingers
	zone are not found in the same row.  However, should a sneak path
	occur,  firmware will not transmit the keys involved until one of
	the keys causing the condition is  released.  This  will  prevent
	the transmission of ghost keys entirely.


    1.1.3  Rollover

	With the exception  of  those  keys  involved  in  a  sneak  path
	arrangement,  the  keyboard will transmit ALL keys depressed.  It
	is, however, limited by transmission speed and the  size  of  its
	output  buffer.  The  keyboard is capable of transmitting 4 bytes
	per scan.  Rollover is determined by the amount of time the  keys
	are  held  down.  If  they are held down for 17 ms., the keyboard
	will scan them twice, and therefore be able to  send  8  keycodes
	from its 4-byte fifo.  Actually, 17 ms. is considered to be below
	the minimum time that the keys can be held closed.  If  the  keys
	are  held down for another scan (25 ms.), then 12 keycodes can be
	transmitted.  Of course, if there are sneak paths  involved,  not
	all keys can be transmitted.



    1.2  TRANSMISSION

    1.2.1  Transmission Buffer and Speed

	The LK200 has a transmission speed of 4800 bps and a fifo size of
	4 bytes.


    1.2.2  Transmission Encoding

	Encoding of transmit and receive data is identical.  Each encoded
	event  is  framed  into  10  single  elements, each element being
	transmitted at equal time intervals.  The first element (0)  will

								   Page 3

	be the start (spacing) element;  the next 8 elements will contain
	data.  The last element will be the stop (1) element.



    1.3  RECEIVE

    1.3.1  Receive Buffer and Speed

	The LK200 has a receive speed of 4800 bps and a fifo  size  of  4
	bytes.  Commands  are  processed  within  1 ms.  after the entire
	command is received.


    1.3.2  Receive Encoding

	Encoding of transmit and receive data is identical.  Each encoded
	event  is  framed  into  10  single  elements, each element being
	transmitted at equal time intervals.  The first element (0)  will
	be the start (spacing) element;  the next 8 elements will contain
	data.  The last element will be the stop (1) element.



    2.0 KEYBOARD FUNCTIONAL DIVISIONS

	The keyboard is divided into 14 functional divisions.

	These fourteen functional divisions are:

		Division	        ________

		1.  48 graphic keys, Spacebar and B13, D13, D99  and  E99
		    on the typewriter mass
		2.  Numeric keypad
		3.  Delete Character(E12)
		4.  Return(C13) and Tab(D00)
		5.  Lock(C00), COMPOSE(A99) and A10
		6.  Shift(B00 and B11) and CTRL (C99)
		7.  Horizontal cursors(B16 and B18)
		8.  Vertical cursors(B17 and C17) and A17
		9.  Six keys directly above the cursor keys (D16-D18  and
		    E16-E18)
	    Function Keys
		10. G99-G04 and H99-H04
		11. G05-G09 and H05-H09
		12. G10-G14 and H10-H14
		13. G15-G16
		14. G20-G23 and H20-H23

	See Appendix IV for keyswitch designators.



    3.0 MODES

	Section 3 explains the overall  function  of  the  three  keycode
	transmission   modes.  For  actual  mode  set  and  special  code

								   Page 4

	transmission protocol, please see  sections  5.1,  6.3  and  6.4.
	Any  one of the keyboard's functional divisions may be set to any
	one of the following modes.

		Mode			Function		____			________

		Down only		Keyboard sends key code when  key
					is first depressed.
	
		Autorepeat, Down	Keyboard sends key code when  key
					is  first  depressed,  then sends
					"metronome"   code   and   sounds
					keyclick   at  the  specified  or
					default rate, until that  key  is
					released.

		Down UP			keyboard sends key code when  key
					is  first  depressed,  and either
					key code or "all ups"  code  when
					key is released.


	See Appendix II for division defaults.


    3.1  Down only

	"Down only" keys transmit a keycode when they are depressed.


    3.2  Down, Autorepeat

	"Autorepeat" keys transmit a keycode when they are depressed.  If
	the key is held down past the specified or default timeout period
	(usually 300 to 500  ms.),  then  a  fixed  "metronome"  code  is
	transmitted.  "metronome"  codes  will  then  be  sent at regular
	intervals until the key is released.


    3.3 Down/up Mode

	"Down up" keys transmit a keycode when they are depressed and  an
	"up code" when they are released.  The "up code" will be either a
	repeat of the keycode or an "all ups"  code.  If  there  are  any
	other  down/up  keys down on the keyboard, it will be a repeat of
	the keycode.  If there are no other  down/up  keys  down  on  the
	keyboard, it will be an "all ups" code.


    3.4  Special Considerations Regarding Autorepeat

	If multiple autorepeating keys are held down,  "metronome"  codes
	will  still  be  generated.  The  metronome  codes  apply  to the
	keycode which was transmitted most recently.  If that  "last  key
	down"  is  released,  and  other  key(s)  is(are) still down, the
	keycode of one of the "down" keys will be retransmitted.

								   Page 5

		Example:  Suppose the "a" key is being held down.
		      	  Transmission will look like this:

		a metronome metronome
	Now suppose the "b" key is depressed.
		a metronome metronome b metronome metronome
	Now the "b" key is released.
		a metronome metronome b metronome metronome a met. met.

	A non-autorepeating keycode or special code  may  be  transmitted
	while  metronome  codes  are being generated for an autorepeating
	key. In this case, the keyboard will transmit, in  the  place  of
	the  next  metronome  code,  the  keycode  of  the  key  which is
	supposed to  be  autorepeating.  This  way,  the  keycode  to  be
	autorepeated is always the LAST BYTE TRANSMITTED.

		Example: Suppose the "a" key is being held down.
			 Transmission will look like this:

		a metronome metronome
	Now suppose the SHIFT key is depressed.
		a metronome metronome shift a metronome
	Now the SHIFT key is released.
		a metronome metronome shift a metronome allups a met...

	If, for any reason, an autorepeating key  should  not  autorepeat
	(such  as  a  CTRL "C", for example), the terminal should issue a
	"temporary  inhibit  autorepeat"  command.  This  will  halt  the
	transmission  of  any  metronome  codes or keyclicks FOR THAT KEY
	ONLY.  Metronome codes will resume when another key is depressed.
	The   command   must   be   issued  after  the  keycode  for  the
	autorepeating key is received.

	Autorepeat can be  enabled  and  disabled  independently  of  the
	division  settings, using the enable/disable autorepeat commands.
	This is an "across the  board"  enable/disable.  Internally,  the
	keyboard  is  still  autorepeating characters while autorepeat is
	disabled,  but  simply  does  not  transmit  metronome  codes  or
	keyclicks.  Therefore,  when autorepeat  is enabled, the keyboard
	will resume metronome transmission at the point where it would be
	if  autorepeat  were not disabled in the first place. This may be
	within EITHER the timeout or interval period, depending upon  the
	time elapsed since key depression.

	During the period that a  key  is  depressed,  the  keyboard  may
	receive  a  request to change that division's mode to autorepeat.
	This change will be implemented by the LK200  immediately.  After
	the  regular timeout period, the keyboard will transmit metronome
	codes for the key depressed.  In place  of  the  first  metronome
	code, the Keyboard will transmit the keycode of the autorepeating
	key.

	It is possible to change the mode of all autorepeating  divisions
	to  down  only with one command.  This and some other across-the-
	board autorepeat  commands  are  grouped  with  the  "peripheral"
	commands. (see section 6.3)

								   Page 6

    3.5  Special Considerations Regarding Down/up Mode.

	If two down/up keys are released simultaneously, (within the same
	scan),  and there are no other down/up keys down on the keyboard,
	only one "all ups" code will be generated.


    3.6  Autorepeat rates

	There are four buffers in the keyboard to store autorepeat rates.
	They  are  numbered  O  through 3.  Two values are stored in each
	buffer.  The first value is the "timeout" value.  The  second  is
	the  "interval"  value.  The values in each buffer can be changed
	by the terminal.

	The "timeout" value reflects  the  amount  of  time  between  the
	detection  of  a  key  down  and  the  transmission  of the first
	metronome  code  (defaults  range  from  300  to  500  ms.)   The
	"interval"  value  reflects  number of metronome codes per second
	(defaults to 30).

	Each division is associated with one of the four  buffers.  Rates
	are  taken  from  the  associated buffer each time the autorepeat
	timers are loaded.  This buffer-to-division  association  can  be
	changed by the terminal or left to default.



    4.0  KEYBOARD PERIPHERALS

	Section 4 is an overall explanation of the peripherals  available
	on  the  keyboard.  See  section 6.3 for information on  terminal
	control of these peripherals.

	Keyclick, bell and LED's are all considered "peripherals" on  the
	keyboard.


    4.1  Audio

	Keyclick is a 2 ms. "beep".  Bell is a 125 ms.  "beep".  Bell  is
	sounded  ONLY  upon  request from the terminal.  Keyclick (if not
	disabled by the terminal) is sounded under three conditions:

		1. When a Key is depressed
		2. When a metronome code is sent.
		3. When a "sound keyclick" command is received  from  the
		   terminal.

	Keyclick will NOT be generated when Keys B11  or  B99  (the  left
	and  right SHIFT keys on the LK201) are depressed.  Keyclick will
	NOT be generated when key C99 (the CTRL  key  on  the  LK201)  is
	depressed,  unless  a command is sent from the terminal to enable
	keyclick on that Key. (see section 6.3, key positions illustrated
	in Appendix IV)

	Either keyclick or bell (or both) may be disabled.  When keyclick
	or  bell  is  disabled,  it  will not sound, even if the terminal

								   Page 7

	requests it. (see  section  6.3  for  enable  and  disable  audio
	commands).

	Both keyclick and bell may be set (independently)  to  one  of  8
	volume levels. Volume levels are as follows:

		000 - highest
		001
		010 - default
		011
		100
		101
		110
		111 - lowest


    4.2  LED's

	The  terminal  is  responsible  for  transmitting   LED   control
	commands, with the following exceptions:

		1. The keyboard will turn OFF all LED's on powerup.
		2. The keyboard will light the Keyboard Locked  LED  upon
		   receipt  of an "inhibit transmission" command and turn
		   it  off  upon  receipt  of  a  "resume   transmission"
		   command.



    5.0  KEYBOARD-TO-TERMINAL PROTOCOL

    5.1  Keycode Transmission

	The  keyboard  is  responsible   for   transmitting   single-byte
	keycodes  which  reflect  the  state of the keyboard matrix.  The
	8-bit codes  above  64  are  used  for  keycodes.  Every  key  is
	identified  by  its  unique  keycode.  There are no special codes
	for shifted or control keys.

	See Appendix I for the complete keycode matrix translation table.


    5.2  Special Code Transmission

	There are also 13 "special" codes, some  with  values  above  64,
	some below.

	Nine special codes have been defined  above  64,  (keycode  value
	range):
		1. ALL UPS		Keycode 179 Dec, B3 Hex
		2. METRONOME CODE	Keycode 180 Dec, B4 Hex
		3. OUTPUT ERROR		Keycode 181 Dec, B5 Hex
		4. INPUT ERROR		keycode 182 Dec, B6 Hex
		5. KBD LOCKED ACK	Keycode 183 Dec, B7 Hex
		6. TEST MODE ACK	Keycode 184 Dec, B8 Hex
		7. PREFIX TO KEYS DOWN  Keycode 185 Dec, B9 Hex
		8. MODE CHANGE ACK 	Keycode 186 Dec, BA Hex
		9. RESERVED 		Keycode 127 Dec, 7F Hex

								   Page 8

	Four special codes have also been defined within the  "below  64"
	value range.
		1. KEYBOARD ID - FIRMWARE (01 Dec, 01 Hex)
		2. KEYBOARD ID - HARDWARE (00)
		3. KEY DOWN ON POWER UP ERROR CODE (61 Dec, 33 Hex)
		4. POWERUP SELF-TEST ERROR CODE (62 Dec, 3E Hex)

	METRONOME CODE indicates to the terminal  that  an  interval  has
	passed,  a keyclick has been generated, and the last key received
	by the terminal is still depressed.

	ALL UPS indicates to the terminal that a  down/up  mode  key  was
	just  released,  and that now there are no more down/up keys down
	on the keyboard.

	OUTPUT ERROR indicates to the terminal that the keyboard's output
	buffer  overflowed  after receipt of a "keyboard inhibit" command
	from the terminal, and that some keystrokes may have been lost.

	INPUT ERROR CODE indicates to  the  terminal  that  the  keyboard
	received a garbage command, or too many or too few parameters.

	KEYBOARD LOCKED CONFIRMATION indicates to the terminal  that  the
	keyboard received an "inhibit transmission" command. (see section
	6.3)

	TEST MODE ACKNOWLEDGE indicates that the keyboard has  gone  into
	TEST  MODE.  This  is  a  special  mode inserted for a production
	bed-of-nails tester.  If the terminal receives  this  acknowledge
	unsolicited,  it  should send "80 HEX", which will terminate test
	mode and jump to powerup.

	MODE CHANGE ACKNOWLEDGE indicates that the keyboard has  received
	and processed a mode change command. (see section 6.4)

	PREFIX TO KEYS down indicates that the next byte is a keycode for
	a  key  already  down  in  a  division  which has been changed to
	down/up. (see Section 6.4)

	Keycode 7F is reserved for internal use.

	KEYBOARD ID is a two byte identification code, transmitted  after
	the  powerup  self-test  is performed.  (see section 5.3) it will
	also be sent upon request from the terminal (see section 6.3)

	POWER UP SELF TEST ERROR CODE indicates to the terminal that  the
	ROM or RAM self-test of the terminal failed. (see section 5.3)

	The keyboard may be locked by command  from  the  terminal.  Upon
	receiving  the  "inhibit transmission" command, the keyboard will
	light the "Keyboard  locked"  LED.  It  will  then  transmit  the
	KEYBOARD  LOCKED  ACKNOWLEDGE  special  code.   The keyboard will
	attempt to buffer characters (up to four) until its output buffer
	overflows.  Then  it  will  stop  scanning  its  matrix. When the
	keyboard is  subsequently  unlocked  by  the  terminal,  it  will
	transmit  all  bytes  collected  in  its  buffer, followed by the
	"OUTPUT ERROR," special code if the buffer overflowed  while  the
	keyboard was locked.

								   Page 9

    5.3  Power Up transmission

	Upon powerup, the LK200 will perform a self test and transmit the
	results of that self-test to the terminal in 4 bytes.

		BYTE 1:   KBID (firmware) - the  keyboard  ID  which   is
					    stored in firmware

		BYTE 2:   KBID (hardware) - the keyboard ID which is read
					    from jumpers in the hardware

		BYTE 3:   ERROR or O - 	    Two  error   codes   indicate
					    either  a)  failure of ROM or
					    RAM  self-test   within   the
					    processor (3E HEX) b) keydown
					    on powerup (3E HEX)

		BYTE 4:   KEYCODE or O -    the keyboard does a  complete
					    scan   for   keys   down   on
					    powerup.   There  should   be
					    none.   If   there  are,  the
			 		    error code  (above)  will  be
					    set    and    first   keycode
					    detected will be sent as  the
					    fourth byte.

	If  the  ROM  self-test  (checksum)  fails,  the  error  may   be
	catastrophic. 	The  keyboard  may  be unable to send anything at
	all.

	If the keyboard finds a key down  on  the  first  scan,  it  will
	continue to look for an "all key UP" condition.  If the offending
	key(s) is  (are)  released,  then  the  keyboard  will  send  the
	corrected  4-byte  powerup  sequence  (unsolicited).  This  is an
	attempt  to  avoid  a  fatal  error   condition   when   a   user
	inadvertently holds down a key while powering up.

	The keyboard LED's are all lit during powerup. If  the  self-test
	passes,  the  keyboard will turn all LED's off.  The terminal may
	transmit a "sound bell" command to the  keyboard  if  a  bell  is
	desired  upon  powerup.  This  should  not be done until the last
	byte of the four-byte sequence is received by the terminal.  This
	will test the serial line and terminal connection.

	Powerup self test will not exceed 70 ms.

	A jump to powerup can be requested at any time from the terminal.
	Please  note  that  a jump to powerup will cause the LED's on the
	keyboard to "blink" on and off once.



    6.0  TERMINAL-TO-KEYBOARD PROTOCOL.

	The terminal can control both the peripherals associated with the
	Keyboard  and some of the keyboard transmit characteristics.  The
	protocol for the transmission of commands and parameters from the
	terminal to the Keyboard is as follows:

								  Page 10

    6.1  Commands

	There are two types of commands--  those  that  control  keyboard
	transmission  characteristics  and  those  that  control keyboard
	peripherals.  The LOW bit of the command is the "TYPE flag".   It
	is  clear  if the command is a TRANSMISSION command. It is set if 	
	the command is a PERIPHERAL command.

		TRANSMISSION COMMANDS		PERIPHERAL COMMANDS    		_____________________		___________________

		mode set			flow control
		autorepeat rate set		led
						audio
						keyboard ID
						reinitiate kbd
						some autorepeat control
						jump to test mode
						reinstate defaults

	The HIGH order bit of every command is the "PARAMS" flag.  It  is
	clear  if  there ARE any parameters to follow. It is set if there
	are NO parameters.


    6.2 Parameters

	The HIGH order bit of every parameter is the  "PARAMS  flag".  It
	is clear if there are more parameters to follow. It is set on the
	last parameter.  The remaining 7 bits of the  parameter  are  for
	data.

				COMMAND SUMMARY (with parameters)

				  7    6   5   4   3    2   1    0
				-------------------------------------
		COMMAND:	| O | representation  | mode or|type|
				|   |		      | off/on |    |
				-------------------------------------

		PARAMETERS:	-------------------------------------
				| O |	 	data	            |
				-------------------------------------
		
				-------------------------------------
				| 1 |		data		    |
				-------------------------------------

								  Page 11

    6.3  Peripheral Commands

		Command			  	Representation		_______			  	______________

		Flow Control			     0001
		LED				     0010
		Keyclick			     0011
		Bell				     0100
		KBD ID				     0101
		Reinitiate keyboard		     0110
		  to defaults (Jmp to PWRUP)
		Keyclick for CTRL key		     0111
		Temporarily inhibit autorepeat	     1000
		Jump to test mode 		     1001

								  Table I


	To send a "Peripheral" type command, set  TYPE  flag  (low  order
	bit).  Bits 6 - 3 contain a COMMAND representation from the above
	chart. Bits 2 and 1 specify on (01), off  (00),  or  sound  (11).
	Bit 7 should be set if there are no parameters to follow.

								  Page 12

	The following chart summarizes the peripheral commands in HEX.


	     -------------------------------------------------------
	    |   FUNCTION		 |   HEX   |   PARAMETERS   |
	    |============================|=========|================|
	    | Flow control 		 |	   |		    |
	    |----------------------------|---------|----------------|
  	    | resume kbd xmission	 |   8B    |      NONE      |
	    | inhibit kbd xmission       |   89    |      NONE      |
	    |----------------------------|---------|----------------|
	    | LED's			 |	   |		    |
	    |----------------------------|---------|----------------|
	    | light LED(s)		 |   13    |  Bit pattern   |
	    | turn off LED(s)	         |   11    |  Bit pattern   |
	    |			         |	   |		    |
	    |----------------------------|---------|----------------|
	    | Audio		         |	   |		    |
	    |----------------------------|---------|----------------|
	    | disable keyclick	         |   99    |      NONE      |
	    | enable click, set vol      |   1B    |      volume    |
	    | disable CTRL keyclick      |   B9    |      NONE      |
	    | enable CTRL keyclick       |   BB    |      NONE      |
	    | sound keyclick	         |   9F    |      NONE      |
	    | disable bell	         |   A1    |      NONE      |
	    | enable bell, set vol       |   23    |      volume    |
	    | sound bell		 |   A7    |      NONE      |
	    |			         |	   |		    |
	    |----------------------------|---------|----------------|
	    | Autorepeat		 |	   |		    |
	    |----------------------------|---------|----------------|
	    | Temp. autorpt inhibit      |   C1    |      NONE      |
	    | Enable AR across kbd       |   E3    |      NONE      |
	    | Disable AR across kbd      |   E1    |      NONE      |
	    | Change all AR to down only |   D9    |      NONE      |
	    |                            |         |                |
	    |----------------------------|---------|----------------|
	    | Other                      |	   |                |
	    |----------------------------|---------|----------------|
	    | Request keyboard ID        |   AB    |      NONE      |
	    | Reinitiate keyboard        |   FD    |      NONE      |
	    | Jump to test mode          |   CB    |      NONE      |
	    | Reinstate defaults         |   D3    |      NONE      |
	     -------------------------------------------------------
	
								 Table II


    6.3.1  FLOW CONTROL

	The terminal can "lock" the keyboard with the  "inhibit  keyboard
	transmission"   command.   When   the  keyboard  is  subsequently
	unlocked, it will respond with an error code  if  any  keystrokes
	may have been missed.  (see section 7.2)

 								  Page 13

    6.3.2  LED'S

	The LED parameter can be summarized as follows:

	 ---------------------------------------------------------------
	|   1   |   0   |   0   |   0   | LED 4 | LED 3 | LED 2 | LED 1 |
	 ---------------------------------------------------------------

	The LED structure on the keyboard can be summarized as follows:
		
		 [O]     [O]     [0]     [0]
	        LED 4   LED 3   LED 2   LED 1
		

    6.3.3  AUDIO

	The audio volume  parameter can be summarized as follows:

	 ---------------------------------------------------------------
	|   1   |   0   |   0   |   0   |   0   |   3-bit volume        |
	 ---------------------------------------------------------------

	Volume levels are as follows:

		000 - highest
		001
		010
		011
		100
		101
		110
		111 - lowest

	Either keyclick or bell (or both) may be disabled.  When keyclick
	or  bell  is  disabled,  it  will not sound, even if the terminal
	requests it.

    6.3.4  AUTOREPEAT

	TEMPORARY AUTOREPEAT INHIBIT - stop autorepeat for this key only.
	Autorepeat   will   automatically  resume  when  another  key  is
	depressed.

	DISABLE/ENABLE   AUTOREPEAT   ACROSS   KEYBOARD   -    stop/start
	transmission  of  metronome  codes  without  affecting autorepeat
	timing or division settings.

	CHANGE ALL AUTOREPEAT TO DOWN ONLY - change division settings for
	all autorepeating divisions to down only.


    6.3.5  OTHER

	REQUEST KEYBOARD ID - keyboard  will  send  2-byte  keyboard  ID.
	Keyboard will not jump to POWER UP.

						 		  Page 14

	REINITIATE KEYBOARD - keyboard will jump to its POWERUP  routine.
	Note:  terminal  should  not try to transmit anything to keyboard
	until the last byte of the powerup sequence has been received.

	JUMP TO TEST MODE - special test mode for production test

	REINSTATE DEFAULTS - set the  following  functions  back  to  the
	powerup default settings:

		Division mode settings
		Autorepeat interval and timeout rates
		Autorepeat buffer selections
		Audio volume
		Control key keyclick



    6.4  Mode Set Commands

    6.4.1  Division Mode Setting

	For an explanation of transmission modes and rates,  see  section
	3.

	Each DIVISION on the keyboard has a unique 4-bit  representation,
	as follows:

		Division			   Representation		________			   ______________
	
		1. 48 graphic keys, Spacebar		0001
		   and B13, D13, D99 and E99 on
		   the typewriter mass
		2. Numeric keypad			0010
		3. Delete character			0011
		4. Return(C13) and Tab(D00)		0100
		5. Lock(C00), COMPOSE(A99) and A10	0101
		6. Shift(B00 and B11) and CTRL (C99)	0110
		7. Horizontal cursors(B16 and B18)	0111
		8. Vertical cursors(B17 and C17)	1000
		   and A17
		9. Six keys directly above the cursor	1001
		   keys(D16-D18 and E16-E18)
	    Function keys
		10. G99-G04 and H99-H04			1010
		11. G05-G09 and H05-H09			1011
		12. G10-C14 and H10-H14			1100
		13. G15-G16				1101
		14. G20-G23 and H20-H23			1110

								Table III

	See Appendix IV for keyswitch designators.
	

								  Page 15

	Each MODE has a unique 2-bit representation.

		Modes			Representation		_____			______________

		Down only		       00
		Autorepeat, Down	       01
		Down Up			       11

								 Table IV

	To set key transmission mode on a particular  keyboard  division,
	the  terminal must send the PARAMS flag, followed by the keyboard
	division representation with the mode representation, followed by
	the TYPE flag (cleared).

		Example: (set main array to down/up)

		|param|      division         |   mode    |type |
		 -----------------------------------------------
		|  1  |  0     0     0     1  |  1     1  |  0  |
		 -----------------------------------------------
		   7     6     5     4     3     2     1     0

	The PARAMS flag of the mode set command will be set to 1 if there
	are  no  parameters.  The  params flag will be clear if there are
	parameters.


    6.4.2  Autorepeat Rate Buffer Association -

	If the mode selected is autorepeat, the  terminal  may  elect  to
	transmit  a  parameter  to  change  the buffer association of the
	selected division.  (See appendix II for defaults)

		Example: (set main array  to  autorepeat,  change  buffer
		  	 association to buffer 3)

		|param|      division         |   mode    |type |
		 -----------------------------------------------
		|  0  |  0     0     0     1  |  0     1  |  0  |
		 -----------------------------------------------
		|  1  |  0     0     0     0     0     1  |  0  |
		 -----------------------------------------------
		   7     6     5     4     3     2     1     0


    6.4.3  Autorepeat Rate Buffer values

	At keyboard powerup time, the four autorepeat rate  buffers  will
	contain  default  values.  (see section 3.6, defaults in appendix
	II) The terminal may change these values, as shown below.

	In the command byte, bit 7 (PARAMS flag) should  be  clear.  Bits
	6-3 should be 1111 (to indicate that this is a RATE SET command).
	Bits 2-1 should be the buffer number (O to 3).  Bit 0 (TYPE flag)
	should  be  clear.  There  should be two parameters, carrying the
	rate set data.

								  Page 16

		Example: change rates in buffer 3

		|param|  rate change command  | buffer #  |type |
		 -----------------------------------------------
		|  0  |  1     1     1     1  |  1     1  |  0  |
		 -----------------------------------------------
		|  0  |           Param 1  (timeout)            |
		 -----------------------------------------------
		|  1  |           Param 2  (interval)           |
		 -----------------------------------------------
		   7     6     5     4     3     2     1     0


	The first parameter should specify TIMEOUT to be  stored  in  the
	selected buffer.  The second parameter should specify INTERVAL.

	    1.  TIMEOUT
		This number represents the amount of  time  the  keyboard
		will wait before autorepeating a character.

	    2.  INTERVAL
		This number is the effective  rate  at  which  characters
		should be transmitted, i.e. once very X ms.

	For example, to set the autorepeat rate to be stored in buffer 1,
	terminal  firmware  will transmit: 00000011 followed by two bytes
	of numeric parameters, as follows:

	The Autorepeat TIMEOUT will be the transmitted  number,  times  5
	ms.  i.e.  In  order  to specify a rate of 5 ms. delay, the first
	parameter received would be 00000001.  The maximum allowed is 630
	ms.,  or 01111110.  THE TERMINAL MUST NOT SEND 631 - or 01111111.
	This code is reserved for internal use of  the  keyboard.  00  is
	also an illegal value.  Autorepeat TIMEOUT will be implemented as
	a multiple of 8.33 ms., which is  the  keyboard's  internal  scan
	rate.  For this reason, TIMEOUT rates can vary +/- 4.15 ms.

	The Autorepeat INTERVAL will be the number of metronome codes per
	second.  In  order  to  specify  a  speed of 16 hertz, the second
	parameter received would be 10010000.  (note that the high  order
	bit  is set because it is the last parameter).  The highest which
	may be sent is 126, or 11111100.  THE TERMINAL MUST NOT SEND  127
	-  or 11111101.  This code is the PWRUP command.  The lowest rate
	which can be implemented by the keyboard is 12 hz.  Values as low
	as 1 may be transmitted, but they will be translated to 12 hz.



    7.0  SPECIAL CONSIDERATIONS

    7.1  Error Handling.

	There are 4 error codes.  The first 2 are sent at power  up  time
	if self-test fails.  (see section 5.3)

								  Page 17

	The other two are the INPUT error code and the OUTPUT error code.
	OUTPUT  error  (B6  HEX)  is  sent ONLY upon receipt of a "resume
	transmission" command, if the output buffer overflowed while  the
	keyboard was locked.

	INPUT error (B6 HEX) is sent whenever the Keyboard detects  noise
	(unidentified command or parameter) on the line.  B6 is also sent
	if the keyboard detects  a  delay  of  more  than  100  ms.  when
	expecting a parameter.


    7.2 Keyboard Locked Condition

	When the keyboard receives a command to "inhibit transmission" it
	will  transmit one more byte.  This is a special code to indicate
	that the Keyboard is locked.  If the terminal receives this  code
	unsolicited,  it  is  an  indication  that  noise on the line was
	interpreted as  an  "inhibit  transmission"  command.  It  should
	immediately  send the "resume transmission" command to unlock the
	keyboard.

	Due to limited RAM within the keyboard, the output FIFO is  small
	(4 bytes).  When the Keyboard is locked it will attempt to buffer
	characters received from  the  keyboard.  When  the  Keyboard  is
	subsequently  unlocked it will transmit all 4 bytes in its output
	buffer.  If any  keystrokes  have  been  missed,  due  to  buffer
	overflow,  the  keyboard will transmit an error code as the fifth
	byte.  Any keys which were not transmitted and  are  still  being
	held  down  when  the keyboard is "unlocked" will be processed as
	new  keys.  Therefore,  an  error  code  upon  keyboard  "unlock"
	indicates to the terminal a POSSIBLE loss of keystrokes.

	The keyboard stops scanning its matrix while its buffer is  full.
	It does, however, process all incoming commands.


    7.3  Reserved Code

	The number 7F (hex) is reserved  for  the  internal  use  of  the
	keyboard input and output buffers handling routines.



    7.4  Test mode

	The keyboard will jump into a  test  mode  by  command  from  the
	QV/DIAGNOSE bed-of-nails tester used in production test.  It will
	transmit a special code to the terminal to confirm test mode.  If
	a  terminal  receives  this  code unsolicited, it should send the
	byte 80(HEX) to resume.  (this will cause a jump to powerup).

								  Page 18

    7.5 Future Expansion

	In order to provide for expansion of functionality, the following
	keycodes  have  been  reserved for future use as special codes or
	keycodes, and should be ignored if received by  a  terminal  that
	does not support them:

		decimal		hex		decimal		hex		_______		___		_______		___
	
		110		56E		173		AD
		122		7A		187		BB
		165		A5		218		DA
		156		A6		228		E4
		172		AC

								  Page 19

    8.0  APPENDIX I -- KEYCODE TRANSLATION TABLE

	Keycodes 00 thru 64 are reserved. keycodes 65 thru 85 are unused.

	Please note that the legends given under "Keycap" are taken  from
	the  keycap  legends  of the LK201AA (American), as known at this
	time.  They are  provided  for  convenience  only,  and  are  not
	necessarily  complete  or  up  to  date.  Those keys which do not
	exist on the LK201 are labeled "unused".  Key  positions  may  be
	referenced in Appendix IV.

	-----------------------------------------------------------------
	DIVISION  POSITION 	  KEYCAP              KEYCODE   KEYCODE
		 (see pg 30)	     		       (dec) 	 (hex)
	-----------------------------------------------------------------
	=================================================================
		    		Function Keys
	-----------------------------------------------------------------
	   10	    G99		HOLD SCREEN 		086	   56
		    G00		PRINT SCREEN 	        087	   57
		    G01 	BREAK			088	   58
		    G02		SETUP			089	   59
		    G03		F5			090	   5A
		    G04		unused			091	   5B
		    H99		unused			092	   5C
		    H00		unused			093	   5D
		    H01		unused			094	   5E
		    H02		unused			095	   5F
		    H03		unused			096	   60
		    H04		unused			097	   61
							098	   62
	-----------------------------------------------------------------
							099	   63
	   11       G05		INTERRUPT		100	   64
		    G06		RESUME			101	   65
		    G07		CANCEL			102	   66
		    G08		MAIN SCREEN		103	   67
		    G09		EXIT			104	   68
		    H05		unused			105	   69
		    H06		unused			106	   6A
		    H07		unused			107	   6B
		    H08		unused			108	   6C
		    H09		unused			109	   6D
		    ---    reserved for future use	110	   6E
	-----------------------------------------------------------------
							111	   6F
	   12	    G10 	unused			112	   70
		    G11 	F11 (ESC)		113	   71
		    G12 	F12 (BS)		114	   72
		    G13 	F13 (LF)		115	   73
		    G14		ADDITIONAL OPTIONS  	116	   74
		    H10 	unused			117	   75
 		    H11 	unused			118	   76
		    H12 	unused			119	   77
		    H13 	unused			120	   78
		    H14 	unused			121	   79
		    ---    reserved for future use	122	   7A


								  Page 20

	-----------------------------------------------------------------
	DIVISION  POSITION 	  KEYCAP              KEYCODE   KEYCODE
		 (see pg 30)	     		       (dec) 	 (hex)
	-----------------------------------------------------------------
							123 	   7B
	   13	    G15 	HELP 			124	   7C
		    G16 	DO 			125 	   7D
	-----------------------------------------------------------------
							126	   7E
		    ---    RESERVED FOR INTERNAL USE 	127	   7F
	   14	    G20		F17			128	   80
		    G21		F18			129	   81
		    G22		F19			130	   82
		    G23		F20			131	   83
		    H20		unused 			132	   84
		    H21		unused			133	   85
		    H22		unused			134	   86
		    H23		unused			135	   87
	=================================================================
				6 basic editing keys
	-----------------------------------------------------------------
							136 	   88
							137 	   89
	   9	    E16 	FIND 			138	   8A
		    E17 	INSERT HERE 		139	   8B
		    E18 	REMOVE 			140 	   8C
		    D16 	SELECT 			141 	   8D
		    D17 	PREV SCREEN 		142	   8E
		    D18 	NEXT SCREEN 		143	   8F
							144	   90
	=================================================================
				Keypad
	-----------------------------------------------------------------
							145	   91
	   2	    A20		0			146	   92
		    A21		unused			147	   93
		    A22		.			148	   94
		    A23		ENTER			149	   95
		    B20 	1			150	   96
		    B21 	2 		 	151 	   97
		    B22 	3 			152	   98
		    C20 	4			153	   99
		    C21 	5 			154 	   9A
		    C22 	6 			155 	   9B
		    C23 	, 			156 	   9C
		    D20 	7 			157 	   9D
		    D21 	8 			158 	   9E
		    D22 	9 			159 	   9F
		    D23 	- 			160 	   A0
		    E20 	PF1 			161 	   A1
		    E21 	PF2 			162 	   A2
		    E22 	PF3 			163 	   A3
		    E23 	PF4 			164 	   A4
		    ---    reserved for future use 	165 	   A5

							 	  Page 21

	-----------------------------------------------------------------
	DIVISION  POSITION 	  KEYCAP              KEYCODE   KEYCODE
		 (see pg 30)	     		       (dec) 	 (hex)
	-----------------------------------------------------------------
	=================================================================
				Cursor Keys
	-----------------------------------------------------------------
		    ---    reserved for future use 	166 	   A6
	   7	    B16 	LEFT 			167 	   A7
		    B18 	RIGHT 			168 	   A8
	-----------------------------------------------------------------
	   8	    B17		DOWN			169	   A9
		    C17		UP			170	   AA
		    A17		unused			171	   AB
		    ---	   reserved for future use	172	   AC
	=================================================================
				Shift, Lock, CTRL, A99 and A10
	-----------------------------------------------------------------
		    ---    reserved for future use 	173 	   AD
	   6 	    B99,B11 	SHIFT	 		174 	   AE
		    C99 	CTRL 			175 	   AF
	-----------------------------------------------------------------
	   5	    C00		LOCK			176	   B0
		    A99		COMPOSE			177	   B1
		    A10		unused			178	   B2
	=================================================================
				Special Codes
	-----------------------------------------------------------------
		    ---		all ups			179	   B3
		    ---		metronome		180	   B4
		    ---		output error		181	   B5
		    ---		input error		182	   B6
		    ---		KBD LOCKED acknowledge	183	   B7
		    ---		TEST MODE acknowledge	184	   B8
		    ---		PREFIX to keys down	186	   B9
		    ---		MODE CHANGE acknowledge 185	   BA
		    ---	   reserved for future use 	187	   BB
	=================================================================
				Delete
	-----------------------------------------------------------------
	   3 	    E13 	DELETE(X) 		188 	   BC
	=================================================================
				Return and Tab
	-----------------------------------------------------------------
	   4 	    C13 	RETURN 			189 	   BD
		    D00		TAB			190	   BE

								  Page 22

	-----------------------------------------------------------------
	DIVISION  POSITION 	  KEYCAP              KEYCODE   KEYCODE
		 (see pg 30)	     		       (dec) 	 (hex)
	-----------------------------------------------------------------
	=================================================================
			48 graphics keys, space
			B13, D13, D99 and E99 on
    			the main typewriter mass.
	-----------------------------------------------------------------
	   1	    E00		TILDE `			191	   BF
		    E01		! 1			192	   C0
		    D01		Q			193	   C1
		    C01		A			194	   C2
		    B01		Z			195	   C3
		    D99		unused 			196	   C4
		    E02		@ 2			197	   C5
		    D02		W			198	   C6
		    C02		S			199	   C7
		    B02		X			200	   C8
		    B00		> <			201	   C9
		    E99		unused			202	   CA
		    E03		# 3 			203	   CB
		    D03		E			204	   CC
		    C03		D			205	   CD
		    B03		C			206	   CE
							207	   CF
		    E04		$ 4			208	   D0
		    D04		R			209	   D1
		    C04		F			210	   D2
		    B04		V			211	   D3
		    A01-A09	SPACE			212	   D4
							213	   D5
		    E05		% 5			214	   D6
		    D05		T			215	   D7
		    C05		G			216	   D8
		    B05		B			217	   D9
		    ---    reserved for future use	218	   DA
		    E06		^ 6			219	   DB
		    D06		Y			220	   DC
		    C06		H			221	   DD
		    B06		N			222	   DE
				unused			223	   DF
		    E07		& 7			224	   E0
		    D07		U			225	   E1
		    C07		J			226	   E2
		    B07		M			227	   E3
		    ---    reserved for future use	228	   E4
		    E08		* 8			229	   E5
		    D08		I			230	   E6
		    C08		K			231	   E7
		    B08		,,			232	   E8
				unused			233	   E9
	   	    E09		( 9			234	   EA
		    D09		O			235	   EB
		    C09		L			236	   EC
		    B09		..			237	   ED
				unused			238	   EE

								  Page 23

	-----------------------------------------------------------------
	DIVISION  POSITION 	  KEYCAP              KEYCODE   KEYCODE
		 (see pg 30)	     		       (dec) 	 (hex)
	-----------------------------------------------------------------
	   1	    E10		) 0			239	   EF
		    D10		P			240	   F0
		    D13		unused			241	   F1
		    C10		: ;			242	   F2
		    B10		? /			243	   F3
				unused			244	   F4
		    E12		+ =			245	   F5
		    D12		} ]			246	   F6
		    C12		, \			247	   F7
				unused			248	   F8
		    E11		_ -			249	   F9
		    D11		{ [			250	   FA
		    C11		" '			251	   FB
		    B13		unused			252	   FC
				unused			253	   FD
				unused			254	   FE
				unused			255	   FF

								  Page 24

    9.0  APPENDIX II - DEFAULTS

	The  following  defaults  have  been  established  regarding  key
	transmission modes:

		Keyboard division	   Mode		AR buffer assoc		_________________	   ____		_______________

		Main Array		autorepeat	      0
		keypad			autorepeat	      0
		Del			autorepeat	      1
		Return and Tab		down only
		Function kevs		down only
		lock,compose,A10	down only	
		shift,ctrl		down/up
		cursor keys		autorepeat	      1
		6 Basic Editing Keys	down only

								  Table V


	Effective Rates stored in Autorepeat buffers:

				TIMEOUT	      INTERVAL				_______	      ________

		Buffer 0:	530 ms.		30 hz
		Buffer 1:	300 ms.		30 hz
		Buffer 2:	500 ms.		40 nz
		Buffer 3:	300 ms.		40 hz

	Audio volume: Both keyclick and bell volumes will  be  2  decimal
	(010 binary) by default.

	The key in position C99 of the keyboard in Appendix IV (the  CTRL
	key in the LK201) will NOT GENERATE a click unless enabled by the
	terminal.  The keys in position B99 and B11 (SHIFT  keys  on  the
	LK201) will NEVER generate a click.

								  Page 25

    10.0  APPENDIX III - KEYBOARD MATRIX

	This is the current matrix for the LK200  keyboard.  Keys  F1-F16
	and  F35-F38  are  not physically possible on the CT100 keyboard.
	For physical key locations see the bottom line in each  location.
	Please  note that the legends given are from the LK201AA as known
	at this time.  They are provided for convenience  only,  and  are
	not  necessarily complete or up to date.  Key positions which are
	non-existent on the LK201 are marked "unused".


    COLUMN 			 ROW
      |     7       6       5       4      3        2       1       0
      v -----------------------------------------------------------------
     17 |unused |  F19  |unused |  F20  |  PF4  |   N-  |   N,  | ENTER |
        |       |       |       |       |       |       |       |       |
        |  H23  |  G22  |  H22  |  G23  |  E23  |  D23  |  C23  |  A23  |
        -----------------------------------------------------------------
     16 |  F18  |  PF3  |unused |   N9  |   |   |   N6  |   N3  |   N.  |
        |       |       |       |       |   v   |       |       |       |
	|  G21  |  E22  |  H21  |  D22  |  B17  |  C22  |  B22  |  A22  |
	-----------------------------------------------------------------
     15 |  F17  |  PF2  |unused |   N8  |   N5  |  -->  |   N2  |   NO  |
	|	|	|	|	|	|	|	| RIGHT |
	|  G20  |  E21  |  H20  |  D21  |  C21  |  B18  |  B21  |  A21  |
	-----------------------------------------------------------------
     14 |  PF1  |next   |remove |   up  |   N7  |   N4  |   N1  |   NO  |
	|	| screen|	|	|	|	|	|  LEFT |
	|  E20  |  D18  |  E18  |  C17  |  D20  |  C20  |  B20  |  A20  |
	-----------------------------------------------------------------
     13 |insert | _ 	|  do 	|prev 	| { 	| "	|unused |unused |
	|   here|     - |	| screen|     [	|     '	| 	|	|
	|  E17 	|  E11 	|  G16  |  D17 	|  D11 	|   C11 |  B13 	|  A17  |
	-----------------------------------------------------------------
     12 | find  | +	| help  |select | } 	| RETURN|  <--  | |	|
	|	|     =	|	|	|     ]	| (bot)	|	|     \	|
	|  E16 	|  E12 	|  G15  |  D16 	|  D12  |  C13  |  B16  |  C12  |
	-----------------------------------------------------------------
     11 |addtnl | DELETE|unused | ) 	|   P 	| RETURN| : 	| ? 	|
	|options|   (X) |	|     O |	| (top) |     ;	|     / |
	|  G14  |  E13  |  H14  |  E10  |  D10  |  D13  |  C10  |  B10  |
	-----------------------------------------------------------------
     10 |unused |  F12  |  F14  |  F13  | ( 	| O 	| L 	| .	|
	|	|	|	|	|     9	|	|	|     . |
	|  H13  |  G12  |  H12  |  G13  |  E09  |  D09  |  C09  |  B09  |
	-----------------------------------------------------------------

								  Page 26

    COLUMN 			 ROW
      |     7       6       5       4      3        2       1       0
      v -----------------------------------------------------------------
      9 |unused |  F11	|unused |unused | *	|   I 	|   K	| , 	|
	|	|	|	|	|     8	|	|	|     ,	|
	|  H11  |  G11	|  H10  |  G10  |  E08  |  D08  |  C08  |  B08	|
	-----------------------------------------------------------------
      8 |unused |main 	|unused | exit 	| & 	|   U   |   J 	|   M	|
	|	| screen|	|	|     7	|	|	|	|
	|  H09  |  G08 	|  H08 	|  G09 	|  E07 	|  D07	|  C07 	|  B07	|
	-----------------------------------------------------------------
      7 |unused |cancel |unused |resume | ^ 	|   Y	|   H 	|   N	|
	|	|	|	|	|     6	|	|	|	|
	|  H07  |  G07  |  H06  |  G06 	|  E06 	|  D06 	|  C06 	|  B06	|
	-----------------------------------------------------------------
      6 |unused |unused |unused |inter- | %	|   T	|   G	|   B   |
	|	|	|	|  rrupt|     5	|	|	|	|
	|  H05  |  G04 	|  H04 	|  G05 	|  E05 	|  D05 	|  C05  |  B05	|
	-----------------------------------------------------------------
      5 | setup	|  F5 	|unused | $ 	|   R 	|   F 	|   V 	| SPACE |
	|	|	|	|     4	|	|	|	|	|
	|  G02	|  G03 	|  H03 	|  E04 	|  D04 	|  C04	|  B04	|A01-A09|
	-----------------------------------------------------------------
      4 |unused |print 	|unused | break | # 	|   E 	|   D 	|   C	|
	|	| screen| 	|	|     3 |	|	|	|
	|  H02 	|  G00 	|  H01 	|  G01 	|  E03 	|  D03 	|  C03 	|  B03	|
	-----------------------------------------------------------------
      3 |hold 	| @	|unused |  TAB 	|   W 	|   S 	|   X 	| > 	|
	| screen|     2 |	|	|	|	|	|     < |
	|  G99 	|  E02  |  H00 	|  D00	|  D02 	|  C02 	|  B02 	|  B00	|
	-----------------------------------------------------------------
      2 |unused |unused |unused | ~ 	| ! 	|   Q 	|   A 	|   Z	|
	| 	|	|	|     `	|     1 | 	|	|	|
	|  E99 	|  D99 	|  H99  |  E00	|  E01 	|  D01  |  C01  |  B01 	|
	-----------------------------------------------------------------
      1 | CTRL 	|  LOCK |COMPOSE|unused |	|	|	|	|
	|	|	|	|	|	|	|	|	|
	|  C99 	|  C00	|  A99  |  A10 	|	|	|	|	|
	-----------------------------------------------------------------
      0 | SHIFT |		        DO NOT USE THIS AREA		|
	|	|			(Phantom key avoidance)		|
	|B99,B11|							|
	-----------------------------------------------------------------

	NO of the numeric keypad is layed out such that it can be  broken
	into  two  keys.  Normally  only  the NO LEFT is implemented as a
	double  size  key.  Thus;  that  is  the  code  which  should  be
	considered  for  that  double key.  The interpretation of the new
	key formed by splitting the double key has yet to be determined.

	The RETURN key is also laid out so as to be able to split it into
	two keys.  The one which is decoded as return is the RETURN (bot)
	key.  If this key is divided the meaning of the  top  portion  is
	TBD.

								  Page 27

    11.0  APPENDIX IV - KEYSWITCH LAYOUT

	Keyswitch Layout, page 1 of 4.







       ------------------------------------------------------------------>
       |unused |unused |unused |unused |unused |unused |unused |unused |
       |       |       |       |       |       |       |       |       |
       |  H99  |  H00  |  H01  |  H02  |  H03  |  H04  |  H05  |  H06  |
       ------------------------------------------------------------------>
       ------------------------------------------------------------------>
       | HOLD  | PRINT | SETUP |  F4   | BREAK |unused |  F6   |  F7   |
       |SCREEN |SCREEN |       |       |       |       |       |       |
       |  G99  |  G00  |  G01  |  G02  |  G03  |  G04  |  G05  |  G06  |
       ------------------------------------------------------------------>


       ------------------------------------------------------------------>
       | un- |  ~ `  |  ! 1  |  @ 2  |  # 3  |  $ 4  |  % 5  |  ^ 6  |
       | used|       |       |       |       |       |       |       |
       | E99 |  E00  |  E01  |  E02  |  E03  |  E04  |  E05  |  E06  |
       -------------------------------------------------------------------
       | un- |    TAB    |   Q   |   W   |   E   |   R   |   T   |   y   |
       | used|           |       |       |       |       |       |	 |
       | D99 |    D00    |  D01  |  D02  |  D03  |  D04  |  D05  |  D06  |
       -------------------------------------------------------------------
       | CTRL  |    LOCK   |   A   |   S   |   D   |   F   |   G   |
       |       |	   |       |       |       |       |       |
       |  C99  |    C00    |  C01  |  C02  |  C03  |  C04  |  C05  |
       ------------------------------------------------------------------>
       |     SHIFT     |  > <  |   Z   |   X   |   C   |   V   |   B   |
       |               |       |       |       |       |       |       |
       |      B99,     |  B00  |  B01  |  B02  |  B03  |  B04  |  B05  |
       ------------------------------------------------------------------>
    		 |    COMPOSE    |			SPACE
    		 |		 |
		 |      A99      |                    A01-A09
		 -------------------------------------------------------->

								  Page 28

	Keyswitch Layout, page 2 of 4.









      <--------------------------------------------------------------------
          |unused |unused |unused |unused |unused |unused |unused |unused |
          |       |       |       |       |	  |	  |	  |	  |
	  |  H07  |  H08  |  H09  |  H10  |  H11  |  H12  |  H13  |  H14  |
      <--------------------------------------------------------------------
      <--------------------------------------------------------------------
	  |  F8   |  F9   |  F10  |unused |  F11  |  F12  |  F13  |  F14  |
	  |       |       |	  |       |  ESC  |  BS   |  LF   |	  |
	  |  G07  |  G08  |  G09  |  G10  |  G11  |  G12  |  G13  |  G14  |
      <--------------------------------------------------------------------


      <--------------------------------------------------------------
	|  & 7  |  * 8  |  ( 9  |  ) 0  |  _ -  |  + =  |  DELETE   |
	|       |       |       |       |       |       |           |
	|  E07  |  E08  |  E09  |  E10  |  E11  |  E12  |  E13      |
      <----------------------------------------------------------------
	    |   U   |   I   |   O   |   P   |  { [  |  } ]  | RETURN  |
	    |       |       |       |       |       |       |	      |
	    |  D07  |  D08  |  D09  |  D10  |  D11  |  D12  |   D13   |
      ---------------------------------------------------------       |
      |   H   |   J   |   K   |   L   |  : ;  |  " '  |  | \  |       |
      |       |       |       |       |       |       |       |       |
      |  C06  |  C07  |  C08  |  C09  |  C10  |  C11  |  C12  |  C13  |
      -----------------------------------------------------------------
	  |   N   |   M   |  , ,  |  . .  |  ? /  |     SHIFT     |unu|
	  |       |       |       |       |       |               |sed|
	  |  B06  |  B07  |  B08  |  B09  |  B10  |      B11      |B13|
      <----------------------------------------------------------------
    		      SPACE		    |     unused      |
    		  			    |                 |
		     A01-A09		    |       A10       |
      <--------------------------------------------------------





								  Page 29

	Keyswitch Layout, page 3 of 4.









			    -------------------------
			    | HELP  |      DO       |
			    |       |               |
			    |  G15  |      G16      |
			    -------------------------


			    -------------------------
		    	    | FIND  |INSERT |REMOVE |
		    	    |       | HERE  |       |
		    	    |  E16  |  E17  |  E18  |
		    	    -------------------------
		    	    |SELECT | PREV  | NEXT  |
		            |       | SCREEN| SCREEN|
		    	    |  D16  |  D17  |  D18  |
		    	    -------------------------
		    	            |  UP   |
		    	            |       |
		    	            |  C17  |
		    	    -------------------------
		    	    | LEFT  | DOWN  | RIGHT |
		    	    |       |       |       |
		    	    |  B16  |  B17  |  B18  |
		    	    -------------------------
		    	            |unused |
		    	            |       |
		    	            |  A17  |
		    	            ---------







								  Page 30

	Keyswitch Layout, page 4 of 4.









			---------------------------------
			|unused |unused |unused |unused |
			|       |       |       |       |
			|  H20  |  H21  |  H22  |  H23  |
			---------------------------------
			---------------------------------
			|  F17  |  F18  |  F19  |  F20  |
			|       |       |       |       |
			|  G20  |  G21  |  G22  |  G23  |
			---------------------------------


			---------------------------------
			|  PF1  |  PF2  |  PF3  |  PF4  |
			|       |       |       |       |
			|  E20  |  E21  |  E22  |  E23  |
			---------------------------------
			|   7   |   8   |   9   |   -   |
			|       |       |       |       |
			|  D20  |  D21  |  D22  |  D23  |
			---------------------------------
			|   4   |   5   |   6   |   ,   |
			|       |       |       |       |
			|  C20  |  C21  |  C22  |  C23  |
			---------------------------------
			|   1   |   2   |   3   | ENTER |
			|       |       |       |       |
			|  B20  |  B21  |  B22  |       |
			-------------------------       |
			|   0   |unused |   .   |       |
			|       |       |       |       |
			|  A20  |  A21  |  A22  |  A23  |
			---------------------------------