MMV110.DOC




		
			   Master Menu User's Guide

				 Version 1.10











				  DISCLAIMER

		This document file was created by scanning  the
		original  document and then editing the scanned
		text.  As much as possible, the  original  text
		format  was restored.  Some format changes were
		made to insure this  document  would  print  on
		current laser printers using 60 lines per page.
		The  original  spelling  and  grammar  has been
		preserved.

		Figures of the  DECmate  hardware  showing  the
		keyboard,   floppy   drives,   etc.  cannot  be
		reproduced with the  ASCII  character  set  and
		are not included in this document.

		1-Oct-1996




								AA-AH12B-TV















		DECmate

		___________________________________________________________
		

		Master Menu User's Guide		       Version 1.10
























				---------------
				|d|i|g|i|t|a|l|		
				---------------



								AA-AH12B-TV
					     Second Printing, November 1984



     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this document.

     The software described in this document is furnished under a license
     and may be used or copied only in accordance with the terms of such
     license.

     Digital Equipment Corporation assumes no responsibility for the use or
     reliability of its software on equipment that is not supplied by
     DIGITAL.



     Copyright (c) 1983, 1984 by Digital Equipment Corporation. All rights
				 reserved.



     The postage prepaid Reader's Comment Form on the last page of this
     document requests the user's critical evaluation to assist us in
     preparing future documentation.


    CP/M (R) is a registered trademark of Digital Research, Inc.

    Multiplan (TM) is a trademark of Microsoft Corporation.

    Daisy-Aids (TM) is a trademark of Escape Computer Software, Inc.

    MS (TM) -DOS is a trademark of Microsoft Corporation.



    The following are trademarks of Digital Equipment Corporation:


	digital (TM)	    DIBOL		    UNIBUS
	DEC		    MASSBUS		    VAX
	DECmate		    PDP			    VMS
	DECSYSTEM-20	    Professional	    Work Processor
	DECUS		    Rainbow		    WPS
	DECwriter	    RSTS
			    RSX




     ______________________________________________________________________
								   CONTENTS


     Preface

	 Intended Reader   vii
	 Manual Structure   vii
	 Conventions Used in This Manual   viii
	 Reference Manuals   xi


     1   Introduction to Master Menu

	 Prerequisites for Master Menu   1-1
	 Master Menu Program Diagram   1-1
	 Special Function Keys   1-3
	   Print Screen Key   1-3
	   Cancel Key   1-3
	   Main Screen Key   1-3


     2   Getting Started with Master Menu

	 Installing and Booting Master Menu on Your Hard Disk   2-1
	 Creating, Displaying, and Deleting a Sample Menu Item   2-1


     3   Installing Master Menu on Your DECmate System
	 Booting the Installation Software Program from the Diskette   3-1
	   COPY - Make Copies of the Installation Diskettes   3-3
	   INST - Install Master Menu   3-4
	   SMPW - Set Master Password   3-6
	   PSWD - List Volume Passwords   3-8
	   MBB - Mark a Bad Block   3-8
	   QUIT - Leave this Program and Go to SETUP to Reboot   3-8
	 Fixed Menu Screen   3-10


     4   Menu Maintenance

	 Menu Items   4-1
	   Creating a Menu Item   4-3
	   Modifying a Menu Item   4-7
	   Deleting a Menu Item   4-8
 	   Selecting a Menu Item   4-9
	 Menu Screens   4-9
	   Adding a Page Marker to the Menu   4-9
	   Deleting a Page Marker from the Menu   4-10
	   Moving a Menu Item   4-10







				      iii



     Contents
     ______________________________________________________________________


     5   Date and Time Functions

	 DAT - Set System Date and Time   5-1
	 SDF - Select New Date Format   5-2


     6   Finished Using the System


     7   Hard Disk Services

	 L - List Directory of Volumes   7-3
	 A - Allocate a New Volume   7-4
	 E - Erase an Existing Volume   7-6
	 B - Back Up Volume(s) to Diskettes   7-18
	 R - Restore a Volume from Diskettes   7-10
	 Q - Quit This Program   7-13
	 N - New Name for an Existing Volume   7-13
	 P - Assign New Passwords for a Volume   7-14
	 S - Select the Startup Volume   7-15
	 U - Unset a Volume-Modified Flag   7-16
	 C - Copy a Volume to an Existing Volume of Equal Size   7-17
	 M - Mark a Bad Block   7-19
	 X - Compress the Empty Space on a Drive   7-20


     8   Using Passwords

	 Master Password   8-1
	 READ Password   8-2
	 WRITE Password   8-2
	 Password Ranges   8-3
	 Passwords and the Hard Disk Services   8-3
	   Erase an Existing Volume   8-3
	   Assign New Name to a Volume   8-3
	   Assign New Passwords   8-3
	   Unset a Volume-Modified Flag   8-3
	   Copy a Volume to an Existing Volume   8-4
	 Password Exceptions   8-4
	 List of Volume Passwords   8-4
 	 Applications and Passwords   8-4


     9   Master Menu and CP/M, COS-310, WPS, and MS-DOS

	 Returning to Master Menu   9-1
	 Device Names for Operating Systems   9-2
	 Hard Disk Device Assignments   9-3
	 Using Master Menu with the CP/M Operating System   9-3
	   Command String Conventions   9-3
	   Date and Time Acceptance   9-4


				      iv



     Contents
     ______________________________________________________________________


	   Booting from the Hard Disk   9-4
	   Booting from a Diskette   9-4
	 Using Master Menu with the COS-310 Operating System   9-4
	   Command String Conventions   9-4
	   Date and Time Acceptance   9-4
	 Using Master Menu with the WPS Operating System   9-5
	   Document Formatting   9-5
	   Command String Conventions   9-6
	   Date and Time Acceptance   9-6
	   Booting from the Hard Disk   9-7
	   Booting from a Diskette   9-7
	 Using Master Menu with the MS-DOS Operating System   9-7
	   Command String Conventions   9-7
	   Date and Time Acceptance   9-7
	   Booting from the Hard Disk   9-8
	   Booting from a Diskette   9-8


     10  What to Do in Case of Trouble

	 How to Get Help   10-1
	 Some Common Symptoms and Their Cures   10-2
	   Freezing   10-2
	   The Display Screen Goes Blank   10-2


     A   Master Menu Error Messages

	 Installation Error Messages   A-1
	 Allocate Error Messages   A-2
	 Erase Error Messages   A-3
	 Backup Error Messages   A-3
	 Restore Error Messages   A-4
	 New Name Error Messages   A-5
	 Assign New Password Error Messages   A-6
	 Select the Startup Volume Error Messages   A-6
	 Unset a Volume-Modified Flag Error Message   A-7
	 Copy Volume Error Messages   A-7
	 Mark a Bad Block Error Message   A-8
	 Master Menu Screen Error Messages   A-8


     B   Command Passing and System Date Storage

	 CP/M and MS-DOS   B-1
	 WPS and COS-310   B-1
	 Date   B-1






				       v



     Contents
     ______________________________________________________________________


     Index   index-1


     Figures

	 1-1  Master Menu Program   1-2
	 1-2  The DECmate Keyboard   1-3
	 3-1  Open Drive Doors   3-1
	 3-2  Press System Unit Power Switch On   3-1
	 3-3  Insert Installation Diskette A into Drive A   3-2


     Tables

	 9-1  Returning to Master Menu   9-1
	 9-2  Device Names by Operating System   9-2
	 9-3  Hard Disk Device Assignments to Volumes   9-3




































				      vi



     ______________________________________________________________________
								    PREFACE





     Product Name:  DECmate Master Menu

     Version:	    1.1



     Intended Reader

     This manual is for first-time users of Master Menu who are running the
     program on a DECmate system that is equipped with a hard disk unit.
     Experienced users can also use portions of this guide as a reference
     manual.  You do not need to know how to program to use this manual or
     the Master Menu program.


     Manual Structure

     This manual is divided into the following chapters and appendixes:

     Chapter 1 contains an overview of Master Menu and describes the three
     special keys on the DECmate keyboard that Master Menu uses.

     Chapter 2 provides a brief description of how to get started with
     Master Menu.

     Chapter 3 describes the procedures that are used to install and verify
     Master Menu on your DECmate system.

     Chapter 4 describes the Menu Maintenance Utility that is used to
     create and maintain customized menu screens.

     Chapter 5 describes the procedures for setting the system date and
     time.  Procedures to change the display format for the system date are
     also described in this chapter.

     Chapter 6 explains the procedures that you are to follow when you
     finish using Master Menu.

     Chapter 7 describes the hard disk functions and utilities that are
     available with Master Menu.

     Chapter 8 describes the password protection that is available for the
     volumes residing on your hard disk.

     Chapter 9 describes how Master Menu interacts with the CP/M(R)
     COS-310, WPS, and MS -DOS operating systems.




				      vii



     Preface
     ______________________________________________________________________


     Chapter 10 explains what to do if you encounter problems when you are
     using Master Menu.

     Appendix A lists the possible error messages the system displays when
     using specific functions.  It also explains how to recover from the
     errors.

     Appendix B indicates the specific location and format that Master Menu
     uses to pass command text and the system date to various DECmate
     operating systems.


     Conventions Used in This Manual

     The following conventions are used throughout the manual:

	o  Braces ({}) enclose areas of the screen with inverted video.

	o  A box is used to enclose the text displayed on	-------
	   a menu, as shown to the right.			|     |
								|     |
								-------

	o  In examples of dialog between you and the computer, what you
	   type is underlined.

	o  In Master Menu functions using both the Return and Do keys,
	   press <Return> to terminate input to the function, and press
	   <Do> to execute the function.

	o  Angle brackets (<>) are used to designate keys on your keyboard.
	   For example, <Return> means press the Return key.

	o  The word "enter" is used whenever the instructions call for you
	   to type information and then to press the Return key.  The
	   Return key will not be specified in the instructions.

	o  The word "type" is used whenever the instructions call for you
	   to type information and then to press a key other than <Return>.
	   The key will be specified in the instructions.

	o  The term "fixed menu screen" is used throughout this manual to
	   refer to the unalterable DECmate Master Menu screen that lists
	   the Master Menu program functions and utilities that are
	   available.  You cannot modify this screen. The fixed menu screen
	   is shown in Screen P-1 on the following page.

	o  The term "submenu" describes DECmate screens corresponding to
	   the functions listed on the fixed menu screen. An example of a
	   submenu screen is shown in Screen P-2.



				     viii



     Preface
     ______________________________________________________________________


	o  The term "menu screen" indicates the customized display screens
	   that you create using the Menu Maintenance Utility. A menu
	   screen is made up of one or more menu items.

	o  The term "menu item" refers to the specific operating system or
	   application listed on a menu screen. A menu item is composed of
	   a tag and a legend.

	o  The term "tag" refers to the acronym used to identify an
	   operating system or application listed on a menu screen. For
	   example, MM on the fixed menu screen is the tag for the Menu
	   Maintenance Utility.

	o  The term "legend" refers to the short title indicating the
	   specific operating system or application that runs when you
	   select its associated tag.  For example, Menu Maintenance
	   Utility is the legend associated with the MM tag on the fixed
	   menu screen.

	o  The symbols <^> and <v> refer to the up and down arrow keys. Use			|	|
	   these keys to move up or down a particular menu.

	o  The term "highlight" corresponds to the reverse video block on a
	   menu screen that you move with <^> and <v> to select a menu					   |	   |
	   item.

	o  The term "cursor" corresponds to the reverse video block on a
	   menu screen that highlights the data that is being input.

     Screen P-1, the DECmate Master Menu (fixed menu) screen, and Screen
     P-2, the Hard Disk Services submenu, illustrate the conventions used
     in this guide.





















				      ix



     Preface
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{ d i g i t a l		    DECmate Master Menu			 }|
     |									  |
     |Screen X Of X	     Thursday 07/12/84 11:16:48	       Version 1.1|
     | __________________________________________________________________ |
     ||									 ||
     || HD    DECmate Hard Disk Services <---------------- Menu Item	 ||
     ||									 ||
     ||	MM    DECmate Menu Maintenance Utility <---------- Legend	 ||
     ||									 ||
     || DAT   Set System Date and Time					 ||
     ||									 ||
     || SDF  Select New Date Format					 ||
     ||									 ||
   ---> F    Finished Using the System					 ||
   | ||									 ||
   | ||									 ||
   | ||									 ||
   | ||__________________________________________________________________||
   | |									  |
   | |Select an item using arrow keys or type its tag; then press DO. {HD}|
   | |	      Press NEXT SCREEN for more items.			       ^  |
   | |								       |  |
   | |								       |  |
   | ------------------------------------------------------------------|---
   |				^				       |
   Tag			Fixed Menu Screen			    Cursor


	Screen P-1























				       x



     Preface
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			      Hard Disk Services			 }|
     |Screen 1 Of 2				Thursday 07/12/84 11:16:06|
     |									  |
   -------------> {L}-- List directory of volumes			  |
   | |									  |
   | |		   A -- Allocate a new volume				  |
   | |									  |
   | |		   E -- Erase an existing volume			  |
   | |									  |
   | |		   B -- Backup Volume(s) to diskettes			  |
   | |									  |
   | |		   R -- Restore a volume from diskettes			  |
   | |									  |
   | |		   Q -- Quit this program				  |
   | |									  |
   | |									  |
   | |									  |
   | |									  |
   | |									  |
   | |									  |
   | | Select an item using arrow keys or type its tag; then press DO.    |
   | |       Press NEXT SCREEN for more items.				  |
   | |									  |
   | ----------------------------------------------------------------------
   |						^
   Highlight				   Submenu Screen

	Screen P-2


     Reference Manuals

     Although this manual uses CP/M, COS-310, MS-DOS, and WPS as examples
     of operating systems you can use with Master Menu, it does not attempt
     to describe those operating systems.  Refer to the following manuals,
     as needed, for a description of the specific operating systems that
     you can install on your DECmate system:

	  COS-310 New User's Guide

	  DECmate CP/M-80 User's Guide

	  DECmate Word Processing User's Guide

	  DECmate MS-DOS User's Guide

	  DECmate MS-DOS Tutorial





				      xi


									  1
     ______________________________________________________________________
						Introduction to Master Menu





     Master Menu is a versatile, easy to use, office automation tool that
     manages the hard disk space on your DECmate system.  The hard disk
     enables Master Menu to address the disk as if it is a large set of
     diskettes (called volumes).  This capability makes the hard disk
     uniquely flexible, and allows you to place multiple operating systems
     and applications on your hard disk.  By using Master Menu, you can
     easily move from one operating system or application to another.

     With Master Menu, you can create menu items that can be used to access
     the operating systems and applications installed on your hard disk. In
     addition, you can use these menu items to access operating systems and
     applications that are on diskettes.

     If you install WPS Word Processing on your hard disk, you can create,
     print, and back up documents.  The storage capacity of the hard disk
     is 10-20 times greater than a diskette, depending upon the size of
     your hard disk.


     Prerequisites for Master Menu

     There are three prerequisites when you install Master Menu on your
     DECmate system for the first time:

	o  Install a hard disk unit on your DECmate system.

	o  Format the hard disk unit.

	o  Use the System Test diskette and run the utility called System
	   Test to ensure the hard disk unit is installed, formatted, and
	   running correctly.

     If you have Version 1.0 of Master Menu, you must update internal data
     on your hard disk before you can install Version 1.1 of Master Menu.
     Use the latest System Test diskette and run the utility called Update
     Internal Data on Hard Disk Drive.

     Instructions for performing these prerequisites are included in the
     "DECmate II Hard Disk Subsystem Installation Guide".  If you have not
     installed and formatted your hard disk subsystem at this time, do so
     before you proceed.


     Master Menu Program Diagram

     Figure 1-1 illustrates the functions and utilities within Master Menu.




				      1-1



     Introduction to Master Menu
     ______________________________________________________________________
						

		      ----------
		      | MASTER |
		      |  MENU  |
		      ----------
			  |
	    ______________|______________
	   |				 |
     --------------		     ----------
     | CUSTOMIZED |		     | FIXED  |
     |   MASTER   |		     |  MENU  |
     |    MENU    |		     | SCREEN |
     |  SCREENS   |		     ----------		      |-- LIST
     --------------			 |		      |
	   |				 |-- HARD DISK -------|-- ALLOCATE
	   |-- USER APPLICATION 1	 |   SERVICES	      |
	   |				 |		      |-- ERASE
	   |-- USER APPLICATION 2	 |-- MENU	      |
	   |				 |   MAINTENANCE      |-- BACKUP
	   |-- USER APPLICATION 3	 |		      |
	   |				 |-- SET SYSTEM	      |-- RESTORE
	   |-- USER APPLICATION 4	 |   DATE AND TIME    |
					 |		      |-- QUIT
					 |-- SELECT NEW	      |
					 |   DATE FORMAT      |-- RENAME
					 |		      |
					 |-- FINISH USING     |-- ASSIGN
					     SYSTEM	      |
							      |-- SELECT
							      |
							      |-- UN-SET
							      |
							      |-- COPY
							      |
							      |-- BAD BLOCK
							      |
							      |-- COMPRESS

								BSED-409

     Figure 1-1  Master Menu Program


     Master Menu consists of the fixed menu screen, and the customized menu
     screens that are created with the Menu Maintenance Utility.  The fixed
     menu screen lists the Master Menu functions and utilities that are
     available;  the customized menu screens list the menu items that have
     been created to access applications.






				      1-2



     Introduction to Master Menu
     ______________________________________________________________________
						

     Special Function Keys

     Figure 1-2  shows the DECmate keyboard.

	

	Figure 1-2 not yet included in this document.

								BSED-408

     Figure 1-2 The DECmate Keyboard


     The three keys shaded on the DECmate keyboard (Print Screen, Cancel,
     and Main Screen) in Figure 1-2 are keys Master Menu uses that may not
     be familiar to you.  These keys are discussed in the following
     paragraphs.  (The Return and Do keys are discussed in the Preface;
     for a complete discussion of all the other keys on the DECmate
     keyboard, refer to the DECmate II Owner's Manual.)


     Print Screen Key

     The Print Screen key stops all screen activity and transfers the
     contents of your screen to the printer.


     Cancel Key

     The Cancel key (F8) lets you cancel data entry in a function, utility,
     or menu screen.  When you press <Cancel> once, Master Menu cancels
     your data entry without recording the entry and redisplays the
     previous screen.


     Main Screen Key

     The Main Screen key (F9) allows you to display the previous menu
     screen after you complete an operation.  For example, when you finish
     using the Backup function, press <Main Screen> to redisplay the Hard
     Disk Services screen.












				      1-3


									  2
     ______________________________________________________________________
					   Getting Started with Master Menu





     The following steps explain how to l) quickly install Master Menu on
     your DECmate system, and 2) create a sample menu item.  These steps
     are only intended to be guidelines.  Refer to Chapter 3, "Installing
     Master Menu on Your DECmate System," for a detailed description of the
     installation procedure;  refer to Chapter 4, "Menu Maintenance," for
     detailed menu maintenance procedures.


     Installing and Booting Master Menu on Your Hard Disk

	1  Turn on your system and immediately insert the Master Menu
	   Installation Diskette A into drive A (or 0).

	2  Make backups of the Master Menu Installation Diskettes A and B
	   by moving the highlight with <v> to the COPY option and pressing					 |
	   <Do>.

	3  Install Master Menu by inserting the Master Menu Installation
	   Diskettes A and B into the appropriate drives, and moving the
	   highlight to the INST option and pressing <Do>.

	4  Reboot the system (load Master Menu again) by moving the
	   highlight to the QUIT option and pressing <Do>.  Press <Remove>,
	   open the door to drives A and B, and press <Do> to boot the
	   system.  At this point, the system date and time prompts
	   display.

	5  Enter today's date (in the format mm/dd/yy) and then the time
	   (in the format hh:mm).  At this point, the system displays the
	   fixed menu screen.


     Creating, Displaying, and Deleting a Sample Menu Item

	1  Select the Menu Maintenance Utility by typing MM and pressing							 __
	   <Do>.

	2  Press <Insert Here> to display a screen named Edit a Menu Line
	   Item.

	3  Create a sample menu item for WPS Word Processing by completing
	   the following fields. (Use <v> to move the highlight to the next				       |
	   field.)
	
		Tag field - Type WPS				 ___

		Legend field - Type Word Processing				    _______________



				      2-1



     Getting Started with Master Menu
     ______________________________________________________________________


		Volumes/System field - Type WPSYSTEM					    ________

		Volumes/Data fields - Leave blank

		Command String field - Leave blank

	4  Press <Do> twice to record the information, and to display the
	   sample menu item that you just created.

	5  Select the Menu Maintenance Utility again (by typing MM and								__
	   pressing <Do>).

	6  Use <v> to move the highlight to the WPS tag, and press <Remove>		|
	   to delete the sample menu item.

	7  Press <Do> to return to the fixed menu screen.  At this point,
	   you are ready to create menu items for the applications you are
	   going to use.



































				      2-2


									  3
     ______________________________________________________________________
			      Installing Master Menu on Your DECmate System





     To install and verify Master Menu on your DECmate system, perform the
     following steps:

	1  Boot the Master Menu Installation software.

	2  Make a copy of the Master Menu Installation software.

	3  Install Master Menu on the hard disk.

	4  Quit the program and verify the installation of Master Menu on
	   the hard disk.


     Booting the Installation Software Program from the Diskette

     To boot the Master Menu Installation software, follow these steps:

	1  Open the diskette drive doors and make sure all drives are
	   empty, as shown in Figure 3-1.



	Figure 3-1 not yet included in this document.


     Figure 3-1  Open Drive Doors


	2  Press the system unit power switch to the on (1) position (see
	   Figure 3-2).  If the power switch is already on, turn it off,
	   wait 4 seconds, then turn it on again.



	Figure 3-2 not yet included in this document.


     Figure 3-2  Press System Unit Power Switch On


	3  Immediately insert the Master Menu Installation Diskette A into
	   drive A and close the drive door.  Make sure the arrow on the
	   diskette lines up with the colored bar on the drive.  (Figure 3-3
	   shows how to insert a diskette into drive A.)

	   Master Menu Installation Diskettes A and B are included with
	   your hard disk documentation.  They should not have write-
	   protect tabs.


				      3-1



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


	   NOTE:  If you do not insert the DECmate Master Menu Installation
	   Diskette A immediately, the system will boot the startup volume
	   of Master Menu that is already established on your hard disk (if
	   one exists).  In other words, you will not boot the DECmate
	   Master Menu that exists on the diskette.  If this should happen,
	   either turn off the system and repeat from step 2, or press
	   <Set-Up>, press <Remove>, insert the Master Menu Installation
	   Diskette A into Drive A, close the drive door, and press <Do>.



	Figure 3-3 not yet included in this document.


     Figure 3-3  Insert Installation Diskette A into Drive A


	   At this point, installation software for Master Menu is booted
	   from the diskette.  After a few seconds, the system displays the
	   DECmate Master Menu Install Diskette menu (Screen 3-1).


     ----------------------------------------------------------------------
     |{		     DECmate Master Menu Install Diskette		 }|
     |						 Panel Code Rom Level: XXX|
     |						 Internal Data Level: YYYY|
     |									  |
     |{INST} Install Master Menu					  |
     |									  |
     | COPY  Make backup copies of installation diskettes		  |
     |									  |
     | SMPW  Set Master password					  |
     |									  |
     | PSW   List volume passwords					  |
     |									  |
     | MBB   Mark a bad block						  |
     |									  |
     | QUIT  Leave this program and go to SETUP to reboot		  |
     |									  |
     |									  |
     |									  |
     |									  |
     | Select an item using arrow keys or type its tag, then press DO.    |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 3-1




				      3-2



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     You can select a menu item in one of two ways:

	o  Type the tag associated with the menu option that you want and
	   press <Do>.

     OR

	o  Use <^> and <v> to move the highlight to the option that you		|	|
	   want and press <Do>.


     COPY - Make Copies of the Installation Diskettes

     Before installing Master Menu on your hard disk, it is advisable to
     make copies of the Master Menu Installation Diskettes A and B.  This
     ensures that you will always have backup copies of the installation
     program.

     To make a copy of the installation software, select the COPY option by
     either typing COPY and pressing <Do>, or by moving the highlight to
     the COPY tag and pressing <Do>.

     The system clears the screen and displays the following:

     ----------------------------------------------------------------------
     | Put diskette to be copied in Drive 0(A).				  |
     | Put diskette that will receive the copy in Drive 1(B).		  |
     | Press DO when ready. Press CANCEL to return to Install menu.	  |
     ----------------------------------------------------------------------

     Insert a blank diskette into drive B, aligning the arrow on the
     diskette with the arrow on the drive, close the door, and press <DO>.
     (Master Menu Installation Diskette A should already be in drive A.)

     The system then begins to copy the installation software that is on
     diskette A.  During the process, the system displays:

     ----------------------------------------------------------------------
     | COPYING TRACK:       0						  |
     ----------------------------------------------------------------------

     The counter (0) increases by one each time a track is copied to the
     blank diskette.  When all the tracks have been copied (80 in total),
     the system redisplays the following:

     ----------------------------------------------------------------------
     | Put diskette to be copied in Drive 0(A).				  |
     | Put diskette that will receive the copy in Drive 1(B).		  |
     | Press DO when ready.  Press CANCEL to return to Install menu.	  |
     ----------------------------------------------------------------------



				      3-3



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     Insert the Master Menu Installation Diskette B into drive A, and
     insert a blank diskette into drive B.  (Again, make sure the arrows
     are aligned properly.) Close the doors to both drives and press <Do>.

     After the installation software on diskette B has been copied, the
     copy instructions display again.  At this point, put the original
     diskettes in their protective envelopes and store them in a safe
     place.  Label the backup diskettes, and then insert the backup
     version of Master Menu Installation Diskette A into drive A, press
     <Cancel>, and then press <Do> to redisplay the DECmate Master Menu
     Install Diskette menu (Screen 3-1).


     INST - Install Master Menu

     After the Master Menu installation software has been copied, you are
     ready to install Master Menu on your hard disk.  To install Master
     Menu, select the INST option and press <Do> (The backup version of
     Master Menu Installation Diskette A should already be in drive A.)

     NOTE:  Master Menu is installed with the volume name MENU.  If you
     already have a volume named MENU on your hard disk, and if this volume
     does not contain the Master Menu system (it is possible that another
     application is named MENU), the contents of the volume is erased when
     you install Master Menu.  Therefore, if you want to keep your MENU
     volume use the Rename function (in CP/M or MS-DOS) to change the
     volume name to another name. (You must rename the volume before you
     install Master Menu.)

     If your hard disk has a volume named MENU, and if the volume does not
     contain the Master Menu system, the following displays:

     ----------------------------------------------------------------------
     | Volume named MENU is not a Master Menu volume. If you proceed,	  |
     | the contents of this volume will be erased. To proceed, press DO.  |
     | To abort, press CANCEL.						  |
     ----------------------------------------------------------------------

     If you do not want to continue with the installation (in other words,
     you want to keep the contents of the volume named MENU), press
     <Cancel> and Screen 3-1 displays again.

     If you want to continue with the installation (in other words, you do
     not need the contents of the volume named MENU), press <Do>.  At this
     point, the system displays the Install Master Menu screen (Screen 3-2).

     If your hard disk does not have a volume named MENU, the system
     displays the Install Master Menu screen (Screen 3-2).  The system also
     displays this screen if your hard disk does contain a volume named
     MENU, but the volume already contains the Master Menu system.



				      3-4



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			      Install Master Menu			 }|
     | Version 1.1							  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 3-2

     If you have already installed a version of Master Menu on your hard
     disk, the following displays on your terminal:

     ----------------------------------------------------------------------
     | Saving your old menu items.					  |
     ----------------------------------------------------------------------

     At this point, the system is saving all the customized menu items that
     have already been created.  When the Master Menu software is
     installed, these menu items will be copied to the new version of
     Master Menu.

     After the software from Master Menu Install Diskette A has been
     installed, and all customized menu items have been saved (if
     appropriate), the following displays:

     ----------------------------------------------------------------------
     | Place {Master Menu Install Diskette B) in Drive 1(B) and close the |
     | door. Press DO when ready.					  |
     ----------------------------------------------------------------------

     If you do not want to continue with the installation, press <Cancel>,
     and then press <Main Screen> to display the DECmate Master Menu
     Install Diskette menu screen again (Screen 3-1).

     If you want to continue with the installation, insert the backup
     version of Master Menu Installation Diskette B into drive B and press
     <Do> to begin installing Master Menu on your hard disk.

     At this point, the following displays:





				      3-5



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     ----------------------------------------------------------------------
     | Installing new Master Menu system.				  |
     |									  |
     | .........................................................	  |
     ----------------------------------------------------------------------

     The row of dots is proportional to the amount of data that is being
     installed on your hard disk.  As the installation process continues,
     the dots change to asterisks, one by one.

     When the installation process is complete, and if menu items were
     saved, the system displays the following:

     ----------------------------------------------------------------------
     | Restoring your old menu items.					  |
     ----------------------------------------------------------------------

     The customized menu items that were copied earlier are now written
     back to the version of Master Menu that you just installed on your
     hard disk.  (Again, you will not have any menu items if this is the
     first time you are installing Master Menu.)

     If menu items were not restored, remove Master Menu Installation
     Diskette B from drive B, and press <Main Screen> to display the
     DECmate Master Menu Install Diskette screen again (Screen 3-1).

     When all of the customized menu items have been restored (if
     appropriate), remove Master Menu Installation Diskette B from drive B,
     and press <Main Screen> to display the DECmate Master Menu Install
     Diskette screen again (Screen 3-1).


     SMPW - Set Master Password

     The Master Password function lets you (or the system manager) assign a
     password to the List Password function.  (The List Password function
     is discussed in the next section.) Although it is not necessary to
     assign a master password, it is a good idea to do so, since it
     prevents unauthorized personnel from displaying the READ and WRITE
     passwords that you have assigned to the volumes on your hard disk.
     In other words, if a master password has been assigned, before you
     (or anyone else) can list the passwords, the master password must be
     entered.

     NOTE:  There is no master password when Master Menu is initially
     installed on your hard disk.  If you (or the system manager) decide to
     assign a master password, make sure you write it down.  If you forget
     the password, or if you lose it, you will not he able to list the
     passwords associated with the volumes on your hard disk.  Refer to
     Chapter 8, "Using Passwords," for the procedures to follow if you
     forget the master password.


				      3-6



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     To assign a master password, select the SMPW option and press <Do> to
     display Screen 3-3.


     ----------------------------------------------------------------------
     |{			      Set Master Password			 }|
     |									  |
     | IMPORTANT: Carefully record the number you enter below for	  |
     | future reference.						  |
     |									  |
     | Enter new Master Password: {  }					  |
     |									  |
     | Enter a number between 1 and 65535 or press RETURN (or zero)	  |
     | for no password.							  |
     |									  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 3-3

     Enter the numeric password that you want to assign to the List Password
     function.  The number cannot be greater than 65535. If you do not want
     to assign a master password, press <Return>.

     If you want to change the master password, select the SMPW option and
     the following displays:

     ----------------------------------------------------------------------
     | Enter current Master Password:					  |
     ----------------------------------------------------------------------

     Enter the password that is currently assigned to the List Password
     function.  (The input is display protected.) If you enter the correct
     password, the system prompts you for the new master password.  If you
     enter the incorrect password, the system displays the DECmate Master
     Menu Install Diskette menu again (Screen 3-1).

     NOTE:  Whenever the system prompts you for the existing master
     password, your input is display protected.  The system protects your
     response from view by displaying an X for each digit you type.  In
     other words, if you enter 123 as the password, XXX displays on your
     terminal screen.  (This prevents other users from seeing the master
     password that has been assigned to the List Password function.)







				      3-7



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     PSWD - List Volume Passwords

     The List Password function lets you list the READ and WRITE passwords
     of every volume on your DECmate system.  If you assigned a master
     password, the list does not display unless the correct master password
     is entered.  (This prevents unauthorized users from displaying the
     passwords that you have assigned to the volumes on your hard disk.) If
     no master password has been assigned, the list displays immediately.

     To display the READ and WRITE passwords, select the PSWD option and
     press <Do>.  The system clears the screen and, if there is a master
     password, displays the following:

     ----------------------------------------------------------------------
     | Enter Master Password:						  |
     ----------------------------------------------------------------------

     Enter the password that is currently assigned to the List Password
     function.  (The input is display protected.) If you enter the correct
     master password, the system displays a list of the READ and WRITE
     passwords associated with the volumes on your hard disk. If you enter
     the incorrect master password, the DECmate Master Menu Install
     Diskette screen displays again (Screen 3-1).

     Refer to Chapter 8, "Using Passwords," for a complete description of
     the passwords and their optional use in allocating volumes.


     MBB - Mark a Bad Block

     This function allows you to isolate a bad block on the hard disk.  Bad
     blocks are areas that are corrupted and cannot be used to store
     information.  The integrity of any information stored in a bad block
     cannot be guaranteed.

     Refer to Chapter 7, "Hard Disk Services," for detailed instructions in
     marking a bad block on your hard disk.


     QUIT - Leave this Program and Go to SETUP to Reboot

     Your hard disk is now installed with Master Menu.  There are two
     procedures that can be used to verify a correct installation:

	o  Select the QUIT option, press <Do>, open the door to drive A,
	   press <Remove>, and then press <Do> again.

	   The system boots the startup volume (MENU) from the hard disk,
	   and then displays Screen 3-4, the Set Date and Time screen. (The
	   startup volume is the operating system that is booted whenever
	   you start your DECmate system without an operating system
	   diskette in drive A.)

				      3-8



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     OR

     Open the door to drive A, turn off your system, and reboot the system
     (by turning on the power switch).  The system displays the Set Date
     and Time screen (Screen 3-4).  This indicates that Master Menu is
     installed on your hard disk and MENU is the startup volume. (Every
     time you turn on the power switch, if the door to drive A is open,
     Master Menu is booted from the hard disk.)

     In both procedures, you opened the door to drive A.  This instructs
     your DECmate system to boot from the hard disk unit.


     ----------------------------------------------------------------------
     |{			       Set Date and Time			 }|
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     | Enter today's date in the form mm/dd/yy: {_}______		  |
     |									  |
     |									  |
     |									  |
     |						 Panel Code Rom Level: XXX|
     |						 Internal Data Level: YYYY|
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 3-4

     Enter the current date in the format that is shown.  There are three
     possible formats mm/dd/yy, yy/mm/dd, or dd/mm/yy, where mm is the
     2-digit month, dd is the 2-digit day, and yy is the 2-digit year.  You
     can enter the date with optional leading zeros or optional slash marks.
     For example, if the format is mm/dd/yy, you can enter February 3, 1984
     as 020384, 2/3/84, or 02/03/84.  (Refer to Chapter 5, "Date and Time
     Functions," for information on changing the system date format.)

     After you enter the date, the date is validated and the following
     displays:

     ----------------------------------------------------------------------
     | Enter the time of day in the form hh:mm: {_}____			  |
     ----------------------------------------------------------------------

     Enter the time in the format shown.  For example, if it is 10:30,
     enter 10:30.  If you do not want to enter the time, press <Return>.


				      3-9



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     After you enter the time, the system clears the screen and displays
     either the fixed menu screen or the first customized menu screen,
     depending upon whether or not you have created any menu screens.  The
     displays the date and time that you enter on this screen.  (The time
     that displays includes seconds.)

     NOTE:  After installing Master Menu and rebooting the system, put the
     backup copies of the Master Menu Installation Diskettes A and B in
     their protective envelopes and store them in a safe place (You should
     have already stored the original diskettes.) This ensures that you
     have control over any reinstallations of Master Menu.  Use the backup
     versions of the diskettes for subsequent installations.


     Fixed Menu Screen

     If you have not created any menu items, the fixed menu screen, Screen
     3-5, is the first screen that appears after the Set Date and Time
     screen.  (If you have created one or more menu screens, the fixed menu
     screen is the last screen.)

     ----------------------------------------------------------------------
     |{  d i 9 i t a l		 DECmate Master Menu			 }|
     |									  |
     | Screen  X Of  X		Thursday 07/12/84 11:16:48     Version 1.1|
     |									  |
     | HD    DECmate Hard Disk Services					  |
     |									  |
     | MM    DECmate Menu Maintenance Utility				  |
     |									  |
     | DAT   Set System Date and Time					  |
     |									  |
     | SDF   Select New Date Format					  |
     |									  |
     | F     Finished Using the System					  |
     |									  |
     |									  |
     |									  |
     |									  |
     | Select an item using arrow keys or type its tag; then press DO.    |
     | Press NEXT SCREEN for more items.				  |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 3-5






				      3-10



     Installing Master Menu on Your DECmate System
     ______________________________________________________________________


     The options available on the fixed menu screen are:

	o  HD Hard Disk Services -- These functions allow you to perform
	   maintenance and other operations on the volumes residing on the
	   hard disk.  Refer to Chapter 7, "Hard Disk Services," for more
	   information on this option.

	o  MM Menu Maintenance Utility -- This is the utility you use to
	   create and maintain customized menu screens.  If Master Menu is
	   not the only volume on your hard disk, use this utility to
	   create menus to access the other volumes.  Refer to Chapter 4,
	   "Menu Maintenance," for more information on this option.

	o  DAT Set System Date and Time -- This function sets the system
	   date and time for your DECmate system.  Refer to Chapter 5,
	   "Date and Time Functions," for more information on this option.

	o  SDF Select New Date Format -- This function allows you to change
	   the format of the system date display.  Refer to Chapter 5,
	   "Date and Time Functions," for more information on this option.

	o  F Finished Using the System -- This function allows you to exit
	   Master Menu.






























				      3-11


									  4
     ______________________________________________________________________
							   Menu Maintenance





     The DECmate Menu Maintenance Utility allows you to create and maintain
     menu items that list the specific operating systems and applications
     residing on your DECmate hard disk system.  You can also create menu
     items to access operating systems and applications that are on
     diskettes.

     The DECmate Menu Maintenance Utility function is an option on the
     fixed menu screen.  To select this function, press <^> or <v> to move							 |	|
     the highlight to the MM tag and press <Do>, or type MM and press <Do>.

     The system displays all of the menu items that have been created to
     date.  The cursor is positioned at the first -------NEW SCREEN-------
     line. (The -------NEW SCREEN------- line separates the menu items into
     menu screens.) If you have not created any menu items, no menu items
     are listed (Screen 4-1).

     ----------------------------------------------------------------------
     |{		       DECmate Menu Maintenance Utility			 }|
     |									  |
     | {-}-------NEW SCREEN-------					  |
     |   <End Of List>							  |
     |									  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     |									  |
     | Valid Keys Are: UPARROW, DOWNARROW, INSERT, REMOVE, SELECT, PAGE,  |
     | DO, CANCEL, CUT and PASTE					  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-1


     Menu Items

     You can tailor menu items to accommodate your needs.  For example, you
     can create a menu item that assigns a device number to one or more WPS
     Word Processing data volumes that are on your hard disk.  This method
     of assigning device numbers is convenient because the numbers stay
     assigned, even when your DECmate system is turned off.

     You can create as many menu items as you want, with up to seven menu
     items on a screen.  However, your total number of items cannot exceed
     64 lines (including blank lines).  For example, if you create three
     menu items, and you skip a line between each item, you are using a
     total of five lines.

				      4-1


     Menu Maintenance
     ______________________________________________________________________


     Each menu item consists of two parts: a tag (or acronym), and a legend
     that describes the item.  You can group related menu items together on
     one screen, or you can separate them from other items by using page
     (screen) markers. (Refer to the section in this chapter called "Menu
     Screens" for information on creating menu screens.)

     Screen 4-2 is an  example of a listing of menu items.


     ----------------------------------------------------------------------
     |{		       DECmate Menu Maintenance Utility			 }|
     |									  |
     |									  |
     | {-}-------NEW SCREEN-------					  |
     |  WPS	  Word Processing					  |
     |  CPM	  CP/M Operating System					  |
     |  MP	  Multiplan						  |
     | --------NEW SCREEN-------					  |
     |  COS	  Select the COS-310 Operating System			  |
     |  DA	  Daley-Aids						  |
     |  CGL	  COS-310 General Ledger Application			  |
     | --------NEW SCREEN-------					  |
     |  WP1	  Peter Sullivan's Word Processing Files		  |
     |  WP2	  Marie Berenson's Word Processing Files		  |
     |  BG1	  1983 Fiscal Budget -- Accounting Department		  |
     |  BG2 	  1983 Fiscal Budget -- Marketing Department		  |
     |  <End Of List>							  |
     |									  |
     |									  |
     |									  |
     | Valid Keys Are: UPARROW, DOWNARROW, INSERT, REMOVE, SELECT, PAGE,  |
     | DO, CANCEL, CUT and PASTE.					  |
     ----------------------------------------------------------------------

	Screen 4-2

     In this example there are ten menu items on three menu screens.  The
     screens contain tags for the menu items.  The applications include
     operating systems that can be run from the hard disk or from a
     diskette (WPS, CPM, COS), program applications that can be executed
     directly from the menu (MP, DA, CGL), and personal word processing
     data and budget files (WP1, WP2, BG1, BG2).

     If these menu items were created for your system, the following screen
     (Screen 4-3) would display each time you start your system.  (Notice
     that this screen is the first menu screen listed in Screen 4-2.)

     The following sections describe the steps you take to create and
     maintain menu items.





				      4-2


     Menu Maintenance
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{  d i g i t a l 		       DECmate Master Menu		 }|
     |									  |
     | Screen 1 Of 4      Tuesday 07/10/84 04:25:10	       Version 1.1|
     |									  |
     |  {WPS}  Word Processing						  |
     |									  |
     |   CPM   CP/M Operating System					  |
     |									  |
     |   MP    Multiplan						  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     | Select an item using arrow keys or type its tag; then press DO. 	  |
     | Press NEXT SCREEN for more items.				  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-3


     Creating a Menu Item

     If you are creating one or more menu items, position the cursor next
     to the tag where you want to insert these items.  (If you have not
     created any menu items, the cursor is already positioned at the
     --------NEW SCREEN------- line.)  Once the cursor is positioned, press
     <Insert Here> to display the following screen (Screen 4-4).

     Perform the following steps for each menu item that you want to
     create:

	1  Type the tag (up to three alphanumeric characters) for the menu
	   item that you are adding.  Use an acronym or code that you are
	   familiar with, so that you can easily recognize the application
	   associated with the tag.  For example, you might want to use WP
	   or WPS to indicate the word processing operating system.  Then,
	   press <v> to move the cursor to the Legend field.		  |

	   NOTE:  If you are installing WPS V2.0 on your hard disk, you do
	   not need to create a menu item for the WPS operating system.
	   WPS Install (the installation software) does this for you.  The
	   system creates a WPS tag and legend, it allocates a WPS system
	   volume (named WPSYSTEM) and assigns it to device #0, and it also
	   allocates and initializes a WPS data volume (named WPSVOL1) and
	   assigns it to device #1.  In addition, if you have the necessary
	   diskettes available during the installation process, WPS Install
	   allocates data volumes for WPS Utility and WPS Dictionary. These
	   volumes (named WPSUTIL and WPSDIC7 respectively) are assigned to
	   device #6 and device #7.

				      4-3


     Menu Maintenance
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			     Edit a menu line item			 }|
     |									  |
     | Tag: {---}						 	  |
     |									  |
     | Legend:								  |
     |									  |
     | --------------------------------------------------------		  |
     |									  |
     | Volumes: System: ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |		Data:   ________					  |
     |									  |
     | Command String:							  |
     |									  |
     | ---------------------------------------------------------	  |
     |									  |
     | Move the highlight with the up and down arrow keys. Blank a field  |
     | by pressing REMOVE. Press DO to store data, or press CANCEL to 	  |
     | redisplay the previous menu.					  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-4

	2  Type the legend (up to 72 characters, including spaces) that you
	   want to display on the menu screen next to the tag.  (If you are
	   creating a menu item for word processing, you might want to use
	   Word Processing or Word Processing Version X for the legend.)
	   Press <v> to move the cursor to the Volumes/System field.		  |

	3  Type the name of the bootable system volume that you want Master
	   Menu to boot when this menu item is selected.  The system volume
	   that you enter must be an uppercase alphanumeric name, up to
	   eight characters in length, and it must be a valid operating
	   system volume that has been allocated to the hard disk.

	   NOTE:  Leave the Volumes/System field blank if you are going to
	   boot the operating system from a diskette, rather than from the
	   hard disk.  If you are going to boot from a diskette, enter the
	   operating system information in the Command String field.

	   If no system volume is entered, and if the command string does
	   not designate a diskette boot, the system defaults to the
	   operating system that is designated as the startup system
	   volume.  (Refer to Chapter 7, "Hard Disk Services," for
	   information about listing all the system volumes that are on the
	   hard disk.)

				      4-4


     Menu Maintenance
     ______________________________________________________________________


	   If you want to enter one or more data volumes, press <v> to move								 |
	   the cursor to the first Volumes/Data field.

	4  You use the Volumes/Data fields to indicate the name of the data
	   volume(s) that you want the system to assign when this menu item
	   is selected.  (A data volume can contain programs for the
	   operating system, data files, or text.)  The data volume that is
	   entered, like the system volume, must be an uppercase
	   alphanumeric name, up to eight characters long.  (Although the
	   volume does not have to be allocated to your hard disk at this
	   time, it must be allocated before you select the menu item for
	   execution.)

	   NOTE:  The data volume(s) that you choose will be assigned to
	   the device number that corresponds to the line number of the
	   data volume.  For example, if you type a data volume name on the
	   third data line, that volume will be assigned to the third
	   device.  (Refer to Table 9-3 for a list of valid devices for
	   each operating system.)

	   After you type all of the required data volume names, press <v>									|
	   until the cursor is at the Command String field.

	5  The Command String field allows you to pass one command to the
	   CP/M or MS-DOS operating system, or a series of commands to the
	   WPS operating system.  The command(s) is executed after the
	   operating system is booted.

	   For example, you can instruct the WPS operating system to
	   execute the command(s) defined in a User Defined Key (UDK). If
	   you set up the menu item to boot WPS from a diskette, you can
	   set up a command string similar to the following:

	   WPS-DISKETTE:<Return>E 4.2<Return><Gold>1<Gold>F

	   If you set up the menu item to boot WPS from the hard disk, you
	   could set up a command string similar to the following:

	   <Return>E 4.2<Return><Gold>1<Gold>F

	   In both examples, whenever the particular menu item is executed,
	   WPS is booted (from a diskette in drive 1(A), or from the hard
	   disk), the Word Processing Date/Time Menu is bypassed, the
	   second document on the data volume that is assigned to device #4
	   is displayed, the commands defined in UDK 1 are executed, and
	   then the document is filed.

	   An example of a command string to a CP/M operating system is:

	   WPSCONV

	   This command calls the utility program that converts CP/M text
	   files to WPS documents, and WPS documents to CP/M text files.

				      4-5


     Menu Maintenance
     ______________________________________________________________________


	   If you are going to boot the operating system from a diskette,
	   rather than from your hard disk, enter the appropriate boot
	   command for the operating system.  (Refer to Chapter 9, "Master
	   Menu and CP/M, COS-310, WPS, and MS-DOS," for command string
	   conventions for the operating systems.)

	   The specific commands that you can enter differ with each
	   operating system.  Refer to the appropriate operating system
	   user's guide for a complete description of the commands and
	   command format used with that system.

	   If the operating system does not need a command string, leave
	   the field blank.

     Screen 4-5 is an example of a menu item that has been created for the
     CP/M operating system.


     ----------------------------------------------------------------------
     |{			     Edit a menu line item			 }|
     |									  |
     | Tag: {D}BM							  |
     |									  |
     | Legend: Data Base Management System____________________		  |
     |									  |
     |	Volumes: System: CPM80SYS					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |		 Data:   ________					  |
     |									  |
     | Command String: DBMS___________________________________		  |
     |									  |
     | Move the highlight with the up and down arrow keys. Blank a field  |
     | by pressing REMOVE. Press DO to store data, or press CANCEL to     |
     | redisplay the previous menu.					  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-5

     In the previous example, a menu item has been created that boots the
     CP/M operating system.  After CP/M is booted, DBMS (a CP/M data base
     management system) is executed.

	6  Once the information has been typed for the menu item, press
	   <Do> to record the information.  At this point, the system
	   redisplays the DECmate Menu Maintenance Utility screen.  The


				      4-6


     Menu Maintenance
     ______________________________________________________________________


	   menu item that you just created is shown on the screen.  Screen
	   4-6 is an example of a menu item created for DBMS.


     ----------------------------------------------------------------------
     |{		       DECmate Menu Maintenance Utility			 }|
     |					 				  |
     | --------NEW SCREEN-------					  |
     | {}DBM 	 Data Base Management System				  |
     | <End Of List>							  |
     |									  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     |									  |
     |									  |
     |									  |
     | Valid Keys Are: UPARROW, DOWNARROW, INSERT, REMOVE, SELECT, PAGE,  |
     | DO, CANCEL, CUT and PASTE					  |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-6

	7  When you have created all the menu items, press <Do> again to
	   save all the items and to return to your first customized menu
	   screen.

	   NOTE:  If you press <Cancel>, rather than <Do>, the menu items
	   that you just created are not saved.


     Modifying a Menu Item

     To modify or change the menu items you created, press <^> or <v> to							    |	   |
     position the cursor next to the menu item that you want to modify, and
     press <Select>.

     The Edit a Menu Line Item screen displays with the information that
     currently exists for the menu item that you selected.  Use <^> or <v>								 |	|
     to position the cursor at the field(s) that you want to change.  When
     you move to a particular field, the system places the cursor on the
     first character of that field.  To change the field, type the correct
     information, or press <Remove> (to delete the contents of the field),
     and then retype the field.

     Screen 4-7 is an example of a menu item that is being modified for
     WPS.  In this example, another data volume (YRLYRPT) is being added.
     (When WPS 2.0 is installed on the hard disk, a menu item is created
     automatically.  The WPS tag and legend are created, and WPSYSTEM,

				      4-7


     Menu Maintenance
     ______________________________________________________________________


     WPSVOL1, WPSUTIL, and WPSDICT are allocated and assigned to specific
     devices.)


     ----------------------------------------------------------------------
     |{			     Edit a menu line item			 }|
     |									  |
     | Tag: {W}PS							  |
     |									  |
     | Legend: Word Processing Version 2.0____________________		  |
     |									  |
     | Volumes:  System: WPSYSTEM					  |
     |		 Data:   WPSVOL1					  |
     |		 Data:   YRLYRPT					  |
     |		 Data:   _______					  |
     |		 Data:   _______					  |
     |		 Data:   _______					  |
     |		 Data:   WPSUTIL					  |
     |		 Data:   WPSDICT					  |
     |									  |
     | Command String: _______________________________________		  |
     |									  |
     | Move the highlight with the up and down arrow keys. Blank a field  |
     | by pressing REMOVE. Press DO to store data, or press CANCEL to	  |
     | redisplay the previous menu.					  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 4-7

     In the previous example, the menu item has been modified to assign
     YRLYRPT to device #2.  In other words, when the menu item is selected,
     the data volumes (WPSVOL1, YRLYRPT, WPSUTIL, and WPSDICT) are assigned
     to devices #1, 2, 6, and 7 respectively.

     After modifying all the appropriate fields for the menu item, press
     <Do> to record the changes.  The system then displays the DECmate Menu
     Maintenance Utility screen again.

     When you have modified all the menu items that need to be changed,
     press <Do> again to save the changes.  At this point, the system
     returns to your first customized menu screen.

     NOTE: If you press <Cancel>, rather than <Do>, the changes that were
     made to the menu items are not saved.


     Deleting a Menu Item

     To delete menu items you have created, press <^> or <v> to position						   |	  |
     the cursor next to the menu item that you want to delete and press
     <Remove>.

				      4-8


     Menu Maintenance
     ______________________________________________________________________


     When you have deleted all the appropriate menu items, press <Do> to
     return to your first customized menu screen.

     NOTE: If you press <Cancel>, rather than <Do>, the items that you
     marked for deletion are not deleted.


     Selecting a Menu Item

     Once a menu item has been created for a particular application, you
     can select that application from the menu screen by pressing <^> or								   |
     <v> to move the highlight to the tag for the menu item and pressing      |
     <Do>.  You can also select the application by typing the tag and
     pressing <Do>.  For example, in Screen 4-3, WPS is the tag for Word
     Processing.

     If the tag refers to a volume that has a READ and/or WRITE password,
     the system prompts for the appropriate passwords.  If valid passwords
     are not entered, access to the volume is denied.  (Refer to Chapter 7,
     "Hard Disk Services," for information on assigning passwords.)

     When you press <Next Screen>, the system displays the second menu
     screen.  Pressing <Next Screen> again displays the third menu screen,
     and so on until you reach the last screen (the fixed menu screen).


     Menu Screens

     You can group menu items together to create menu screens.  Three menu
     screens are shown in Screen 4-2. Each screen is preceded by a
     --------NEW SCREEN-------- line.

     If you want to add a menu screen between two existing screens, use <^>									 |
     and <v> to move the cursor to the --------NEW SCREEN-------- line that	  |
     precedes the beginning of the second screen. For example, using the
     screens and menu items shown in Screen 4-2, if you want to add a new
     menu screen between the second and third screens, move the cursor to
     the --------NEW SCREEN-------- line that designates the beginning of
     the third screen, and press <Page>.  A "blank" screen is created
     between the second and third screens.  You are now ready to add menu
     items to this screen. Refer to the section in this chapter called
     "Creating a Menu Item" for instructions on how to add menu items to
     this screen.

     If you want to add another menu screen to the end of the screens that
     have already been created, move the cursor to <End Of List>, and press
     <Page> to create a "blank" screen.


     Adding a Page Marker to the Menu

     Use <Page> to add another page marker to your menu.  For example, if
     you have one menu screen with six items on it, and you want to have

				      4-9


     Menu Maintenance
     ______________________________________________________________________


     two menu screens with three items each, locate the screen that you
     want to change, move the cursor to the fourth menu item, and press
     <Page>.  The system adds a page marker before the fourth menu item.

     After you add the page marker(s), press <Do> to return to your first
     customized menu screen.

     NOTE: If you press <Cancel>, rather than <Do>, the page marker is not
     added.


     Deleting a Page Marker from the Menu

     Use <Remove> to delete a page marker from your menu. For example, if
     you have two menu screens with three items each, and you want to have
     one menu screen with six items on it, move the cursor to the
     appropriate --------NEW SCREEN-------- page marker, and press
     <Remove>.  The system deletes the page marker and moves the three menu
     items up to the previous screen.

     After you delete the page marker(s), press <Do> to return to your
     first customized menu screen.

     NOTE: If you press <Cancel>, rather than <Do>, the page marker is not
     deleted from the screen.


     Moving a Menu Item

     Use <Cut> and <Paste> to move a menu item from one area to another.
     (You can move the menu item to another area on the same menu screen or
     you can move the menu item to a different menu screen.) The procedure
     involves two steps:

	1  Use <^> and <v> to move the cursor to the menu item that you		|	|
	   want to move, and press <Cut>.  The system then displays a copy
	   of the menu item on the bottom line of the screen in reverse
	   video.  (The item also remains displayed in its original
	   location.)

	2  Move the cursor to the area where you want to insert the menu
	   item that was "cut", and press <Paste>.  The system then deletes
	   the menu item from its original position, inserts it in the new
	   area, and scrolls the remaining menu items up to fill the empty
	   space.

     After you move the menu item(s), press <Do> to return to your first
     customized menu screen.

     NOTE:  If you press <Cancel>, rather than <Do>, the menu item is not
     inserted in the new area.  Also, if you press <Cut> but do not press
     <Paste>, the menu item remains in its original location.


				     4-10


									  5
     ______________________________________________________________________
						    Date and Time Functions





     Master Menu provides you with the ability to set the system date and
     time on your hard disk.  It also provides you with the ability to
     change the format that is used by the system to display the date.


     DAT - Set System Date and Time

     The Set System Date and Time function sets the system date and time
     for the operating systems that you run on your DECmate system.
     However, the current version of the operating system may not accept
     the date and time.  Refer to Chapter 9, "Master Menu and CP/M,
     COS-310, WPS, and MS-DOS," for specific operating system information.

     NOTE: If you return to Master Menu (from an operating system) by
     pressing <Set-Up>, <Remove>, and <Do>, the system date and time are
     not passed to Master Menu (regardless of whether or not the operating
     system was booted from the hard disk or a diskette).

     The Set System Date and Time function is an option on the fixed menu
     screen.  To select this function, use <^> or <v> to move the highlight					    |	   |
     to the DAT tag and press <Do>, or type DAT and press <Do>.  In either
     case, the Set Date and Time screen (Screen 5-1) displays.

     NOTE:  Screen 5-1 also displays every time you boot Master Menu.


     ----------------------------------------------------------------------
     |{			       Set Date and Time			 }|
     |									  |
     |									  |
     |									  |
     |									  |
     | Enter today's date in the form mm/dd/yy: {_}_______		  |
     |									  |
     |									  |
     |									  |
     |									  |
     |						 Panel Code Rom Level: XXX|
     |						 Internal Data Level: YYYY|
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 5-1

     Enter the current date in the format that is shown.  There are three
     possible formats - mm/dd/yy, yy/mm/dd, or dd/mm/yy, where mm is the
     2-digit month, dd is the 2-digit day, and yy is the 2-digit year.  You

				      5-1


     Date and Time Functions
     ______________________________________________________________________


     can enter the date with optional leading zeros or optional slash
     marks.  For example, if the format is mm/dd/yy, you can enter February
     3, 1984 as 020384, 2/3/84, or 02/03/84.  (Refer to the following
     section, "SDF - Select New Date Format," for information on changing
     the system date format.)

     After you enter the date, the date is validated and the following
     prompt displays:

     ----------------------------------------------------------------------
     | Enter time of day in the form hh:mm: _____			  |
     ----------------------------------------------------------------------

     Enter the time in the format shown.  For example, if it is 10:30,
     enter 10:30.  If you do not want to enter a time, press <Return>.

     After you enter the time, the system displays either the fixed menu
     screen or the first customized menu screen, depending upon whether or
     not you have created any menu screens.  The date and time that you
     entered displays on this screen.  (The time that displays includes
     seconds.)


     SDF - Select New Date Format

     The Select New Date Format function is also an option on the fixed
     menu screen.  This function allows you to change the format for the
     system date display.

     Master Menu displays the system date in one of the following formats:

	o  mm/dd/yy

	o  dd/mm/yy

	o  yy/mm/dd

     For example, the system can display February 14, 1984 as 02/14/84,
     14/02/84, or 84/02/14.

     Whenever you change the format, Master Menu automatically changes the
     format on every screen that displays the system date.

     To select the Select New Date Format function, move the highlight to
     the SDF tag and press <Do>, or type SDF and press <Do> In either case,
     Screen 5-2 displays.








				      5-2


     Date and Time Functions
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			      Select Date Format			 }|
     |									  |
     | There are three date formats:					  |
     |									  |
     |      1.  mm/dd/yy						  |
     |									  |
     |	    2.  yy/mm/dd						  |
     |									  |
     |	    3.  dd/mm/yy						  |
     |									  |
     |									  |
     | Enter your selection (1, 2, or 3) and press RETURN: {}		  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 5-2

     Enter the number that corresponds to the desired system date format
     and press <Return>.

     If you just press <Return>, the system does not change the system date
     format.





























				      5-3


									  6
     ______________________________________________________________________
						  Finished Using the System


     When you are through using your DECmate system, select the Finished
     Using the System option on the fixed menu screen.

     Type F and press <Do>, or move the highlight to the F tag and press
     <Do>.  The system clears the screen and displays the following on your
     terminal:

     ----------------------------------------------------------------------
     |			Finished using the system.			  |
     |		      Press RETURN to go to Master Menu. { }		  |
     ----------------------------------------------------------------------

     If you want to return to Master Menu, press <Return>.  Otherwise, open
     the doors to both drives, remove the diskettes and put them in their
     protective envelopes, and turn off the system.






































				      6-1


									  7
     ______________________________________________________________________
							 Hard Disk Services





     This chapter explains the hard disk functions that are available with
     Master Menu.

     With Master Menu, you can:

	o  List the names of all volumes on the hard disk

	o  Allocate new volumes to the disk

	o  Erase existing volumes from the disk

	o  Back up volumes (using RX50 diskettes)

	o  Restore existing volumes to the disk (using RX50 backup
	   diskettes)

	o  Change the name of a volume

	o  Assign new passwords to a volume

	o  Designate a system volume as the startup volume

	o  Unset (or remove) the volume-modified flag from a volume

	o  Copy one volume to an existing volume of equal size

	o  Remove a known bad block on the hard disk from service and
	   replace it with a new block

	o  Compress separate empty spaces on the hard disk into one
	   contiguous space

     Because of the number of hard disk services Master Menu provides, the
     system displays the list of functions on two menu screens (Screens 7-1
     and 7-2).  Press <Next Screen> or <Prev Screen> to move from one
     screen to the other.  (Pressing <Next Screen> places the highlight on
     the first item of the next screen;  pressing <Prev Screen> places the
     highlight on the last item of the previous screen.)

     Select the Hard Disk Services from the fixed menu screen by moving the
     highlight to the HD tag and pressing <Do>, or by typing HD and
     pressing <Do>.

     Refer to the following sections for information on each hard disk
     service that is available.





				      7-1


     Hard Disk Services
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			      Hard Disk Services			 }|
     |									  |
     | Screen 1 Of 2 			 Thursday 07/12/84 12:10:18	  |
     |									  |
     |		   {L}-- List directory of volumes			  |
     |									  |
     |		    A -- Allocate a new volume				  |
     |									  |
     |		    E -- Erase an existing volume			  |
     |									  |
     |		    B -- backup Volume(s) to diskettes			  |
     |									  |
     |		    R -- Restore a volume from diskettes		  |
     |									  |
     |		    Q -- Quit this program				  |
     |									  |
     |									  |
     |									  |
     | Select an item using arrow keys or type its tag; then press DO.    |
     |	Press NEXT SCREEN for more items.				  |
     |									  |
     ----------------------------------------------------------------------

	Screen 7-1


     ----------------------------------------------------------------------
     |{			      Hard Disk Services			 }|
     |									  |
     | Screen 2 Of 2			 Thursday 07/12/84 12:15:11	  |
     |									  |
     |		   {N}-- New name for an existing volume		  |
     |									  |
     |		    P -- Assign new passwords for a volume		  |
     |									  |
     |		    S -- Select the startup volume			  |
     |									  |
     |		    U -- Un-set a volume-modified flag			  |
     |									  |
     |		    C -- Copy a volume to an existing volume of equal size|
     |									  |
     |		    M -- Mark a bad block				  |
     |									  |
     |		    X -- Compress the empty space on a drive		  |
     |									  |
     |									  |
     | Select an item using arrow keys or type its tag; then press DO.    |
     |	     Press NEXT SCREEN for more items.				  |
     |									  |
     ----------------------------------------------------------------------

	Screen 7-2

				      7-2


     Hard Disk Services
     ______________________________________________________________________


     L - List Directory of Volumes

     The List function on the Hard Disk Services menu displays the volumes
     that are on your hard disk.  When you select L and press <Do>, the
     system displays a list of all the volumes and unused areas on your
     hard disk.  A typical directory is shown in Screen 7-3.


     ----------------------------------------------------------------------
     |{			   List directory of volumes			 }|
     |									  |
     | Volume   Size    Type       Attributes		Last Backup	  |
     |									  |
     |	Index      32K  reserved					  |
     | CPM80SYS   784K  CP/M	   system		11/03/83 09:00	  |
     | MSDOSSYS   784K  MS-DOS	   system				  |
     | MENU 	  392K  MENU	   system modified startup		  |
     | WPSYSTEM   400K  WPS-8	   system 		06/26/84 11:45	  |
     | <empty>   7368K							  |
     |									  |
     ~									  ~
     |									  |
     | 5 volumes use 2392K. 7368K unused in 1 areas; largest is 7368K.	  |
     |									  |
     | Press MAIN SCREEN to redisplay the Hard Disk Services menu.	  |
     |									  |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 7-3

     The Volume field lists the names of all volumes that have been
     allocated on the hard disk.  You can have up to 60 volumes (including
     the Index volume and all the unused areas) in your directory.

     The Index volume is a volume that is created when you format the hard
     disk.  It contains the information that the DECmate system needs to
     access volumes on the hard disk.  You cannot access this volume.  The
     MENU volume is the Master Menu volume that you created with the
     installation procedure.  Unused area on the disk is identified as
     <empty>.

     The Size field lists the size of each volume in K bytes (one K byte is
     1024 bytes, or 2 blocks).

     The Type field shows the operating system associated with the
     particular volume.  (Possible operating systems are CP/M, COS-310,
     WPS-8, MS-DOS, and MENU.)  The Index volume always has "reserved" in
     this field;  MENU volumes (volumes containing the Master Menu system)
     always have "MENU" or "reserved" in this field.  ("MENU" indicates you


				      7-3


     Hard Disk Services
     ______________________________________________________________________


     are using Version 1.1 of Master Menu;  "reserved" indicates you are
     using Version 1.0 of Master Menu.)

     The Attributes field describes the characteristics of each volume.
     The word "modified" indicates that the volume has been modified since
     you created it, or it has been backed up, or the volume-modified flag
     has been reset.  The word "startup" indicates that the volume has been
     designated as the startup volume.  This means that, when you start
     your DECmate system without an operating system diskette in drive A,
     the system automatically boots from the startup volume on the hard
     disk.  (You can have only one startup volume on the hard disk at a
     time.)  The word "system" indicates that the volume contains a copy of
     an operating system, and it can be used as a startup volume.  If
     "system" is not displayed, the volume is a data volume. (A data volume
     can contain programs for the operating system, data files, or text.)

     The Last Backup field indicates the last date and time you backed up
     the volume (using the Backup function).

     If your volume list exceeds the number of lines that the system can
     display on one screen, the following message displays:

     ----------------------------------------------------------------------
     | Press any key to continue					  |
     ----------------------------------------------------------------------

     Press any key on the DECmate keyboard to continue displaying the list
     of volumes.

     After displaying the characteristics for all of the volumes, the
     system displays the total number of volumes on your hard disk, the
     total amount of space that these volumes occupy, the total amount of
     unused area, the number of unused areas, and the size of the largest
     unused area.  (Because each volume must reside in a single area of
     contiguous space on the hard disk, the size of the largest unused area
     determines the maximum size of a volume you can create.)

     When you want to return to the Hard Disk Services menu, press <Main
     Screen>.


     A - Allocate a New Volume

     The Allocate function on the Hard Disk Services menu allows you to
     reserve space on the hard disk for a new volume (system or data) that
     is being added.  If you have already installed a particular operating
     system on your hard disk (for example, WPS Word Processing), and if
     you want to create one or more volumes that are to be used for
     document storage, use this function to supply the volume name(s) and
     size(s).

     When you select A and press <Do>, the system responds with the display
     shown in Screen 7-4.

				      7-4


     Hard Disk Services
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			     Allocate a new volume			 }|
     |									  |
     | Note: The largest unused area is 8576k bytes.			  |
     |									  |
     |									  |
     | Name for new volume........................ { }			  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-4

     The note at the top of the screen lists the largest area of unused
     space available on the hard disk.  Since a volume always consists of
     contiguous space on the disk, this number represents the maximum size
     you can allocate, or reserve, for your new volume.

     Enter the name of the volume you are creating.  Volume names must be
     uppercase alphanumeric characters (A-Z, 0-9).  The name cannot be
     greater than eight positions and no special characters or spaces are
     allowed.  If you try to enter lowercase characters, the system sounds
     the terminal buzzer.  If you enter a volume name that already exists,
     the system displays an error message and you have to enter another
     name.

     NOTE: If you are installing WPS V2.0, you do not need to allocate a
     WPS system volume.  WPS Install (the installation software) does this
     for you.  The system allocates a system volume (named WPSYSTEM) and a
     data volume (named WPSVOL1).  In addition, if you have the necessary
     diskettes available during the installation process, WPS Install
     allocates data volumes for WPS Utility and WPS Dictionary (named
     WPSUTIL and WPSDICT respectively).

     After you enter a valid name (for example, TEST), the following prompt
     displays:

     ----------------------------------------------------------------------
     | Usage......................................			  |
     |									  |
     | Enter one of the following operating				  |
     | names: CP/M, COS310, WPS, MS-DOS					  |
     ----------------------------------------------------------------------

     Enter the name of the operating system (usage) that you want to be
     associated with the volume that you are allocating.

     The system then prompts for the volume size:



				      7-5


     Hard Disk Services
     ______________________________________________________________________


     ----------------------------------------------------------------------
     | Size (in K bytes)..........................			  |
     ----------------------------------------------------------------------

     Enter the size of the new volume.  The number must be within the range
     shown in the message at the bottom of the screen.  (The minimum and
     maximum sizes depend upon the operating system that you indicated, and
     the amount of space that is available on your hard disk.)  The number
     must also be a multiple of 8.  If it is not, the system will accept
     what you enter, but it will round the number up to the next number
     that is a multiple of 8.  For example, if you enter 63 as the volume
     size, the system rounds the number up to 64.

     The system then prompts for READ and WRITE passwords.  Issuing
     passwords is an optional feature, and you can skip these fields by
     entering zero or by pressing <Return>.  If you do want to assign a
     password, enter the READ and/or WRITE password(s).  Each password must
     be numeric, between 1 and 65535.

     After you enter all of the identifying information for the new volume,
     the system displays the following message:

     ----------------------------------------------------------------------
     | Press DO to continue or CANCEL to redisplay the Hard		  |
     | Disk Services menu.						  |
     ----------------------------------------------------------------------

     If you want to allocate the volume, press <Do>.  If you want to cancel
     the command and redisplay the Hard Disk Services menu, without
     creating the volume, press <Cancel>.

     When you press <Do>, the system indicates its success in allocating
     space for the new volume by displaying:

     ----------------------------------------------------------------------
     | Volume has been successfully allocated and the directory has been  |
     | initialized.							  |
     ----------------------------------------------------------------------

     Press <Main Screen> to redisplay the Hard Disk Services menu screen.


     E - Erase an Existing Volume

     The Erase function on the Hard Disk Services menu allows you to erase
     a volume from the hard disk.  When you select E and press <Do>, the
     system responds with the display shown in Screen 7-5.







				      7-6


     Hard Disk Services
     ______________________________________________________________________


     ----------------------------------------------------------------------
     |{			   Erase an existing volume			 }|
     |									  |
     |									  |
     |      Name of volume to erase............... { }			  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-5

     Enter the name of the volume that you want to erase (for example,
     TEST).  If the volume has a WRITE password, the following displays:

     ----------------------------------------------------------------------
     | Enter WRITE password for TEST :					  |
     ----------------------------------------------------------------------

     Enter the current WRITE password.  Each letter that you input for the
     password is display protected.  The system protects your response from
     view by displaying an X for each digit you type.  In other words, if
     you enter 123 as the password, XXX displays on your terminal screen.


     ----------------------------------------------------------------------
     |{			   Erase an existing volume			 }|
     |									  |
     |									  |
     |   Name of volume to erase.............. TEST			  |
     |									  |
     |									  |
     |	 --------------------------------------------------------	  |
     |	 | 			 WARNING 			|	  |
     |	 |							|	  |
     |	 |      This erases the volume from the hard disk       |	  |
     |	 |   and discards the entire contents of the volume.    |	  |
     |	 |  Press DO only if you are sure you don't need them.  |	  |
     |	 --------------------------------------------------------	  |
     |									  |
     |									  |
     | Press DO to continue or CANCEL to redisplay the Hard 		  |
     | Disk Services menu.					{ }	  |
     |									  |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 7-6

				      7-7


     Hard Disk Services
     ______________________________________________________________________


     (This prevents other users from seeing the password that you assigned
     to this volume.)  If you enter the wrong password, an error message
     displays.

     After you enter the WRITE password (if appropriate), the system
     displays a warning that the volume and all of its data will be deleted
     from the hard disk (Screen 7-6).

     If you press <Cancel>, the system does not erase the volume and the
     Hard Disk Services menu displays again.  If you press <Do>, the
     system erases the volume and the Hard Disk Services menu displays
     again.


     B - Back Up Volume(s) to Diskettes

     The Backup function on the Hard Disk Services menu allows you to copy
     one or more volumes from the hard disk to diskettes.  (The diskettes
     that are used with this function are used by the Restore function to
     restore the volume(s) back to the hard disk.)

     NOTE:  The diskettes that are used to back up volumes on the hard disk
     can be used interchangeably by the Master Menu, CP/M, and MS-DOS HD
     Services.  In other words, the applications can read the data on these
     diskettes.  WPS, on the other hand, cannot read data from the
     diskettes.

     When you back up a volume, the volume-modified flag is reset.  (Refer
     to the Unset function in this chapter for more information on this
     flag.)

     When you select B and press <Do>, the system responds with the display
     shown in Screen 7-7.


     ----------------------------------------------------------------------
     |{			 Backup volume(s) to diskettes			 }|
     |									  |
     |		     Enter name of volume to backup			  |
     |		     or press RETURN to backup all volumes...... { }	  |
     |									  |
     | Enter 1-8 uppercase letters end/or digits end press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-7

     If you only want to back up one volume, enter the name of that volume
     (for example, TEST).  If you want to back up multiple volumes, press
     <Return>.

				      7-8


     Hard Disk Services
     ______________________________________________________________________


     If you are backing up multiple volumes, the system displays the
     following for the first volume that is on your hard disk:

     ----------------------------------------------------------------------
     | Volume name......  XXXXXXXX					  |
     | Backup this volume (Y/N)?					  |
     ----------------------------------------------------------------------

     The Xs indicate the name of the volume. Enter Y or N, depending upon
     whether or not you want to back up this particular volume.  If you
     enter N, the system displays the same prompt for the next volume that
     is on your hard disk.

     When the volume to be backed up has been identified, the system
     prompts for the information (remarks) pertinent to the volume that you
     are backing up:

     ----------------------------------------------------------------------
     | Remarks...							  |
     ----------------------------------------------------------------------

     Enter a note to yourself about the volume you are backing up (50
     characters maximum).

     You may need more than one diskette, depending upon the size of the
     volume you are backing up.  The system calculates the number of
     diskettes that are required (based upon 392K bytes of information per
     diskette), indicates the number of blank diskettes that you will need,
     and displays the following:

     ----------------------------------------------------------------------
     | X diskettes are required for the backup copy			  |
     |									  |
     | Insert a blank diskette in drive 1 (drive B:) 			  |
     | Press DO when diskette is ready or CANCEL to recall menu instead   |
     ----------------------------------------------------------------------

     X indicates the number of blank diskettes.  For example, if you need
     two diskettes to back up a particular volume, the system displays:

     ----------------------------------------------------------------------
     | 2 diskettes are required for the backup copy			  |
     |									  |
     | Insert a blank diskette in drive 1 (drive B:) 			  |
     | Press DO when diskette is ready or CANCEL to recall menu instead   |
     ----------------------------------------------------------------------

     Have the required number of diskettes ready.  Insert the first blank
     diskette into drive B, close the drive door, and press <Do>.  The
     system then displays the following:




				      7-9


     Hard Disk Services
     ______________________________________________________________________


     ----------------------------------------------------------------------
     | Writing diskette X of Y						  |
     |									  |
     | ..............................................			  |
     ----------------------------------------------------------------------

     X indicates the sequence number of the diskette that is being written
     (for example, 1 of 2);  Y indicates the total number of diskettes
     required for the backup.  The row of dots is proportional to the
     amount of data the Backup function has to copy onto the diskette.

     As the copying process proceeds, the dots change to asterisks, one by
     one.  When the copy process is complete, the system displays:

     ----------------------------------------------------------------------
     | Diskette X completed. Remove and label it.			  |
     ----------------------------------------------------------------------

     Remove the diskette.  If multiple diskettes are required for the
     backup, insert another blank diskette into drive B.  Repeat this
     process until you have backed up the entire volume.

     When the backup is complete, the system displays the following:

     ----------------------------------------------------------------------
     | Diskette X completed. Remove and label it. 			  |
     |Back up completed successfully. Volume-modified flag has been reset.|
     ----------------------------------------------------------------------

     If you are only backing up one volume, press <Main Screen> to
     redisplay the Hard Disk Services menu.  If you are backing up multiple
     volumes, press <Return> to back up the next volume.  (The system will
     prompt you with the next volume that is on your hard disk.  Repeat the
     backup procedure until you have backed up all the required volumes.)

     Although each volume is copied to a diskette, it still remains on your
     hard disk.  In addition, the volume-modified flag is reset.  In other
     words, "modified" does not appear as an attribute in your directory if
     a particular volume has been backed up.

     Label the backup diskettes and store them in their protective
     envelopes in a safe place until you are ready to restore the volume.


     R - Restore a Volume from Diskettes

     The Restore function on the Hard Disk Services menu allows you to take
     any volume that has been backed up from the hard disk (with a hard
     disk utilities program) and restore it back to the hard disk.  For
     example, if you used Master Menu, CP/M, or MS-DOS to back up a volume
     named TEST, you can use the Restore function to restore the contents
     of TEST back to the hard disk.  (You can also use the Restore function
     in CP/M or MS-DOS to restore the volume to the hard disk.)

				     7-10


     Hard Disk Services
     ______________________________________________________________________


     NOTE:  You do not have to restore to the same hard disk that you used
     to back up the volume.  In other words, you can back up a volume on
     your hard disk and restore the volume to someone else's hard disk
     (provided there is enough space available on that hard disk).

     When you select R and press <Do>, the system responds with the display
     shown in Screen 7-8.


     ----------------------------------------------------------------------
     |{			Restore a volume from diskettes			 }|
     |									  |
     |									  |
     |									  |
     | Insert first diskette of backup copy in drive 1 (drive B:)	  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     |									  |
     | Press DO when diskette is ready or CANCEL to redisplay 		  |
     | Hard Disk Services menu.					{ }	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-8

     Have the diskette(s) ready that contain the volume that you want to
     restore.  Insert the first diskette into drive B, and press <Do>.  The
     system then displays information about the backup diskette.  Screen
     7-9 is a sample of the kind of information that could be displayed for
     a particular diskette.

     If you want the restored volume to have a different name, enter Y.
     The system then prompts you for a new volume name:

     ----------------------------------------------------------------------
     | Enter name to use for restored volume....			  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     ----------------------------------------------------------------------

     Enter the new name that is to be assigned to the restored volume.  The
     name must be uppercase alphanumeric characters (A-Z, 0-9).  The name
     cannot be greater than eight positions and no special characters or
     spaces are allowed.  If you try to enter lowercase characters, the
     system sounds the terminal buzzer. If you enter a volume name that


				     7-11


     Hard Disk Services
     ______________________________________________________________________


     already exists, the system displays an error message and you have to
     enter another name.


     ----------------------------------------------------------------------
     |{			Restore a volume from diskettes			 }|
     |									  |
     |									  |
     |									  |
     |									  |
     | Backup diskette contents:					  |
     |									  |
     |	    Volume name: TEST     Size:  568       Type: WPS-8		  |
     |									  |
     |	    Copy made on 02/14/84 at 09:05				  |
     |									  |
     |	    Remarks: Backup of data files with test information. 	  |
     |									  |
     | Do you wish to restore with a different volume name { [Y,N]? }	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-9

     If you want to use the same name for the volume, enter N.  (Remember,
     if you use the same name, the volume cannot be currently residing on
     the hard disk.)

     After you enter the volume name, the system displays the following:

     ----------------------------------------------------------------------
     | Reading diskette 1 of X						  |
     |									  |
     | .........................................................	  |
     ----------------------------------------------------------------------

     X is the number of diskettes containing the contents of the volume
     that you are backing up.  The row of dots is proportional to the
     amount of data on the diskette.  As the data is copied onto the hard
     disk volume, the dots change to asterisks, one by one.

     If there is more than one diskette to restore, the system prompts you
     to insert the remaining diskettes.  When the restoration to the hard
     disk is complete, the system displays the following:

     ----------------------------------------------------------------------
     | Volume restored successfully.				 	  |
     ----------------------------------------------------------------------

     Press <Main Screen> to redisplay the Hard Disk Services menu.

				     7-12


     Hard Disk Services
     ______________________________________________________________________


     Q - Quit This Program

     The Quit function allows you to exit the Hard Disk Services menu.
     When you select Q and press <Do>, the system displays the fixed menu
     screen or the first customized menu screen, depending upon whether or
     not you have created any menu screens.


     N - New Name for an Existing Volume

     The New Name function on the Hard Disk Services menu allows you to
     rename a volume that is currently on the hard disk.

     When you select N and press <Do>, the system responds with the display
     shown in Screen 7-10.

     ----------------------------------------------------------------------
     |{			New name for an exist ng volume			 }|
     |									  |
     |		     Current name of volume................. { }	  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-10

     Enter the name of the volume as it currently exists (for example,
     TEST).  If the volume is not on your hard disk, an error message
     displays.

     If the volume is allocated with an optional WRITE password, the system
     displays the following:

     ----------------------------------------------------------------------
     | Enter WRITE password for TEST :					  |
     ----------------------------------------------------------------------

     Enter the current WRITE password. (The input is display protected.)
     If you enter the wrong password, an error message displays.

     After the WRITE password is entered (if appropriate), the following
     displays:

     ----------------------------------------------------------------------
     | New name for volume....................				  |
     ----------------------------------------------------------------------

     Enter the new name that is to be assigned to the volume (for example,
     TEST1).  The name must be uppercase alphanumeric characters (A-Z,

				     7-13


     Hard Disk Services
     ______________________________________________________________________


     0-9).  The name cannot be greater than eight positions and no special
     characters or spaces are allowed.  If you try to enter lowercase
     characters, the system sounds the terminal buzzer.  If you enter a
     volume name that already exists, the system displays an error message,
     and you have to enter another name.

     After you enter the new volume name, the system displays the
     following:

     ----------------------------------------------------------------------
     | Volume renamed							  |
     ----------------------------------------------------------------------

     The volume has been renamed to the volume that was input.  (The new
     volume keeps the same READ and WRITE passwords.) Press <Main Screen>
     to redisplay the Hard Disk Services menu.


     P - Assign New Passwords for a Volume

     As indicated earlier in this chapter (Allocate function), you have the
     option of protecting the volumes that you create on your hard disk
     with READ and/or WRITE passwords.  This password protection ensures
     that your volumes are not altered, copied, erased, or renamed by any
     other user.

     Master Menu also provides you with the ability to change these
     passwords as often as you want.  You can also assign passwords to
     volumes that were not given password protection when they were
     allocated initially.

     When you select P and press <Do>, the system responds with the display
     shown in Screen 7-11.


     ----------------------------------------------------------------------
     |{		       Assign New Passwords to a Volume			 }|
     |									  |
     |		    Name of volume.......................... { }	  |
     |									  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.     	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-11

     Enter the name of the volume to which you want to assign new passwords
     (for example, TEST).  The volume must be on your hard disk, and it
     cannot be your startup volume, or an error message displays.

				     7-14


     Hard Disk Services
     ______________________________________________________________________


     If the volume has a READ password, the system displays the following:

     ----------------------------------------------------------------------
     | Current passwords:						  |
     |									  |
     |		   Enter READ password for TEST  :			  |
     ----------------------------------------------------------------------

     Enter the current READ password.  (The input is display protected.)
     If you enter the wrong password, an error message displays.

     If the volume has a WRITE password, the following displays:

     ----------------------------------------------------------------------
     | Current passwords:						  |
     |									  |
     |		   Enter WRITE password for TEST  :			  |
     ----------------------------------------------------------------------

     Enter the current WRITE password.  Again, the input is display
     protected.  If you enter the wrong password, an error message
     displays.

     After entering the current passwords (if appropriate), the following
     displays:

     ----------------------------------------------------------------------
     | New passwords							  |
     |									  |
     | READ password:							  |
     |									  |
     | Enter a number between 1 and 65535 or press RETURN (or zero) for   |
     | no password.							  |
     ----------------------------------------------------------------------

     You can now enter a new READ password for the volume or you can enter
     zero, or press <Return>, to bypass the prompt.  (The input is not
     display protected.)

     The system then prompts for the WRITE password.  Again, you can enter
     a new password for the volume, or you can skip the prompt.

     After assigning new READ and/or WRITE passwords, press <Main Screen>
     to redisplay the Hard Disk Services menu.


     S - Select the Startup Volume

     The Select Startup function on the Hard Disk Services menu allows you
     to change the volume on the Hard Disk that has been designated as the
     startup volume.  (The startup volume contains the operating system
     that the system boots when you first start your DECmate system.)


				     7-15


     Hard Disk Services
     ______________________________________________________________________


     When you install Master Menu on your hard disk after installing other
     operating systems (such as CP/M or COS-310), Master Menu automatically
     changes the startup volume to itself, so the system boots Master Menu
     whenever you start your DECmate system.

     When you select S and press <Do>, the system responds with the display
     shown in Screen 7-12.


     ----------------------------------------------------------------------
     |{			   Select the STARTUP volume			 }|
     |									  |
     |									  |
     |									  |
     |		     Name of volume to become STARTUP volume... { }	  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------
 	
	Screen 7-12

     Enter the name of the system volume that you want to designate as the
     startup volume.  The volume that is entered must be on the hard disk,
     and it must also be designated as a "system" volume.  In addition, the
     volume cannot have a READ or WRITE password.  (Refer to the List
     function section in this chapter for more information on startup
     volumes.)

     When you enter a system volume, the following displays:

     ----------------------------------------------------------------------
     | Volume marked as startup volume					  |
     ----------------------------------------------------------------------

     Press <Main Screen> to redisplay the Hard Disk Services menu.


     U - Unset a Volume-Modified Flag

     The Unset function on the Hard Disk Services menu allows you to remove
     a volume-modified flag for a volume on the hard disk.  (The flag
     indicates that the volume has been modified since it was allocated,
     backed up, or reset.)

     When the volume-modified flag is unset for a volume, the "modified"
     attribute is removed from your volume directory for the particular
     volume.  Since the flag is automatically reset each time a volume is
     backed up, you can use this function to remove the flag from the


				     7-16


     Hard Disk Services
     ______________________________________________________________________


     modified volumes that you have determined do not need to be backed up
     (possibly they have bad data in them).

     When you select U and press <Do>, the system responds with the display
     shown in Screen 7-13.


     ----------------------------------------------------------------------
     |{			 Unset a volume-modified flag			 }|
     |									  |
     |		     Name of volume..................... { }		  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-13

     Enter the name of the volume that you want to reset (for example,
     TEST).  The volume must be on your hard disk or an error message
     displays.

     If the volume has a WRITE password, the following displays:

     ----------------------------------------------------------------------
     | Enter WRITE password for TEST   :				  |
     ----------------------------------------------------------------------

     Enter the WRITE password. (The input is display protected.)

     When you enter the current password (if appropriate), the following
     displays:

     ----------------------------------------------------------------------
     | Volume-modified flag reset.					  |
     ----------------------------------------------------------------------

     Press <Main Screen> to redisplay the Hard Disk Services menu.


     C - Copy a Volume to an Existing Volume of Equal Size

     The Copy function on the Hard Disk Services menu allows you to copy
     the contents of one volume on the hard disk to another volume on the
     hard disk.  The volumes must be the same size, and they both must
     exist on the hard disk.

     This function copies all of the contents, attributes (for example, the
     operating system type), and passwords of the FROM volume.


				     7-17


     Hard Disk Services
     ______________________________________________________________________


     When you select C and press <Do>, the system responds with the display
     shown in Screen 7-14.


     ----------------------------------------------------------------------
     |{		   Copy contents from one volume to another		 }|
     |									  |
     |		    Name of FROM volume.................. { }		  |
     |									  |
     | Enter 1-8 uppercase letters and/or digits and press RETURN.	  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-14

     Enter the name of the volume that you want to copy (for example,
     TEST).  The volume must be on the hard disk or an error message
     displays.

     After the FROM volume is entered, the following displays:

     ----------------------------------------------------------------------
     | Name of TO volume....................				  |
     ----------------------------------------------------------------------

     Enter the name of the volume on which you want to copy (for example,
     TESTl).  This volume must also be on the hard disk, and it must be the
     same size as the FROM volume.

     If the FROM volume has a READ password, the system displays:

     ----------------------------------------------------------------------
     | Enter READ password for TEST  :					  |
     ----------------------------------------------------------------------

     If you entered the correct password, and if the TO volume has a WRITE
     password, the system displays:

     ----------------------------------------------------------------------
     | Enter WRITE password for TEST1  :				  |
     ----------------------------------------------------------------------

     After entering the correct passwords (if appropriate), press <Do> to
     continue with the Copy function, or <Cancel> to return to the Hard
     Disk Services menu.  If you want to continue, the system displays the
     following:

     ----------------------------------------------------------------------
     | Tracks left to copy:      X					  |
     ----------------------------------------------------------------------

				     7-18


     Hard Disk Services
     ______________________________________________________________________


     X indicates the number of tracks remaining in the FROM volume that the
     system has yet to copy to the TO volume. As the system copies a track,
     it subtracts one from X.  After copying the last track (track 1), the
     following displays:

     ----------------------------------------------------------------------
     | Copy is complete.						  |
     ----------------------------------------------------------------------

     At this point, the TO volume has ''modified'' as an attribute.  Press
     <Main Screen> to redisplay the Hard Disk Services menu.


     M - Mark a Bad Block

     The Mark a Bad Block function on the Hard Disk Services and the
     DECmate Master Menu Install Diskette screens allows you to isolate a
     bad block.  Bad blocks are areas on the hard disk that are corrupted
     and cannot be used to store information.  The integrity of any
     information stored in a bad block cannot be guaranteed.

     The operating systems that are on your hard disk (for example, WPS,
     MS-DOS, COS-310 or CP/M) have different formats for displaying error
     messages when they encounter a bad block. However, each error message
     indicates the location of the bad block in a format that states the
     location of the cylinder, head, and sector number of the bad block.

     If you encounter a bad block error message, be sure to write down the
     location of the block (cylinder, head, and sector numbers). You use
     this information to remove the block from data storage.

     NOTE: If you have a printer connected to your DECmate system, you can
     press <Print Screen> and print the bad block information that the
     system displays.

     When you select M and press <Do>, the system responds with the display
     shown in Screen 7-15.


     ----------------------------------------------------------------------
     |{			       Mark a bad block				 }|
     |									  |
     |									  |
     |	      Enter cylinder number (decimal) of bad block: { }		  |
     |									  |
     |									  |
     | Enter a number between X and Y.					  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-15

				     7-19


     Hard Disk Services
     ______________________________________________________________________


     Enter the cylinder number that was displayed in the error message.
     (If your system has a 10-megabyte storage capacity, the cylinder was
     in the range of 1-305;  if your system has a 5-megabyte storage
     capacity, the cylinder was in the range of 1-152.)

     NOTE:  The system will not allow you to mark a bad block on cylinder
     0.  If an error message indicates that there is a bad block on
     cylinder 0, call your representative at the DIGITAL Help Line
     (1-800 DEC-8000).

     After you enter the cylinder number, the system displays:

     ----------------------------------------------------------------------
     | Enter head number of bad block:					  |
     ----------------------------------------------------------------------

     Enter the head number displayed in the error message (a number in the
     0-3 range).

     After you enter the head number, the system displays:

     ----------------------------------------------------------------------
     | Enter sector number of bad block (decimal):			  |
     ----------------------------------------------------------------------

     Enter the sector number displayed in the error message (a number in
     the 0-15 range).

     Once you enter the block information, press <Do> to mark the area or
     <Cancel> to return to the Hard Disk Services menu.  If you press <Do>,
     the block corresponding to the cylinder, head, and sector that you
     entered is marked bad and no data will be stored there;  another
     sector is used in its place.  The system attempts to copy the data
     from the bad block to the replacement block.  However, the integrity
     of the data cannot be guaranteed.


     X - Compress the Empty Space on a Drive

     The Compress function on the Hard Disk Services menu allows you to
     restructure the hard disk space by moving information from one track
     to another until all the empty space is in one contiguous area.

     When you erase volumes from the hard disk, the system does not
     consolidate the space that results from the erasure.  It leaves the
     spacing on the hard disk intact.  In other words, the amount of space
     that was allocated to a volume before it was erased, is allocated to
     empty space in your directory after the volume is erased.

     For example, you could have 2000K bytes of empty space on your hard
     disk that is spread across three separate areas of empty space in your
     directory (200K bytes, 300K bytes, and 1500K bytes).  Although you
     have 2000K bytes of empty space in total, you cannot allocate space

				     7-20


     Hard Disk Services
     ______________________________________________________________________


     for a volume that requires more than 1500K bytes of space.  (1500K
     bytes is the largest single area of contiguous space that is
     available on the hard disk.)  However, if you compress the empty
     space, you would have one area of contiguous space (2000K bytes).

     When you select X and press <Do>, the system responds with the display
     shown in Screen 7-16.


     ----------------------------------------------------------------------
     |{			Compress Empty Space on a Drive			 }|
     |									  |
     | Press DO to continue or CANCEL to redisplay the Hard 		  |
     | Disk Services menu.				    { }		  |
     |									  |
     |									  |
     ~									  ~
     |									  |
     ----------------------------------------------------------------------

	Screen 7-16

     Press <Do> to consolidate the empty space on the disk, or press
     <Cancel> to skip the procedure and redisplay the Hard Disk Services
     menu.

     If you press <Do>, the system displays the following message:

     ----------------------------------------------------------------------
     | Copying from track      X  to      Y				  |
     ----------------------------------------------------------------------

     X represents the track that is being copied and Y represents the track
     that is receiving the copy.  During this procedure, the volumes are
     rewritten (from track X to track Y, starting with track 1), and all
     empty space is allocated to tracks at the end of the disk.

     After the system compresses all the empty space, the Hard Disk
     Services menu redisplays.















				     7-21


									  8
     ----------------------------------------------------------------------
							    Using Passwords





     As indicated in Chapter 7, "Hard Disk Services," you have the option
     of protecting the system and data volumes on your hard disk with READ
     and WRITE passwords.  This password protection ensures that your
     volumes are not altered, copied, erased, or renamed by any other user.

     You can assign READ and/or WRITE passwords to a volume when it is
     initially allocated on the hard disk.  (The Allocate function on the
     Hard Disk Services menu prompts for both the READ and WRITE password.)
     You can also assign passwords to volumes that were not assigned
     passwords when they were allocated.  (Use the Assign New Passwords
     function on the Hard Disk Services menu.)

     In addition, you can change the READ and/or WRITE password(s) for a
     volume, or you can remove the password(s) altogether.  (Again, use the
     Assign New Passwords function.)


     Master Password

     Master Menu lets you (or the system manager) assign a password to the
     List Password function.  (This option is available on Master Menu
     Installation Diskette A.)  The Master Password function is designed to
     ensure that no unauthorized person be allowed to use the List Password
     function to display the READ and WRITE passwords that you have
     assigned to the volumes on your hard disk.  Without these passwords,
     no unauthorized person can access your system and data volumes.  In
     other words, unless you tell someone the master password, you are the
     only person who has access to your volumes.

     It is a good idea to write down the master password that you assign
     and put it in a safe place.  This procedure ensures that you will
     always have access to the password.  If you forget or lose the master
     password, you will not be able to use the function that displays the
     READ and WRITE passwords that you have assigned to the volumes on your
     hard disk.  If you forget these pass words, you will not be able to
     run some or all of the applications on your hard disk (depending upon
     which applications have passwords).

     If you forget your master password, you must do the following:

	o  Back up all the system and data volumes on your hard disk.

	o  If you feel it is necessary, write down the tag and legend for
	   each menu item you have created.  (Menu items are erased when
	   the disk is reformatted.)

	   NOTE:  If you have a printer connected to your DECmate system,
	   you can press <Print Screen> and print each menu screen.


				      8-1


     ----------------------------------------------------------------------
     Using Passwords


	o  Reformat your hard disk.  (All the data on your hard disk will
	   be erased and the master password will be set back to zero.)

	o  Use the latest System Test diskette and run the utility called
	   System Test to ensure that your hard disk unit is formatted
	   correctly.

	o  Use your backup copies of the Master Menu Installation
	   Diskettes A and B and reinstall Master Menu.

	o  Restore all your volumes from the backup diskettes.  (These
	   volumes retain the READ and WRITE passwords that were originally
	   assigned.)

	o  Assign another master password to your Master Menu system and
	   write the password down and put it in a safe place.


     READ Password

     A READ password protects a volume from being read or accessed.  If you
     try to retrieve a volume that is protected with a READ password, the
     system prompts you for that password.

     For example, if you have a volume named CPM on your hard disk and you
     assigned it a READ password, every time you select the menu item that
     references this volume, the system displays the following:

     ----------------------------------------------------------------------
     | Enter READ password for CPM:					  |
     ----------------------------------------------------------------------

     You must enter the correct READ password or the system will not make
     this volume available.

     NOTE:  Whenever the system prompts you for the existing READ password,
     your input is display protected.  The system protects your response
     from view by displaying an X for each digit you type.  In other words,
     if you enter 123 as the password, XXX displays on your terminal
     screen.  (This prevents other users from seeing the password that you
     assigned to this volume.)


     WRITE Password

     A WRITE password protects a volume from being altered when it is
     accessed. If you want to write (or store) new information or alter
     existing information on a volume that is protected with a WRITE
     password, the system prompts you for that password.

     For example, if you have a data volume on your system (WP1) and you
     assigned it a WRITE password, the system displays the following each
     time you select the WP1 tag:

				      8-2


     ----------------------------------------------------------------------
     Using Passwords


     ----------------------------------------------------------------------
     | Enter WRITE password for WP1:					  |
     ----------------------------------------------------------------------

     You must enter the correct WRITE password or the system will not make
     the WP1 data volume available.  (Like the READ password, the input for
     the WRITE password is display protected.)


     Password Ranges

     A READ or WRITE password can be any number between 1 and 65535.  When
     you initially allocate a volume to your hard disk or when you are
     changing or removing existing passwords, you can bypass the READ and
     WRITE password prompts by pressing <Return>.


     Passwords and the Hard Disk Services

     The following Hard Disk Services functions prompt for current READ
     and/or WRITE passwords.


     Erase an Existing Volume

     The Erase function prompts for a WRITE password if a password has been
     assigned to the volume that you are attempting to erase.  If you do
     not enter the correct WRITE password, the volume is not removed from
     your hard disk.


     Assign New Name to a Volume

     The New Name function prompts for a WRITE password if a password has
     been assigned to the volume that you are attempting to rename.  If you
     do not enter the correct WRITE password, the name of the volume is not
     changed.


     Assign New Passwords

     The New Password function prompts for READ and/or WRITE password(s) if
     you are attempting to change passwords for a volume that already has
     passwords.  If you do not enter the correct READ and/or WRITE
     password(s), the passwords are not changed.


     Unset a Volume-Modified Flag

     The Unset function prompts for a WRITE password if a password has been
     assigned to the volume that you are attempting to reset.  If you do
     not enter the correct WRITE password, the modified flag is not reset.


				      8-3


     ----------------------------------------------------------------------
     Using Passwords


     Copy a Volume to an Existing Volume

     The Copy function prompts for a READ password if a password has been
     assigned to the volume that you are attempting to copy.  You are also
     prompted for a WRITE password if a password has been assigned to the
     volume on which you are attempting to copy (or write).  If you do not
     enter the correct READ and/or WRITE password(s), the volume is not
     copied.


     Password Exceptions

     You cannot assign passwords to a volume that has been designated as
     the startup volume.  Conversely, a password-protected volume cannot be
     designated as a startup volume.  (The startup volume is the volume
     that the system boots whenever you start your DECmate system without a
     system diskette in drive A.)


     List of Volume Passwords

     Master Menu Installation Diskette A has an option that allows you to
     list all the volumes on your hard disk, along with their associated
     READ and/or WRITE passwords.  (The master password is not listed.)
     This feature can be very useful if you forget the password(s) for one
     or more of the volumes on your hard disk.  However, to eliminate the
     risk of these passwords becoming available to an unauthorized user,
     you should take sufficient precautions to ensure that this diskette is
     stored in a safe place.

     NOTE:  If you assign a master password, the list of READ and WRITE
     passwords does not display unless the correct master password is
     entered. This precepts unauthorized users from displaying the
     passwords.


     Applications and Passwords

     You can allocate application volumes on your hard disk with READ
     and/or WRITE passwords.  If you do assign passwords, the system
     prompts you for them when you select the particular application from a
     customized menu.  If you do not enter valid passwords, the system
     denies access to the application.











				      8-4


									  9
     ----------------------------------------------------------------------
			     Master Menu and CP/M, COS-310, WPS, and MS-DOS





     This chapter discusses how Master Menu interacts with the CP/M,
     COS-310, WPS, and MS-DOS operating systems.  It defines procedures and
     conventions specific to the operating systems.


     Returning to Master Menu

     Each operating system, whether it runs on the hard disk or from a
     diskette, can return to the Master Menu program.  However, each
     operating system has a different method of returning to Master Menu.
     Table 9-1 lists, by operating system, the procedures that you must
     follow whenever you want to return to Master Menu.


     Table 9-1  Returning to Master Menu

     ----------------------------------------------------------------------
     Operating		Executed from	   Executed from
     System		Hard Disk	   Drive 0 (A)
     ----------------------------------------------------------------------
     CP/M		Enter MENU	    Press <Set-Up>, <Remove>,
					    open the drive door, press <Do>

     COS-310 V9.3	Press <Set-Up>,	    Press <Set-Up>, <Remove>,
			<Remove>, <Do>	    open the drive door, press <Do>

     WPS V1.5/V1.6*	N/A		    Press <Return> at Finish Menu


     WPS V2.0*		Press <Return> at   Press <Return> at Finish Menu
			Finish Menu

     MS-DOS		Enter MENU	    Press <Set-Up>, <Remove>,
					    open the drive door, press <Do>

     * When you return to Master Menu, all assigned data volumes are
       deassigned.
     ----------------------------------------------------------------------












				      9-1


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Device Names for Operating Systems

     Each operating system has a different convention for naming the
     storage devices on the DECmate system.  Table 9-2 lists the device
     names that are used with each operating system.


     Table 9-2  Device Names by Operating System

     ----------------------------------------------------------------------
     Device			   Operating System
     ----------------------------------------------------------------------
			CP/M       COS-310    WPSV1.5     WPSV2.0    MS-DOS
					      WPSV1.6    (Hard Disk)
					      WPSV2. 0
					     (Diskette)
     ----------------------------------------------------------------------
     RX50 Upper		A	   DZ0	      0*	  8**	     A
	  Lower		B	   DZ1	      1* 	  9** 	     B

     Hard Disk		E	   RD0	      2		  0*** 	     E
			F	   RD1	      3		  1	     F
			G	   RD2	      4		  2	     G
			H	   RD3	      5		  3 	     H
			-	   -	      6		  4	     -
			-	   -	      7		  5	     -
			_ 	   _	      -		  6 	     -
			_	   _	      -		  7 	     -


       *  For WPS versions 1.5/1.6, and version 2.0 (if booted from a
	  diskette), devices 0 	and 1 are always assigned to a diskette
	  drive.  Device O always contains the 	system software.

      **  For WPS version 2.0, devices 8 and 9 are always assigned to a
	  diskette drive (if WPS is booted from the hard disk).

     ***  For WPS version 2.0, device 0 always contains the system software.
     ----------------------------------------------------------------------















				      9-2


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Hard Disk Device Assignments

     Each operating system has a different convention for assigning data
     volumes to hard disk devices. Table 9-3 lists the hard disk device
     assignments for each operating system.


     Table 9-3  Hard Disk Device Assignments to Volumes

     ----------------------------------------------------------------------
					  Operating System
     ----------------------------------------------------------------------
			CP/M       COS-310    WPSV1.5     WPSV2.0    MS-DOS
					      WPSV1.6    (Hard Disk)
					      WPSV2. 0
					     (Diskette)
     ----------------------------------------------------------------------
	Volumes:       Device	   Device      Device	  Device     Device
	    System	 E	    RD0		N/A	    O	       E
	    Data	 F	    RD1		1*	    1	       F
	    Data	 G	    RD2		2	    2	       G
	    Data	 H	    RD3		3	    3	       H
	    Data	 	     -		4	    4	       -
	    Data	 	     -		5	    5	       -
	    Data	 	     -		6	    6	       -
	    Data	 	     -		7	    7	       -

     *  It is not advisable to assign a volume to device 1, since you will
	not be able to access drive 1(B) with a diskette.
     ----------------------------------------------------------------------


     Using Master Menu with the CP/M Operating System

     In addition to the conventions identified in Tables 9-1, 9-2, and 9-3,
     the following relationships exist between Master Menu and CP/M.


     Command String Conventions

     The command string line in the Menu Maintenance function can contain
     one valid CP/M command.  For example, to call the CP/M to WPS
     conversion utility, you can enter WPSCONV in the command string.  To
     execute a series of CP/M commands, you can enter a SUBMIT command in
     the following format:

     SUBNIT MYCOMB

     MYCOMB, in this example, is a CP/M file of commands that you created.
     Therefore, whenever MYCOMB is used in the command string, the CP/M
     commands will be executed in the sequence that you defined in the
     file.  If you want to return to Master Menu after the commands are
     executed, the last command in the series must be MENU.

				      9-3


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     NOTE:  Do not use a carriage return with the CP/M command in the
     command string field.


     Date and Time Acceptance

     The system date and time are not displayed when you are using CP/M,
     but they are available for use in CP/M application programs.


     Booting from the Hard Disk

     The CP/M operating system can be booted from your hard disk.  Refer to
     the DECmate CP/M-80 User's Guide for instructions on installing CP/M
     on your hard disk.


     Booting from a Diskette

     You can boot CP/M from a diskette if your command string starts with
     the following:

     CPM-DISKETTE:

     If you want to call a specific utility within CP/M, follow the
     diskette boot command with the appropriate CP/M command.  (You can
     only enter one CP/M command in the command string, and no carriage
     return is allowed.)

     If you do boot the CP/M operating system from a diskette, you must
     insert the CP/M system diskette into drive A.


     Using Master Menu with the COS-310 Operating System

     In addition to the conventions identified in Tables 9-1, 9-2, and 9-3,
     the following relationships exist between Master Menu and COS-310.


     Command String Conventions

     The COS-310 operating system V9.3 does not accept command strings.


     Date and Time Acceptance

     The COS-310 operating system V9.3 does not accept the date or time
     from Master Menu.  You must enter the date and time when you access
     the COS-310 operating system.





				      9-4


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Using Master Menu with the WPS Operating System

     In addition to the conventions identified in Tables 9-1, 9-2, and 9-3,
     the following relationships exist between Master Menu and the WPS
     operating system (WPS V1.5/V1.6 and V2.0).


     Document Formatting

     Before you can put WPS documents on the hard disk, you must first
     allocate and initialize the space on the hard disk for the volume.
     (The Hard Disk Services Allocate function does this for you.)  After
     the system allocates the volume and initializes the space, you can
     assign the volume and create and store your WPS documents on it.

     NOTE:  If you are installing WPS V2.0, you do not need to allocate a
     WPS system volume.  WPS Install (the installation software) does this
     for you.  The system allocates a system volume (named WPSYSTEM) and a
     data volume (named WPSVOL1).  In addition, if you have the necessary
     diskettes available during the installation process, WPS Install
     allocates data volumes for WPS Utility and WPS Dictionary (named
     WPSUTIL and WPSDICT respectively).

     Screen 9-1 is an example of a data volume that has been allocated for
     WPS.


     ----------------------------------------------------------------------
     |{			     Allocate a new volume			 }|
     |									  |
     | Note: The largest unused area is XXXXk bytes.			  |
     |									  |
     |		Name for new volume....................   YRLYRPT	  |
     |									  |
     |		Usage..................................   WPS		  |
     |									  |
     |		Size (in K bytes)......................   400		  |
     |									  |
     |		READ Password: 123     WRITE Password: 456		  |
     |									  |
     |									  |
     | Volume has been successfully allocated and the directory has been  |
     | initialized.  							  |
     |									  |
     | Press MAIN SCREEN to redisplay the Hard Disk Services menu. { }	  |
     |									  |
     |									  |
     |									  |
     ----------------------------------------------------------------------

	Screen 9-1



     				      9-5


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Refer to Chapter 7, "Hard Disk Services," for information on
     allocating volumes to the hard disk.


     Command String Conventions

     The command string line in the Menu Maintenance function can contain
     one or more valid WPS commands (for example, the backup command). Each
     command must end with a <Return>.  In other words, if you want to set
     up a series of WPS commands to perform one or more WPS functions,
     enter the same commands, in the same sequence, that you would use if
     you were in WPS.

     Screen 9-2 is an example of a WPS menu item that has been modified to
     include 1) the assignment of another WPS data volume, and 2) commands
     in the Command String field.


     ----------------------------------------------------------------------
     |{			     Edit a menu line item			 }|
     |									  |
     | Tag: {W}PS							  |
     |									  |
     | Legend: Word Processing Version 2.0				  |
     |									  |
     |-------------------------------------------------------		  |
     |									  |
     | Volumes: System: WPSYSTEM					  |
     |		Data: 	WPSVOL1						  |
     |		Data:	YRLYRPT						  |
     |		Data:	_______						  |
     |		Data:	_______						  |
     |		Data: 	_______						  |
     |		Data:	WPSUTIL						  |
     |		Data:	WPSDICT						  |
     |									  |
     | Command String:							  |
     |									  |
     | E 2.Yearly Report<Return>____________________________		  |
     |									  |
     | Move the highlight with the up and down arrow keys. Blank a field  |
     | by pressing REMOVE. Press Do to store data, or press CANCEL to 	  |
     | redisplay the previous menu.					  |
     ----------------------------------------------------------------------

	Screen 9-2


     Date and Time Acceptance

     Master Menu passes the system date to WPS V1.5/V1.6 and V2.0;  Master
     Menu also passes the system time to WPS V2.0.  (Since the date and
     time is passed, WPS V2.0 bypasses the Date/Time menu.)

				      9-6


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Booting from the Hard Disk

     WPS V2.0 can be booted from the hard disk;  WPS V1.5/V1.6 cannot be
     booted from the hard disk.  (WPS V1.5/V1.6 can only be booted from a
     diskette.)


     Booting from a Diskette

     You can boot WPS V1.5/V1.6 and V2.0 from a diskette if your command
     string starts with the following:

     WPS-DISKETTE:

     If you want to execute one or more WPS commands, follow the diskette
     boot command with the appropriate WPS command(s).  Remember to
     separate each command with a carriage return.


     Using Master Menu with the MS-DOS Operating System

     In addition to the conventions identified in Tables 9-1, 9-2, and 9-3,
     the following relationships exist between Master Menu and MS-DOS.


     Command String Conventions

     The command string line in the Menu Maintenance function can contain
     one valid MS- DOS command.  For example, to call the MS-DOS to WPS
     conversion utility, you can enter CONVERT in the command string.  To
     execute a series of MS-DOS commands, enter the batch file name that
     contains the commands that you want to execute.  The following is an
     example of a command to execute a batch file:

     MYCOMB

     MYCOMB, in this example, is a MS-DOS batch file of commands that you
     created. Therefore, whenever MYCOMB is used in the command string, the
     MS-DOS commands will be executed in the sequence that you defined in
     the file.  If you want to return to Master Menu after the commands are
     executed, the last command in the series must be MENU.

     NOTE:  Do not use a carriage return with the MS-DOS command in the
     command string field.


     Date and Time Acceptance

     The system date and time is passed by Master Menu to MS-DOS and both
     display when you are using the operating system.




				      9-7


     ----------------------------------------------------------------------
     Master Menu and CP/M, COS-310, WPS, and MS-DOS


     Booting from the Hard Disk

     The MS-DOS operating system can be booted from your hard disk.  Refer
     to the DECmate MS-DOS User's Guide for instructions on installing
     MS-DOS on your hard disk.


     Booting from a Diskette

     You can boot MS-DOS from a diskette if your command string starts with
     the following:

     DOS-DISKETTE:

     If you want to call a specific utility within MS-DOS, follow the
     diskette boot command with the appropriate MS-DOS command.  (You can
     only enter one MS-DOS command in the command string, and no carriage
     return is allowed.)

     If you do boot the MS-DOS operating system from a diskette, you must
     insert the MS-DOS system diskette into drive A.

































				      9-8


									 10
     ----------------------------------------------------------------------
					      What to Do in Case of Trouble





     For a computer user, trouble is any behavior on the part of the
     computer that does not conform to the user's expectations.  Trouble
     can be caused by any of the following:

	o  An electronic component fails

	o  An essential connection breaks

	o  A program contains undetected bugs

	o  A volume copy is corrupted

	o  The user asks the computer to do inappropriate or impossible
	   operations

     When trouble occurs, double check to make sure you did not cause it.
     If an operation seems to fail, reread the documentation covering that
     operation to make sure that you did not skip a step.  Then try the
     operation again, carefully checking each step to make sure that you
     use all required commands, arguments, and references.

     When you are sure that your command or commands are not at fault,
     think about the trouble symptoms, and see if you can reason out an
     explanation.  If, for example, you suddenly begin having trouble with
     one of the Master Menu Installation diskettes and the particular
     diskette seemed to work properly on a previous occasion, make another
     copy of the original (from your master diskette) and try again.
     Flexible diskettes are physically and magnetically fragile.  A crease
     in the diskette sheath or a dent or a fingerprint on the diskette
     surface is all it takes to ruin the diskette.


     How to Get Help

     If you have a problem that you cannot solve, you or your system
     manager should call the DIGITAL Help Line at 1-800-DEC-8000.  A
     DIGITAL representative will connect you to a specialist who will
     answer your questions.  The specialist will determine whether or not
     the problem is software related.  If it is determined that you have a
     hardware failure, the specialist will contact your local Field Service
     office and apprise them of the problem.

     When you initially call the DIGITAL Help Line, if you are under
     warranty, you will be given an Access Number that identifies your
     DECmate system.

     Before you call the Help Line:



				     10-1


     What to Do in Case of Trouble
     ----------------------------------------------------------------------


	o  Have your DECmate system near so that you can help the
	   specialist find the problem quickly.

	o  Have your Access Number (or system box serial number) handy.
	   The serial number is located on the back of the system box.

	o  Be ready to identify your operating system by number to the
	   representative.  (For example, CP/M-80, V2.1.)

	o  Have your documentation manuals handy.

	o  Be ready to describe the problem to the specialist.

     If Master Menu behaves in ways contrary to the definitions and
     examples in this guide, call the DIGITAL Help Line.


     Some Common Symptoms and Their Cures


     Freezing

     If Master Menu or an application suddenly seems to go dead, or if the
     characters you type suddenly stop appearing on the screen, you may
     have accidentally pressed the Hold Screen key.  If the Hold Screen
     light at the top right side of the keyboard is on, press <Hold Screen>
     again to unfreeze the screen.


     The Display Screen Goes Blank

     If you are running Master Menu or an operating system volume on your
     DECmate system, and you do not type anything at the keyboard for about
     30 minutes, your display screen will go blank.  This is not a problem.
     It is an energy-saving feature of your DECmate system which prolongs
     the life of your display screen.  Press <Ctrl> once to restore the
     display.

















				     10-2


									  A
     ----------------------------------------------------------------------
								 Appendix A





     Master Menu Error Messages

     The error messages listed in this appendix can occur when you are
     using Master Menu.  The errors are grouped by function.  Following
     each error message is a description of the error (if appropriate) and
     the steps that you must take to recover from the error.

     NOTE:  If you have a printer connected to your DECmate system, you can
     press <Print Screen> to print the error messages.


     Installation Error Messages

     The following error messages can occur when you are using the
     installation options listed on the Master Menu Installation Diskette
     A.


     RX ERROR:  012G
     Backup Incomplete.  Press CANCEL to quit or RETURN to retry.

     You are attempting to copy your installation diskettes and, either
     there is no diskette in drives A or B, or one of the drive doors is
     open.  Make sure that the diskette that you are copying is in drive A
     and that a blank diskette is in drive B.  Close the doors to both
     drives, press <Return> and try again.


     RX ERROR:  XXXX
     Backup incomplete Press CANCEL to quit or RETURN to retry.

     You are attempting to copy your installation diskettes and the blank
     diskette that is in drive B is bad (corrupted).  Put another diskette
     in drive B, press <Return> and try again.  (The Xs indicate a bad
     physical address on the diskette.)  If the message displays again, you
     may have a bad, or corrupted, installation diskette.  If you have WPS,
     you can use the WPS Verify Diskette feature of the Maintenance option
     to check for bad blocks on the diskette structure.  If the diskette is
     bad, use your original Master Menu Installation Diskette to make
     another backup diskette and try again.  If your new backup diskette is
     also bad, call your representative at the DIGITAL Help Line (1 -
     800-DEC-8000).

     ----------------------------------------------------------------------
     | Insert proper diskette in drive 1 (B). Press DO when ready.	  |
     ----------------------------------------------------------------------




				      A-1


     Appendix A
     ----------------------------------------------------------------------


     There is a diskette in drive B;  however, it is not the Master Menu
     Installation Diskette B.  Locate the right diskette, put it into drive
     B, close the door and press <Do>.

     ----------------------------------------------------------------------
     | Not enough contiguous space on device (392K required). 		  |
     | Press CANCEL to redisplay Install menu.				  |
     ----------------------------------------------------------------------

     You cannot install Master Menu because there is not enough contiguous
     space available on your hard disk.  (You need at least 392K.)  If this
     message occurs, use the Erase function to erase one or more volumes
     (back up the volumes first unless you no longer need them), and use
     the Compress function to consolidate the unused areas into one
     contiguous space.

     ----------------------------------------------------------------------
     | Internal Data must be updated to XXX or greater to install this 	  |
     | version of Master Menu. Use the latest System Test Diskette.	  |
     ----------------------------------------------------------------------

     You cannot install Master Menu until internal data on the hard disk is
     updated.  Press <Set-Up>, and <Remove>, insert the latest System Test
     diskette into drive A, close the door, and press <Do>.  When the
     System Test Menu displays, select the Update Internal Data on Hard
     Disk Drive option, and press <Do> to execute the update.  When the
     System Test Menu displays again, select the Return to Setup to Change
     Diskette option, press <Remove>, insert the Master Menu Installation
     Diskette A into drive A, close the door, and press <Do> to continue
     with the installation.


     Allocate Error Messages

     The following error messages can occur when you are allocating a new
     volume on your hard disk:

     ----------------------------------------------------------------------
     | Your Directory 15 full!						  |
     ----------------------------------------------------------------------

     You cannot have more than 60 volumes on your hard disk, including
     unused areas (empty space).  If this message occurs, use the Erase
     function to erase some volumes (back up the volumes first unless you
     no longer need them), and then use the Compress function to
     consolidate the unused areas into one contiguous space.

     ----------------------------------------------------------------------
     | There is already a volume with this name!			  |
     ----------------------------------------------------------------------

     You cannot allocate a volume to your hard disk if a volume with the
     same name already exists on the disk.  Either change the volume name

				      A-2


     Appendix A
     ----------------------------------------------------------------------


     for the existing volume (New Name function), or erase the existing
     volume (Erase function), or allocate the volume with a different name.

     ----------------------------------------------------------------------
     | Volume size entered is out of range. Try again.			  |
     ----------------------------------------------------------------------

     You cannot allocate a volume with a size that is outside the range
     shown on the bottom of your terminal screen.  Start again and enter a
     volume size that is within the range displayed.  (The minimum and
     maximum sizes are contingent upon the operating system that you are
     allocating, as well as on the amount of contiguous space available on
     your hard disk.)

     ----------------------------------------------------------------------
     | There is no space large enough on your volume!			  |
     ----------------------------------------------------------------------

     There is not enough contiguous space to support the operating system
     that you are allocating.  If this message occurs, use the Erase
     function to erase some volumes (back up the volumes first unless you
     no longer need them), and then use the Compress function to
     consolidate the unused areas into one contiguous space.


     Erase Error Messages

     The following error messages can occur when you are erasing a volume
     from your hard disk:

     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the names of the volumes that are on
     your hard disk.

     ----------------------------------------------------------------------
     | Password error. Press CANCEL to redisplay Hard Disk Services 	  |
     | menu.								  |
     ----------------------------------------------------------------------

     You did not enter the correct WRITE password, therefore the volume
     will not be erased.  Use the List Password function (on the Master
     Menu Installation Diskette A) to list all the passwords for your
     volumes, and try again.


     Backup Error Messages

     The following error messages can occur when you are backing up one or
     more volumes on your hard disk:


				      A-3


     Appendix A
     ----------------------------------------------------------------------


     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the names of the volumes that are on
     your hard disk.

     ----------------------------------------------------------------------
     | Diskette write error. Backup is incomplete.			  |
     ----------------------------------------------------------------------

     Either there is no diskette in drive B, or the drive door is open.
     Make sure a blank diskette is in the drive, close the door and start
     again.  If the message occurs again, your blank diskette may be bad.
     If you have WPS, you can use the WPS verify diskette feature of the
     maintenance option to check for bad blocks on the diskette structure.
     If the diskette is bad, use another diskette and try again.  If you
     continue to have problems, call your representative at the DIGITAL
     Help Line (1-800-DEC-8000).


     Restore Error Messages

     The following error messages can occur when you are restoring a volume
     (from a backup diskette) to your hard disk:

     ----------------------------------------------------------------------
     | Not enough empty space on the hard disk				  |
     ----------------------------------------------------------------------

     You cannot restore the volume until there is sufficient space on your
     hard disk.  Use the erase function to erase some volumes (back up the
     volumes first unless you no longer need them), and then use the
     Compress function to consolidate the unused areas into one contiguous
     space.

     ----------------------------------------------------------------------
     | You must choose a volume that is not presently on the disk.	  |
     ----------------------------------------------------------------------

     You already have a volume on your hard disk with the same name that
     you are assigning to the volume that you are restoring.  Either use
     the New Name function to change the name of the existing volume, or
     assign a different name to the volume that you are restoring.

     ----------------------------------------------------------------------
     | Diskette is not a valid BACKUP diskette.				  |
     ----------------------------------------------------------------------

     You cannot restore a volume that was not originally backed up with a
     hard disk utilities program.



				      A-4


     Appendix A
     ----------------------------------------------------------------------


     ----------------------------------------------------------------------
     | Diskette is not sequence #nnn.					  |
     ----------------------------------------------------------------------

     You must restore the diskettes in sequence.  In other words, if three
     diskettes were used to back up a particular volume, you must restore
     (copy back to the l hard disk) the diskettes in the same sequence.
     (#nnn is the sequence number | that the system is expecting.)

     ----------------------------------------------------------------------
     | Diskette is not from the correct BACKUP set.			  |
     ----------------------------------------------------------------------

     You cannot restore a volume from a diskette that does not belong to
     the particular set of diskettes.  In other words, Master Menu does not
     allow you to mix up volumes.  This message displays if you
     inadvertently try to restore a diskette that, although it has the
     right sequence number, is not one of the diskettes that was used to
     back up the volume.

     ----------------------------------------------------------------------
     | Diskette read error. Press DO to retry or CANCEL to re-display 	  |
     | the Hard Disk Services menu.					  |
     ----------------------------------------------------------------------

     Either there is no diskette in drive B, or the drive door is open.
     Make sure that your backup diskette is in the drive, close the door
     and start again. If the message occurs again, your backup diskette may
     be bad.  Try again if you have another backup diskette for the same
     volume.


     New Name Error Messages

     The following error messages can occur when you are changing the name
     of one of the volumes on your hard disk:

     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the volumes that are on your hard disk.

     ----------------------------------------------------------------------
     | Password error. Press CANCEL to redisplay Hard Disk Services 	  |
     | menu.								  |
     ----------------------------------------------------------------------

     You did not enter the correct WRITE password, therefore you cannot
     change the name of the volume.  Use the List Password function (on the
     Master Menu Installation Diskette A) to list all the passwords for
     your volumes and try again.


				      A-5


     Appendix A
     ----------------------------------------------------------------------


     Assign New Password Error Messages

     The following error messages can occur when you are assigning new
     passwords to the volumes on your hard disk:

     ----------------------------------------------------------------------
     | there is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the volumes that are on your hard
     disk.

     ----------------------------------------------------------------------
     | Password error. Press CANCEL to redisplay Hard Disk Services 	  |
     | menu.								  |
     ----------------------------------------------------------------------

     You did not enter the correct READ or WRITE password.  therefore you
     cannot change the READ and/or WRITE passwords for this volume.  Use
     the List Password function (on the Master Menu Installation Diskette
     A) to list all the passwords for your volumes and try again.

     ----------------------------------------------------------------------
     | STARTUP volume may not have passwords.				  |
     ----------------------------------------------------------------------

     You cannot assign READ and/or WRITE password(s) to the startup volume


     Select the Startup Volume Error Messages

     The following messages can occur when you are selecting the startup
     volume:

     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the volumes that are on your hard
     disk.

     ----------------------------------------------------------------------
     | Startup volume not reset - this was not a SYSTEM volume.		  |
     ----------------------------------------------------------------------

     You cannot designate a data volume as the startup volume.  Use the
     List function to display the volumes that are on your hard disk.  If a
     volume is a system volume, "system" displays as an attribute for that
     volume.  If "system" is not displayed, the volume is a data volume.

     ----------------------------------------------------------------------
     | Startup volume not reset. Volume has passwords.			  |
     ----------------------------------------------------------------------

				      A-6


     Appendix A
     ----------------------------------------------------------------------


     You cannot designate a system volume as a startup volume if the volume
     has a READ and/or WRITE password assigned to it.  Use the Assign New
     Password function to change the passwords to O (zero).


     Unset a Volume-Modified Flag Error Message

     The following error message can occur when you are resetting the
     volume-modified flag for volumes on your hard disk:

     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the volumes that are on your hard
     disk.


     Copy Volume Error Messages

     The following messages can occur when you are copying the contents of
     one volume into another volume:

     ----------------------------------------------------------------------
     | There is no volume with this name!				  |
     ----------------------------------------------------------------------

     Use the List function to display the volumes that are on your hard
     disk.

     ----------------------------------------------------------------------
     | Password error. Press CANCEL to redisplay Hard Disk Services	  |
     | menu.								  |
     ----------------------------------------------------------------------

     Either you did not enter the correct READ password for the volume that
     you want to copy, or you did not enter the correct WRITE password for
     the volume on which you want to copy, therefore the volume will not be
     copied.  Use the List Password function (on Master Menu Installation
     Diskette A) to list all the passwords for your volumes and try again.

     ----------------------------------------------------------------------
     | Not allowed to copy volumes of unequal sizes			  |
     ----------------------------------------------------------------------

     The volume that you are copying from must be the same size as the
     volume that you are copying to.  Use the List function to display the
     size of each volume that is on your hard disk.






				      A-7


     Appendix A
     ----------------------------------------------------------------------


     Mark a Bad Block Error Message


     The following message can occur when you are marking a bad block on
     your hard disk:

     ----------------------------------------------------------------------
     | No more space in the bad block list.				  |
     ----------------------------------------------------------------------

     When you record a bad block (cylinder, head, and sector number), the
     location of the block is written to a file.  Master Menu, in turn,
     does not write any data in the areas that are identified in the file.
     The file can only hold 16 locations.  If you find more than 16 bad
     blocks, the above message displays.  At this point, you must do the
     following:

	o  Back up all the system and data volumes on your hard disk.

	o  If you feel it is necessary, write down the tag and legend for
	   each menu item you have created.  (Menu items are erased when
	   the disk is reformatted.)

	   NOTE:  If you have a printer connected to your DECmate system,
	   you can press <Print Screen> and print each menu screen.

	o  Reformat your hard disk.

	o  Use the latest System Test diskette and run the utility called
	   System Test to ensure that your hard disk is formatted
	   correctly.

	o  Use your backup copies of the Master Menu Installation Diskettes
	   A and B and reinstall Master Menu.

	o  Restore all your volumes from the backup diskettes.

	o  Assign a master password to your Master Menu system.


     If you encounter the 16 bad blocks again, call your representative at
     the DIGITAL Help Line (1-800-DEC-8000).


     Master Menu Screen Error Messages

     The following messages can occur when you are using the customized
     menu screens:

     ----------------------------------------------------------------------
     | Error:  Tag not found. Try again.				  |
     ----------------------------------------------------------------------


				      A-8


     Appendix A
     ----------------------------------------------------------------------


     Type a valid tag and press <Do>, or move the highlight to the
     appropriate tag and press <Do>.

     ----------------------------------------------------------------------
     | Error while attempting to mount this volume:			  |
     ----------------------------------------------------------------------

     You are attempting to boot a system or data volume that does not exist
     on your hard disk.  Either use the Menu Maintenance function to
     correct the spelling of the volume, or use the Allocate function to
     allocate the volume, or use a system diskette to install the
     particular operating system on your hard disk.

     ----------------------------------------------------------------------
     | Read access denied						  |
     ----------------------------------------------------------------------

     or

     ----------------------------------------------------------------------
     | Write access denied						  |
     ----------------------------------------------------------------------

     You did not enter the correct READ or WRITE password for the volume
     that is associated with the tag that you entered.  Use the List
     Password function (on the Master Menu Installation Diskette A) to list
     all the passwords for your volumes and try again.

     ----------------------------------------------------------------------
     | ERROR!  You may not add any more menu items			  |
     |	       because you now have 64!					  |
     ----------------------------------------------------------------------

     The total number of menu items cannot exceed 64 lines (including blank
     lines).  Before you can add another menu item, you must delete one or
     more existing menu items.  (Refer to Chapter 4, "Menu Maintenance,"
     for information on deleting menu items.)

















				      A-9


									  B
     ----------------------------------------------------------------------
				    Command Passing and System Date Storage





     The following describes the protocol that the system uses to pass
     command text and the system date from Master Menu to an operating
     system.

     CP/M and MS-DOS


     The system places the command text at location 77600 in main memory in
     following formats:

	o  CPM_cmd<nul><len><text><nul>

	o  DOS_cmd<nul><len><text><nul>


     WPS and COS-310


     The system places the command text at location 167600 in panel memory
     in the following formats:

	o  WPS_cmd<nul><len><text><nul>

	o  COS_cmd<nul><len><text><nul>


     NOTE:  Each operating system should remove the command text to ensure
     it does not run the command when recalled.


     Date

     The system places the system date at the command text location plus
     132 octal. The format is as follows:

	o  mm/dd/yy<null>














				      B-1


     ----------------------------------------------------------------------
								      Index





     A					  Customized menu screens, 1-2,
     Allocate a new volume, 7-6 to	    3-10, 3-11, 4-7, 4-8, 4-10,
       7-8				    5-2, 8-4
     Angle brackets, viii		  Cylinder number, 7-19 to 7-20,
     Assign new passwords for a		    A-8
       volume, 7-14 to 7-15, 8-3
     Attributes, 7-4, 7-10, 7-16,
       7-17, 7-19			  D
					  DAT
					    set system date and time,
     B					      3-11, 5-1 to 5-3
     Back up volume(s) to diskettes,	  Data volume, 4-5 to 4-5, 7-3,
       7-8 to 7-10			    9-5 to 9-6
     Blank display screen, 10-2		  Date function, 2-1, 3-9 to
     Boot from diskette, 4-4 to 4-6	    3-11, 5-1 to 5-3
       using CP/M, 9-4			  Device names, 9-2
       using MS-DOS, 9-8		  Drive doors, 3-1
       using WPS, 9-7
     Boot from hard disk, 4-4 to 4-5,
       7-4				  E
       using CP/M, 9-3			  Erase an existing volume, 7-6
       using MS-DOS, 9-8		    to 7-8, 8-3
       using WPS, 9-7			  Errors
     Booting Master Menu, 2-1, 3-5	    allocate, A-2
					    assign new password, A-6
					    backup, A-3
     C					    copy volume, A-7
     Cancel key, 1-3			    erase, A-3
     Command string, 4-5 to 4-6,	    installation, A-1 to A-2
       9-3, 9-6 to 9-8			    mark a bad block, A-8
     Command text, B-1			    Master Menu screen, A-8 to
     Compress the empty space on a	      A-9
       drive, 7-20 to 7-21		    new name, A-5
     COPY				    restore, A-4
       copies of the installation	    select startup, A-6
       diskettes, 3-3			    unset volume-modified flag,
     Copy a volume to an existing	      A-7
       volume of equal size, 7-17
       to 7-19, 8-4
     COS-310, 7-3, 7-5, 7-8, 7-16,	  F
       7-18, 9-5, B-1			  Finished using the system, 3-11,
     CP/M, 3-4, 4-5 to 4-6, 7-3,	    6-1
       7-5, 7-8, 7-10 7-16, 7-18,	  Fixed menu screen, viii, 1-2,
       9-2 to 9-4, B-1			    2-2, 3-10 to 3-11, 4-1, 4-9,
     Creating menu items, 4-3 to 4-7	    5-2, 6-1
     Cursor, ix				  Freezing, 10-2





				    Index-1


     Index
     ----------------------------------------------------------------------


     Function key			  M
       Cancel (F8), 1-3			  Main Screen key, 1-3
       Main Screen (F9), 1-3		  Mark a bad block, 3-8,
       Print Screen, 1-3		    7-19 to 7-20
					  Master Menu
					    prerequisites, 1-2
     H					    program diagram, 1-2
     Hard disk device assignments, 9-3      with COS-310, 9-4
     HD					    with CP/M, 9-3 to 9-4
       hard disk services, 3-15, 7-1	    with MS-DOS, 9-7 to 9-8
	 to 7-2				    with WPS, 9-5 to 9-7
	 A - Allocate, 7-4 to 7-6	  Master password, 3-6 to 3-8,
	 B - Back Up, 7-8 to 7-10	    8-1 to 8-2, 8-4, A-10
	 C - Copy, 7-17 to 7-19, 8-4      MBB
	 E - Erase, 7-6 to 7-8, 8-3	    mark a bad block, 3-8
	 L - List, 7-3 to 7-4		    Menu items, ix, 1-1, 1-2, 3-5
	 M - Mark, 7-19 to 7-20		      to 3-6, 4-1 to 4-3
	 N - New Name, 7-13 to		    creating, 2-1, 4-1, 4-3
	   7-14, 8-3			      to 4-7
	 P - Assign Passwords, 7-14	    deleting, 2-2, 4-8
	   to 7-15, 8-3			    modifying, 4-7 to 4-9
	 Q - Quit, 7-13			    moving, 4-10
	 R - Restore, 7-10 to 7-12	    selecting, 3-3, 4-9
	 S - Select, 7-15		  Menu screens, ix, 1-2, 4-1, 4-9
	 U - Unset, 7-16 to 7-17, 8-3       to 4-10
	 X - Compress, 7-20 to 7-21	    adding a page marker to the
     Head number, 7-19 to 7-20, A-8	       menu, 4-9
     Help				    deleting a page marker from
       how to get help, 10-2		    the menu, 4-10
     Highlight, ix			  MENU volume, 3-4, 3-9, 7-3 to
					    7-4
					  MM
     I					    menu maintenance utility,
     Index volume, 7-3			      3-11, 4-1
     INST				  Modified flag, 7-4, 7-10, 7-16
       install Master Menu, 3-4 to 3-6      to 7-19, A-7
     Installation diskette, 3-3 to 3-4    MS-DOS, 3-4, 4-6, 7-3, 7-5, 7-8,
     Installing Master Menu, 2-1, 3-1       7-10, 7-18, 9-7 to 9-8, B-1
     Internal data, 1-2, A-2

					  N
     K					  New name for an existing
     Keyboard, 1-3			    volume, 7-13 to 7-14, 8-3


     L					  O
     Last backup, 7-4			  Operating systems, 7-3, 7-4
     Legend, ix, 4-2, 4-4	  
     List directory of volumes, 7-3
       to 7-4
     List volume passwords, 3-8, 8-4



				    Index-2


     Index
     ----------------------------------------------------------------------


     P					  S
     Page marker, 4-2, 4-9 to 4-10	  SDF
     Passwords				  select new date format, 3-11,
       assigning passwords, 7-14 to	    5-3
	 7-15, 8-1, 8-3			  Sector number, 7-19 to 7-20, A-8
       exceptions, 8-4			  Select the startup volume, 7-15
       listing of passwords, 3-8, 8-4     Size, 7-3, 7-6
       master password, 3-7 to 3-8,       SMPW
	 8-1 to 8-2, 8-4		    set master password, 3-6 to
       ranges, 8-3			      3-8
       READ passwords. 3-6, 3-8,	  Startup volume, 4-4, 7-4, 7-15,
	 4-9, 7-5, 7-14, 7-15,		    8-4, A-6
	 7-18, 8-1 to 8-4		  System test diskette, 1-2, 8-2
       with applications, 8-4		  System volume, 4-4, 7-4
       with the hard disk services
	 8-3 to 8-4
       WRITE passwords, 3-6, 3-11,	  T
	 4-9, 7-5 to 7-8, 7-13 to	  Tag, ix, 3-3, 4-2, 4-4, A-9
	 7-16, 7-18, 8-1 to 8-4		  Time function, 2-1, 3-12 to
     Power switch, 3-1 to 3-2		    3-15, 5-1 to 5-3
     Prerequisites for Master Menu,       Trouble, 10-1 to 10-2
       1-2				  Type, 7-3
     PSWD
       list volume passwords, 3-11
     Print Screen key, 1-3, 7-19,	  U
       8-1, A-8				  Unset a volume-modified flag,
					    7-16 to 7-17, 8-3, A-7

     Q
     QUIT				  V
       leave this program and go to	  Volume, 7-4
	 SETUP to reboot, 3-8, 7-13
    Quit this program, 7-13
					  W
					  WRITE passwords, 3-6, 3-8,
     R					    4-9, 7-7 to 7-8, 7-13 to 7-16,
     READ passwords, 3-6, 3-11, 4-9,	    7-18, 8-1 to 8-4
       7-5, 7-14, 7-15, 7-18, 8-1 to      WPS, 1-1, 4-3 to 4-6, 4-7 to
       8-4				    4-8, 7-3, 7-4, 7-5, 7-8,
     Restore a volume from		    7-18, 9-5 to 9-7, B-1
       diskettes, 7-10 to 7-12
     Returning to Master Menu,	9-1












				    Index-3



								    DECmate
								Master Menu
							       User's Guide

     Reader's Comments 

     Your comments and suggestions will help us in our continuous effort to
     improve the quality and usefulness publications.

     What is your general reaction to this manual?

			     Excellent    Very Good    Good    Fair    Poor
       Accuracy			[]	     []		[]	[]	[]
       Completeness		[]	     []		[]	[]	[]
       Organization		[]	     []		[]	[]	[]
       Format			[]	     []		[]	[]	[]

     What features are most useful?
     (Notes, Tables, Illustrations, etc.) _________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________

     Does the publication satisfy your needs?		[] Yes	[] No

     What errors have you found?
     (Ref. page no., table., figure no.)___________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________

     Additional  Comments _________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________

     Name -----------------------------   Street __________________________
     Title ____________________________   City ____________________________
     Company __________________________   State/Country ___________________
     Department _______________________	  Zip _____________________________

     The Docmentation Products Directory and the DECdirect Guide contain
     information on the remainder of DIGITAL's technical documentation.

     Copies of the above Directory and Guide, as well as additional copies
     of this document, are available by writing or calling:

	  Digital Equipment Corporation
	  Accessories and Supplies Group
	  P.O. Box CS2008
	  Nashua, New Hampshire 03061

	  Attension:  Documentation Products
	  Telephone:  1-800-258-1710
	  Order Number:  AA-AH12B-TV





     -----------------Do Not Tear - Fold Here and Staple-------------------


	+-+-+-+-+-+-+-+				       +------------------+
	|d|i|g|i|t|a|l|				       |    No Postage    |
	+-+-+-+-+-+-+-+				       |    Necessary     |
						       | if Mailed in the |
						       |  United States   |
						       +------------------+
								   ========
								   ========
	     ------------------------------------------------	   ========
	     |		   BUSINESS REPLY MAIL		    |	   ========
	     |	FIRST CLASS   PERMIT NO. 33   MAYNARD MASS  |	   ========
	     ------------------------------------------------	   ========
		    POSTAGE WILL BE PAID BY ADDRESSEE		   ========
								   ========
								   ========
								   ========
		Digital Equipment Corporation			   ========
		Business Systems Engineering Documentation	   ========
		Continental Blvd. (MK01-2/L06)			   ========
		Merrimack, NH 03054				   ========





     -----------------Do Not Tear - Fold Here and Staple-------------------