RTS8V1.DOC















    				  DISCLAIMER

		This document file was created by scanning  the 
		original  document and then editing the scanned 
		text.  As much as possible, the  original  text 
		format  was restored.  Some format changes were 
		made to insure this  document  would  print  on 
		current laser printers using 60 lines per page.
    		The  original  spelling  and  grammar  has been 
    		preserved.


		1-Apr-1996















							DEC-08-ORTMA-A-D









    			      RTS-8 USER'S MANUAL


    				   Version 1


































	   |-------------------------------------------------------|
	   |  Order additional copies as directed on the Software  |
	   |  Information page at the back of this document.       |
	   |-------------------------------------------------------|


    	     digital equipment corporation - maynard massachusetts


						First Printing June 1974





     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this manual.

     The software described in this document is furnished to the purchaser
     under a license for use on a single computer system and can be copied
     (with inclusion of DIGITAL's copyright notice) only for use in such
     system, except as may otherwise be provided in writing by DIGITAL.

     Digital Equipment Corporation assumes no responsibility for the use
     or reliability of its software on equipment that is not supplied by
     DIGITAL.





     Copyright @ 1974 by Digital Equipment Corporation, Maynard, Mass.







     The HOW TO OBTAIN SOFTWARE INFORMATION page, located at the back of
     this document, explains the various services available to DIGITAL
     software users.

     The postage prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in
     preparing future documentation.





     The following are trademarks of Digital Equipment Corporation:

       CDP		DIGITAL	  	 INDAC		  PS/8
       COMPUTER LAB	DNC		 KA10		  QUICKPOINT
       COMSYST		EDGRIN		 LAB-8		  RAD-8
       COMTEX		EDUSYSTEM	 LAB-8/e	  RSTS
       DDT		FLIP CHIP	 LAB-K		  RSX
       DEC		FOCAL		 OMNIBUS	  RTM
       DECCOMM		GLC-8		 OS/8		  RT-ll
       DECTAPE		IDAC		 PDP		  SABR
       DIBOL		IDACS		 PHA		  TYPESET 8
    							  UNIBUS


   				   CONTENTS
    								       Page

     PREFACE								 v

     CHAPTER 1	       INTRODUCTION				       1-1

     CHAPTER 2	       USING TASKS UNDER RTS-8			       2-1

	     2.1       THE STRUCTURE OF RTS-8 TASKS		       2-1

	     2.2       CONCEPTS OF TASK COMMUNICATION		       2-2
	     2.2.1     Task Synchronization and Event Flags	       2-2
	     2.2.2     Intertask Messages			       2-3

     CHAPTER 3	       RTS-8 EXECUTIVE REQUESTS			       3-1

	     3.1       COMMUNICATION WITH THE RTS-8 EXECUTIVE	       3-1

	     3.2       ERs USED TO SEND AND RECEIVE MESSAGES	       3-1
	     3.2.1     SEND					       3-1
	     3.2.2     WAITE					       3-2
	     3.2.3     SENDW					       3-2
	     3.2.4     RECEIVE					       3-2
	     3.2.5     POST					       3-3

	     3.3       INTER-TASK CONTROL THROUGH TASK FLAGS	       3-5
		       TABLE ENTRY

	     3.4       ERs USED TO SET AND CLEAR WAIT BITS	       3-6
	     3.4.1     BLKARG					       3-6
	     3.4.2     UNBARG					       3-6
	     3.4.3     SUSPND					       3-6
	     3.4.4     RUN					       3-7

	     3.5       DERAILING THE EXECUTION OF A TASK	       3-8
	     3.5.1     DERAIL					       3-8

	     3.6       USING INTERRUPTS IN RTS-8		       3-9
	     3.6.1     SKPINS					       3-9

	     3.7       ADVANCED RTS-8 PROGRAMMING TECHNIQUES	       3-11
	     3.7.1     WAITM					       3-11
	     3.7.2     Direct References to System Tables	       3-12

     CHAPTER 4	       RTS-8 SYSTEM TASKS			       4-1

	     4.1       CLOCK HANDLER				       4-1
	     4.1.1     Examples of Clock Handler Calls		       4-2

	     4.2       TERMINAL HANDLER				       4-3
	     4.2.1     Examples of Terminal Handler Messages	       4-5

	     4.3       LINE PRINTER HANDLER			       4-5

	     4.4       MASS STORAGE HANDLERS			       4-5
	     4.4.1     Example of Mass Storage Handler Call	       4-7


    				      iii

								       Page

	     4.5       POWER FAIL TASK				       4-7

	     4.6       OS/8 SUPPORT TASK			       4-8

	     4.7       OS/8 FILE SUPPORT TASK			       4-9

	     4.8       UDC HANDLER				       4-10
	     4.8.1     Analog Output				       4-11
	     4.8.2     Analog Input				       4-11
	     4.8.3     Digital Output				       4-12
	     4.8.4     Digital Input				       4-12
	     4.8.5     Generic Code				       4-12
	     4.8.6     Enable Counter				       4-13
	     4.8.7     Read Counter				       4-14
	     4.8.8     Disable Counter				       4-14
	     4.8.9     Enable Contacts				       4-14
	     4.8.10    Change of State				       4-15
	     4.8.11    Disable Contacts				       4-15
	     4.8.12    UDC Assembly Parameters			       4-16
	     4.8.13    UDC Error Conditions			       4-16

	     4.9       CASSETTE HANDLER				       4-17

	     4.10      CASSETTE LABEL SUPPORT HANDLER		       4-18

     CHAPTER 5	       MONITOR CONSOLE ROUTINE			       5-1

	     5.1       MCR COMMAND ARGUMENTS			       5-1

	     5.2       MCR COMMANDS				       5-2
	     5 2.1     Date					       5-2
	     5.2.2     Time					       5-2
	     5.2.3     Name					       5-2
	     5.2.4     Request					       5-3
	     5.2.5     Stop					       5-4
	     5.2.6     Disable					       5-4
	     5.2.7     Enable					       5-4
	     5.2.8     Cancel					       5-4
	     5.2.9     Systat					       5-4
	     5.2.10    Open Address				       5-5
	     5.2.11    Examine Address				       5-6
	     5.2.12    Deposit Address				       5-6
	     5.2.13    Post Address				       5-6
	     5.2.14    Exit					       5-6
  
	     5.3       MCR ERRORS				       5-6

     CHAPTER 6	       ASSEMBLING AND LOADING TASKS FOR RTS-8	       6-1

     CHAPTER 7	       DEMONSTRATION PROGRAM			       7-1

     APPENDIX A	       RTS-8 DISTRIBUTED SOURCE FILES		       A-1
     APPENDIX B        RTS-8 COMPONENT SIZES			       B-1
     GLOSSARY						        GLOSSARY-1
     INDEX						           INDEX-1


				      iv







				     PREFACE



     This manual describes the PDP-8 Real-Time System (RTS-8) and  provides
     information  and  examples necessary for its efficient use.  Knowledge
     of PDP-8 machine language programming is essential;  in addition,  the
     user should be familiar with real-time systems in general and with the
     use and operation of the OS/8 system.

     The  following  PDP-8  handbooks  will  be  helpful  for  review   and
     reference:   INTRODUCTION TO PROGRAMMING, THE SMALL COMPUTER HANDBOOK,
     the OS/8  HANDBOOK  (DEC-S8-OSHBA-A-D),  the  UDC8  UNIVERSAL  DIGITAL
     CONTROL  SUBSYSTEM  MAINTENANCE MANUAL (DEC-08-HZDC-D), and the CAPS-8
     USER'S MANUAL (DEC-8E-OCASA-A-D).







































				       v





				   CHAPTER 1

				 INTRODUCTION



     A real-time system is a software framework under which  the  resources
     at hand (core, CPU time, peripheral devices) are divided among several
     tasks.  The term "task" is difficult to define, as  it  overlaps  with
     the definitions of "program" and "subroutine", but basically a task is
     a  portion  of  machine  code  which  performs  a  specific  function;
     sometimes  this  function is an end in itself, sometimes it is related
     only to the needs of other tasks.  The  real-time  system  distributes
     resources to tasks at any time depending on whether the tasks can make
     use of them, and whether a  more  privileged  (higher  priority)  task
     wants to pre-empt resources already in use.

     Most real-time systems consist of a group of programs  or  tasks  that
     run  at  varying  times  or  frequencies  and  alternate between being
     compute  bound  and  I/O  bound.   To  efficiently  use  the   central
     processor,  these  tasks  cannot  be  run  in series since the central
     processor will be poorly utilized during the periods  that  tasks  are
     I/O bound.   In  addition,  real-time  tasks are time-dependent in one
     sense or another and in general cannot wait for a slow, less important
     I/O  or  compute  bound  task  to  finish  before  starting execution.
     Multiprogramming and some sort of priority scheme for  scheduling  the
     central processor are thus required.

     Multiprogramming allows many tasks to be in some  state  of  execution
     simultaneously.   When  one  task cannot use all the available central
     processor time because it must wait for an I/O operation or is blocked
     by  some  other  condition,  the  central processor can be switched to
     another task to make use of the available time.  It is  possible  even
     in  a  multiprogramming environment that there may not be a task in an
     executable  state  to  utilize  this  available  time.    While   this
     condition  is  certainly  possible, it is less likely to occur than in
     a uni-programming environment.

     A priority scheme is needed to distinguish the relative importance  of
     the various tasks in the system.  It must be possible to interrupt the
     execution of a less important task to  execute  a  critical  real-time
     program.   A  fixed  priority  scheme has been chosen.  Fixed priority
     meets the above requirement, is simple and adequate, and requires  low
     scheduling overhead.

     RTS-8 is a small real-time system which uses any family-of-8 processor
     (with  the exception of the PDP-8/S).  It allows up to 63 tasks to run
     concurrently, competing  for  resources  on  a  fixed-priority  basis.
     Included  in  the  RTS-8  system  are  system tasks which control most
     standard Digital Equipment Corporation I/O devices (listed in  Chapter
     4),  a  task  which allows interactive system control from the console
     terminal, and a task which allows a single copy of  the  OS/8  monitor
     system to run in the background.



				      1-1





				   CHAPTER 2

	    		    USING TASKS UNDER RTS-8



     2.1  THE STRUCTURE OF RTS-8 TASKS

     The controlling program in an RTS-8 System  is  the  RTS-8  Executive.
     The  Executive  decides  which  task  should  be running (based on the
     priorities of the tasks which are  able  to  run)  and  also  provides
     services  to the tasks by means of Executive Requests, discussed later
     in Chapter 3.

     Each task in an RTS-8 system has  an  associated  unique  Task  Number
     between 1 and 63, which serves the following purposes:

	  1.  The Task Number is used by the RTS-8 Executive as an index to
	      various system tables where information about tasks is kept.

	  2.  The Task Number is used by other  tasks  in  the  system  for
	      reference in Executive Requests.

	  3.  The Task Number determines the task's  priority;   the  lower
	      the Task Number, the higher the priority of the task.

     The Executive uses three internal tables to maintain information about
     the  tasks  in the system. Each task's Task Number is used as an index
     into these tables to retrieve and update information  for  that  task.
     The internal tables are:

	  1.  The Task State Table - a table of 4-word entries holding  the
	      most  recent  contents  of  CPU  registers  for  each task as
	      follows:

	           Word 1 - contains the link (bit 0)
				     the data field (bits 9-11)
				     the instruction field (bits 6-8)

		   Word 2 - contains the program counter (PC)

		   Word 3 - contains the accumulator (AC)

		   Word 4 - contains the multiplier quotient (MQ)

	      Whenever a task is executed, the contents of its  Task  State
	      Table  are  loaded  into the corresponding CPU registers, and
	      whenever a task stops executing, its Task State  Table  entry
	      is set to the new contents of these registers.

	  2.  The Task Flags Table - a  table  of  l-word  entries  holding
	      various  bits  for  each task to determine whether or not the




				      2-1


     Using Tasks Under RTS-8


	      task is runnable (a detailed description  of  these  bits  is
	      provided in Section 3.3). A task is runnable only if its Task
	      Flags Table entry contains zero.

	  3.  The Task Input Message Queue Header  Table   -   a  table  of
	      2-word  entries  which  represent  the  "head"  of  the input
	      message queue for each task:

		   Word 1 - if zero, there are no messages  in  the  queue;
			    if  non-zero, the word is a CDF to the field of
			    the first message in the queue.

		   Word 2 - if word 1 was not zero, this word is a  pointer
			    to the first message in the queue.

	      Messages are discussed later in this chapter.


     2.2 CONCEPTS OF TASK COMMUNICATION

     There are two main  types  of  task  communication  in  RTS-8--message
     sending  and  synchronization.   Since  synchronization  is  the  more
     fundamental of the two, it will be discussed first.


     2.2.1 Task Synchronization and Event Flags

     Whenever two processes occur independently, there may be  a  need  for
     one  to  wait  while  the  other  finishes execution.  The most common
     example of this is the PDP-8 terminal interface.  The  terminal  waits
     for  the  PDP-8  to produce a printable character.  When the PDP-8 has
     one, it alerts the terminal by issuing  a  TLS  instruction.   If  the
     PDP-8  then  has  another  character to print, it must first wait in a
     TSF;JMP .-1 loop until the  terminal  signals  that  it  has  finished
     printing  the  character  by  raising  the ready flag.  Then the PDP-8
     exits from its loop and proceeds to print the next character.

     Similarly, tasks in RTS-8 may synchronize with each other by means  of
     Event Flags.  An Event Flag is a location which contains the status of
     an Event.  An Event can be a  physical  occurrence  such  as  a  clock
     ticking,  a valve closing, or a device ready flag raising, or an Event
     can be conceptual, as for example, a result, an  inconsistency,  or  a
     certain  string  of  characters  typed  by  the  operator.   Like  the
     terminal ready flag, an Event Flag  has  the  states  PENDING(>0)  and
     FINISHED(=0).   Thus a task can (via a message) direct another task to
     perform some action, at which time it  will  set  a  (mutually  agreed
     upon)  Event  Flag  to  the  PENDING  value.   When  the  second  task
     finishes it sets the Event  Flag  to  the  FINISHED  value  (known  as
     Posting  the  Event Flag).  If the first task has been waiting for the
     Event Flag with the instructions:

	       TAD Event Flag; SZA CLA; JMP .-2

     then the Posting of the Event Flag will cause the first task  to  exit
     from its loop.

				      2-2

     Using Tasks Under RTS-8

     Unfortunately,  the  above  loop   ties   up   a   vitally   important
     resource--the  PDP-8  processor.   Therefore, under RTS-8, Event Flags
     have an additional state: WAITING(<0).  Thus in the example above, the
     first  task  can  tell  the RTS-8 Executive it wants to WAIT until the
     Event Flag is FINISHED.  The monitor saves the  task's  PC  and  marks
     in  its Task Flags Table word that it is Waiting on an Event Flag; the
     Event Flag is set to the proper  WAITING  state  (in  this  case,  the
     proper  WAITING  state  is  octal  4000  plus  the waiting task's Task
     Number).  When the Event Flag is POSTed (via an RTS-8 Executive  call)
     the  task  which  is  WAITING  for  it  is  automatically  started  by
     RTS-8. The mnemonic for the RTS-8 Executive Request which Waits for an
     Event Flag is WAITE.


     2.2.2 Intertask Messages

     Just as Event Flags under  RTS-8  are  analogous  to  hardware  device
     flags,   messages   are   analogous   to   data-sending  hardware  I/O
     instructions (for example,  TLS).  That  is,  messages  start  a  task
     (providing  the  task  is  WAITING for a message) and at the same time
     pass information to the task.

     A message under RTS-8 is a contiguous area  of  core  storage.   RTS-8
     requires the first three words of the message (the Message Header) for
     its use.  The first word of the Message Header is the Event  Flag  for
     the  message.   When  the  message is sent, the Event Flag is set in a
     PENDING state by the RTS-8 Executive; this signifies that the  message
     has  been  sent  but  not yet completed. No action occurs to the Event
     Flag upon receipt of the message by the receiving task; however  RTS-8
     protocol requires that when the receiver has performed whatever action
     is specified (or implied) by the message, it  POSTS  the  Event  Flag.
     This  posting  serves two purposes: it informs the task which sent the
     message (the "sender") that the requested action has  been  completed,
     and it "frees" the message so that it can be sent again (see 2 below).

     The second and third words  of  the  Message  Header  are  used  as  a
     CDF-address  pair to link the message to the next queue entry.  If the
     receiving task is not actively waiting for a message, the  message  is
     placed on the receiving task's Input Message Queue.  Messages are then
     queued in order of decreasing priority of the sender (increasing  task
     number) and in the order issued if a task sends more than one message.

     The rest of the message may contain any desired information.   Sending
     a  message  does  not  physically  move the message information to the
     receiving task, but provides the receiver with the field  and  address
     of the first data word of the message.

     Note again that the information in a message is not  copied  into  the
     receiver's area; this has several implications:

	  1.  Data in a message should not be modified by the sender  while
	      the Event Flag for the message is PENDING.

	  2.  The same message cannot be sent  a  second  time  before  its
	      Event  Flag  is FINISHed the first time.  RTS-8 enforces this
	      by checking the Message Event Flag on a  SEND  operation  and

				      2-3

     Using Tasks Under RTS-8


	      putting the sender into Event Flag Wait  if  the  message  is
	      still PENDING.

	  3.  It is legal for the receiving task to  store  information  in
	      the  body  of  the  message.   In this way an "answer" to the
	      message can be returned without the complications of  sending
	      a  return  message  back  to the sender.  For example, when a
	      task sends a message to the disk driver task requesting  I/O,
	      the  error  status  of the completed operation is placed in a
	      specific word in  the  message  by  the  driver  to  indicate
	      whether an error occurred.













































				      2-4







    				   CHAPTER 3

    			   RTS-8 EXECUTIVE REQUESTS



     3.1  COMMUNICATION WITH THE RTS-8 EXECUTIVE

     RTS-8  tasks  communicate  with  the  RTS-8  Executive  via  Executive
     Requests  (abbreviated  as  ERs).  In  order to make ERs simple across
     field boundaries, RTS-8 uses locations  20-27  in  every  field  as  a
     communication  region  for  ERs.  The  Executive  can be called in any
     field via a JMS 20 instruction (hereafter referred to as a  CAL).  The
     Data Field (DF) does not have to be any specific value when the CAL is
     given, as the code in location 20 sets the DF to the Instruction Field
     (IF),  sets  the  IF  to  0  and jumps to the RTS-8 Executive.  (Other
     instruction definitions used throughout the manual  and  described  in
     Chapter  3 are POSTDS which is defined as JMP I 24, and WAITM, defined
     as JMS I 25.)

     Because the architecture  of  the  PDP-8  does  not  permit  reentrant
     programs,    the    RTS-8   Executive   runs   with   task   switching
     inhibited, i.e., interrupts are on, but higher priority tasks may  not
     request  the  CPU  until the Executive has finished its request.  When
     the Executive finishes processing the request, it checks  whether  any
     higher-priority  tasks  have  become runnable while task switching was
     inhibited, and, if so, it runs the highest-priority task of these.
     
     Also, because of the non-reentrant  architecture  of  the  PDP-8,  the
     RTS-8  Executive  will  not  honor any request to switch tasks arising
     from an interrupt if the interrupted task's Program Counter  (PC)  was
     less  than  100.  This  is done to protect the RTS-8 Executive's entry
     point (location 20 in each field) from  being  destroyed.  User  tasks
     should  be  careful  NEVER  to execute any instructions below 100 in a
     field.


     3.2  ERs USED TO SEND AND RECEIVE MESSAGES
     
     There are five ERs  associated  with  the  Messages  and  Event  Flags
     described in Chapter 2. Descriptions of these follow and an example of
     their usage is presented in Section 3.2.5.
     

     3.2.1  SEND  Send Message

	       Format:   CAL
			 SEND
			 TSKNUM
			 MESSAG

     


				      3-1

     RTS-8 Executive Requests

     
     SEND sends the message located at MESSAGE in the current field to  the 
     task  whose  number  is  TSKNUM.  If the receiving task is of a higher
     priority than the sender and is waiting for a message, the  sender  is
     temporarily  suspended and the receiver runs.  In any case, the sender 
     is not put into any WAIT state once the message is sent.  However,  if 
     the  event  flag in location MESSAG is PENDING (non-zero), meaning the
     message is still busy from a previous SEND, the  sender  will  be  put 
     into  Event Flag Wait on location MESSAG, and only when the Event Flag
     becomes FINISHED (zero) will this SEND be performed.

     
     3.2.2  WAITE  Wait on Event Flag

	       Format:   CAL
			 WAITE
			 EFLG
     
     WAITE checks the status of  location  EFLG  and  if  it  is  FINISHED, 
     returns  control  to  the  caller.  If  EFLG  is PENDING, its state is 
     changed to WAITING and the calling task is put into Event  Flag  WAIT. 
     When location EFLG is POSTed by another task or interrupt routine, the
     calling task becomes runnable again.

     
     3.2.3  SENDW  Send and Wait
     
	       Format:   CAL
			 SENDW
			 TSKNUM
			 MESSAG
     
     SENDW is exactly equivalent to the sequence:
     
	       CAL
	       SEND	 /SEND THE MESSAGE
	       TSKNUM
	       MESSAG
	       CAL
	       WAITE	 /WAIT FOR RECEIVER TO ACKNOWLEDGE
	       MESSAG

     
     3.2.4  RECEIVE  Receive Message

	       Format:	     TAD RESTRICTION     /ONLY TO RESTRICT
			     CAL		 /SENDING TASKS
			     RECEIVE
		      MADDR, 0			 /MESSAGE ADDRESS STORED
						 /HERE; CDF TO MESSAGE
						 /FIELD IN AC ON RETURN
     
     If the AC is zero when the RECEIVE ER is issued,  the  calling  task's
     Input Message Queue is examined.  If there are messages in the calling
     task's Input Message Queue, the first (i.e., highest-priority) message
     is dequeued and the address of its first data word is placed in MADDR.
     
     				      3-2

     RTS-8 Executive Requests
     
     A CDF to the field of the message is stored in the AC.  If  there  are 
     no  messages,  the  task  is placed in Message Wait until such time as 
     there are any.  There is no ER which will allow a task  to  check  for 
     messages and not be placed in Message Wait if there are none;  however 
     a task may examine its Input Message Queue Header in field 0 first  to 
     determine the state of the Input Message Queue.
     
     If the AC is non-zero when the  RECEIVE  ER  is  issued,  the  calling 
     task's  Input  Message  Queue is searched for a message whose sender's 
     Task Number matches the contents of the AC.   If  such  a  message  is 
     found,  it  is  removed from the queue as specified above;  if none is 
     found the issuing task is placed in Message Wait.

     
     3.2.5  POST  Post Event Flag
     
	       Format:	       TAD EFPTR   /POINTER TO EVENT FLAG
			       CAL
			       POST
			EFCDF, CDF EFFLD   /FIELD OF EVENT FLAG
     
     The Event Flag pointed to by the AC at the CAL, in the field specified
     by  EFCDF, is set to the FINISHED (zero) state.  If its previous state
     was WAITING, the task which was waiting for it is cleared of its Event
     Flag  Wait.   This ER never sets the calling task in a WAIT state, but 
     if the task Waiting for the Event Flag is of a  higher  priority  than 
     the  calling task, the calling task is temporarily suspended while the 
     other is run.
     
     This example illustrates the RTS-8 ERs dealing with Messages and Event
     Flags.   Since  I/O and interrupts under RTS-8 have not been discussed
     yet, this example is trivial;  i.e., there is no advantage to  keeping
     the  functions  of the two tasks separate, and the entire send/receive
     structure is being used here  as  an  elaborate  subroutine  call.   A
     description follows the example.
     
				     Task A				     ______
     
     A1	      ALOOP,  CAL
		      SEND		 /SEND TASK B A MESSAGE
		      B
		      MES1
     A2		      CAL
		      SEND		 /AND ANOTHER
		      B
		      MES2
     A3		      CAL
		      WAITE		 /WAIT FOR FIRST ONE
		      MES1
     A4		      JMP ALOOP		 /LOOP
     	       MES1,  ZBLOCK 3
		      15		 /RANDOM NUMBERS
		      37
		      23
	       MES2,  ZBLOCK 3
		      -1
		      4     
			 	      3-3

     RTS-8 Executive Requests
     

    				     Task B    				     ______
     
     B1	      BLOOP,  CAL
		      RECEIV		 /GET A MESSAGE
	      MADDR,  0
     B2		      DCA EFCDF		 /SAVE CDF FOR POST
     B3		      TAD EFCDF
     B4		      DCA .+1		 /PUT CDF INLINE
     B5		      HLT		 /CDF TO MESSAGE FIELD
     B6		      TAD I MADDR	 /GET 1ST DATA WORD OF MESSAGE
     B7		      CLA
     B8		      STA CLL RTL	 /-3 IN AC
     B9		      TAD MADDR		 /AC POINTS TO MESSAGE
     B10	      CAL		 /EVENT FLAG
		      POST
	      EFCDF,  HLT		 /CDF TO MESSAGE FIELD HERE
     Bll	      JMP BLOOP		 /LOOP
     
     The flow of execution in this example depends  on  which  of  the  two 
     tasks  has  higher  priority.  Assuming that at some time both A and B 
     become runnable and task  A  has  higher  priority,  the  sequence  of 
     execution is as follows:
     
	  Instructions			   Why Executed	  ____________			   ____________
     
	       A1	      Task A has higher priority than task B.
	       A2	      Task A has higher priority than task B.
	       A3	      Task A has higher priority than task B.
	       B1	      Task A is now in Event Flag Wait  since  MES1
			      was PENDING; MES1 is now in WAITING state.
	       B2-B10	      Task A is still  WAITing--the  RECEIV  at  B1
			      received MES1
	       A4	      The POST at B10 posted MES1 and "woke up"  A,
			      which has higher priority than B.
	       A1	      A continues executing.
	       A2	      A tries to send MES2 again;  B  has  not  yet
			      processed it;  MES2 is PENDING.
	       Bll	      Therefore, A is put into Event Flag Wait  and
			      B is resumed; MES2 is now WAITING.
	       Bl-B10	      B now receives and posts MES2.
	       A2	      This brings A out of Event  Flag  Wait;   the
			      RTS8  Executive has modified task A's Program
			      Counter  so  that  it  will  re-execute   the
			      offending SEND.
	       A3	      A3 now waits for MES1 to be POSTed.
     
     If task B has higher priority, the sequence of execution is:
     
	  Instructions			   Why Executed	  ____________			   ____________

	       B1	      Task B has higher priority than task A.
	       A1	      Task B is placed in Message Wait since  there
			      are no messages in its input queue.
	       A1	      Loops back to A1 and sends MES1 again.


     				      3-4

     RTS-8 Executive Requests
     
	       B2-B10	      Task A's message brings task B out of Message
		              Wait;   since  B  has  higher  priority, A is
			      stopped and B runs.
	       Bll	      The POST at B10 sets MES1 to FINISHED but has
			      no other effect.
	       B1	      Now task B tries to get another message.
	       A2	      There are none, so task B is put  in  Message
			      Wait and A is run.
	       B2-Bll	      Task A sends  MES2  which  "wakes  up"  B;  B
			      processes MES2 and
	       B1	      returns for more,
	       A3	      and is put in Message Wait.   Since  MES1  is
			      FINISHED
	       A4	      the WAITE at A3 has no effect and task A
	       A1	      loops back to A1 and sends MES1 again.
     
     3.3  INTER-TASK CONTROL THROUGH TASK FLAGS TABLE ENTRY
     
     A task's Task Flags Table entry is used by RTS-8 to determine  if  the
     task  can  run.   A  zero  Task Flags Table entry indicates a runnable 
     task.  Each bit which is set in a non-zero word indicates a reason why 
     the  task  cannot run.  The currently defined bits and their meanings,
     if set, are:
     
          Octal	   Symbolic	          Meaning          _____    ________	          _______
     
          0001	   DNEWT      Does Not Exist Wait - This  task  cannot
			      run because it is nonexistent.

          4000	   MSGWT      Message Wait - This task is  waiting  to
			      be sent a message.

          2000	   EFWT       Event Flag Wait - This task  is  waiting
			      for  an  Event  Flag  (which  contains a
			      WAITing  value  corresponding  to   this
			      task) to be POSTed.

          0400	   SWPWT      Swap Wait - This task cannot run because
			      it  is not in core (this bit is reserved
			      for future RTS-8 releases).

          1000	   RUNWT      Run Wait - This task is  waiting  for  a
			      RUN ER to be executed with its number in
			      the AC, or  for  the  operator  to  type
			      "REQUEST  task"  to  the Monitor Console
			      Routine (see Chapter 5).

          0200	   EORMWT     Event or Message Wait  -  This  task  is
			      waiting for an Event Flag to be set or a
			      message  to  arrive,  whichever  happens
			      first.

          0040	   ENABWT     Enable Wait - This task is waiting to be
			      Enabled.   Use of this bit is restricted
			      to the Monitor Console Routine  for  use
			      by  the "ENABLE task" and "DISABLE task"
			      commands.
     				      3-5

     RTS-8 Executive Requests
    

          0100	   USERWT     User Wait - This bit is reserved for use
			      by  user-written  tasks.  RTS-8 does not
			      use this bit.
     

     3.4  ERs USED TO SET AND CLEAR WAIT BITS
     
     Several ERs exist which allow a task to explicitly set and clear  wait
     bits in the Task Flags Table entry of another task, and to set bits in
     its own table-entry.

     
     3.4.1  BLKARG  Block Task for Specified Reason
     
	       Format:  TAD TASKNUM	     /OR 0 IF SELF
			CAL
			BLKARG
			WAITBITS
     
     TASKNUM contains the number of the task to be blocked (or not  allowed
     to  run),  and  WAITBITS  specifies one or more bits to be set in that
     task's Task Flags word.  Assuming  WAITBITS  is  non-zero,  this  will 
     cause  the specified task to become non-runnable.  If TASKNUM contains 
     0, the issuing task will be blocked on the specified wait  bits.   The 
     TASKNUM=0 form of this ER is the only legal way to specify the issuing 
     task as the task to be blocked;  if TASKNUM is equal  to  the  issuing 
     task number the action of this ER is undefined.

     
     3.4.2  UNBARG  Unblock Task for Specified Reason
     
	       Format:	TAD TASKNUM
			CAL
			UNBARG
			WAITBITS
     
     TASKNUM contains the number of  the  task  to  unblock,  and  WAITBITS
     specifies  one  or  more  bits to be cleared in that task's Task Flags
     word.  If the Task Flags  word  becomes  zero  as  a  result  of  this
     operation, the specified task becomes runnable;  if the specified task
     has  higher  priority  than the issuing task and becomes runnable, the
     issuing task is temporarily suspended while that task runs.
     
     This ER is a no-op if issued with TASKNUM equal to the issuing  task's
     number.

     
     3.4.3  SUSPND  Suspend a Task's Execution
      
	       Format:	TAD TASKNUM	     /0 IF SELF
			CAL
			SUSPND
     



				      3-6

     RTS-8 Executive Requests


     This ER is identical in action to the following instructions:
     
	    TAD TASKNUM
		CAL
		BLKARG
		RUNWT

     
     3.4.4  RUN  Run a Task
     
	       Format:	TAD TASKNUM
			CAL
			RUN
     
     This ER is identical in action to the following instructions:
     
	       TAD TASKNUM
	       CAL
	       UNBARG
	       RUNWT
     
     The SUSPND and RUN ERs  exist  because  their  function  is  performed
     sufficiently  often enough to warrant a shorthand version.  An example 
     of how they can be used follows.
     
     A data collection task is to print a report  every  1000  data  points
     without interrupting the data collection/reduction process.
     
				   Data Task				   _________
     
	      DLOOP,  TAD (-1750	 /1000 DECIMAL
		      DCA COUNT
	      DATALP, CAL
		      WAITE
		      DATAEF
		      .     
		      .     
		      .     
	    	      .			 /GET A DATA POINT
	    	      ISZ COUNT		 /AND PROCESS IT
	    	      JMP DATALP	 /COUNT OFF 1000
	    	      TAD (REPORT	 /POINTS
	    	      CAL		 /RUN REPORT TASK
	    	      RUN
	    	      JMP DLOOP		 /KEEP COLLECTING
	       COUNT, 0
     
     








	    			      3-7

     RTS-8 Executive Requests


	    			  Report Task	    			  ___________
     
	      RLOOP,  CAL		 /AC=0, SUSPEND
	    	      SUSPND		 /UNTIL NEEDED
	    	      JMS TITLE		 /HAS BEEN RUN
	    	      .
	    	      .			 /PRINT REPORT
	    	      .			 /WITH TITLE    
	    	      JMP RLOOP		 /REPORT OVER-GO
	    				 /BACK AND WAIT
     
     To eliminate interference with the data collection, REPORT should have
     a lower priority than DATA.

     
     3.5  DERAILING THE EXECUTION OF A TASK
     
     There is one task control ER which does not cause any wait bits to get
     set or cleared, but which terminates the execution of a specified task
     and transfers control to a subroutine.

     
     3.5.1  DERAIL  Derail a Task's Execution
     
	       Format:  TAD TASKNUM
			CAL
			DERAIL
			ADDR
     
     This ER causes a "JMS ADDR" to be simulated for the task whose  number
     is  contained  in TASKNUM (the "derailed" task). ADDR is assumed to be 
     in the same field  in  which the  derailed  task  is  executing.   The 
     derailed  task's  PC  (from  its  Task State Table entry) is stored in 
     ADDR;  the PC entry in its Task State  Table  entry  is  then  set  to 
     ADDR+1.  Two  important  points  to  note  about  the operation of the 
     DERAIL ER are:
     
	  1.  The derailed task's AC, Link, and Data Field settings are not
	      saved  by  the  DERAIL  ER;  therefore they must be saved and
	      restored by the derail subroutine. In this  sense,  a  derail
	      subroutine is very much like an interrupt at the task level.
     
	  2.  The contents of the derailed task's Task Flags word  are  not
	      affected  by  the  DERAIL  ER.   If  the derailed task is not
	      runnable, the derail subroutine will not be executed until it
	      becomes runnable.
     
     The DERAIL ER is generally used to signal an  emergency  condition  to
     another  task.   For  example, in a process-control environment, it is
     sometimes necessary to abort all operations if  the  room  temperature
     exceeds  some  critical  value.   This  can be checked by a task which
     measures room temperature every 10 seconds.   It  is  inefficient  and
     unmodular  to  include  shutdown  code in this "watchdog task" for all
     machinery being  controlled.   A  better  solution  is  to  provide  a
     

				      3-8

     RTS-8 Executive Requests
     

     location to which each equipment-controlling task can be  DERAILED  in
     order  to  shut down its own piece of equipment.  The RTS-8 Power-Fail
     task uses the DERAIL ER to provide a similar  facility  on  power-fail
     recovery (see Section 4.5).

     
     3.6  USING INTERRUPTS IN RTS-8
     
     The RTS-8 Executive contains code to receive  and  dismiss  interrupts 
     and  to  perform  interrupt-initiated  task switching, but it does not 
     provide room for an interrupt skip chain.  Instead, the skip chain  is 
     literally a chain and is built up dynamically via the SKPINS ER.

     
     3.6.1  SKPINS  Insert Code Into Skip Chain
     
	       Format:   CAL
			 SKPINS
			 MODULE
     
     MODULE  is  the  address  (in  the  current  field)  of  an  interrupt 
     processing  module.   An interrupt processing module has the following 
     format:
     
	      MODULE, 0			 /THIS WORD GETS A POINTER
					 /TO THE NEXT MODULE
		      0			 /MODULE ENTERED HERE - CONTAINS
					 /CDF CIF NEXT MODULE FIELD
		      SKDR		 /SKIP ON DEVICE READY
		      (SKP)		 /(ONLY IF SKDR REALLY MEANS SKIP
					 /ON DEVICE NOT READY)
		      JMP I MODULE	 /NOT READY - GO TO NEXT MODULE IN
					 /CHAIN
		      CDF CIF CUR	 /THIS ONE IS MINE - SET DF AND IF
					 /CORRECTLY
		      .			 /INTERRUPT PROCESSING
		      .
		      .     
		      CIF 0
		      POSTDS		 /DISMISS THE INTERRUPT, MAYBE POST
					 /AN EVENT FLAG
     
     The RTS-8 interrupt skip chain initially consists of one  such  module
     for  the  system  clock.   Whenever  a  task executes a SKPINS ER, the
     interrupt chain is broken at the very end  and  the  user's  interrupt
     module is inserted.  The last interrupt module points to the interrupt
     dismiss routine as its "next module", so that RTS-8 will try to  avoid
     superfluous  interrupts.  Notice that SKPINS always inserts at the end 
     of the skip chain.  This implies that the skips in the skip chain will 
     be  ordered roughly by priority of the task which inserted them, since 
     any SKPINS ERs in a task are usually executed  as  once-only  code  at 
     system startup time.
     
     Once an interrupt module receives control  (by  having  its  I/O  skip
     succeed) there are several restrictions on its execution:
     
				      3-9

     RTS-8 Executive Requests

     
	  1.  The Data Field and Instruction Field are those  of  the  NEXT
	      interrupt module;  this must be corrected before any indirect
	      addressing or jumps are performed.
     
	  2.  An interrupt module may not issue any RTS-8 ERs.
     
	  3.  An interrupt module should  not  compute  excessively,  since
	      interrupts  are  off.  Typical execution time should be under 
	      75 microseconds;  if considerably more computing than this is 
	      needed,  a task should be scheduled to perform it rather than 
	      computing excessively with interrupts off.
     
	  4.  Interrupt modules must not turn interrupts on, as  the  state 
	      of  the  interrupted  task  may  be  destroyed  by  a  second 
	      interrupt.
     
	  5.  On entry to the interrupt module,  the  AC,  Link,  and  Data 
	      Field  have  already  been saved, but the Multiplier Quotient 
	      (MQ) has not.  Therefore interrupt modules wishing to use the 
	      MQ  should save it first and restore it before dismissing the 
	      interrupt.
     
	  6.  Interrupt modules must dismiss the interrupt by  setting  the
	      Instruction  Field  to  0  and  issuing a POSTDS instruction.
	      POSTDS is currently defined as a JMP I  24  instruction.   An
	      Event  Flag  may be POSTed when the interrupt is dismissed by
	      setting the Data Field to the field of  the  Event  Flag  and
	      placing  the  location  of  the Event Flag in the AC prior to
	      issuing the POSTDS.  For example:
     
		   CDF CUR 	/DF = THIS FIELD
		   TAD (EVFLG 	/EVFLG MAY NOT BE AT LOC 0
		   CIF 0
		   POSTDS 	/DISMISS INTERRUPT AND POST EVFLG
     
     For example, an RTS-8 Paper Tape  Punch  handler  task  might  contain
     sections of code such as the following:
     
     In the initialization code:
     
			  CAL		/LINK THE PUNCH
			  SKIP
			  SKPINS	/INTO THE SKIP CHAIN
			  PTPINT
			  .     
			  .
			  .








     
				      3-10

     RTS-8 Executive Requests
     
     As a character punch subroutine:
     
	       PUNCH,	 0		/ENTER WITH CHAR IN AC
			 DCA TEMP	/SAVE CHAR
			 CAL		/WAIT UNTIL PUNCH READY
			 WAITE
			 PTPEF
					/SET PUNCH EVENT FLAG
			 ISZ PTPEF	/PENDING
			 TAD TEMP
		 	 PLS		/PUNCH CHAR
			 CLA
			 JMP I PUNCH
			 .     
			 .
			 .
     Interrupt skip chain code:
     
	       PTPINT,   ZBLOCK 2	/USED TO CHAIN SKIPS
			 PSF		/CHECK PUNCH FLAG
			 JMP I PTPINT	/NOT READY
			 CDF CIF CUR	/SET CORRECT DF, IF
			 PCF		/CLEAR PUNCH FLAG
			 TAD (PTPEF
			 POSTDS		/DISMISS INTERRUPT,
					/POSTING PTPEF
			 .
			 .
			 .     
	       PTPEF,	 0		/PUNCH INITIALLY READY
	       TEMP,	 0
     
     RTS-8 does not currently provide a mechanism for  dynamic  removal  of
     entries from the interrupt skip chain.

     
     3.7  ADVANCED RTS-8 PROGRAMMING TECHNIQUES
     
     The information in this section is for the experienced RTS-8 user  and
     should  be  ignored  until  the  user  has gained familiarity with the
     system.

     
     3.7.1  WAITM  Waiting For Multiple Event Flags
     
     Sometimes it is desirable to wait for a logical  combination  (AND  or 
     OR) of Event Flags.  Waiting for the logical AND of two Event Flags is 
     quite simple.  The sequence:
     
	       CAL
	       WAITE
	       A	 /WAIT FOR EVENT FLAG A
	       CAL
	       WAITE
	       B	 /AND THEN WAIT FOR EVENT FLAG B
     
     waits until both A and B have been POSTed.
				      3-11

     RTS-8 Executive Requests
     

     Waiting for the logical OR of several event flags  is  more  difficult
     since there is a possible race condition between the various tests and
     the interrupts  (or  task  executions)  which  POST  the  Event  Flags
     involved.  The  key  to  waiting  for  an  OR  of  several Event Flags
     successfully is not to allow  any  interrupts  to  occur  between  the
     testing  of the first Event Flag and the placing of the task in a Wait
     state if none of the flags were POSTed.
     
     To accomplish this requires a special sequence of instructions  and  a
     special  RTS-8  call  named  WAITM. WAITM is currently defined to be a 
     JMS I 25.  It must be executed with interrupts  off,  the  Instruction 
     Field  set  to  0  and the Data Field set to the current field, and it 
     must be followed by a word containing the blocking bit(s) to be set in 
     the Task Flags Table.  The action of WAITM is equivalent to the action 
     of the RTS-8 ER BLKARG except that  a  fast  path  through  the  RTS-8 
     Executive  is  taken and interrupts remain off until the blocking bits 
     are on in the Task Flags Table.
     
     For an example of the use of WAITM, assume that a task "TASK" wants to
     test  two  Event  Flags A and B.  If A is POSTed, control should go to
     location ADONE, and if B is  POSTed  control  should  go  to  location 
     BDONE.   If neither is POSTed, the task must wait until one of them is 
     POSTed.  The code to perform this function is:
     
	       TESTAB, IOF 		/INTERRUPTS OFF - DELICATE CODE
	       TAD A
	       SNA CLA
	       JMP ADONE 		/ADONE MUST TURN INTERRUPTS ON
	       TAD (4000+TASK 		/SET A TO "WAITING' STATE
					/INDICATING
 	       DCA A			/THAT THIS TASK IS WAITING ON IT
	       TAD B
	       SNA CLA
	       JMP BDONE		/BDONE MUST TURN INTERRUPTS ON
	       TAD (4000+TASK 		/SET B TO "WAITING" STATE
					/INDICATING
	       DCA B			/THAT THIS TASK IS WAITING ON IT
	       CIF 0
	       CDF CUR
	       WAITM
	       EFWT			/BLOCK TASK ON EVENT FLAG WAIT
	       JMP TESTAB		/WE'RE BACK - ONE OF THE TWO
					/EVENT FLAGS HAS BEEN POSTED.
					/GO BACK TO FIND OUT WHICH ONE
     
     3.7.2  Direct References to System Tables
     
     A task may directly refer to locations in the RTS-8  Executive  tables 
     to  obtain  information about itself or any other task, as long as two
     restrictions are observed:
     
	  1.  Due to the interrupt-driven nature of the system, these table
	      entries  may change at any time; therefore, interrupts should 
	      be inhibited while these entries are tested.
     

				      3-12

     RTS-8 Executive Requests
     

	  2.  System table  entries  may  be  changed  only  through  RTS-8
	      Executive Requests.
     
     Symbols have been defined  in  the  system  parameter  table  to  make
     references into these tables symbolic.  The symbolic expressions which 
     yield the address of the system table entries for task N are:
     
	       N+TFTABL	      Task Flags Table Entry for task N;  if  zero,
			      task N is runnable.

	       N^2+MSGTBL     Input Message Queue Header  for  task  N;  if
			      zero, task N has no messages in its queue.

	       N^4+TSTABL     First Word of Task State Table Entry for task
			      N.
     
     For example, for a task to determine whether it had  messages  in  its
     input queue without issuing a RECEIV request, the code would be:
     
	     CDF 0 	     /EXEC TABLES IN FIELD 0
	     IOF 	     /TURN INTERRUPTS OFF
	     TAD I (TASK^2+MSGTBL
	     SNA CLA 	     /ANY MESSAGES?
	     JMP NONE 	     /NO
	     ION 	     /YES
     
     The code at NONE must eventually turn interrupts back on.
     



























     
				      3-13





       				   CHAPTER 4

    			       RTS-8 SYSTEM TASKS

      The sources of the System Tasks are supplied with  the  RTS-8  system.
      The  tasks  referred  to  as "handlers" are completely message-driven,
      i.e., when idle they are in the Message Wait state.  Other tasks  send
      these  handlers  I/O  request messages, and when the handler completes
      the I/O operation it sets the Event Flag associated with  the  request
      message and issues another RECEIVE ER.


      4.1  CLOCK HANDLER

     This task can be assembled to  handle  any  of  four  hardware  clocks
     (DR8EA, DK8EC, DK8EP, KW12). It accepts requests (in the form of RTS-8
     messages) to perform actions after a specified time has  elapsed.  The
     clock  handler  uses  an  interval  queue  (whose  length  is fixed at
     assembly time by the definition of the symbol CLKQLN in the  parameter
     file) to keep track of its pending requests.

     The format of a clock message is:

	      CLKMSG,  ZBLOCK 3	       /3 WORDS RESERVED FOR RTS-8
		       COMMAND+TASKNO  /TASKNO=0 MEANS TASKNO=SENDING TASK
		       TIMEHI
		       TIMELO
		       EXTRA1
		       EXTRA2

     The words TIMEHI and TIMELO specify a time interval from  the  present
     time  in  terms  of  "system  ticks".  The number of system ticks in a
     second is specified by the user in the RTS-8 parameter  file  via  the
     parameter  SHERTZ.   The  hardware  tick rate (in ticks per second) is
     specified by the parameter HERTZ.  HERTZ must be an exact multiple  of
     SHERTZ.   For example, the parameters for a line-frequency clock might
     be:

		      DECIMAL
		      HERTZ= 60
		      SHERTZ= 10

     indicating that only 1/10 second resolution is necessary in the  clock
     handler.   Note  that  the  maximum interval which can be expressed in
     TIMEHI and TIMELO is (2**24)/SHERTZ seconds.  This is approximately  3
     days if SHERTZ=60.

     The clock handler is referred to by other RTS-8 system tasks  via  the
     symbol  CLOCK.   This  symbol should be defined in the RTS-8 parameter






    				      4-1

     RTS-8 System Tasks


     file to be equal to the clock handler's Task  Number.   It  should  be
     undefined if no clock handler is to be included in the system.

     COMMAND is the type of request and has the following meanings:

	  0000 - POST the event flag CLKMSG after  the  specified  interval
		 elapses. TASKNO, EXTRA1, and EXTRA2 are ignored.

	  1000 - POST CLKMSG immediately. Execute a  RUN  ER  on  the  task
		 specified  by TASKNO after the specified interval elapses.
		 EXTRA1 and EXTRA2 are ignored.

	  2000 - POST CLKMSG immediately.  DERAIL  the  task  specified  by
		 TASKNO  into  a  subroutine  whose address is specified in
		 EXTRA1 after the specified interval  elapses.   EXTRA2  is
		 ignored.

	  3000 - POST CLKMSG immediately.  Execute a RUN  ER  on  the  task
		 specified  by TASKNO after the specified interval elapses,
		 and re-queue this command with the parameters  EXTRA1  and
		 EXTRA2 in place of TIMEHI and TIMELO.  This has the effect
		 of running the specified task periodically with  a  period
		 specified by EXTRA1 and EXTRA2.

	  7000 - Delete from the clock queue  all  requests  for  the  task
		 specified  by  TASKNO.  TIMEHI, TIMELO, EXTRA1, and EXTRA2
		 are ignored.  POST CLKMSG.

     The clock handler also maintains the current  time-of-day  (in  system
     ticks  until  midnight), in locations TODH (high-order) and TODL (low-
     order) in Page 0 of Field  0.   When  this  time-of-day  reaches  zero 
     (i.e.,  at  midnight), it is reset to the quantity -(SHERTZ*86400) (24 
     hours until midnight) and an OS/8-format date word in location DATE in 
     Page 0 of Field 0 is incremented by one day.

     Note that in order for the quantity SHERTZ*86400 to be contained in 24
     bits,  SHERTZ must be less than 192.  If SHERTZ is larger, an assembly
     error will result while assembling the clock handler.


     4.1.1  Examples of Clock Handler Calls

			 CAL		/WITH A 50HZ SYSTEM TICK RATE,
			 SENDW		/THIS CAUSES THE CURRENT TASK
			 CLOCK		/TO "GO TO SLEEP" FOR 2 SECONDS.
			 SLEEPM
			 .
			 .
		SLEEPM,  ZBLOCK 3	/RTS-8 MESSAGE OVERHEAD
			 0		/SET EVENT FLAG AFTER INTERVAL
			 0; 144		/INTERVAL IS 100 (DECIMAL) SYSTEM
					/TICKS




				      4-2

     RTS-8 System Tasks


     Note that by changing the 144 to the assembler expression 2^SHERTZ the
     above sequence becomes configuration-independent.

			 CAL		/RUN THE TASK REPORT ONCE
			 SEND		/EVERY HOUR, INDEFINITELY,
			 CLOCK		/ASSUMING A 50HZ SYSTEM TICK RATE
			 RUNMSG
			 .
			 .
		RUNMSG,  ZBLOCK 3	/RTS-8 MESSAGE OVERHEAD
			 3000+REPORT	/RUN REPORT AFTER SPECIFIED
					/INTERVAL AND PERIODICALLY
					/THEREAFTER,
			 0;1		/FIRST RUN IS ALMOST IMMEDIATELY
					/(1/50 SECOND)
			 53;7440	/PERIOD BETWEEN RUNS IS 180000
					/(DECIMAL) SYSTEM TICKS = 3600
					/SECONDS = 1 HOUR.


	4.2  TERMINAL HANDLER

     The RTS-8 terminal handler handles a single terminal in either line or
     character mode.  Input in line mode is terminated by a carriage return
     or an ALTMODE character and may be edited  using  the  RUBOUT  and  ^U
     characters.   The  RUBOUT  character  deletes the last valid character 
     typed and prints a backslash;  the ^U  character  deletes  the  entire 
     line and returns the carriage.  Character mode input is not echoed and 
     is terminated by overflow of a specified character count.  If multiple
     terminals  are to be handled, multiple copies of this terminal handler
     must be assembled.  Assembly parameters in the  body  of  the  handler
     specify  which  device  codes  the  handler  should  use to access its
     terminal and whether the handler is to be a "console" terminal handler
     (the  console  terminal handler invokes the MCR whenever a ^C is typed 
     on the keyboard;  non-console terminal handlers treat ^C as any  other
     character).  The parameters edited into the distributed version of the
     terminal handler assemble it to handle the PDP-8 console terminal as a
     "console" device.

     A message to the terminal handler performs a  (possibly  null)  output
     operation  followed (optionally) by an input operation.  The format of
     messages to the terminal handler is:

	       TTYMSG, ZBLOCK 3
		       PACK+CRLF+IND+LINE+ASSIGN+LENGTH
		       INBUF
		       OUTTXT

     where:

		PACK   =0     If output  text  is  in  6-bit  packed  ASCII
			      format.
		       =4000  If output text  is  in  unpacked  ASCII  (one
			      character per word, zero word terminates).


				      4-3

     RTS-8 System Tasks

		CRLF   =0     If output message should  be  followed  by  a 
			      carriage return/line feed.
		       =2000  If output message should not be followed by a
			      carriage return/line feed.

		IND    =0     If OUTTXT is the first  word  of  the  output 
			      text.
		       =1000  If OUTTXT points to the  first  word  of  the
			      output text.

		LINE   =0     If input  is  in  line  mode  (terminated  by 
			      carriage return or ALTMODE).
		       =400   If input is  in  character  mode  (terminated 
			      after  "LENGTH"  input  characters  have been 
			      read).

		ASSIGN =0     For normal I/O operations.
		       =200   "Assigns" the terminal handler  to  the  task
			      specified  by  the  LENGTH  field.  This will 
			      cause the terminal  handler  to  only  accept 
			      messages from the specified task.  If another 
			      task tries to SEND a message to the  terminal 
			      handler  while  it  is  assigned, the message 
			      will be  placed  in  the  terminal  handler's 
			      Message  Input  Queue but will not be removed 
			      for processing by the terminal handler  until 
			      the  assignment  is  released.   The  task to 
			      which the terminal handler  is  assigned  can 
			      release  the  assignment by sending a message 
			      assigning the terminal handler to task number 
			      0.   No  I/O  operation  is  performed  by an 
			      assignment message.

		LENGTH	      Is a  seven-bit  field  which  specifies  the
			      maximum  size of the input buffer if input is
			      in line mode, the  number  of  characters  to
			      input  if  input  is in character mode, and a
			      task number if the ASSIGN  bit  is  set.   If
			      input  is in line mode and there are LENGTH-1
			      characters in the  input  buffer,  characters
			      other  than  carriage return, ALTMODE, RUBOUT
			      and ^U will not be accepted or echoed.

		INBUF	      Is a pointer to the input buffer;  if  it  is
			      zero, no input is taken.  The input buffer is
			      filled with input characters packed  one  per
			      word with the parity bit forced on.  If input
			      is in line mode, the last  character  of  the
			      line  is  followed  by  a  zero  word  (if  a
			      carriage return terminated  the  line)  or  a
			      negative   word   (if  an  ALTMODE  character
			      terminated the line).

		OUTTXT	      Is either the first word of the  output  text
			      string  (if  IND=0) or a pointer to the first
			      word of the output string (if IND=1000).

				      4-4

     RTS-8 System Tasks


     4.2.1  Examples of Terminal Handler Messages

	       HIYA,   ZBLOCK 3      /RTS-8 MESSAGE OVERHEAD
		       0 	     /PACKED TEXT, END WITH CR/LF
		       0 	     /NO INPUT
		       TEXT /HELLO/  /TEXT TO BE OUTPUT

     Sending the above message to the terminal handler prints HELLO on  the
     terminal.

	       QUEST,  ZBLOCK 3	     /RTS-8 MESSAGE OVERHEAD
		       2060	     /PACKED TEXT, NO CR/LF,
				     /48-CHARACTER INPUT LIMIT
		       ANSWER	     /POINTER TO INPUT BUFFER
		       TEXT /TYPE THE ANSWER:/

     Sending the above message to the  terminal  handler  prints  TYPE  THE
     ANSWER:   on  the  terminal and inputs a reply without first returning 
     the carriage.  The answer obtained from the  above  message  could  be 
     printed on the terminal by sending the following message:

	       TYPANS, ZBLOCK 3      /THE USUAL OVERHEAD
		       5000	     /UNPACKED TEXT, INDIRECT, WITH CR/LF
		       0	     /NO INPUT
		       ANSWER	     /POINTER TO OUTPUT TEXT


     4.3  LINE PRINTER HANDLER

     The RTS-8 line printer handler outputs to an LE8,  LS8E  or  LV8  line
     printer.   The  format  of  messages  to  the  line printer handler is
     identical to the format of messages to the terminal handler,  but  the
     INBUF word and the LINE bit are ignored (the INBUF word must, however,
     be present).  Refer to Chapter 7  for  an  example  showing  the  line 
     printer handler message.


     4.4  MASS STORAGE HANDLERS

     This group of handlers all accept the same request message  format  to
     read  or  write blocks on various mass storage devices.  Handlers have
     been written for TC08 DECtape, DF32 and RF08 fixed-head disks, and RK8
     and RK8E moving-head disks.

     The format of messages to mass storage handlers is:

	       MSMESG, ZBLOCK 3
		       UNIT
		       RW + PAGES + FIELD
		       BUFADD
		       BLOKNO
		       STATUS




				      4-5

     RTS-8 System Tasks


     where:

	       UNIT    Is the number of the unit on which the operation  is 
		       to be performed.
		       DF32 and RF08 disks consist of only one unit.
		       TC08 DECtape has  units  0-7  corresponding  to  its
		       physical units 0-7.
		       RK8 disk has units 0-3 corresponding to its physical
		       units 0-3.
		       RK8/E disk has units 0-7. Units  0-3  correspond  to 
		       the  outer  (lower  track  number)  half of physical 
		       units 0-3, and units 4-7  correspond  to  the  inner 
		       (higher track number) half of physical units 0-3.

	       RW      Is  0  for  a  read  operation,  4000  for  a  write
		       operation.

	       PAGES   Specifies  the  number  of   (128-word)   pages   to 
		       transfer,  times 100(8)(i.e., if PAGES=2000 it means 
		       transfer 20(8) pages  or  2048  words;  if  PAGES=0, 
		       40(8) pages or 4096 are transferred).

	       FIELD   Is the PDP-8  field  in  which  the  transfer  takes 
		       place,  times  10(8)  i.e., if FIELD=30 the transfer 
		       takes place in field 3).

	       BUFADD  Is  the  starting  address  of  the  buffer  to   be
		       transferred.

	       BLOKNO  Is the block number on the  device  from  which  the
		       transfer  will  begin.   All  devices are assumed to 
		       have 256-word blocks.  On  DECtape,  the  first  128 
		       words  of  each  of  an  even/odd  pair  of 129-word 
		       DECtape records are considered to be a block.

	       STATUS  Is a word which is set by the handler on  completion 
		       of  the  operation.   It  will contain a zero if the
		       operation was successful, otherwise it will  contain 
		       a  non-zero  quantity  which  is  the  device status
		       register.  Tasks which use the mass storage handlers
		       should  test  this  word after the I/O operation has
		       been completed (i.e., after the Event Flag has  been
		       POSTed)  to  determine if any errors occurred during
		       the transfer.  All RTS-8 mass storage handlers retry
		       operations  three  times  if  errors are encountered
		       before setting the STATUS word non-zero.

     Note that the middle three words  of  a  message  to  the  RTS-8  mass 
     storage  handlers  are  identical  to the arguments to an OS/8 handler 
     which performs the same operation.






				      4-6

     RTS-8 System Tasks


     4.4.1  Example of Mass Storage Handler Call

		       CAL
		       SENDW
		       DTA 	   /SEND A MESSAGE TO THE DECTAPE HANDLER
		       DTAMSG      /AND WAIT FOR COMPLETION
		       TAD STATUS  /CHECK THE STATUS OF THE OPERATION
		       SZA CLA
		       JMP ERR	   /BAD - GO TO ERROR ROUTINE

	       DTAMSG, ZBLOCK 3    /RTS-8 MESSAGE OVERHEAD
		       4	   /DECTAPE UNIT 4
		       4210	   /WRITE 256 WORDS FROM FIELD 1
		       BUFFER	   /LOCATION BUFFER
		       55	   /INTO BLOCK 55 (RECORDS 132 & 133)
	       STATUS, 0	   /STATUS OF OPERATION STORED HERE


     4.5  POWER FAIL TASK

     The Power Fail  Task  provides  the  mechanism  by  which  the  system 
     recovers  from power failure.  If the power-fail/auto-restart hardware 
     option is present and if the system parameter PWRFAL was equated to  a 
     non-zero value, the SPL (Skip on Power Low) instruction is included in 
     the interrupt skip chain.   If  a  power  low  condition  occurs,  the 
     processor  state  is  saved  and  the processor is halted.  When power 
     comes back, the processor state is  restored  and  an  Event  Flag  is 
     POSTed  which  wakes  up  the  Power  Fail  Task.  The Power Fail Task 
     restores the clock, console terminal and OS/8  terminal  if  they  are 
     present, and also performs an action for each task in the system based 
     on the contents of an internal table.  Each task has a one-word  entry 
     in this table, which contains:

	  0	  If nothing should be done for this task (default value)

	  -1	  If the EFWT (Event Flag Wait) bit should  be  cleared  in
		  the Task Flags Table entry for this task (i.e., this task
		  should be taken out of Event Flag Wait)

	  ADDR	  If the task should be DERAILed to location  ADDR  in  the
		  field in which it is executing as well as having its EFWT
		  bit cleared.

     Each task in the system may alter its entry in the Power  Fail  Task's
     table  by  sending a message to the Power Fail Task. The format of the
     message is:

	       PWRMSG, ZBLOCK 3         /RTS-8 OVERHEAD
		       WORD

     where:

	  WORD	       is the new contents of the Power Fail  Task's  table
		       entry for the sending task.


				      4-7

     RTS-8 System Tasks

     4.6  OS/8 SUPPORT TASK

     This task supports the execution of the OS/8  operating  system  as  a 
     task  under RTS-8.  OS/8 is run in the top two (or more) memory fields 
     under control of the KT8/E (standard on PDP-8/E, /F, or /M with 8K  or 
     more  of core memory) or TSS-8 time sharing hardware option.  The OS/8 
     Support task is configured at  system  startup  time  to  establish  a 
     correspondence between OS/8 devices and RTS-8 handler tasks.  Terminal 
     input and output from OS/8 is ring-buffered by several  characters  to 
     minimize  input  loss  due to usurpation of the CPU by tasks of higher 
     priority.  Because of the large number of trapped CDF instructions  in 
     OS/8  and  its  CUSPs, response time is slower than a stand-alone OS/8 
     system but is still quite reasonable.

     Several parameters in the system parameter file control  the  assembly 
     of the OS/8 support task.  They are:

	       OSFLDS  Defined as the number of fields to be  dedicated  to 
		       OS/8.  OSFLDS=2 specifies 8K for OS/8.

	       OSKBDV  Set equal to the  keyboard  IOT  code  of  the  OS/8
		       terminal (OS/8 requires its own dedicated terminal).
		       Example:  OSKBDV=03 will use  the  console  terminal
		       keyboard for OS/8.

	       OSTTDV  Set equal to the teleprinter IOT code  of  the  OS/8
		       terminal.
		       Example:    OSTTDV=04   will   use    the    console 
		       teleprinter for OS/8.

	       OSNULL  Specifies how many null  characters  must  follow  a 
		       line-feed  character  on  the  OS/8  terminal.  This 
		       allows high-speed VT05 terminals to be used as  OS/8
		       terminals.  For standard Teletypes and parallel LA30
		       terminals this parameter should be set to zero.

	       OSSYSD  Equated to the task number of the OS/8 system device
		       handler.
		       Example: OSSYSD=DTA would specify DTA0 as  the  OS/8
		       system device.

     The OS/8 system which runs under the OS/8 Support  Task  may  run  all 
     OS/8 CUSPs except BUILD and FRTS, the FORTRAN IV run-time system.  All
     references to  the  keyboard  and  teleprinter  are  diverted  to  the
     specified  OS/8  keyboard  and teleprinter.  References in OS/8 to the 
     LE8, LS8E or LV8 line printers are diverted to the RTS-8 line  printer
     handler  if  the  system parameter LPT is defined;  otherwise they are
     executed directly by the Support Task.  References  to  the  following 
     OS/8  device names will be diverted to the corresponding RTS-8 handler 
     if one is defined:

	       DTA0-DTA7
	       RKA0-RKA3
	       RKB0-RKB3
     ___________________________
     1) Teletype is a registered trademark of the Teletype Corporation.

				      4-8

     RTS-8 System Tasks


     In addition, the OS/8 handlers SYS and DSK are diverted to the handler
     specified  by  the parameter OSSYSD. Other references to I/O under the
     supported OS/8 system may cause the OS/8 support task  to  hang  in  a
     loop.


     4.7  OS/8 FILE SUPPORT TASK

     The OS/8 File Support Task (hereafter  referred  to  as  OS8F)  allows 
     other  tasks  to lookup, create, and delete files in OS/8 directories. 
     It is included in the same source file as the OS/8 Support  Task,  but 
     may  be assembled independently of that task (depending on which tasks 
     were defined in the system parameter file).  The format of messages to 
     OS8F is:

	       OSFMSG, ZBLOCK 3 /RTS-8 OVERHEAD
		       DEVHND^10+UNIT+FUNCT
		       FILPTR 
		       STATUS 
		       BLOKNO
		       LENGTH

     where:

	       DEVHND	       Is the task number of the  handler  for  the
			       desired device.

	       UNIT	       Is the unit number on which the operation is
			       to be performed.

	       FILPTR	       Is a pointer to a four-word  filename.   The
			       PAL8  pseudo-op  FILENAME  may  be  used  to
			       generate these filenames.

	       FUNCT 	       Represents the function to be performed.  It
			       may have the following values:

				    0     Look up the specified  file  name
					  and  return  its  starting  block
					  number   in    BLOKNO   and   its
					  (positive) length in LENGTH.

				    2000  Enter  the  specified  file  name
					  into the first empty space on the
					  device whose length is  equal  to
					  or  exceeds  the value in LENGTH.
					  Return the starting block  number
					  of  the new file in BLOKNO.  If a
					  file of the same name  previously
					  existed   on  the  device  it  is
					  deleted.  The value of LENGTH  is
					  unchanged.

				    4000  Delete the specified file name.

	
				      4-9

     RTS-8 System Tasks

	       STATUS	       Describes the final status of the operation
			       as follows:

				    0	  Operation successful.
				    1	  File  not  found  on  Lookup   or
					  Delete.
				    2	  No room for file on Enter.
				    >2	  I/O error  occurred  -  value  is
					  hardware error status of device.
				    -1	  Invalid directory on device.

     If both OS8F and the OS/8 Support Task are present  in  a  system,  an
     interlock  is  set  up  to  prevent simultaneous updating of directory
     blocks by both systems.  Because OS/8 tends to leave directory  blocks 
     in  core  for  long  periods  of  time,  this interlock scheme is very
     restrictive.  Before a Delete or Enter operation  is  performed,  OS8F
     waits until OS/8 is in a state in which:

	  1.  There  is  no  active  temporary  file  on  the  OS/8  device
	      corresponding to DEVHND and UNIT.

	  2.  OS/8 has just loaded the Keyboard Monitor,  Command  Decoder,
	      or USR into core.

     Lookup operations are not interlocked since they  do  not  modify  the
     directory.


     4.8  UDC HANDLER

     This handler gives the user the  capability  of  controlling  all  the
     various  types  of  UDC functional devices.  This handler performs two
     types of actions--immediate and deferred.  Immediate  actions  include
     reading  and  sending  analog  and  digital  values to appropriate UDC
     functional devices.  Deferred  actions  may  be  linked  to  specified 
     events  within  the  UDC (counters overflowing, switches being thrown) 
     and include:

	  1.  Run a specified task when the event occurs
	  2.  Set the Event Flag when the event occurs
	  3.  DERAIL a specified task when the event occurs

     The number of deferred requests which may be pending simultaneously is
     an assembly parameter of the handler.

     The UDC handler permits the following operations:

          1.  Analog Output - send a 10-bit value to an analog channel

	  2.  Analog Input - accept input from analog subchannel

	  3.  Digital Output - send a 12-bit value to a digital channel

	  4.  Digital Input - read a digital channel



				      4-10

     RTS-8 System Tasks


	  5.  Get Generic Code - determine the generic code for a specified
				 channel

	  6.  Enable Counter   - permit interrupts from a counter channel

	  7.  Read Counter     - read current value of counter channel

	  8.  Disable Counter  - disable interrupts from a counter channel

	  9.  Enable Contacts  - permit interrupts from a contact channel

	 10.  Change Of State  - find the current COS value for  a  contact
				 channel

	 11.  Disable Contacts - ignore interrupts from a contact channel

     Each operation is discussed in detail below, including the  format  of
     the message for specifying the operation.  As with all RTS-8 messages, 
     a 3-word header is required for use by the Executive.  Word 4  of  all 
     UDC   messages  specifies  one  of  the  eleven  UDC  operations.   An 
     additional one to five words is also required in the  UDC  message  to 
     completely  specify  the  operation.   Word  10  of  all  UDC messages 
     contains the error state.


     4.8.1  AO  Analog Output

	       Format:   AO channel number
			 subchannel & value

     Channel number is the analog output channel. The subchannel and  value
     word  is formed by the subchannel (0-3) in bits 0 and 1 and the 10-bit
     value in bits 2-11.  For example,  a  message  for  an  analog  output
     operation:

	       AOEX, ZBLOCK 3
		     AO		/ANALOG OUTPUT
		     23		/CHANNEL 23
		     4614	/SUBCHANNEL 2, VALUE 614
		     ZBLOCK 3
	       AOER, 0		/ERROR INDICATOR


     4.8.2  AI  Analog Input

	       Format:   AI channel
			 subchannel & gain
			 answer


     where channel is the analog input channel.  The  subchannel  and  gain 
     word need only specify the gain in bits 1-3 and the subchannel in bits 
     9-11.  The handler automatically sets bits 0 and 7 (enable  conversion 
     and read control register).  The result is put in answer.


				      4-11

     RTS-8 System Tasks


	        AIEX, ZBLOCK 3
		      AI	/ANALOG INPUT
		      17	/CHANNEL 17
		      3		/SUBCHANNEL 3, GAIN 0
	       AIANS, 0		/RESULT HERE
		      ZBLOCK 2
	       AIERR, 0		/ERROR INDICATOR

     It is the user's responsibility to ensure for each major channel  that
     there  is  sufficient  time  (approximately 250 microseconds) for each
     subchannel conversion to be completed before another is indicated.  In
     general,  it may be helpful if all A/D conversions for a major channel
     are initiated from the same task.


     4.8.3  DO  Digital Output

	       Format:   DO
			 channel
			 value

     Channel is a legal digital output channel and value is the  number  to
     be output.  For example:

	       DOEX, ZBLOCK 3
		     DO		/DIGITAL OUTPUT
		     20		/CHANNEL 20
		     7777	/VALUE = 7777
		     ZBLOCK 3
	       DOER, 0		/ERROR INDICATOR


     4.8.4  DI  Digital Input

	       Format:   DI
			 channel
			 result

     Channel is the appropriate  digital  input  channel  and  result  will
     contain the value of the channel when read.  For example:

	       DIEX,  ZBLOCK 3
		      DI	/DIGITAL INPUT
		      27	/CHANNEL 27
	       DIANS, 0		/VALUE OF CHANNEL 27 WILL BE PUT HERE
		      ZBLOCK 3
	       DIER,  0		/ERROR INDICATOR


     4.8.5  GC  Generic Code

	       Format:   GC
			 channel
			 result


				      4-12

     RTS-8 System Tasks

     The generic code of the specified  channel  is  put  in  result.   For
     example:

	       GCEX,  ZBLOCK 3
		      GC	/DETERMINES GENERIC CODE
		      27	/CHANNEL 27
	       GCANS, 0		/GENERIC CODE PUT HERE
		      ZBLOCK 3
	       GCER,  0		/ERROR INDICATOR


     4.8.6  EC  Enable Counter

	       Format:   EC 
			 channel
			 initial value
			 reload value
			 event action
			 address

     Channel is the counter channel to be enabled,  initial  value  is  the
     first  value  to  be loaded into that channel, and reload value is the
     value with which to reload the channel  after  every  event.   If  the 
     reload  value is 0, the counter is not reloaded.  The event action and 
     address words specify what is to happen when the  counter  interrupts. 
     There are three mutually exclusive possibilities, indicated by setting 
     the appropriate bit in the event action word:

	       bit 0 = 1 =    set  event  flag  of  this   job;    continue
			      execution  of this job when the event occurs. 
			      Address word not used.

	       bit 1 = 1 =    run a task; run task specified by  bits  4-11 
			      of event action word.  Address word not used.

	       bit 2 = 1 =    DERAIL the task; the  address  word  is  only 
			      used  by  the  DERAIL operation and specifies 
			      the address of the DERAIL  subroutine.   That 
			      subroutine  must  be in the same field as the 
			      calling task. 

     Bit 3 indicates how many times the action is to occur:

	       bit 3 = 1 =    do action just once. If bit 3 = 0,  specified
			      action is performed after each interrupt.

     Several enable counter examples follow:

	       ECEX1,  ZBLOCK 3
		       EC	/ENABLE COUNTER
		       4	/CHANNEL 4
		       7700	/INITIAL VALUE OF 7700
		       7710	/RESET TO 7710 AFTER EACH EVENT
		       4000	/POST EVENT FLAG ON EVENT
		       0	/UNUSED
	       ECER1,  0	/ERROR INDICATOR

				      4-13

     RTS-8 System Tasks

	       ECEX2,  ZBLOCK 3
		       EC	/ENABLE COUNTER
		       4	/CHANNEL 4
		       1205	/INITIAL VALUE OF 1205
		       0	/DON'T RESET
		       2016	/RUN TASK 16 ON EVENT
		       0	/UNUSED
	       ECER2,  0	/ERROR INDICATOR

	       ECEX3,  ZBLOCK 3
		       EC	/ENABLE COUNTER
		       5	/CHANNEL 5
		       10	/INITIAL VALUE OF 10
		       7700	/RESET TO 7700
		       1015	/DERAIL TO TASK 15	
		       5620	/AT LOCATION 5620
	       ECER3,  0	/ERROR INDICATOR


     4.8.7  RC  Read Counter

	       Format:   RC
	    		 channel
	    		 result

     where channel is the counter channel whose  current  value  is  to  be 
     read.  That value is placed in result. For example:

	       RCEX,  ZBLOCK 3
		      RC	/READ COUNTER
		      6		/CHANNEL 6
	       RCANS, 0		/VALUE OF CHANNEL 6 PUT HERE
		      ZBLOCK 3
	       RCER,  0		/ERROR INDICATOR


     4.8.8  DC  Disable Counter

	       Format:   DC
	    		 channel

     where channel is the counter channel from which interrupts are  to  be
     ignored.  For example:

	       DCEX, ZBLOCK 3
		     DC		/DISABLE COUNTER
		     6		/CHANNEL 6
	       DCER, ZBLOCK 4
		     0		/ERROR INDICATOR


     4.8.9  ECT  Enable Contacts

	       Format:   ECT 
	    		 bit & channel 
	    		 event action
	    		 address
	    			      4-14

     RTS-8 System Tasks


     where the bit & channel word specifies the bit on the contact  channel
     from  which  to  enable interrupts.  Channel is specified in bits 4-11 
     and the contact bit is packed in bits  0-3  as  a  value  from  0 - 13 
     (octal).

     Event action and address are specified in the same manner  as  in  the
     enable counter function.  For example:

	       ECTEX1,  ZBLOCK 3	
			ECT	      /ENABLE CONTACTS
			5401	      /FROM BIT 13(8) OF CHANNEL 1
			2013	      /RUN TASK 13 AFTER AN EVENT OCCURS
			ZBLOCK 3
	       ECTE1R,  0	      /ERROR INDICATOR

	       ECTEX2,  ZBLOCK 3
			ECT	      /ENABLE CONTACT
			1001	      /FROM BIT 2 OF CHANNEL 1
			4000	      /ON 1ST OCCURRENCE OF EVENT, POST
				      /EVENT FLAG
			ZBLOCK 3
	       ECTE2R,  0	      /ERROR INDICATOR


     4.8.10  CS  Change of State

	       Format:   CS
			 channel
			 result

     where channel is the contact channel whose  current  change  of  state
     value is to be placed in result.  For example:

	       COSEX,   ZBLOCK 3
			CS	      /READ COS
			1	      /CHANNEL 1
	       COSANS,  0	      /RESULT HERE
			ZBLOCK 3
	       COSER,   0	      /ERROR INDICATOR


     4.8.11  DCT  Disable Contacts

	       Format:   DCT 
			 bit & channel

     where bit & channel is specified as in enable contact, that  is,  bits 
     0-3  specify the bit (0 - 13(octal)) and bits 4-11 specify the channel
     to be disabled.  For example:

	       DCTEX,   ZBLOCK 3
			DCT	      /DISABLE CONTACTS
			5401	      /FROM CHANNEL 1, SUBCHANNEL 13(8)
			ZBLOCK 4
	       DCTANS,  0	      /ERROR INDICATOR

				      4-15

     RTS-8 System Tasks


     4.8.12  UDC  Assembly Parameters

     The UDC handler has several assembly parameters that must be specified
     by the user to indicate his UDC configuration.  They are:

	       RINGBF	      Number of interrupts that can  be  stored  in
			      ring buffer.

	       NCNTR	      Number of counter channels.

	       NCNTC	      Number of contact channels.

	       NAD	      Number of analog input channels.

	       FCTR	      Address of first counter.  The counters  must
			      be at contiguous channels.

	       FCT	      Address of first contact.  Contacts must also
			      be at contiguous channels.

	       FAD	      Address of first A/D channel.   Analog  input
			      channels must be at contiguous channels.

     These parameters are used mainly  to  specify  the  sizes  of  several 
     tables in the UDC handler, allocated as 30(8) words/contact channel, 3 
     words/counter channel, and 16(8) words/analog channel.  Note that  the 
     UDC  handler currently assumes that the handler and all its tables are
     entirely within the same data field (although the  user  could  easily
     reprogram this).

     When considering the size of RINGBF, keep in mind that when the buffer
     is  full,  UDC  interrupts  are  disabled  until  there is room in the 
     buffer. Each interrupt requires two  entries  in  the  buffer;   i.e., 
     actual buffer size is 2 * RINGBF.


     4.8.13  UDC  Error Conditions

     To indicate error conditions, a value is placed in the tenth  word  of
     the task's message by the UDC handler.  The values and meanings are:

	  1.  Illegal generic code for specified channel and operation

	  2.  Channel or subchannel value not valid

	  3.  Illegal function code

     It is the user's responsibility to  initialize  and  check  the  error 
     word.  A no error condition puts a 0 in this location.

     Only errors encountered at non-interrupt time  are  returned  in  this
     manner,  thus  they may also indicate a faulty UDC hardware functional
     device.  Generic codes of 0 or 1 encountered  at  interrupt  time  are
     ignored.


				      4-16

     RTS-8 System Tasks


     4.9  CASSETTE HANDLER

     This handler (CSA) allows the user to read and  write  variable-length
     records  on  DECassettes, as well as perform various special functions
     (rewind, write end-file, etc).

     There are two general categories of cassette operation:

	  1.  Handler functions - read and write

	  2.  Utility functions - rewind, backspace file  gap,  write  file 
	      gap, backspace block gap, and skip to file gap

     It is up to the user to call these functions in a meaningful sequence.
     For both functions, word 1 of the message defines the cassette unit in
     bits 9-11 and function in bit 0 (where bit 0 = 0 means a utility  call
     and bit 0 = 1 means a handler call). For a handler function, four more 
     words are required:

	       word 2  bit    0 = 0 - read
			      0 = 1 - write
		       bits 6-8     - field of buffer
		       bit   11	    - do not store data (applicable to read 
				      only)
	       word 3		    - buffer address
	       word 4		    - record size in bits 4-11
	       word 5		    - status return

     Cassette conventions specify a record size of 200 bytes, but the  user
     may use any size up to 377, according to his requirements.  The buffer
     specified by the message cannot cross field boundaries.   For  a  read
     operation,  the  buffer  is optional (although its word in the message
     must be included), according to bit  11  of  word  2.   The  non-store
     capability  can  be  used  for  advancing through a long file.  Word 5
     contains the contents of status register B, which is  defined  by  the  
     bit setting as follows:

			      Bit     Meaning			      ___     _______

			       4  = CRC /block error
			       5  = timing
			       6  = EOT/BOT
			       7  = EOF
			       8  = drive empty
			       9  = read/write
			       10 = write lockout
			       11 = ready

     Word 5 should be examined by the user at  the  end  of  each  cassette
     operation to check for errors encountered.

     For example, to write 100 words from a buffer  starting  at  21200  to
     cassette unit 3, the message is:



				      4-17

     RTS-8 System Tasks


	      MSG1, ZBLOCK 3
		    4003	/HANDLER OPERATION ON UNIT 3
		    4020	/WRITE FROM FIELD 2 THE
		    1200	/BUFFER AT 1200 WHICH IS
		    0100	/100 BYTES LONG
		    0000	/STATUS RETURN

     To read and not store 200 words from unit 2, the message is:

	      MSG2, ZBLOCK 3
		    4002	/HANDLER OPERATION ON UNIT 2
		    0001	/READ AND DON'T STORE
		    0000	/UNUSED
		    0200	/200 BYTES
		    0000	/STATUS RETURN

     For a utility operation, the format of the rest of the message is:

	       word 2  (function in bits 6-8): 10 = Rewind
					       30 = Backspace file gap
					       40 = Write file gap
					       50 = Backspace block gap
					       70 = Skip to file gap

	       word 3 Status return

     For example, to request a rewind on unit 1, the message is:

	      MSG3, ZBLOCK 3
		    0001      /UTILITY OPERATION ON UNIT 1
		    0010      /REWIND
		    0000      /STATUS RETURN

     If an error is encountered, the operation is retried 3  times,  except
     write lock out on a write operation or error while reading CRC.

     The CAPS-8 USER'S MANUAL (DEC-8E-OCASA-A-D) is suggested  reading  for
     users who are unsure of cassette conventions.


     4.10  CASSETTE LABEL SUPPORT HANDLER

     This handler supports the DEC standard cassette format and allows  the
     calling  task  to  lookup and enter files on cassettes in that format.
     This "handler" requires the cassette handler to perform the actual I/O
     operations involved.

     The cassette operations ENTER, LOOKUP and CLOSE are performed  by  the
     task  CSAF  which in turn calls the cassette handler (CSA).  ENTER and
     LOOKUP require the user to put appropriate  information  in  a  record
     header  area with which CSAF performs the file operations.  The header
     area must be  at  least  forty  words  long  and  cannot  cross  field
     boundaries.  The format of a CSAF message is:



				      4-18

     RTS-8 System Tasks

	       word 1 bit 0 = 1 = ENTER
		      bit 1 = 1 = LOOKUP
		      bit 2 = 1 = CLOSE
		      bits 9-11 = unit

	       word 2 Address of header for ENTER and LOOKUP
		      Status return for CLOSE

	       word 3 Field of header for ENTER and LOOKUP

	       word 4 Status return for ENTER and LOOKUP

     In all cases, the status return is the contents of Status Register B.

     For ENTER and LOOKUP, the format of the header area must conform  with
     cassette  standards  (and  therefore  will be compatible with CAPS-8). 
     This format is:

		    Byte	       Use		    ____	       ___

		    0-5		   Filename

		    6-10	   Filename extension

		    11		   File type
					1 = ASCII
					0 = undefined

 		    12-13	   File record length.  Currently  word  12 
				   must be 0

		    14-15	   Unused

		    16-23	   Date (ASCII) specified as ddmmyy

		    24-37	   Unused

     For an ENTER operation, if a file  with  the  name  specified  in  the 
     header area is found on the specified unit, it is deleted.

     For a LOOKUP operation, the record  size  of  the  specified  file  is
     returned in location header+13 (byte 13).  If the file is not found or
     if an error occurs, this location contains 0.

     The CLOSE operation is automatically followed by a REWIND.

     Examples of messages follow.

	       MSG4, ZBLOCK 3
		     4000	/ENTER ON UNIT 0
		     6400	/INFORMATION IN HEADER STARTING AT 6400
		     0010	/OF FIELD 1
		     0000	/STATUS RETURN
	       MSG5, ZBLOCK 3
		     1003	/CLOSE ON UNIT 3
		     0000	/STATUS RETURN

				      4-19





    				   CHAPTER 5

    			    MONITOR CONSOLE ROUTINE


     The Monitor Console Routine (MCR) provides functions  which  the  user
     can  request  from  the console terminal in order to control, inspect,
     and (to some extent) debug his system.

     The MCR indicates that it is ready to  accept input  by  printing  the
     prompting character ">" on the terminal.  An MCR command consists of a
     command word (of which only the first 2  characters  are  significant)
     followed by arguments and terminated by either a carriage return or an
     altmode.  Commands may be a maximum of 40  characters  long.   If  the
     command is terminated by a carriage return, the MCR will return to the
     terminal  for  another command when it finishes processing the current
     command;  if an altmode terminates the command line the MCR  will  put
     itself  in  a  WAIT state when it finishes processing the command;  it
     can be brought out of this wait state by typing ^C  (CTRL  C)  on  the
     console  terminal.   When  the  MCR  has  prompted with its ">" and is
     waiting for  input,  no  other  RTS-8  tasks  can  use  the  terminal;
     therefore  if  the  terminal  is  used  for  something  other  than an
     exclusive MCR terminal (for instance for error logging)  the  operator
     should  type ^C, type his MCR command and terminate it with an altmode
     character.  This way the MCR will not tie up the terminal.



     5.1  MCR COMMAND ARGUMENTS

     Certain syntactic constructions are used as arguments to  several  MCR
     commands;  these are defined below:

	     ,		 A single comma or  a  single  space  may  be  used
			 interchangeably   to  separate  arguments  to  MCR
			 commands.

	     Task-ID	 A Task-ID is either a number or a name.  If it  is
			 a  number  it  represents  the internal RTS-8 Task
			 Number, which is also  the  task  priority,  of  a
			 task.   If it is a name, the first 4 characters of
			 the name are looked up  in  the  MCR's  Task  Name
			 table to produce a Task Number.

	     Time-of-day A Time-of-day is  of  the  form  hh:mm,  where  hh
			 represents  hours  past midnight and mm represents
			 minutes past hh:00.

	     Address	 An Address is an octal number from 1 to  5  digits
			 in length which represents a PDP-8 memory address.
			 If the address is less than 5 digits long the high
			 order digits are assumed to be 0.

	     Word	 A Word is an octal number from 1 to 4 digits long.


    				      5-1

     Monitor Console Routines

     A list of the  MCR  commands  follows.  In  the  header  line  of  the
     description,    the   significant  portion  of  the  command  word  is
     capitalized.  Optional arguments are enclosed in square brackets  ([])
     and   choices  will  be  embedded  in  parentheses  and  separated  by
     exclamation  points  (!).   Following  the  header  line  will  be   a 
     description  of  the  action  which the command causes and possibly an 
     example.

     Commands which are preceded by asterisks (*) are not  present  if  the
     symbol  CLOCK  is  not defined in the RTS-8 parameter file (indicating
     that there is no clock in the system).


     5.2  MCR COMMANDS


     5.2.1  * DAte [mm/dd/yyyy [,Time-of-day]]

     The date mm/dd/yyyy, if specified, becomes the system date.  Only  the
     last digit of the year is significant;  all others are ignored and 197
     assumed.  The  RTS-8  system  date  is  automatically  incremented  at
     midnight,  but  all months are treated as being 31 days in length.  If 
     the second argument is specified, the system Time-of-day is set  equal 
     to  it.   If  no  arguments  are specified, the current system date is 
     printed on the console terminal in the form mm/dd/197y.


     5.2.2  * TIme [Time-of-day]

     If a Time-of-day is specified, it becomes the system time-of-day.   If 
     no argument is specified the current system time-of-day is printed out 
     on the console terminal in the form hh:mm.


     5.2.3  NAme Task-ID,Newname

     The character  string  Newname  becomes  the  new  name  of  the  task 
     specified  by  Task-ID.   The  old name of that task (if any) is lost. 
     Newname may be any length but only the first 4 characters are  stored. 
     Newname  should  not be the name of any other task or an error message 
     will result.

     Examples:

	       >NAME 7 REPORT

     Task number 7 is given the name REPO.

	       >NAME REPORT, FOO

     Task number 7, which is known as REPO, is now known as FOO.






				      5-2

     Monitor Console Routines


				     NOTE

		   The MCR name  table  is  initialized  at
		   assembly  time  to  contain the names of 
		   any DEC-supplied tasks which are  listed 
		   in  the  parameter  file  (e.g.,  if the 
		   symbol CLOCK is defined in the parameter 
		   file  as CLOCK=2, task number 2 will get 
		   the name CLCK).  The MCR name table  may 
		   be  modified  by the user to include his 
		   own task names  permanently  by  editing 
		   the file MCR.PA after the label NMTBL.

     5.2.4  REquest Task-ID [,(@Time-of-day ! Interval)[,Interval]]

     Where Interval is of the form:

		   nH 	     n hours 
		   nM 	     n minutes
		   nS 	     n seconds 
		   nT 	     n system ticks

     This command requests a task to run immediately (if  only  Task-ID  is
     specified),  at  a  given  Time-of-day,  or  after  a  given Interval.
     Requesting a task clears the RUNWT bit in the Task Flags  Table  entry
     for  that  task.  If the third argument is specified the task is rerun
     periodically with the Interval given in  the  third  argument  as  the
     period.   If  the  parameter  CLOCK in the RTS-8 parameter file is not
     defined, the second and third arguments of this  command  are  ignored 
     and the given task is always run immediately.

     Examples:

	       >REQUEST X

     Will run task X immediately.

	       >RE FOO,@2:00

     Will run task FOO at 2:00 A.M. (if it is after 2 A.M., FOO will be run
     tomorrow at 2 A.M.).

	       >RE 5,lOM,5M

     Will run task number 5  10  minutes  from  now  and  every  5  minutes
     thereafter.

	       >REQ HIPR,1T,6T

     On a machine with a 60 Hz clock, this command will run the  task  HIPR
     immediately,  that  is, .016 seconds from now, and 10 times per second
     thereafter.




				      5-3


     Monitor Console Routines

				     NOTE

		   If, at the time the REQUEST  command  is
		   executed,  (which  may  be several hours
		   after it is typed in) the task specified
		   by  Task-ID  does not have the RUNWT bit
		   set in its Task Flags Table entry,  then
		   the   REQUEST   command   is   a  no-op.
		   Similarly, if the task  had  other  bits
		   set  besides  RUNWT  it  will not be run 
		   upon execution of the  REQUEST  command, 
		   but  will be run when the other blocking 
		   bits are cleared.


     5.2.5  STop Task-ID

     Suspends execution of the task specified by  Task-ID  by  turning  the 
     RUNWT  bit  on  in  the  Task Flags Table entry for that task.  A task 
     which has been stopped may be resumed via the REQUEST MCR command  (in 
     this instance it is easier to think of it as the resume MCR command).


     5.2.6  DIsable Task-ID

     Disables future execution of the specified task by setting the  ENABWT
     bit on in the Task Flags Table entry for that task.


     5.2.7  ENable Task-ID

     Clears the ENABWT bit in the Task Flags Table entry for the  specified
     task,  thus  enabling  it  to run.  If the ENABWT bit was not set, the
     command is a no-op.


     5.2.8  * CAncel Task-ID

     Cancels any clock queue entries involving the task specified by 
     Task-ID.  This includes any entries made by the MCR (from previous 
     timed REQUEST commands), entries involving the specified task made by 
     other tasks (e.g., a timed DERAIL) and entries made by the specified 
     task involving itself (e.g., a timed POST).  Note that in the case of 
     the timed POST the event flag will not be POSTed and the task may hang 
     up forever waiting for it.


     5.2.9  SYstat [Task-ID]

     If no argument is specified, the SYSTAT command prints a system status
     report.   Each  line  of  the report describes an existent task in the
     system.  The data printed for each task are its Task  Number/priority,
     its  name  (if  it has one), and what blocking bits are on in its Task
     Flags Table entry.  Each blocking bit is printed as a one-letter code,
     preceded by a space.  The possible one letter codes and their meanings
     are
				      5-4

     Monitor Console Routines

	      E Waiting for event flag
	      M Waiting for a message
	      O Waiting for an event flag or a message
	      R Waiting to be REQUESTed or RUN
	      S Waiting to be swapped in (not in Phase 1)
	      D Disabled
	      U USERWT bit set

     In addition, an asterisk is printed at the end of the line if the task
     has any messages waiting in its input queue.

     A more detailed status report on a single  task  may  be  obtained  by
     specifying  the  Task-ID  of  that  task  as an argument to the SYSTAT
     command.  The detailed report contains  all  the  information  in  the
     general report, followed by five octal words:

	      WORD 1 The location of the Task State Table entry  containing 
		     words 2-5.  This word is followed by a colon.
	      WORD 2 Task Link in sign bit, IF in bits 6-8, DF in bits 9-11. 
	      WORD 3 Task PC 
	      WORD 4 Task AC 
	      WORD 5 Task MQ

     Examples:

     A general SYSTAT command might produce  the  following  sample  output
     line:

	       13  CARD   E *

     meaning task number 13, named "CARD", is in Event Flag  Wait  and  has
     input messages pending.  The command:

	       >SYSTAT CARD 

     might produce the single line:

	       13  CARD   E *  1320: 0022  1741  0000  2525

     indicating that CARD is stopped at location 21741 with its AC and Link
     zero and 2525 in its MQ.

     The SYSTAT command may be left out of the MCR assembly by setting  the
     system  parameter  MCRSYS  equal  to zero in the RTS-8 parameter file,
     saving one page of code.


     5.2.10  OPen Address [,Count]

     If Count is not specified it is  assumed  to  be  1.  Count  locations
     starting  at Address are displayed in octal on the console terminal in
     the form:

	       lllll/ cccc

     The range of locations displayed may cross a field boundary.

				      5-5

     Monitor Console Routines


     5.2.11  EXamine Address [,Count ]

     The EXAMINE command is identical to the OPEN command.


     5.2.12  DEposit Address,Word [,Word] [,Word]....

     The  second  through  nth  arguments  are  deposited  into   core   at 
     consecutive   locations  starting  at  Address.   As  in  OPEN,  field 
     boundaries may be crossed.  For example:

	       >DEPOSIT 26132 7700,7200,50

     Deposits 7700 into location 26132, 7200 into location 26133, and  0050 
     into location 26134.


     5.2.13  POst Address

     POSTs the Event Flag at the specified address. This command is  useful
     when  debugging  a  system  for  simulating the effects of nonexistent 
     tasks or devices.


     5.2.14  EXIT

     The EXIT command causes the MCR to terminate  RTS-8  execution  (after
     pausing  approximately  1  second  for  pending  I/O  to complete) and 
     returns to the OS/8 monitor at location 07600. This  command  must  be 
     typed out completely or it will be regarded as an EXAMINE command.


     5.3  MCR ERRORS

     The MCR checks each command line for errors  and,  if  it  finds  one,
     issues one of the following messages and reprompts on the terminal for
     a corrected command:

	  BAD CHAR	 Character was not expected where it occurred

	  BAD NUMBER	 Number out of legal range or missing

	  BAD DELIM	 No space or comma where one was expected

	  BAD NAME	 Task name not in name table or duplicate











				      5-6






				   CHAPTER 6

		    ASSEMBLING AND LOADING TASKS FOR RTS-8


     RTS-8 tasks are assembled with the OS/8 PAL8 assembler and the use  of 
     a  parameter file.  RTS-8 parameter files are all edited versions of a
     master parameter file which is included  in  the  distributed  sources 
     (see  Appendix A).  All definitions in the master file which are to be
     supplied by the user are left blank in the file;  i.e., a sample  line 
     in the file might be:

	       PDP8E= /SET TO 1 IF PDP8E OR PDP8A, ELSE 0

     There should be a  unique  parameter  file  created  for  every  RTS-8
     environment,  where  environment  is  a  combination  of the available
     hardware and the set of tasks being run. The parameter file is divided
     into 5 sections:

	  1.  Executive specifications - these specifications  control  the
	      assembly  of the RTS-8 Executive and therefore are essential;
	      specifications include whether the machine is a PDP-8/E,  how
	      much  core  is available, whether to save/restore the MQ, how
	      many tasks exist in the system, etc.

	  2.  Task definitions - this section defines  symbolic  names  for 
	      the  various  system  tasks.   The  names of all system tasks 
	      which are to be included in  the  system  should  be  defined 
	      here,  and  any system task which is not included should have 
	      the line which defines it deleted from this section.   It  is 
	      recommended  that  this  deletion be performed by inserting a 
	      slash (/) character at the beginning of the line, making  the 
	      entire  line  a  comment.   The  user  is  encouraged  to add 
	      symbolic definitions of his own tasks to this section.

	  3.  System task specifications - these specifications control the
	      assemblies  of various system tasks. They include the desired
	      clock rate, the number of fields to allocate  to  OS/8,  etc. 
	      The  set  of  parameters  controlling  a task are all grouped 
	      together and assembled conditionally only if the task name is 
	      defined.

	  4.  System wide definitions - these include  the  definitions  of 
	      the  symbols  used in this document to describe the Executive
	      Requests  and  Task  Flag  bits,  plus  many   other   useful
	      definitions.  This section should not be altered by users.









				      6-1

     Assembling and Loading Tasks

	  5.  Task setup - this section uses four symbols  defined  in  the 
	      body of the user's task to initialize the RTS-8 table entries
	      needed to put that task in  the  system.   The  four  symbols 
	      needed are:

	       TASK	 Defined  to  be  the  task  number  of  the  task,
			 generally by a statement of the form:

			     TASK=symbol

			 where "symbol" is the symbolic name for  the  task
	    		 which  the user has defined in the RTS-8 parameter
	    		 file.

	       CUR	 Defined  to  contain  the  field  of  the   task's
 			 starting address in bits 6-8 (e.g., CUR=10)

					        NOTE

			      It is the user's responsibility to place
			      the  task's  starting  code in the field
			      specified by CUR.  This is done  by  the
			      PAL8 assembler pseudo-op:

				   FIELD CUR%10

	       START	 Defined to be the  task's  starting  address  (not
			 necessarily the lowest address in the task)

	       INIWT	 Defines the initial wait bits in  the  Task  Flags
	    		 Table  entry for this task; INIWT=0 means the task
	    		 is runnable when the system starts up.

     Up to three tasks may be defined in one assembly; see TASK above. (The
     demonstration  program in Chapter 7 uses only one.)  The corresponding
     symbols for the other tasks are TASK2 and TASK3, CUR2 and  CUR3,  etc.
     The  task  setup  section  places  its  data  into the RTS-8 tables by
     origining into them; no executable code is generated.

     To create a real-time system using RTS-8, first lay out the tasks  you
     will  need on paper.  Then create a parameter file with the parameters
     for that system, and allocate core storage among  the  Executive,  the
     system  tasks, and your own tasks.  Write your tasks and assemble each
     task preceded by the parameter file.  Load the resulting binaries with
     OS/8  ABSLDR,  placing  the RTS-8 binary first.  At this point you may
     start your system, or save it as a core image file to be run later.

     Each RTS-8 system task contains assembler code which causes it  to  be
     assembled  for  loading  into  a  specific area of core.  The user may
     assemble his own tasks to load into the areas of core not used by  the
     system  tasks in his configuration, or he may edit the system tasks so
     that they load wherever he wishes.  Page zero locations and auto-index
     registers  used  by  system tasks can also be redefined by editing the
     tasks involved.



	    			      6-2

     Assembling and Loading Tasks

     The OS/8 BITMAP program can be extremely useful in determining that no
     two  RTS-8 tasks are loading into the same area or using the same Page
     0 locations.  OS/8 BITMAP accepts a list of binary files as input  and
     produces  as  output  a  map  of  core.   Each  location  of  core  is 
     represented in this map by a single  digit  which  has  the  following 
     meaning:

	       0    Nothing has been loaded into this location

	       1    Information has been loaded into this location

	       2    Information has been loaded into this location twice

	       3    Information has been loaded into this location three or
		    more times

     There are only two places in core where twos are allowed to appear  in
     the  bit map.  These areas are the RTS-8 Executive Tables (starting at
     location 01200) and the MCR name table in the MCR.   Appearance  of  a
     three or a two in an area (other than those just mentioned) in the bit
     map is an indication that two or more tasks have loaded something into
     the same location.

     An RTS-8 system created as above has a starting address of 00200.   If
     RTS-8  was  not  specifically  configured  for  a PDP 8/E it will halt
     initially so that the operator  may  clear  any  stray  device  flags.  
     Press  START  to  resume  operation on a PDP 8, 8/I or 8/L;  press I/O 
     PRESET followed by CONTINUE on a PDP-12.





























	    			      6-3







    				   CHAPTER 7

    			     DEMONSTRATION PROGRAM


     This system will show OS/8 execution in the  background  with  several
     foreground  task  executions, i.e., CLOCK, MCR and a line printer on a
     16K PDP-8/E.  OS/8 will use a 2400 baud VT05 terminal (device codes 32
     and  33)  and RK8E as the system device.  Below is a discussion of the
     parameter file (lines 1-162) found in the program which follows  (note
     that   more   tasks  than  necessary  have  been  defined  for  system 
     execution):


	  Line #		   Description	  ______		   ___________

	    48	    Running on a PDP-8/E or PDP-8/A
	    49	    No tasks use the MQ, so there is no need  to  save  and
		    restore it
	    50	    No powerfail hardware
	    51	    16K machine
	    52      Eleven (octal) tasks
	   *59	    System has a clock (DK8-EA), this task is priority #1
	    61	    Terminal module this task is priority #3
	   *62	    Line printer module, this task is priority #2
	    63	    MCR module, this task is priority #7
	    65	    RK8E module required for OS/8 as  system  device,  this
		    task is priority #4
	    71	    OS/8 background task, this task is priority #11
	    74	    User task #1, this task is priority #5 (this is  TICK),
		    see lines 163-213
	    75	    User task #2 (to be defined  by  user),  this  task  is
		    priority #10
	    80	    OS/8 requires two memory fields
	    81      OS/8 terminal input device code=32
	    82	    OS/8 terminal output device code=33
	    83	    OS/8 system device=RK8E
	    84	    VT05 at 2400 BAUD  (without  KL8-JA)  requires  4  fill
		    characters
	    87	    MCR SYSTAT facility should be included in MCR assembly
	   *90	    Clock is DK8EA or DK8-EC
	    91	    Twenty entries in clock queue
	   *93 	    Hardware clock runs at 120 ticks/second
	   *94	    Number of system ticks

     ________________
     *  This demo will show a user task (UT1) as  printing  "TICK"  on  the
	line  printer every half second.  If the user does not have a clock
	or line printer do not execute any of the MCR commands shown before
	those that deal with "TIME" or starting or stopping the task  named
	"TICK". Also do not perform the assembly named TICKER.



				      7-1

     Demonstration Program


     .R PAL8
     *RTS8.BN<DEMOPM,RTS8.PA	 \
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |
				  |
     .R PAL8			  |
     MCR.BN<DEMOPM,MCR.PA	  |
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |
				  |
     .R PAL8			  |
     *CLOCK.BN<DEMOPM,CLOCK.PA	  |
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |
				  |
     .R PAL8			  |  Assembly of Digital-Supplied Modules
     *TTY.BN<DEMOPM,TTY.PA	  |
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |  (DEMOPM is a Parameter File;
				  |  see following listing, lines 1-162)
     .R PAL8			  |
     *LPT.BN<DEMOPM,LPT.PA	  |
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |
				  |
     .R PAL8			  |
     *OS8SUP.BN<DEMOPM,OS8SUP.PA  |
     ERRORS DETECTED: 0		  |
     LINKS GENERATED: 0		  |
				  |
     .R PAL8			  |
     *RK8E.BN<DEMOPM,RK8E.PA	  |
      ERRORS DETECTED: 0	  |
      LINKS GENERATED: 0	 /

     .R PAL8			 \
     *TICKER.BN<DEMOPM,TICKER.PA  |  User Task (see listing, lines 163-213)
     ERRORS DETECTED: 0	          |
     LINKS GENERATED: 0		 /

















				      7-2

     Demonstration Program


     .R ABSLDR 
     *RTS8.BN,MCR.BN,CLOCK.BN,TTY.BN,LPT.BN,OS8SUP.BN,RK8.BN,TICKER.BN/G <-
     >DATE	      \  MCR prints ">"; Type "DATE"			  |
     02/06/74	       | Current OS/8 Date is Printed			  |
     >TIME 13:00       | Enter Time (1:00 PM)				  |
     >TIME	       | Ask for Time		  ________________________|
     13:00	      /				  |
    						  |_/ Loading Binaries into
     >SYS	      \  Ask for System Status	    \ Core with OS/8 ABSLDR.
     01  CLCK 0	       |
     02  LPT  M	       |
     03  TTY  M	       |
     04  RK8  M	       |
     05       R	       |
     07  MCR	       |
     11  OS8  E	      /

     >NAME 5 TICK     \  Call Task #5 "TICK"
     >SYS	       | Ask for System Status
     01  CLCK 0	       |
     02  LPT  M	       |
     03  TTY  M	       |
     04  RK8  M	       |
     05  TICK R	       |
     07  MCR	       |
     11  OS8  E	      /

     >REQUEST TICK    \  Start TICK running; "TICK" is printed on LPT every 
    		       |   1/2 second.
     >STOP TICK	       | Stop TICK
     >TIME	       | Ask Time Again
     13:02	      /

     >REQ TICK,@l3:05 \	 Ask TICK to Run at 1:05
     >TIME	       |
     13:02	       | Time = 1:02
     >TIME	       |
     13:03	       | Time = 1:03
     >TIME	       |
     13:04	       | Time = 1:04
     >TIME	       | TICK Starts Running Again
     13:05	      /  Time Now 1:05

     >STOP TICK       \  Stop TICK Task
     >EXIT	       | Return to OS/8 Monitor
    		       |
      ...	      /









  				      7-3




	      Type this program with the OS/8 Editor and save it
	      on the  system device under the name of TICKER.PA.



/PARAMETERS FOR RTS-8 TASKS 		PAL8-V9B  05/22/74  PAGE 1

1		   /PARAMETERS FOR RTS-8 TASKS
2		   /
3		   /
4		   /
5		   /
7		   /
8		   /
9		   /
10	 	   /
11	 	   /COPYRIGHT	(C)   1974 BY DIGITAL EQUIPMENT CORPORATION
12		   /
13		   /
14		   /
15		   /
16		   /
17		   /
18		   /
19		   /
20		   /
21		   /
22		   /THE INFORMATION IN THIS DOCUMENT IS SUBJECT TO CHANGE 
23		   /WITHOUT NOTICE AND SHOULD NOT BE CONSTRUED AS A 
24		   /COMMITMENT BY DIGITAL EQUIPMENT CORPORATION.  DIGITAL 
25		   /EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY FOR 
26		   /ANY ERRORS THAT MAY APPEAR IN THIS DOCUMENT.
26		   /
27		   /THE SOFTWARE DESCRIBED IN THIS DOCUMENT IS FURNISHED TO 
28		   /THE PURCHASER UNDER A LICENSE FOR USE ON A SINGLE 
29		   /COMPUTER SYSTEM AND CAN BE COPIED (WITH INCLUSION OF 
30		   /DIGITAL'S COPYRIGHT NOTICE) ONLY FOR USE IN SUCH SYSTEM 
31		   /EXCEPT AS MAY OTHERWISE BE PROVIDED IN WRITING BY 
32		   /DIGITAL.
33		   /
34		   /DIGITAL EQUIPMENT CORPORATION ASSUMES NO RESPONSIBILITY 
35		   /FOR THE USE OR RELIABILITY OF ITS SOFTWARE ON EQUIPMENT 
36		   /THAT IS NOT SUPPLIED BY DIGITAL.
37		   /
38		   /
39		   /
40		   /
41		   /
42		   /
43		   /
44		   /






    				      7-4

/PARAMETERS FOR RTS-8 TASKS 		PAL8-V9B  05/22/74  PAGE 2
45
46	           /RTS8 EXEC PARAMETERS - EDITED BY USER
47
48	     0001  PDP8E=  1	   /1 IF PDP 8/E
49	     0000  EAE=    0	   /1 IF SYSTEM SHOULD SAVE MQ
50	     0000  PWRFAL= 0	   /1 IF POWER FAIL/RESTART ENABLED IN HARDWARE
51	     0030  HGHFLD= 30      /HIGHEST FIELD USED (EG 30 FOR A 16K MACHINE)
52	     0011  NTASKS= 11      /NUMBER OF TASKS IN SYSTEM
53
54	           /COMMON TASK NUMBERS - EDITED BY USER
55	           /IT IS ADVISABLE TO DEFINE ALL TASKS HERE.  NAMES GIVEN 
56    		   /BELOW ARE USED BY SOME SYSTEM TASKS AND SHOULD BE DELETED 
57    		   /FROM THIS LIST IF THE CORRESPONDING TASK IS NOT INCLUDED 
    		   /IN THE SYSTEM
58
59	     0001  CLOCK=  1       /CLOCK HANDLER - SHOULD BE HIGH PRIORITY
60	           /PWRF=	   /POWER FAIL HANDLING TASK
61	     0003  TTY=    3       /TELETYPE DRIVER TASK
62	     0002  LPT=    2       /LINE PRINTER DRIVER TASK
63	     0007  MCR=    7       /MONITOR CONSOLE ROUTINE
64	           /DTA=	   /DECTAPE DRIVER TASK
65	     0004  RK8=    4       /RK8 OR RK8E DISK DRIVER TASK
66	           /RFO8=	   /RF08 DISK DRIVER TASK
67	           /DF32=          /DF32 DISK DRIVER TASK
68	           /CSA=	   /CASSETTE DRIVER TASK
69	           /CSAF=          /CASSETTE FILE SUPPORT TASK
70	           /UDC=	   /UNIVERSAL DIGITAL CONTROLLER TASK
71	     0011  OS8=    NTASKS  /OS/8 SUPPORT - NORMALLY LOWEST PRIORITY
72	           /OS8F=	   /OS/8 FILE SUPPORT
73
74	     0005  UT1=    5       /USER TASK 1
75	     0010  UT2=    10      /USER TASK 2
76
77	           /SOFTWARE PARAMETERS - EDITED BY USER
78
79		           IFDEF   OS8     <
80	     0002  OSFLDS= 2	   /NUMBER OF FIELDS TO ALLOCATE TO OS/8 (EG 2)
81	     0032  OSKBDV= 32      /OS/8 KEYBOARD DEVICE CODE (EG 03 = CONSOLE)
82	     0033  OSTTDV= 33      /OS/8 TELEPRINTER DEVICE CODE (EG 04)
83	     0004  OSSYSD= RK8     /OS/8 SYSTEM DEVICE DRIVER TASK (E.G. RK8)
84	     0004  OSFILL= 4       /# FILLS NEEDED AFTER LINE FEED
85		           >       /(EG 4 FOR 2400 BAUD VT05)
















    				      7-5



86		           IFDEF   MCR     <
87	     0001  MCRSYS= 1       /1 IF MCR SYSTAT FACILITY DESIRED
88		           >
89		           IFDEF   CLOCK  <
90   	     0000  CLKTYP= 0       /0(DK8EA/DK8EC) OR 1(KW12) OR 2(VT8E) OR 
				   /3(DK8FP)
91	     0020  CLKQLN= 20      /MINIMUM NUMBER OF ENTRIES ON THE CLOCK 
				   /OUEUE
92		           DECIMAL
93	     0170  HERTZ=  120     /NUMBER OF HARDWARE TICKS PER SECOND
94	     0074  SHERTZ= 60      /NUMBER OF SYSTEM TICKS PER SECOND
95		           OCTAL
96		           >




/PARAMETERS FOR RTS-8 TASKS		PAL8-V9B  05/22/74  PAGE 3

97	            /EQUIVALENCES:
98
99	     7344  AC7776= CLL STA RAL
100	     7346  AC7775= CLL STA RTL
101	     7330  AC4000= CLA STL RAR
102	     7350  AC3777= CLL STA RAR
103	     7332  AC2000= CLA STL RTR
104	     7326  AC0002= CLA STL RTL
105	
106	           /MONITOR CALL VALUES:
107
108	     4020  CAL=    JMS     20	    /CALL THE EXECUTIVE
109	     5424  POSTDS= JMP I   24	    /DISMISS AN INTERRUPT
110	     4425  WAITM=  JMS I   25	    /WAIT FOR MULTIPLE EVENTS
111
112	     0000  SEND=   0	   /SEND MESSAGE
113	     0001  RECEIV= 1       /RECEIVE MESSAGE
114	     0002  WAITE=  2       /WAIT FOR EVENT FLAG
115	     0003  RUN=    3       /CONTINUE TASK EXECUTION
116	     0004  SUSPND= 4	   /SUSPEND TASK EXECUTION
117	     0005  POST=   5       /POST AN EVENT FLAG
118 	     0006  SKPINS= 6       /INSERT CODE INTO INTERRUPT SKIP CHAIN
119	     0007  DERAIL= 7       /INITIATE END-ACTION
120	     0010  BLKARG= 10      /BLOCK TASK FOR REASON SPECIFIED IN ARG
121	     0011  SENDW=  11      /SEND MESSAGE AND WAIT
122	     0012  UNBARG= 12      /UNBLOCK TASK FOR REASON SPECIFIED IN ARG













    				      7-6



123
124		           IFDEF UDC	   <AO=0;DO=1;DI=2;GC=3;EC=4;RC=5
125				           DC=6;ECT=7;CS=10;DCT=11;AI=12>
126
127	           /TASK STATUS FLAGS:
128
129	     4000  MSGWT=  4000    /MESSAGE WAIT
130	     2000  EFWT=   2000    /EVENT FLAG WAIT
131	     1000  RUNWT=  1000    /SCHEDULE WAIT
132	     0400  SWPWT=  0400    /SWAPPER WAIT
133	     0200  EORMWT= 0200    /EVENT FLAG OR MESSAGE WAIT
134	     0100  USERWT= 0100    /USER SPECIFIED WAIT
135	     0040  ENABWT= 0040    /ENABLE WAIT
136	     0001  DNEWT=  0001    /DOES NOT EXIST WAIT
137
138		   /SYSTEM LOCATIONS
139
140	     1176  MSGTBL= 1200-2  		/TASK MESSAGE TABLE
141	     1220  TSTABL= NTASKS+2^2+MSGTBL-4  /TASK STATE TABLE - HOLDS
142					        /TASK LINK,UM,DF,IF,PC,AC,MQ
143	     1273  TFTABL= NTASKS+2^4+TSTABL-l  /TASK FLAGS TABLE - HOLDS
144					        /TASK STATUS FLAGS
145
146	     0035  TSWFLG= 35      /TASK SW INHIBIT FLAG   IN FIELD 0
147	     0036  TODL=   36      / LOW ORDER TIME OF DAY IN FIELD 0
148	     0037  TODH=   37      /HIGH ORDER TIME OF DAY IN FIELD 0
149	     0040  DATE=   40      /DATE IN OS8 FORMAT     IN FIELD 0
150	     0041  MCREF=  41      /MCR START EVENT FLAG   IN FIELD 0
151


/PARAMETERS FOR RTS-8 TASKS		PAL8-V9B  05/22/74  PAGE 4

152	           /TASK TABLE SETUP - "TASK", "CUR","INIWT" AND "START"
153	           /MUST BE DEFINED BY TASK:
154
155	     1210	   *TASK^2+MSGTBL
156   01210  0000	   ZBLOCK 2	   /MESSAGE BUFFER INITIALLY CLEAR
157	     1244	   *TASK^4+TSTABL
158   01244  0011	   CUR%10+CUR	   /INITIAL FLAGS
159   01245  5000	   START
160   01246  0000	   0		   /INITIAL AC 0
161	     1300	   *TASK+TFTABL
162   01300  1000	   INIWT














    				      7-7

/TASK TO PRINT "TICK" ON THE LINE PRINT   PAL8-V9B  05/22/74  PAGE 5

163		  /TASK TO PRINT "TICK" ON THE LINE PRINTER TWICE A SECOND
164
165		  /DEFINITIONS OF TASK PARAMETERS FOR RTS8:
166
167	     0005  TASK=  UT1     /I HAVE DEFINED UT1 IN MY PARAMETER FILE!
168	     0010  CUR=	  10	  /THIS TASK STARTS IN FIELD 1
169	     1002  INIWT= RUNWT   /THIS TASK IS NOT RUNNABLE INITIALLY. IT 
170    				  /IS IN "RUN WAIT". THE ONLY WAY TO MAKE 
171    				  /THIS TASK RUNNABLE IS FOR ANOTHER TASK 
172    				  /TO ISSUE A "RUN" EXECUTIVE REQUEST 
173    				  /SPECIFYING THIS TASK, OR FOR THE OPERATOR 
    				  /TO TYPE A "REQUEST" COMMAND TO THE MCR 
    				  /SPECIFYING THIS TASK.
174
175	     0001	 FIELD CUR%10	/SET FIELD FOR ASSEMBLER
178	     5000	 *5000		/SET ORIGIN
177
178   15000  4020  START, CAL		/"START" IS STARTING ADDRESS OF TASK
179   15001  0011	  SENDW		/SEND A MESSAGE TO THE CLOCK HANDLER 
180   15002  0001 	  CLOCK		/AND WAIT FOR THE MESSAGE EVENT FLAG
181   15003  5011	  SLPMSG	/THIS IS A POINTER TO THE MESSAGE
182
183		  /THE MESSAGE TO THE CLOCK HANDLER TELLS IT TO POST THE 
184		  /MESSAGE EVENT FLAG IN HALF A SECOND
185
188   15004  4020  	  CAL		/NOW SEND A MESSAGE TO THE LINE 
187   15005  0011	  SENDW		/PRINTER TASK AND WAIT FOR IT TO 
188   15008  0001	  LPT		/COMPLETE.
189   15007  5017	  TCKMSG
190
191   15010  5200	  JMP	 START	/LOOP MINDLESSLY - THIS WILL ANNOY 
192					/THE OPERATOR NO END, AS THE LINE 
193					/PRINTER WILL GO "TICK...TICK...TICK"
194					/UNTIL HE STOPS THIS TASK WITH THE 
					/MCR "STOP" COMMAND.
195
196   15011  9000  SLPMSG,ZBLOCK 3	/THREE WORDS REQUIRED BY RTS8 FOR 
					/MESSAGE HEADER
197   15014  0000	  0		/0 HERE MEANS "SET MESSAGE EVENT FLAG 
					/AFTER INTERVAL"
198   15015  0000	  0;SHERTZ%2	/DOUBLEWORD QUANTITY = 1/2 SECOND 
199   15016  0036			/SINCE















    				      7-8



200
201					/"SHERTZ" IS THE NUMBER OF TICKS/
202					/SECOND.  LAST 2 PARAMETERS NOT 
203					/NEEDED IN THIS TYPE OF MESSAGE.
204
205   15017  0000  TCKMSG, ZBLOCK 3	/MESSAGE HEADER
206   15022  0000	  0		/FLAG WORD - THIS COMBINATION OF FLAG 
207					/BITS MEAN: PACKED ASCII MESSAGE CR/LF 
208					/AFTER TEXT INCLUDED IN MESSAGE
209   15023  0000	  0		/UNUSED - THIS SPECIFIES INPUT BUFFER
210					/FOR TELETYPE MESSAGES.
211   15024  2411	  TEXT \TICK!\	/ACTUAL TEXT TO BE OUTPUT
212   15025  0313
213   15026  4100
214			  $





/TASK TO PRINT "TICK" ON THE LINE PRINT   PAL8-V9B  05/22/74  PAGE 6

     AC0002 7326      TODL   0036
     AC2000 7332      TSTABL 1220
     AC3777 7350      TSWFLG 0035
     AC4000 7330      TTY    0003
     AC7775 7346      UNBARG 0012
     AC7776 7344      USERWT 0100
     BLKARG 0010      UT1    0005
     CAL    4023      UT2    0010
     CLKQLN 0020      WAITE  0002
     CLKTYP 0000      WAITM  4425
     CLOCK  0001
     CUR    0010
     DATE   0040
     DERAIL 0007
     DNEWT  0001
     EAE    0000
     EFWT   2000
     ENABWT 0040
     EORMWT 0200
     HERTZ  0170
     HGHFLD 0030















	                              7-9



     INIWT  1000
     LPT    0002
     MCR    0007
     MCREF  0041
     MCRSYS 0001
     MSGTBL 1176
     MSGWT  4000
     NTASKS 0011
     OSFILL 0004
     OSFLDS 0002
     OSKBDV 0032
     OSSYSD 0004
     OSTTDV 0033
     OS8    0011 
     PDP8E  0001
     POST   0005
     POSTDS 5424
     PWRFAL 0000
     RECEIV 0001
     RK8    0004
     RUN    0003 
     RUNWT  1000 
     SEND   0000 
     SENDW  0011 
     SHERTZ 0074 
     SKPINS 0006 
     SLPMSG 5011
     START  5000
     SUSPND 0004 
     SWPWT  0400
     TASK   0005
     TCKMSG 5017
     TFTABL 1273
     TODH   0037





     ERRORS DETECTED: 0
     LINKS GENERATED: 0

















    				      7-10



     AC0002     104#
     AC2000     103#
     AC3777     102#
     AC4000     101#
     AC7775     100#
     AC7776      99#
     AI         130#
     AO         124#
     BLKARG     120#
     CAL        108#  176   188
     CLKQLN      91#
     CLKTYP      90#
     CLOCK       59#   89   180
     CS         127#
     CT         125#
     CUR        158    158  168#  175
     DATE       149#
     DCT        129#
     DERAIL     119#
     DNEWT      136#
     EAE         49#
     ENABWT     135#
     EORMWT     133#
     HERTZ       93#
     HGHFLD      51#
     INIWT      162   169#
     LPT         62#  188
     MCR         63#   86
     MCREF      150#
     MCRSYS      87#
     MSGTBL     140#  141   155
     NTASKS      52#   71   141   143
     OSFILL      84#
     OSFLDS      80#
     OSKBDV      81#
     OSSYSD      83#
     OSTTDV      82#
     OS8         71#  79
     PDP8E       48#
     POST       117#
     POSTDS     109#
     PWRFAL      50#
















	                              7-11



     RECEIV      113#
     RK8          65#   83
     RUN         115#
     RUNWT       131#  169
     SEND        112#
     SENDW       121#  179   187
     SHERTZ       94#  199
     SKPINS      118#
     SLPMSG      181   196#
     START       159   178#  191
     SUSPND      116#
     SWPWT       132#
     TASK        155   157   161   167#
     TCKMSG      189   205#
     TFTABL      143#  161
     TODH        148#
     TODL        147#




     TSTABL      141#  145   157
     TSWFLG      146#
     TTY          61#
     UDC         124#
     UNBARG      122#
     USERWT      134#
     UT1          74#  167
     UT2          75#
     WAITE       114#
     WAITM       110#

     V3

























    				      7-12

     Notes for the bitmap below:

     Locations		What is there     _________          _____________

     00000-00002	RTS-8 Page 0 locations
     00010
     00017-00047

     00200-01177	RTS-8 Task

     01200-01377	Task Tables ( two's are legal; three's are not)

     01400-01777	Clock Task

     02000-02177	Clock Queue and Initializer

     03000-03377	TTY Task

     03400-03777	RK8E Task

     06200-07577	OS/8 Support Task



     10021-10025	Field 1 RTS-8 Resident

     10100-10116	MCR Page 0 Locations

     14600-14777	LPT Task

     15000-15026	User "Foreground" Task



     20021-20025	Field 2 RTS-8 Resident destroyed by OS/8 "field 1".



     30021-30025	Field 3 RTS-8 Resident destroyed by OS/8 "field 0".

     03400-34377	OS/8 Support unit code to set up fake OS/8 in 
    			fields 3 and 2.
















     	
    				      7-13

     BITMAP V4    FIELD 0


00000 11100000 10000001 11111111 11111111 11111111 00000000 00000000 00000000
00100 00000000 00000000 00000000 00000000 00000000 00000000 00000011 11111111

00200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
00300 11111111 11111100	00000000 00000000 00000000 00000000 00000000 00000111

00400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
00500 11111111 11111111 11111111 11000000 00000000 00000000 00000000 01111111

00600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
00700 11111111 11111111 11111111 11111111 11111111 11111111 11111000 00111111

01000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
01100 11111111 11111111 11111111 11111111 11111111 11111111 11111001 11111111

01200 22222222 22112211 22222221 22212221 22212221 11112221 11112221 22212222
01300 21212200 00000000 00000000 00000000 00000000 00000000 00000000 00000000

01400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
01500 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111

01600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
01700 11111111 11111111 11111111 11111111 11111111 11000000 00111111 11111111

02000 11111111 11111111 11111111 11111111 11111111 11111110 00000000 00000000
02100 00000000 00000000 00000000 00000000 00000000 00000000 00000000 00111111

02200
02300

02400
02500

02600
02700

03000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
03100 11111111 11111111 11111111 11111111 11111111 11111111 11100011 11111111

03200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
03300 11111111 11111111 11111111 11111111 00000000 00000111 11111111 11111111

03400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
03500 11111111 11111111 11111111 11111111 11111111 11111111 01111111 11111111

03600 11111111 11111111 11111111 11111111 11111110 00000000 00000000 00000000
03700 00000000 00000000 00000000 00000000 00000000 00000000 00000000 11111111









    				      7-14

     BITMAP V4    FIELD 0


04000
04100

04200
04300

04400
04500

04600
04700

05000
05100

05200
05300

05400
05500

05600
05700

06000
06100

06200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
06300 11111111 11111111 11111111 11111111 11111100 00000000 00000111 11111111

06400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
06500 11111111 11111111 11111111 11111111 10000000 00000011 11111111 11111111

06600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
06700 11111111 11111111 11111111 11111111 11111111 11111111 01111111 11111111

07000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
07100 11111111 11111111 11111111 11111111 11111111 10000000 00111111 11111111

07200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
07300 11111111 11111110 00000000 00000000 00000000 00000000 00000001 11111111

07400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
07500 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111100

07600
07700









    				      7-15

     BITMAP V4    FIELD 1


10000 00000000 00000000 01111100 00000000 00000000 00000000 00000000 00000000
10100 11111111 11111110 00000000 00000000 00000000 00000000 00000000 00000000

10200
10300

10400
10500

10600
10700

11000
11100

11200
11300

11400
11500

11600
11700

12000
12100

12200
12300

12400
12500

12600
12700

13000
13100

13200
13300

13400
13500

13600
13700









    				      7-16

     BITMAP V4    FIELD 1


14000
14100

14200
14300

14400
14500

14600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
14700 11111111 11111111 11111111 11111111 11111111 11111111 11110000 00011111

15000 11111111 11111111 11111110 00000000 00000000 00000000 00000000 00000000
15100

15200
15300

15400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
15500 11111111 11111111 11111111 11111111 11111111 11111111 11110000 11111111

15600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
15700 11111111 11111111 11111111 11111111 11111111 11000000 00000111 11111111

16000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
16100 11111111 11111111 11111111 11111111 11111111 11111111 11100000 01111111

16200 22222222 11112211 22111111 11111111 11111111 11111111 11111111 11111111
16300 11111111 11100000 00000000 00000000 00000000 00000000 00011111 11111111

16400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
16500 11111111 11111111 11111111 11111111 11111111 11110000 00111111 11111111

16600 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
16700 11111111 11111111 11111111 11111111 11111111 11111111 11110000 11111111

17000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
17100 11111111 11111111 11111111 11111111 11111111 11111111 10111111 11111111

17200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
17300 11111111 11111111 11111111 11111111 11100000 00000011 11111111 11111111

17400 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
17500 11111111 11111111 11111111 11111111 11111111 11111101 11111111 11111111

17600
17700









    				      7-17

     BITMAP V4    FIELD 2


20000 00000000 00000000 01111100 00000000 00000000 00000000 00000000 00000000
20100

20200
20300

20400
20500

20600
20700

21000
21100

21200
21300

21400
21500

21600
21700

22000
22100

22200
22300

22400
22500

22600
22700

23000
23100

23200
23300

23400
23500

23600
23700









    				      7-18

     BITMAP V4    FIELD 2


24000
24100

24200
24300

24400
24500

24600
24700

25000
25100

25200
25300

25400
25500

25600
25700

26000
26100

26200
26300

26400
26500

26600
26700

27000
27100

27200
27300

27400
27500

27600
27700









    				      7-19

     BITMAP V4    FIELD 3


30000 00000000 00000000 01111100 00000000 00000000 00000000 00000000 00000000
30100

30200
30300

30400
30500

30600
30700

31000
31100

31200
31300

31400
31500

31600
31700

32000
32100

32200
32300

32400
32500

32600
32700

33000
33100

33200
33300

33400
33500

33600
33700









    				      7-20

     BITMAP V4    FIELD 3


34000 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
34100 11111110 00000000 00000000 00000000 00000000 00000000 00000000 00011111

34200 11111111 11111111 11111111 11111111 11111111 11111111 11111111 11111111
34300 11111111 11100000 00000000 00000000 00000000 00000000 00000000 00011111

34400
34500

34600
34700

35000
35100

35200
35300

35400
35500

35600
35700

36000
36100

36200
36300

36400
36500

36600
36700

37000
37100

37200
37300

37400
37500

37600
37700









    				      7-21







    				  APPENDIX A

    			RTS-8 DISTRIBUTED SOURCE FILES



     The RTS-8 source files included on the distribution tape are:

	FILE	 TASK(S)		     COMMENTS	____     _______		     ________


     PARAM.PA	 -		   System parameter file with  all  equates
				   blank.   Should  never  be  altered, but
				   should  be  edited  to  create  specific
				   parameter files
     RTS8.PA	 - (null task)	   RTS-8 Executive
     MCR.PA	 MCR		   Monitor Console Routine
     OS8SUP.PA   OS8		   OS/8 Support Task
     		 OS8F		   OS/8 File Support Task
     PWRF.PA	 PWRF		   Power Fail Task
     CLOCK.PA	 CLOCK		   Clock handler Task
     TTY.PA	 TTY		   Terminal driver Task
     LPT.PA	 LPT		   Line printer driver Task
     DTA.PA	 DTA		   TC08 DECtape driver Task
     RK8.PA	 RK8		   RK8 disk driver Task
     RK8E.PA	 RK8		   RK8E disk driver Task
     RF08.PA	 RF08/DF32	   RF08/DF32 fixed-head disk driver Task
     CSA.PA	 CSA		   Cassette driver Task
     CSAF.PA	 CSAF		   Cassette File Support Task
     UDC.PA	 UDC		    Universal  Digital  Controller  handler
				   Task






















				      A-1






				  APPENDIX B

			     RTS-8 COMPONENT SIZES

     The following table gives the approximate size and default origins  of
     each  component  of  the  RTS-8  system as of the first release of the
     system.

	  NTASKS = Number of tasks in system
	  CLKQLN = Number of entries in clock queue
	  MCRSYS = 1 if MCR SYSTAT function desired, else 0

     Any fractions from divides should be dropped.



				   Table B-1
			    RTS-8 Component Sizes


   -------------------------------------------------------------------------
   |		  |		  | NUMBER OF PAGES |			   |
   |  SOFTWARE    |    DEFAULT    | REQUIRED (1 PAGE|			   |
   |  COMPONENT   |    ORIGIN	  | =128 WORDS      |       COMMENTS       |
   |--------------|---------------|-----------------|----------------------|
   |		  |		  |		    |			   |
   | RTS-8	  |    00200	  | 5+NTASKS/18     | Must be in locations |
   | Executive    |		  |		    | 00200-01200. Uses    |
   |		  |		  |		    | page 0 locations 0-3 |
   |		  |		  |		    | and 20-47 and	   |
   |		  |		  |		    | auto-index register  |
   |		  |		  | 		    | 17.		   |
   |		  |		  |		    |			   |
   | Clock Module | 1st page	  | 3+CLKQLN/22     | Must be in field 0.  |
   |		  | after end of  | 		    | Uses auto-index      |
   |		  | of RTS-8 	  |		    | register 10.	   |
   |		  | Executive	  |		    |		  	   |
   |		  |		  |		    |			   |
   | Console 	  |    03000	  | 2		    |			   |
   | Terminal	  |		  |		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | Non-Console  |     --        | 2		    |			   |
   | Terminal	  |		  |		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | Line Printer |    14600	  | 1		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | TC08 DECtape |    15000	  | 2		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   -------------------------------------------------------------------------

    				      B-1


     RTS-8 Component Sizes




    			       Table B-1 (Cont.)
    			     RTS-8 Component Sizes

   -------------------------------------------------------------------------
   |		  |		  | NUMBER OF PAGES |			   |
   |  SOFTWARE    |    DEFAULT    | REQUIRED (1 PAGE|			   |
   |  COMPONENT   |    ORIGIN	  | =128 WORDS      |       COMMENTS       |
   |--------------|---------------|-----------------|----------------------|
   |		  |		  |		    |			   |
   | RK8E Disk 	  |    03400	  | 2		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | DF32/RF08 	  |    04000	  | 1		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | RK8 Disk	  |    03400	  | 1		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | Power Fail	  |    10200	  | 1+NTASKS/32	    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   | UDC Module	  |    10600	  | 7-9 depending   | Uses page 0	   |
   |		  |		  | on table space  | locations 130-144	   |
   |		  |		  | desired.	    |			   |
   |		  |		  |		    |			   |
   | Cassette	  |    13200	  | 3		    |			   |
   | Module	  |		  |		    |			   |
   |		  |		  |		    |			   |
   |Cassette Label|    12400	  | 3		    | Requires cassette	   |
   |Support Module|		  |		    | handler.		   |
   |		  |		  |		    |			   |
   | OS/8 File    | 04600 if OS/8 | 6		    | Requires a mass	   |
   |Support Module| support       |		    | storage handler.	   |
   |		  | present,	  |		    | Must run in field 0. |	
   |		  |otherwise 06200|		    |			   |
   |		  |		  |		    |			   |
   | OS/8 Support |    06200	  | 6		    | Must run in field    |
   | Task	  |		  |		    | 0 - requires 8K for  |
   |		  |		  |		    | OS/8 plus a mass     |
   |		  |		  |		    | storage handler.     |
   |		  |		  |		    | Uses page	0	   |
   |		  |		  |		    | locations 164-177.   |
   |		  |		  |		    |			   |
   | Monitor 	  | 17600 minus   | 5+3 (if clock   | Requires "console"   |
   | Console	  | length (15200 | functions 	    | terminal handler	   |
   | Routine Task | with all	  | desired) +	    | and page 0	   |
   |		  | options)	  | MCRSYS +	    | locations 100-117    |
   |		  |		  | (NTASKS+40)/64. |			   |
   |		  |		  |		    |			   |
   -------------------------------------------------------------------------



    				      B-2









    				   GLOSSARY

     Accumulator:   the  register  in  which  arithmetic   operations   are 
	  performed (abbreviated AC).
     Analog:  representation of information by continuous variables.
     Analog Channel:  a UDC functional device.
     Argument:  a variable or constant which is given  in  the  call  of  a
	  subroutine   as information to it a variable upon whose value the 
	  value of a function depends; the known reference factor necessary 
	  to find an item in a table or array (i.e., the index).
     Assembler:  a program which translates symbolic op-codes into  machine
	  language   and   assigns   memory  locations  for  variables  and 
	  constants.
     Auto-index Register: whenever one of the absolute locations from  0010
	  through  0017  in  any  memory field is addressed indirectly, the
	  contents of that location is incremented by one, rewritten in the
	  same  location,  and used as the effective address of the current
	  instruction.
     Auto-restart:  the ability to start the CPU automatically on power-up.

     Baud:  a unit of measure of data flow (one bit per second).
     Bit:  a binary digit (each PDP-8 word is composed of 12 bits).
     Bit Map:  a method of keeping track of used  and  unused  entities  by
	  assigning one bit in a table to each entity.
     Block Gap:  the blank space between blocks on a recording medium.
     Block:  a set of  consecutive  machine  words,  characters  or  digits 
	  handled  as  a unit, particularly with reference to I/O;  also to 
	  inhibit a process from continuing.
     Blocking Bits:  bits in an RTS-8 Monitor table  which  specify  why  a 
	  given task is blocked.
     Byte:  a group of binary digits usually operated upon as a unit.

     Cassette:  a magnetic tape device used for program and data storage.
     Central Processing Unit:  the unit of a computing system that includes
	  the circuits controlling  the  interpretation  and  execution  of
	  instructions; also central processor (abbreviated CPU).
     Clear:  to erase the contents of a storage location by  replacing  the
	  contents, normally with zeroes.
     Clock:   a  time-keeping  or  frequency-measuring  device  within  the 
	  computer system.
     Communication Region:   locations  20-27  of  every  field,  used   to 
	  simplify passing executive requests across field boundaries.
     Compute Bound:  requiring extensive (or total) use of the CPU relative
	  to other hardware elements (such as I/O devices).
     Configuration:  the number and types of hardware present on a system.
     Contact Channel:  a UDC functional device.
     Contiguous:  code which resides in core immediately adjacent to  other
	  sections of code.
     Controller:  the circuitry which controls a device.
     Counter Channel:  a UDC functional device.

				  GLOSSARY-1


     Core Image File:  a file in core image format (i.e.,  a  'picture'  of
	  core).
     Core Storage:  the main high-speed storage  of  a  computer  in  which 
	  binary  data is represented by the switching polarity of magnetic 
	  cores.
     CPU Registers:   high-speed  circuitry  used  to   store   information 
	  affecting the operation of the CPU (e.g., PC, IF, DF).

     Data:  a general term used  to  denote  any  or  all  facts,  numbers, 
	  letters  and  symbols.  It connotes basic elements of information
	  which can be processed or produced by computer.
     Data Field:  a 3-bit register which determines the memory  field  from
	  which  operands  are  taken  in indirectly addressed instructions
	  (abbreviated DF).
     Debug:  to detect, locate and correct mistakes in a program.
     Deferred Actions:  actions which are considered low-priority  and  are 
	  not performed until higher-priority actions are serviced.
     Deferred Requests:  requests which are considered low-priority and are
	  serviced after high-priority requests.
     Derail:  to transfer control or execution of a  specified  task  to  a
	  subroutine.
     Device Codes:  numbers assigned to each device in the system.
     Device Status Register:  a register which contains the current  status 
	  of a device.
     Digital:  representation of information by discrete units.
     Digital Channel:  a UDC functional device.
     Driver:  see Handler.
     Dynamic:  pertaining to a quantity that is affected by some  condition
	  (such as time) and is therefore relative to the condition.

     Entry Point:  the location in  a  routine  to  which  control  can  be
	  transferred and execution begun.
     Event Flag:  the location which contains the status of an event (event
	  being either a result of some operation, or a physical
	  occurrence).
     Executive:  the program which controls the execution of other programs
	  or routines.
     Executive Requests:  means of  communication  between  tasks  and  the 
	  RTS-8 Executive.

     Field:  a division of memory on a PDP-8 computer  referring  to  a  4K
	  section of core.
     File Gap:  a  fixed  length  of  blank  tape  separating  files  on  a 
	  recording  medium;   generally  several times the size of a block 
	  gap.
     Functional Devices:  the devices  available  for  use  under  the  UDC
	  handler.

     Gain:  an increase in signal power.
     Generic Codes:  codes used to identify which type  of  UDC  functional
	  device  caused  an  interrupt  and  to  direct program control to
	  service routines.

     Handler:  a routine which is designed to control the  operation  of  a
	  device.



    				  GLOSSARY-2


     I/O Bound:  a condition in which a process is performing much I/O  but
	  using very little CPU time.
     Indirect  Address:  an  address  in  a  computer   instruction   which 
	  indicates  a location where the address of the referenced operand 
	  is to be found.
     Initialization  Code:   code  which  sets  counters,   switches,   and 
	  addresses to zero or other starting values at the beginning of or 
	  at prescribed points in a computer routine.
     Input Buffer:  a section of memory used for storage of input data.
     Instruction Field:  a register which holds  the  contents  determining 
	  from  which field the operand of a directly addressed instruction 
	  should be taken (abbreviated IF).
     Interactive:  highly responsive to real-world inputs.
     Interface:  the common boundary between two devices or systems.
     Interlock Scheme:  arranging the control  of  devices  so  that  their
	  operation is interdependent.
     Interrupt:  a break  in  execution  caused  by  some  external  event;
	  execution is usually resumed at a later time.
     Interrupt Processing Module:  a routine which acts upon  the  external
	  event which caused an interrupt.
     Interval Queue:  a list of actions to perform, each accompanied by the
	  interval  of  time which is to elapse from the previous action to
	  the current one.

     Line-frequency Clock:  a clock which determines when to tick according
	  to the state of the current flowing in a power-supplying wire.
     Link:  a one-bit register in the PDP-8; an address  pointer  generated
	  automatically by PAL8 or MACRO-8 assemblers to indirectly address
	  an off-page symbol.
     Logical OR:  a logical function of two inputs which is  true  whenever
	  either input is true.
     Loop:  a sequence of instructions that is executed repeatedly until  a
	  terminal condition prevails.

     Mass Storage Device:  a device such as disk or  DECtape  which  stores
	  large   amounts   of  data  readily  accessible  to  the  central 
	  processing unit.
     Master Parameter File:  a file included in the distributed sources  of
	  RTS-8  which the user can edit to indicate parameters specific to
	  his system configuration.
     Memory Address:  a register which holds the  address  specified  by  a
	  memory reference instruction.
     Message:  a contiguous area of memory which contains information about
	  execution of tasks.
     Message-driven:  an RTS-8 task is called  message-driven  if  it  only
	  executes in response to messages received from other tasks.
     Mnemonic:  alphabetic representation of a function  or  octal  machine
	  instruction.
     Module:  a routine which handles a particular function.
     Monitor Console Routine:  the Monitor routine which provides the  user
	  with functions which allow him to control, inspect, and debug his
	  system.
     Multiplier Quotient:  a 12-bit register used in conjunction  with  the
	  accumulator to perform mathematical operations (abbreviated MQ).
     Multi-programming:  two or more programs in  core  at  the  same  time 
	  which  execute  alternately depending on the current state of the 
	  system.

				  GLOSSARY-3


     No-op:  no operation occurs; control proceeds to the next  instruction 
	  in sequence.
     Null Characters:  characters with ASCII code 000.

     Overflow:  a condition  that  occurs  when  a  mathematical  operation 
	  yields  a  result  whose magnitude is greater than the program is 
	  capable of handling.

     Pack:  to conserve memory by combining information.
     Page:  a 128-word section of PDP-8 core memory beginning at an address
	  which is a multiple of 200.
     Parameter file:  a file used to record arguments which may be assigned
	  different values.
     Parity Bit:  a bit which indicates whether the total number of  binary
	  one digits in a word is even or odd.
     Pointer:  a word containing the address of another word in memory.
     Posted:  one of the states of an event flag, indicating that the event
	  is complete.
     Power-fail:  an interruption of power to the computer.
     Priority  Scheme:   a  scheme  by  which  certain  operations  or  the 
	  execution of a set of instructions is given preference over other
	  operations.
     Program Counter:  a register which contains the address  of  the  next
	  instruction to be executed (abbreviated PC).
     Prompting Character:  a character which prints on the console terminal
	  and cues the user to perform some action.

     Queue:  a  waiting  list  (e.g.,  a  queue  of  programs  waiting  for 
	  processing time).

     Ready Flag:  a bit which a device controller sets when it is ready  to
	  accept commands from the CPU.
     Real-time System:  a system in which computation is performed while  a
	  related  physical process is occurring so that the results of the
	  computation can be used in guiding the physical process.
     Receiver:  the task which has received a  message  from  another  task
	  (sender).
     Record:  a collection of related items of data treated as a unit.
     Record Header Area:  an area of at least  40  words  in  length  which
	  contains information necessary to perform cassette operations.
     Ring-buffer:   a  storage  area  for  data  accessed  on  a  first-in, 
	  first-out basis.

     Scheduling:  the operation of sharing resources among computing tasks.
     Sender:  the task which has sent a message to another task (receiver).
     Sign Bit:  the bit which contains the sign of a number.
     Simulate:  to represent the function of a device,  system  or  program 
	  with another device, system or program.
     Skip Chain:  an instruction sequence which determines the source of an
	  interrupt request on a PDP-8.
     State:  a complete description of the condition of a piece of hardware
	  or of a task.
     Status:  that portion of the state which other devices or tasks  might 
	  be interested in.
     Subchannel:  1 of the 4 channels of a UDC analog functional device.
     Suspend:  to temporarily halt execution of a task while  another  task 
	  of higher priority runs.

				  GLOSSARY-4


     Symbols:  names which can be assigned values or which can be  used  to
	  indicate specific locations in a program.
     Synchronization:  a means of processing tasks (through event flags) so
	  that one task executes while others wait.
     System Ticks:  an RTS-8 convention designed to obviate  the  tasks  in 
	  the system from knowing the frequency of the clock.

     Task:  a routine which performs a specific function.
     Task Flags Table:  a table of l-word entries in  the  RTS-8  Executive
	  whose contents determine whether or not a task is runnable.
     Task Input Message Queue Header Table:   a  table  of  2-word  entries 
	  which  represent  the  head  of  the input message queue for each 
	  task.
     Task Number:  a unique number between 1 and 63 assigned to  each  task 
	  in an RTS-8 system.
     Task State Table:  a table of 4-word entries which contains  the  most
	  recent contents of CPU registers for each task.
     Task Switching:  the  act  of  stopping  execution  of  one  task  and 
	  continuing execution of another from the point that it was last
	  stopped.
     Task Synchronization:  logically ordering the execution of tasks.
     Terminal:  a peripheral device in a  system  through  which  data  can  
	  enter or leave the computer.

     Utilities:  routines to perform non-Monitor related functions.

     Word:  in the PDP-8, a 12-bit unit of data which may be stored in  one
	  addressable location.






























				  GLOSSARY-5


    				     INDEX


     Address, 5-1 			   POst, 5-6			
     Advanced programming techniques,	   REquest, 5-3			
	3-11				   STop, 5-4			
     AI (Analog Input), 4-11		   SYstat, 5-4
     ALTMODE character, 4-3, 5-1	   TIme, 5-2
     Analog I/O, 4-11			Component sizes, B-1		
     > (angle bracket) MCR response,	Console terminal handler, 4-3
	5-1				Console terminal module, B-1
     AO (Analog Output), 4-11		Core storage, 2-3, 6-3
     Assembler code, 6-2		Creating a real-time system, 6-2
     Assembling and loading tasks, 6-1	CS (Change of State), 4-15
     Assembly parameters, UDC, 4-16 	CTRL/C, 4-3, 5-1
     * (asterisk), 			CTRL/U, 4-3
	at end of line, 5-5 		CUR symbol, 6-2
     Auto-index registers, 6-2
     Auto-restart hardware option, 4-7
					Data Field, 3-10
					DAte command, 5-2
					DC (Disable Counter), 4-14
     BITMAP, 6-3			DCT (Disable Contacts), 4-15
     BLKARG ER (Block Task for speci-	DECassettes, 4-17
	fied reason), 3-6		Definitions, 6-1
					Deletion of a line or character, 4-3
					Demonstration program, 7-1
     CAL, 3-1				DEposit command, 5-6
     CAncel command, 5-4		DERAIL ER (Derail a Task's Execu-
     Carriage return, 4-3, 5-1		   tion), 3-8
     Cassette handler, 4-17		DF32 fixed-head disk, 4-5
     Cassette Label Support handler,	DF32/RF08 module, B-1
	4-18				DI (Digital Input), 4-12
     Cassette Label Support module, B-2 Digital I/O, 4-12
     Cassette module, B-2		Direct references to System Tables,
     Character mode input, 4-3		   3-12
     Character punch subroutine code, 	DIsable command, 5-4
	3-11 				Distribution tape, A-1
     Clear Wait bits, 3-6 		DO (Digital Output), 4-12
     Clock Handler, 4-1, 4-2 		Does Not Exist Wait, (DNEWT), 3-5
     Clock Handler calls, examples of,
	4-2
     Clock module, B-1 			EC (Enable Counter), 4-13
     Clock queue entries cancelled, 5-4 ECT (Enable Contacts), 4-14
     CLOSE, 4-18, 4-19			Emergency condition signals, 3-8
     Comma, 5-1				ENable command, 5-4
     Command arguments (MCR), 5-1	Enable Wait, (ENABWT), 3-5
     Commands, MCR			ENTER, 4-18, 4-19
	CAncel, 5-4			ER example, 3-3
	DAte, 5-2			ER (Executive Request), 3-1
	DEposit, 5-6			Error conditions, UDC, 4-16
	DIsable, 5-4			Errors, MCR, 5-6
	ENable, 5-4			Event Flag, 2-3
	EXamine, 5-6			Event Flag Wait, (EFWT), 3-5
	EXIT, 5-6			Event or Message Wait, (EORMWT), 3-5
	NAme, 5-2			EXamine command, 5-6
	OPen, 5-5

				    INDEX-1


     Examples,				Logical OR, 3-12
        Clock handler call, 4-2		LOOKUP, 4-18, 4-19
        ER, 3-3
        Mass Storage handler call, 4-7
        SUSPND and RUN ERs, 3-7		Mass storage handlers, 4-5
        Terminal handler messages, 4-5	   call, 4-7
     Executive, 2-1, B-1		MCR command arguments, 5-1
     Executive Requests (ERs), 3-1	MCR errors, 5-6
     Executive specifications, 6-1	MCR name table, 5-3
     EXIT command, 5-6			Memory address, 5-1
    					Message, cassette, 4-18
    					Message Header, 2-3
     Fields, 3-10, 4-8			Message Wait, (MSGWT), 3-5
     FINISHED value, 2-2		Messages, intertask, 2-3
     Fixed priority, 1-1		Messages to terminal handler, 4-3
     Flags Table, 2-1			Monitor Console Routine (MCR), 5-1
    					Monitor Console Routine task, B-2
    					Multiple terminals, 4-3
     GC (Generic Code), 4-12		Multiplier Quotient (MQ), 3-10
    					Multiprogramming, 1-1

     Handlers, 4-1
	Cassette, 4-17			NAme command, 5-2
	Cassette Label Support, 4-18	Non-console Terminal module, B-1
	Clock, 4-1			Null characters, 4-8
	Console terminal, 4-3
	Line Printer, 4-5
	Mass Storage, 4-5		OPen command, 5-5
	Terminal, 4-3			OR of several Event Flags, 3-12
	UDC, 4-10			OS/8 File Support module, B-2
     Hardware clocks, 4-1		OS/8 File Support Task, 4-9
     Header area, cassette, 4-18	OS/8 Support Task, 4-8


     Initialization code, 3-10		Page zero locations, 6-2
     INIWT symbol, 6-2			Parameter file, 6-1
     I/O, analog and digital, 4-10	PENDING value, 2-2
     Input Message Queue, 2-3, 3-2	POst command, 5-6
     Input Message Queue Header, 3-3	POSTDS instruction, 3-10
     Input Message Queue Header Table,	POST ER (Post Event Flag), 3-3
	2-2				Posting, 2-3
     Input mode, 4-3			Power Fail Task, 4-7
     Instruction field, 3-10		Power Fail module, B-2
     Interrupts, 3-9			Priorities, 1-1, 2-1
     Interrupt skip chain code, 3-11	Program Counter (PC), 3-1
     Intertask control, 3-5
     Intertask messages, 2-3
					Race condition, 3-12
					RC (Read Counter), 4-14
     Keyboard IOT code, 4-8		Real-time systems, 1-1
					RECEIVE ER (Receive Message), 3-2
					Record size of cassettes, 4-17
     LA30 terminals, 4-8		Reentrant programs, 3-1
     Line mode input, 4-3		REquest command, 5-3
     Line Printer handler, 4-5		RF08 fixed-head disk, 4-5
     Line printer module, B-1		RK8 disk module, B-2
     Loading tasks, 6-1			RK8E disk module, B-1

				     INDEX-2


     RK8 moving-head disks, 4-5		TSS-8 timesharing hardware option, 
     RK8E moving-head disk, 4-5		   4-8
     RUBOUT, 4-3
     RUN ER (Run a Task), 3-7
     Run Wait, (RUNWT), 3-5		UDC assembly parameter, 4-16
     					UDC Error conditions, 4-16
    					UDC handler, 4-10
     Scheduling tasks, 5-3		UDC assembly parameter, 4-16 
     SEND ER (Send Message), 3-1	UDC Error conditions, 4-16 
     SENDW ER (Send and Wait), 3-2	UDC handler, 4-10 
     Set Wait bits, 3-6			UDC module, B-2
     Sizes of components, B-1		UNBARG ER (Unblock Task for
     SKPINS ER (Insert Code into Skip	   Specified Reason), 3-6 
        Chain), 3-9			User Wait, (USERWT), 3-6
     Slash (/) character, 6-1		Using Interrupts, 3-9 
     Source files, A-1			Utility function, cassettes, 4-17
     Space, 5-1
     Starting address, 6-3
     START symbol, 6-2			VT05 terminals, 4-8
     State Table, 2-1
     STop command, 5-4
     Structure of RTS-8 tasks, 2-1	Wait Bits, 3-6 
     SUSPND ER (Suspend a Task's	WAITE ER (wait on Event Flag), 3-2 
	Execution), 3-6, 3-7 		WAITING state, 2-3 
     Swap Wait, (SWPWT), 3-5 		WAITM (Waiting for Multiple Event 
     Symbolic names, 6-1		   Flags), 3-11 
     Synchronization of tasks, 2-2	Word, 5-1
     SYstat command, 5-4
     System parameter file, 4-8
     system tables, direct references
	to, 3-12
     System tasks, 4-1
     System task specifications, 6-1
     System Wide definitions, 6-1


     Task (definition of), 1-1
     Task definitions, 6-1
     Task Flags Table, 2-1
     Task Flags Table entry, 3-5
     Task-ID, 5-1
     Task Input Message Queue Header
	Table, 2-2
     Task number, 2-1
     Task setup, 6-2
     Task State Table, 2-1
     Task switching, 3-1
     TASK symbol, 6-2
     TC08 DECtape, 4-5
     TC08 DECtape module, B-1
     Teleprinter IOT code, 4-8
     Terminals, 4-8
     Terminal handler, 4-3
     Ticks, 4-1
     TIme command, 5-2
     Time-of-day, 4-2, 5-1


				     INDEX-3

   		      HOW TO OBTAIN SOFTWARE INFORMATION

     SOFTWARE NEWSLETTERS, MAILING LIST     __________________________________

     The Software Communications Group, located at corporate headquarters in
     Maynard, publishes newsletters and Software Performance Summaries (SPS)
     for the various Digital products.  Newsletters are published monthly,
     and contain announcements of new and revised software, programming
     notes, software problems and solutions, and documentation corrections.
     Software Performance Summaries are a collection of existing problems
     and solutions for a given software system, and are published periodi-
     cally.  For information on the distribution of these documents and how
     to get on the software newsletter mailing list, write to:

			     Software Communications
			     P. O. Box F
			     Maynard, Massachusetts 01754

     SOFTWARE PROBLEMS     _________________

     Questions or problems relating to Digital's software should be reported
     to a Software Support Specialist.  A specialist is located in each
     Digital Sales Office in the United States.  In Europe, software problem
     reporting centers are in the following cities.

		    Reading, England 	    Milan, Italy
		    Paris, France 	    Solna, Sweden
		    The Hague, Holland      Geneva, Switzerland
		    Tel Aviv, Israel 	    Munich, West Germany

     Software Problem Report (SPR) forms are available from the specialists
     or from the Software Distribution Centers cited below.

     PROGRAMS AND MANUALS     ____________________

     Software and manuals should be ordered by title and order number.  In
     the United States, send orders to the nearest distribution center.

	  Digital Equipment Corporation     Digital Equipment Corporation
	  Software Distribution Center      Software Distribution Center
	  146 Main Street 		    1400 Terra Bella
	  Maynard, Massachusetts 01754 	    Mountain View, California 94043

     Outside of the United States, orders should be directed to the nearest
     Digital Field Sales Office or representative.

     USERS SOCIETY     _____________

     DECUS, Digital Equipment Computer Users Society, maintains a user
     exchange center for user-written programs and technical application
     information.  A catalog of existing programs is available.  The society
     publishes a periodical, DECUSCOPE, and holds technical seminars in the
     United States, Canada, Europe, and Australia.  For information on the
     society and membership application forms, write to:

	   DECUS			    DECUS
	   Digital Equipment Corporation    Digital Equipment, S.A.
	   146 Main Street		    81 Route de l'Aire
	   Maynard, Massachusetts 01754     1211 Geneva 26
     					    Switzerland