SRT8.DOC















    				  DISCLAIMER

		This document file was created by scanning  the 
		original  document and then editing the scanned 
		text.  As much as possible, the  original  text 
		format  was restored.  Some format changes were 
		made to insure this  document  would  print  on 
		current laser printers using 60 lines per page.
    		The  original  spelling  and  grammar  has been 
    		preserved.



   SSSSSSSSSSSS      RRRRRRRRRRRR	  TTTTTTTTTTTTTTT	  888888888
   SSSSSSSSSSSS      RRRRRRRRRRRR	  TTTTTTTTTTTTTTT	  888888888
   SSSSSSSSSSSS      RRRRRRRRRRRR	  TTTTTTTTTTTTTTT	  888888888
SSS		     RRR	 RRR		TTT	       888 	   888
SSS		     RRR	 RRR		TTT	       888 	   888
SSS		     RRR	 RRR		TTT	       888 	   888
SSS		     RRR	 RRR		TTT	       888 	   888
SSS		     RRR	 RRR		TTT	       888 	   888
SSS		     RRR	 RRR		TTT	       888 	   888
   SSSSSSSSS	     RRRRRRRRRRRR		TTT 		  888888888
   SSSSSSSSS	     RRRRRRRRRRRR		TTT 		  888888888
   SSSSSSSSS	     RRRRRRRRRRRR		TTT 		  888888888
	    SSS	     RRR   RRR			TTT	       888	   888
	    SSS	     RRR   RRR			TTT	       888	   888
	    SSS	     RRR   RRR			TTT	       888	   888
	    SSS	     RRR      RRR		TTT	       888 	   888
	    SSS	     RRR      RRR		TTT	       888 	   888
	    SSS	     RRR      RRR		TTT	       888 	   888
SSSSSSSSSSSS	     RRR	 RRR		TTT		  888888888
SSSSSSSSSSSS	     RRR	 RRR		TTT		  888888888
SSSSSSSSSSSS	     RRR	 RRR		TTT		  888888888
				



DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC
DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC
DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDD	    DDD      OOO 	 OOO	  CCC
DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC
DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC
DDDDDDDDDDDD		OOOOOOOOO	     CCCCCCCCCCCC



LPTSPL Version 4(137)	Running on LPTl
 *START* User LARY,RICHARD [120,266] job  SRT8 seq, 10096 Date 07-Feb-74 14:51:10
Request created: 07-Feb-74 10:50:18
Flle: DSKB0:SRT8.DOC[l20,266] Created: 07-Feb-74 10:30:00 <057> Printed: 07-Feb-74
QUEUE Switches:  /PRINT:ARROW /FILE:ASCII /COPIES:3 /SPACING:l /LIMIT:302




	      The information in this  document  is  subject  to
	      change  without notice and should not be construed
	      as a commitment by Digital Equipment  Corporation.
 	      Digital    Equipment    Corporation   assumes   no
	      responsibility for any errors that may  appear  in
	      this manual.

  	      The  Software  described  in  this   document   is
	      furnished to the purchaser under a license for use
	      on a single computer  system  and  can  be  copied
	      (with  inclusion  of  DIGITAL's  copyright notice)
	      only  for  use  in  such  system,  except  as  may
	      otherwise be provided in writing by DIGITAL.

	      Digital   Equipment   Corporation    assumes    no
	      responsibility  for  the use or reliability of its
	      software on equipment  that  is  not  supplied  by
	      DIGITAL.

	      Copyright.  (C)   1973,   by   Digital   Equipment
	      Corporation.


      SRT-8 User's Manual					      Page 2
      Introduction


			   What is a Real-Time System?



      A real-time System is a software framework under which  the  resources
      at  hand  (core,  CPU  time,  peripheral  devices) are divided up in a
      deterministic  manner  among  Several  tasks.   The  term  "task"   is
      difficult  to define, as it overlaps with the definitions of "program"
      and "subroutine", but basically a task is  a  piece  of  machine  code
      which  performs  a specific function, sometimes related to the outside
      world and sometimes related only to the needs  of  other  tasks.   The
      real-time  system distributes resources to tasks at any time depending
      on whether they can make use of them, and whether  a  more  privileged
      (higher priority) task wants to pre-empt them.



				  What is SRT-8?

	

      SRT-8 is a real-time system for the family-of-8. It allows  up  to  64
      tasks to run concurrently, competing for resources on a fixed-priority
      basis, included in the SRT-8 system are  system  tasks  which  control
      standard  Digital  Equipment Corporation I/O gear, a task which allows
      interactive system control from the console Teletype and a task  which
      allows  a  single  copy  of  the  OS/8  monitor  system  to run in the
      background.


      SRT-8 User's Manual					      Page 3
      Introduction


			     What is a task under SRT-8?



      A task under SRT-8 Consists of the following parts:

	   1.  A  Task  Number, a  number  from  1  to  the  maximum  number
	       assembled  into  the  system  (but always less than 64) which
	       determines the task's priority (the  lower  the  number,  the
	       higher the priority) and also serves as an index into various
	       system tables.

	   2.  A Task State Table entry, four words long, which is  used  to
	       store the task's PC, AC, etc. when the task is not running.

	   3.  A Task Flags table entry, one word long, which contains  bits
	       which indicate if the task can run, or why it cannot.

	   4.  A Task input Message Queue Header, two words long,  which  is
	       the   beginning  of  the  task's  input  message  queue,  all
	       inter-task communication in SRT-8,  is  done  via  "messages"
	       (blocks of core) sent between tasks.

	   5.  The task coding itself, which consists of PDP-8  instructions
	       interspersed with calls to the SRT-8 executive for services.



      SRT-8 User's Manual					      Page 4
      Concepts


    			    How Do Tasks communicate?



      There are two main types  of  task  communication  in  SRT-8 - message
      sending  and  synchronization, since synchronization is more basic, we
      will discuss it first.

      Task Synchronization and Event Flags

      Whenever two processes occur independently, there will be a  need  for
      one  to  wait  on  the  other.  The most common example of this is the
      PDP-8 Teletype interface.  The Teletype sits  there  waiting  for  the
      PDP-8  to produce a character worth printing.  When the PDP-8 has one,
      it "wakes up" the Teletype by issuing a TLS instruction.  If the PDP-8
      then  has another character to print, it must first "go to sleep" in a
      TSF;JMP .-1 loop until the Teletype signals that  it  is  finished  by
      raising  the  ready flag.  Then the PDP-8 "wakes up" from its loop and
      proceeds to print the next character.

      Similarly, tasks in SRT-8 may synchronize with each other by means  of
      Event Flags.  An Event Flag is a location which contains the status of
      an Event.  An Event is anything which is  important  enough  that  you
      would  want  to  keep track of it with an Event Flag (How's that for a
      circular definition?). Like the Teletype ready flag, an Event Flag has
      the  states  PENDING(>0)  and  FINISHED(<0).  So,  a task could (via a
      message) direct another task to perform some action, at which time  it
      would  set  a  (mutually agreed upon) Event Flag to the PENDING value.
      When the other task was finished it would set the Event  Flag  to  the
      FINISHED value (this is known as Posting the Event Flag). If the first
      task had been waiting for the Event Flag with a:

      TAD Event Flag;  SZA CLA;  JMP .-2

      then the Posting of the Event Flag would "wake up" the first task from
      its loop.

      Unfortunately, the above mentioned loop ties up  a  vitally  important
      resource - the  PDP-8  processor.   Therefore,  in SRT-8 (and here the
      analogy to  the  Teletype  breaks  down)  Event  Flags  have  a  third
      state:  WAITING(<0).  In  the example above, the first task would tell
      the SRT-8 executive it  wanted  to  wait  until  the  Event  Flag  was
      FINISHED - the  monitor  would save the task's PC and mark in its Task
      Flags Table word that it was waiting on an Event  Flag,  and  set  the
      Event Flag to the proper WAITING state (the proper WAITING state being
      octal 4000 plus the waiting task's Task Number).  When the Event  Flag
      is POSTed (via an SRT-8 executive call) the task which was waiting for
      it will automatically be "awakened" by SRT-8.  The  mnemonic  for  the
      SRT-8 Executive Request which waits for an event flag is WAITE.


      SRT-8 User's Manual					      Page 5
      Concepts


      Intertask Messages

      Just as Event Flags in SRT-8 are analogous to hardware  device  flags,
      messages are analogous to instructions like TLS - i.e. they start up a
      task (provided the task  was  waiting  for  a  message)  and  pass  it
      information at the same time.  A Message in SRT-8 is a contiguous area
      of core storage.  SRT-8 requires the first three words of the  message
      (the  Message  Header)  for  its use; the rest may contain any desired
      information.  Sending a message does not physically move  the  message
      information  to the receiving task, but provides the receiver with the
      field and address of the first data word of the message,

      If the receiving task is not waiting  for  messages,  the  message  is
      placed  on  the  receiving  task's  input Message Queue.  Messages are
      queued in order of decreasing priority (increasing task number) of the
      Sender  (and  in  the order issued if equal priority).  The Second and
      third words of the Message Header are used as a  CDF-address  Pair  to
      link the message to the next queue entry.

      The first word of the Messages  Header  is  the  Event  Flag  for  the
      message.   When  the  message  is  sent,  the Event Flag is put in the
      PENDING state by the SRT-8 Executive; nothing  happens  to  the  Event
      Flag  on  receipt  of  the  message  by  the receiving task, but SRT-8
      protocol requires that when the receiver is done with the  message  he
      Posts the Event Flag.

      Note again that the information in a message is not  copied  into  the
      receiver's area - this has several implications:

	   1.  Data in a message should not be modified by the sender  while
	       the Event Flag for the message is PENDING.

	   2.  The same message cannot be sent a  second  time  before  it's
	       Event  Flag  is FINISHED from the first time.  SRT-8 enforces
	       this by checking the Message Event Flag on a  SEND  operation
	       and  putting  the  sender into Event Flag Wait if it is still
	       PENDING.

	   3. It is legal for the receiving task to store  information  into
	      the  body  of  the  message - in  this  way an "answer" to the
	      message  can   be   returned   without   going   through   the
	      complications  of sending a return message back to the sender.
	      For example, when a task sends a message to  the  disk  driver
	      task  requesting  I/O,  the  error  status  of  the  completed
	      operation is placed in a specific word in the message  by  the
	      driver to indicate whether an error occurred.


      SRT-8 User's Manual					      Page 6
      Executive Requests


			SRT-8 Executive Requests (E.R.s)



      SRT-8  tasks  communicate  with  the  SRT-8  Executive  via  Executive
      Requests  (abbreviated  as ERs).  In order to make E.R.s simple across
      field boundaries, SRT-8 uses locations  20-27  in  every  field  as  a
      Communication  region for E.R.s.  The Executive is called in any field
      via a JMS 20 instruction (hereafter referred to as a  CAL).  The  Data
      field  does not have to be any specific value when the CAL is given as
      the code in location 20 sets the DF to the IF, sets the IF  to  0  and
      jumps to the SRT-8 Executive.

      Because the architecture of  the  PDP-8  does  not  permit  re-entrant
      programs,    the    SRT-8    Executive    runs   with   task-switching
      inhibited - i.e. interrupts are on but higher priority tasks  may  not
      grab  the  CPU  until  the  Executive  has finished its Request.  When
      the Executive finishes processing on the request it checks whether any
      higher  priority  tasks  became  runnable  while  task  switching  was
      inhibited, and if so it runs the highest priority of these.

      Also, because of the non-reentrant  architecture  of  the  PDP-8,  the
      SRT-8  Executive  will  not  honor any request to switch tasks arising
      from an interrupt if the interrupted task's PC was less than 100. This
      is  done  to  protect location 20 in each field (the SRT-8 Executive's
      entry point) from being destroyed. User tasks should BE CAREFUL  NEVER
      to execute any instructions below 100 in a field.

      There are 5  E.R.s  associated  with  the  Messages  and  Event  Flags
      described in the last section, They are:



		SEND	  Send Message

		format:	  CAL
			  SEND
			  TSKNUM
			  MESSAG

      This ER sends the message located at MESSAG in the  current  field  to
      the   task   whose  number  is  TSKNUM.   If  the  receiving  task  is
      higher-priority than the sender, and was waiting for  a  message,  the
      sender  is  temporarily suspended and the receiver runs.  In any case,
      the sender is not put into any Wait state once the  message  is  sent.
      As stated previously, however, if the event flag in location MESSAG is
      PENDING (non-zero) meaning the message is still busy from  a  previous
      SEND,  the sender will be put into Event Flag Wait on location MESSAG.
      and only when the Event Flag becomes FINISHED (zero) will this SEND be
      performed.	


      SRT-8 User's Manual					      Page 7
      Executive Requests


		WAITE 	  Wait on Event Flag

		format:   CAL
			  WAITE
			  EFLG

      This ER checks the  status  of  location  EFLG - if  it  is  FINISHED,
      control returns to the caller.  If it is PENDING, its state is changed
      to WAITING and the calling task is put into  Event  Flag  Wait.   When
      location  EFLG  is  POSTed  by  another task or interrupt routine, the
      calling task becomes runnable again.



		SENDW	  Send and wait

		format:	  CAL
			  SENDW
			  TSKNUM
			  MESSAG

      This ER is exactly equivalent to the sequence:

			  CAL
			  SEND	    /Send the message
			  TSKNUM
			  MESSAG
			  CAL
			  WAITE
			  MESSAG    /Wait for receiver to acknowledge


      SRT-8 User's Manual					      Page 8
      Executive Requests


		RECEIVE   Receive message

		format:	  TAD RESTRICTION     /Only if we want to restrict
			  CAL		      /sending tasks
			  RECEIVE
		   MADDR, 0	    /Message address-stored here
				    /CDF to message field in AC
				    /on return

      If the AC is zero when the RECEIVE ER  is  issued,  RECEIVE  works  as
      follows:

      If there are messages in the calling task's Input Message  Queue,  the
      first  (i.e.  highest-priority) message is dequeued and the address of
      its first data word is placed in MADDR.  A CDF to  the  field  of  the
      message  is  put  in  the  AC.  If there were no messages, the task is
      placed in message wait until such time as there are any.  There is  no
      ER  which  allows  a task to check for messages without being put into
      Message Wait if there are none, but  a  task  may  examine  its  Input
      Message Queue Header in field 0 to find this out.

      If the AC is non-zero when the  RECEIVE  ER  is  issued,  the  calling
      task's  input  Message  Queue is searched for a message whose sender's
      Task Number matches the contents of the AC.   If  such  a  message  is
      found,  it  is  removed  from the queue as specified above; if none is
      found the issuing task is placed in Message Wait.



		POST	  Post Event Flag

		format:	  TAD EFPTR   /Pointer to Event Flag
			  CAL
			  POST
		   EFCDF, CDF EFFLD   /Field of Event Flag

      The Event Flag pointed to by the AC at the CAL,in the field  specified
      by  EFCDF, is set to the FINISHED (zero) state.  If its previous state
      was WAITING, the task which was waiting on it is cleared of its  Event
      Flag  Wait.   This ER never puts the calling task in a Wait state, but
      if the task waiting for the Event Flag is higher priority the  calling
      task is temporarily suspended while that one is run.


      SRT-8 User's Manual					      Page 9
      Executive Requests


    				     Example



      This example illustrates the SRT-8 E.R.s  dealing  with  messages  and
      Event  Flags.   Since  we  have not discussed I/O and interrupts under
      SRT-8 yet, this example is trivial; i.e. there are  no  advantages  to
      keeping  the  functions  of  our  two  tasks  separate,  and the whole
      send/receive structure is being used as an elaborate subroutine call.

		    TASK A 			    TASK B

      LOOP, CAL 			 LOOP,	CAL
	    SEND   /send B a message      (4) 	RECEIV	    /get a message
       (1)  B				 MADDR, 0
	    MES1				DCA EFCDF   /save CDF for POST
	    CAL					TAD EFCDF
       (2)  SEND   /and another			DCA .+1	    /Put CDF inline
	    B					HLT	    /CDF to message
	    MES2					    / field
    	    CAL				  (5)	TAD I MADDR /Get 1st data word
       (3)  WAITE  /Wait for first one 			    / of message
	    MES1				CLA	    /I said this was
       	    JMP LOOP /loop	  			    / trivial example!	
	    					STA CLL RTL /-3 in AC
      MES1, ZBLOCK 3				TAD MADDR   /AC points to
	    15					CAL	    / message
	    37					POST	    / event-flag
	    23				EFCDF,  HLT	    /CDF to message
	    TEXT   /HIKE!/				    / field here
	    					JMP LOOP    /loop
      MES2, ZBLOCK 3		
	    -1
	     4

      The flow of execution in this example depends  on  which  of  the  two
      tasks  is higher priority.  Assuming that at some point in time both A
      and B both become runnable, if task A is higher priority the  sequence
      of execution is:

	   1, 2, 3, 4, 5, 1, 2, 4 (2 cannot be executed because MES2 is
	   Still PENDING), 5, 2, 3, 4, 5, 1, 2, 4, 5, 2, 3, 4, 5, etc.

      if task B is higher priority the sequence is:

	   4, 1, 5, 4, 2, 5, 4, 3, 1, 5, 4, 2, 5, 4, 3, etc.


      SRT-8 User's Manual					     Page 10
      Executive Requests


		Inter-task control through Task Flags Table entry

      A task's Task Flags Table entry is used by SRT-8 to determine  if  the
      task  can  run.   A  zero  Task Flags Table entry indicates a runnable
      task.  Each bit which is on in a non-zero word indicates a reason  why
      the task cannot run.  The currently defined bits and their meaning, if
      set, are:

		DNEWT	  Does Not Exist Wait - This Task cannot run because
			  it is non-existent.

		MSGWT	  Message Wait - this task is waiting for someone to
			  send it a message.

		EFWT	  Event Flag Wait - this task is  waiting  for  some
			  Event   Flag   (which  contains  a  WAITING  value
			  corresponding to this task) to be Posted.

		SWPWT     Swap Wait - This Task cannot run because it is not
			  in  core  -  this bit is reserved for future SRT-8
			  releases.

		RUNWT     Run Wait - this task is waiting for a RUN ER to be
			  executed  with  its  number  in the AC, or for the
			  operator to type "REQUEST  task"  to  the  Monitor
			  Console Routine.

		EORMWT    Event or Message Wait - this task is  waiting  for
			  an  Event  Flag  to be set or a message to arrive,
			  whichever comes first.

		ENABWT	  Enable Wait - this task is waiting to be  Enabled.
			  Use  of  this  bit  is  restricted  to the Monitor
			  Console Routine for use by the "ENABLE  task"  and
			  "DISABLE task" commands.

		USERWT    User Wait -  this  bit  is  reserved  for  use  by
			  user-written tasks.  SRT-8 will not touch this bit
			  at all.


      SRT-8 User's Manual					     Page 11
      Executive Requests


      Several ER's exist which allow a task to explicitly set and clear wait
      bits  in  other  task's Task Flags Table entry, and to set bits in its
      own.


	  BLKARG - Block task for specified reason:

			  Format: TAD TASKNUM	/OR 0 IF MYSELF
				  CAL
    				  BLKARG
    				  WAITBITS

      Where TASKNUM contains the number of  the  task  to  be  blocked,  and
      WAITBITS  specifies  one or more bits to be set on in that task's Task
      Flags word.  Assuming  WAITBITS  is  non-zero,  this  will  cause  the
      specified  task  to  become  non-runnable.   If TASKNUM contains 0 the
      issuing task  will  be  blocked  on  the  specified  wait  bits.   The
      TASKNUM=0 form of this ER is the only legal way to specify the issuing
      task as the task to be blocked; if TASKNUM is  equal  to  the  issuing
      task number the action of this ER is undefined.



	  UNBARG - Unblock task for specified reason

		Format:   TAD TASKNUM
			  CAL
			  UNBARG
			  WAITBITS

      Where TASKNUM contains the number of the task to unblock, and WAITBITS
      specifies  one  or  more  bits to be cleared in that task's Task Flags
      Word.  If the Task-Flags  word  becomes  zero  as  a  result  of  this
      operation  the  specified task becomes runnable. If the specified task
      is of higher priority than the issuing task and becomes runnable,  the
      issuing task is temporarily suspended while that task runs.

      This ER is a no-op if issued with TASKNUM equal to the issuing  task's
      number.



      SRT-8 User's Manual					     Page 12
      Executive Requests


	  SUSPND - Suspend a task's execution

		Format:	  TAD TASKNUM 		 /0 IF MYSELF
			  CAL
			  SUSPND

      This E.R. is identical in action to the following:

			  TAD TASKNUM
			  CAL
			  BLKARG
			  RUNWT



	  RUN - Run a task

		Format:	  TAD TASKNUM
			  CAL
			  RUN

      This E.R. is identical in action to the following:

			  TAD TASKNUM
			  CAL
			  UNBARG
			  RUNWT

      The SUSPND and RUN E.R.s exist because  their  function  is  performed
      sufficiently  often to warrant a shorthand version.  An example of how
      they could be used is:



      SRT-8 User's Manual					     Page 13
      Executive Requests


      A data collection task would like to print a report  every  1000  data
      points without interrupting the data collection/reduction process.

	      DATA task				  REPORT task

      LOOP,   TAD (1750   /1000 DECIMAL	    LOOP, CAL       /AC=0, SUSPEND
	      DCA COUNT				  SUSPND    /ME UNTIL NEEDED
      DATALP, CAL				  JMS TITLE /I'VE BEEN RUN
	      WAITE				  .
	      DATAEF				  .	    /PRINT REPORT
	      .		  /GET A DATA POINT       .	    /WITH TITLE.
	      ISZ COUNT   /AND PROCESS IT.	  .
	      JMP DATALP  /COUNT OFF 1000	  .
	      TAD (REPORT /POINTS		  .
	      CAL 	  /RUN REPORT TASK	  JMP LOOP  /REPORT OVER.
	      RUN					    /GO BACK AND
	      JMP LOOP    /KEEP COLLECTING		    /WAIT.
      COUNT,  0

      Of course, to eliminate interference with the data collection,  REPORT
      Should be a lower priority task than DATA.


      There is one task control ER which does not cause any wait bits to get
      set  or  cleared,  but which derails the execution of a specified task
      into a subroutine:

	   DERAIL - Derail a task's execution

		Format:   TAD TASKNUM
	 		  CAL
			  DERAIL
			  ADDR

      This ER causes a "JMS ADDR" to be simulated for the task whose  number
      is  contained  in TASKNUM.  ADDR is assumed to be in the same field in
      which the specified task is executing.  The specified task's PC  (from
      its Task State Table entry) is stored in ADDR, and the PC entry in its
      Task State Table entry is then set to ADDR+1.  Two important things to
      note about the operation of the DERAIL ER:

	   a.  The specified task's AC, LINK, and Data Field setting are not
	       saved  by  the  DERAIL  ER - therefore they must be saved and
	       restored by the derail subroutine.  In this sense,  a  derail
	       subroutine is very much like an interrupt at the task level.

	   b.  The contents of the specified tasks Task Flags word  are  not
	       affected  by  the  DERAIL  ER.  If the specified task was not
	       runnable, the derail subroutine would not be  executed  until
	       it became runnable.


      SRT-8 User's Manual					     Page 14
      Executive Requests


			Waiting for multiple Event Flags


      Sometimes it is desirable to wait on a logical combination (AND or OR)
      of  event  flags.   Waiting  on  the logical AND of two event flags is
      quite simple; the sequence:

			  CAL
			  WAITE
			  A 	    /WAIT FOR EVENT FLAG A
			  CAL
			  WAITE
			  B	    /AND THEN WAIT FOR EVENT FLAG B

      Waits until both A and B have been posted.

      Waiting on the logical OR of several event flags  is  more  difficult,
      since there is a possible race condition between the various tests and
      the interrupts  (or  task  executions)  which  POST  the  Event  Flags
      involved.   The  key  to  waiting  for  an  OR  of several Event Flags
      successfully is not to allow  any  interrupts  to  occur  between  the
      testing  of the first Event Flag and the placing of the task in a wait
      state if none of the flags were POSTed.

      To accomplish this requires a special sequence of instructions  and  a
      special  SRT-8  call  named WAITM.  WAITM is currently defined to be a
      JMS I 25.  It must be executed with interrupts  off,  the  Instruction
      Field  set  to  0  and the Data Field set to the current field, and it
      must be followed by a word containing the blocking bit(s) to be set in
      the Task Flags Table.  The action of WAITM is equivalent to the action
      of the SRT-8 ER BLKARG except that  a  fast  path  through  the  SRT-8
      Executive  is  taken and interrupts remain off until the blocking bits
      are on in the Task Flags Table.


      SRT-8 User's Manual					     Page 15
      Executive Requests


      For an example of the use of WAITM, assume that a task "TASK" wants to
      test two event flags A and B. If A is POSTed we want to go to location
      ADONE, and if B is POSTed we want to go to location BDONE.  If neither
      is  POSTed  we want to wait until one of them is.  The code to perform
      this function is:

      TESTAB, IOF	       /INTERRUPTS OFF - DELICATE CODE!
	      TAD A
	      SNA CLA
	      JMP ADONE	       /ADONE must turn interrupts on!
	      TAD (4000+TASK
	      DCA A	       /set A to WAITING state
	      TAD B
	      SNA CLA
	      JMP BDONE	       /BDONE must turn interrupts on!
	      TAD (4000+TASK
	      DCA B	       /set B to WAITING state
	      CIF 0
	      CDF CUR
	      WAITM
	      EFWT 	       /block task on EFWT
	      JMP TESTAB       /we're back - one of them is POSTed - which?


      SRT-8 User's Manual					     Page 16
      Executive Requests


			       Interrupts in SRT-8	



      The SRT-8 executive contains code to receive  and  dismiss  interrupts
      and  to  perform  interrupt-initiated  task switching, but it does not
      provide room for an interrupt skip chain, instead,  the  "skip  chain"
      is literally a chain and is built up dynamically via the following ER:

		SKPINS    Insert code into skip chain

		Format:	  CAL
			  SKPINS
			  MODULE

      Where MODULE is the address (in the current  field)  of  an  interrupt
      processing  module.   An interrupt processing module has the following
      format:

	MODULE, 0 		  /this word gets a pointer
				  /to the next module
		0		  /module entered here - contains
				  /CDF CIF next module field
		SKDR		  /skip on device ready
		(SKP)		  /(only if SKDR really means skip on
				  /device not ready)
		JMP I MODULE	  /not ready - go to next module in chain
		CDF CIF CUR	  /this one is mine - set DF and IF
				  /correctly
		.		  /interrupt processing
		.
		.
		CIF 0
		POSTDS 		  /dismiss the interrupt, maybe POST
				  /an Event Flag

      The SRT-8 interrupt skip chain initially consists of one such  module,
      for  the  system  clock.   Whenever  a  task executes a SKPINS ER, the
      interrupt chain is broken at the very  end  and  the  users  interrupt
      module is inserted.  The last interrupt module points to the interrupt
      dismiss routine as its "next module", so that SRT-8 will try to  avoid
      superfluous  interrupts.  Notice that SKPINS always inserts at the end
      of the skip chain.  This implies that the skip in the skip chain  will
      be  ordered roughly by priority of the task which inserted them, since
      SKPINS E.R.s in a task are  usually  executed  as  once-only  code  at
      system startup time.


      SRT-8 User's Manual					     Page 17
      Executive Requests


      Once an interrupt module receives control  (by  having  its  I/O  skip
      succeed) there are several restrictions on its execution:

	   a.  The Data Field and Instruction Field are those  of  the  NEXT
	       interrupt module - this must be corrected before any indirect
	       addressing or Jumps are performed.

	   b.  An interrupt module may not issue SRT-8 E.R.s

	   c.  An interrupt module should  not  compute  excessively,  since
	       interrupts  are  off  - typical execution time should be < 50
	       microseconds.  If considerably more time than this is needed, 
	       it  should be done at the task level and not at the interrupt 
	       level.

	   d.  Interrupt modules should not turn interrupts on, as the state
	       of  the  interrupted  task  may  be  destroyed  by  a  second
	       interrupt;

	   e.  On entry to the interrupt module the AC, Link, and Data Field
	       have  already  been  saved,  but  the  MQ has not.  Therefore
	       interrupt modules wishing to use the MQ should save it  first
	       and restore it before dismissing.

	   f.  Interrupt module should dismiss the interrupt by setting  the
	       Instruction  Field  to  0  and  issuing a POSTDS instruction,
	       POSTDS is currently a JMP I 24.  An Event Flag may be  posted
	       when  the interrupt is dismissed by setting the Data Field to
	       the field of the Event Flag and placing the location  of  the
	       Event  Flag  in  the  AC  prior  to  issuing the POSTDS - for
	       example.

	       CDF CUR	     /DF = THIS FIELD
	       TAD (EVFLG    /EVFLG MAY NOT BE AT LOC 0!
	       CIF 0		
	       POSTDS	     /DISMISS INTERRUPT AND POST EVFLG

      SRT-8 does not currently provide a mechanism for  dynamic  removal  of
      entries  from  the  interrupt skip chain.  When a disk - resident task
      facility is added, dynamic removal will be implemented as well.


      SRT-8 User's Manual					     Page 18
      System Generation


    		      Assembling and Loading Tasks for SRT-8

      SRT-8 tasks are assembled with the OS/8 PAL8 assembler and the use  of
      a  parameter file.  SRT-8 parameter files are all edited versions of a
      master parameter file which is included in  the  distributed  sources.
      All  definitions  in  the  master file which are to be supplied by the
      user are left blank in the file; i.e. a sample line in the file  might
      be:

      PDP8E= /SET TO 1 IF PDP8E, ELSE 0

      THERE SHOULD RE A  UNIQUE  PARAMETER  FILE  CREATED  FOR  EVERY  SRT-8
      ENVIRONMENT.   WHERE  ENVIRONMENT  IS  A COMBINATION  OF THE AVAILABLE
      HARDWARE AND THE SET OF  TASKS  BEING  RUN.   THE  PARAMETER  FILE  IS
      DIVIDED INTO 5 SECTIONS:

       A.  EXEC SPECIFICATIONS - THESE SPECIFICATIONS CONTROL  THE  ASSEMBLY
	   OF  THE SRT-8 EXEC AND THEREFORE MUST BE INCLUDED.  THEY INCLUDE:
	   WHETHER THE MACHINE IS A PDP-8E,  HOW  MUCH  CORE  IS  AVAILABLE,
	   WHETHER  TO  SAVE/RESTORE  THE  MQ, HOW MANY TASKS IN THE SYSTEM,
	   ETC.

       B.  TASK DEFINITIONS - THIS SECTION DEFINES SYMBOLIC  NAMES  FOR  THE
	   VARIOUS  SYSTEM  TASKS  IN  THE  SYSTEM.  THE NAMES OF ALL SYSTEM
	   TASKS WHICH ARE TO BE INCLUDED IN THE SYSTEM  SHOULD  BE  DEFINED
	   HERE,  AND  ANY SYSTEM TASK WHICH IS NOT INCLUDED SHOULD HAVE THE
	   LINE WHICH DEFINES IT DELETED FROM THIS  SECTION.   THE  USER  IS
	   ENCOURAGED  TO  ADD SYMBOLIC DEFINITIONS OF HIS OWN TASKS TO THIS
	   SECTION.

       C.  SYSTEM TASK SPECIFICATIONS -  THESE  SPECIFICATIONS  CONTROL  THE
	   ASSEMBLIES  OF  VARIOUS  SYSTEM  TASKS.  THEY INCLUDE THE DESIRED
	   CLOCK RATE, THE NUMBER OF FIELDS TO ALLOCATE THE OS/8, ETC.   THE
	   SET OF PARAMETERS CONTROLLING A TASK ARE ALL GROUPED TOGETHER AND
	   ASSEMBLED CONDITIONALLY, ONLY IF THE TASK NAME IS DEFINED.

       D.  SYSTEMWIDE DEFINITIONS - THESE INCLUDE  THE  DEFINITIONS  OF  THE
	   SYMBOLS  USED IN THIS DOCUMENT TO DESCRIBE THE EXECUTIVE REQUESTS
	   AND TASK FLAG BITS, PLUS MANY  OTHER  USEFUL  DEFINITIONS.   THIS
	   SECTION SHOULD NOT BE ALTERED BY USERS.


      SRT-8 User's Manual					     Page 18
      System Generation


       E.  TASK SETUP - THIS SECTION USES FOUR SYMBOLS DEFINED IN  THE  BODY
	   OF THE USER'S TASK TO SETUP THE SRT-8 TABLE ENTRIES NEEDED TO PUT
	   THAT TASK IN THE SYSTEM.  THE FOUR SYMBOLS NEEDED ARE:

	   TASK	     DEFINED TO BE THE TASK NUMBER OF THE TASK

	   CUR	     DEFINED TO CONTAIN THE  FIELD  OF  THE  TASKS  STARTING
		     ADDRESS IN BITS 6-8 (E,G,, CUR=10)

	   START     DEFINED  TO  BE  THE  TASK'S  STARTING   ADDRESS   (NOT
		     NECESSARILY THE LOWEST ADDRESS IN THE TASK)

	   INIWT     DEFINES THE INITIAL WAIT BITS IN THE TASK FLAGS TABLE -
		     INIWT=0 MEANS THE TASK IS RUNNABLE WHEN THE SYSTEM
		     STARTS UP,

	   UP  TO  THREE  TASKS  MAY  BE  DEFINED  IN  ONE  ASSEMBLY  -  THE
	   CORRESPONDING  SYMBOLS  FOR  THE OTHER TASKS ARE TASK2 AND TASK3,
	   CUR2 AND CUR3, ETC.  THE TASK SETUP SECTION PLACES ITS DATA  INTO
	   THE  SRT-8  TABLES BY ORIGINING INTO THEM - NO EXECUTABLE CODE IS
	   GENERATED.

      TO CREATE A REAL-TIME SYSTEM  USING SRT-8, FIRST LAYOUT THE TASKS  YOU
      WILL  NEED ON PAPER.  THEN CREATE A PARAMETER FILE WITH THE PARAMETERS
      FOR THAT SYSTEM, AND ALLOCATE CORE STORAGE AMONG  THE  EXECUTIVE,  THE
      SYSTEM  TASKS, AND YOUR OWN TASKS.  WRITE YOUR TASKS AND ASSEMBLE EACH
      TASK PRECEDED BY THE PARAMETER FILE.  LOAD THE RESULTING BINARIES WITH
      OS/8  ABSLDR,  PLACING  THE SRT-8 BINARY FIRST.  AT THIS POINT YOU MAY
      START YOUR SYSTEM, OR SAVE IT AS CORE IMAGE FILE TO BE RUN LATER.

      AN SRT-8 SYSTEM CREATED AS ABOVE HAS A STARTING ADDRESS OF 00200.   IF
      SRT-8  WAS  NOT  SPECIFICALLY  CONFIGURED  FOR  A PDP 8/E IT WILL HALT
      INITIALLY SO THAT THE OPERATOR  MAY  CLEAR  ANY  STRAY  DEVICE  FLAGS.
      PRESS  START  TO  RESUME  OPERATION  ON A PDP 8, 8/I OR 8/L; PRESS I/O
      PRESET FOLLOWED BY CONTINUE ON A PDP-12.



      SRT-8 User's Manual					     page 20
      SYSTEM TASKS


			       SRT-8 SYSTEM TASKS


      THE SOURCES OF THE SYSTEM TASKS ARE SUPPLIED WITH  THE  SRT-8  SYSTEM.
      THE  TASKS  REFERRED  TO AS "HANDLERS" ARE COMPLETELY MESSAGE-DRIVEN -
      I.E. WHEN IDLE THEY ARE IN THE MESSAGE WAIT STATE,  OTHER  TASKS  SEND
      THESE  HANDLERS  I/O  request messages, and when the handler completes
      the I/O operation it sets the Event Flag associated with  the  request
      message and issues another RECEIVE ER.

	   1.  Clock Handler

	       This task can be assembled to handle  any  of  four  hardware
	       clocks  (DK8EA, DK8EC, DK8EP, KW12. , It accepts requests (in
	       the form of  SRT-8  messages)  to  perform  actions  after  a
	       specified  time  has  elapsed.   The  clock  handler  uses an
	       interval queue whose length is fixed at assembly time to keep
	       track of its pending requests.

	       The format of a clock message is:

	       CLKMSG,	ZBLOCK 3	/3 WORDS RESERVED FOR SRT-8
			COMMAND+TASKNO	/TASKNO=0 MEANS TASKNO=SENDING TASK
			TIMEHI
			TIMELO
			EXTRA1
			EXTRA2

	       The words TIMEHI and TIMELO specify a time interval from  the
	       present  time  in terms of "system ticks".  The duration of a
	       "system tick" is specified by the user in the SRT-8 parameter
	       file  via  the  parameter  SHERTZ.  The hardware tick rate is
	       specified by the parameter HERTZ.  HERTZ  must  be  an  exact
	       multiple  of  SHERTZ.   For  example,  the  parameters  for a
	       line-frequency clock might be:

			DECIMAL
			HERTZ=  60
			SHERTZ= 10

	       Indicating that only l/10 Second resolution is  necessary  in
	       the clock handler.

	       The clock handler is referred to by other SRT-8 system  tasks
	       via  the  symbol CLOCK.  This symbol should be defined in the
	       SRT-8 parameter file to be equal to the clock handler's  Task
	       number.   It should be undefined if no clock handler is to be
	       included in the system.


      SRT-8 User's Manual					     page 21
      SYSTEM TASKS


	       COMMAND  is  the  type  of  request  and  has  the  following
	       meanings:

	  0000 - POST the event flag CLKMSG  after  the  specified  interval
		 elapses.  TASKNO, EXTRA1 and EXTRA2 are ignored.

	  1000 - Execute a RUN ER on the task specified by TASKNO after  the
		 specified   interval  elapses.   POST  CLKMSG  immediately.
		 EXTRA1 and EXTRA2 are ignored.

	  2000 - DERAIL the task  specified  by  TASKNO  into  a  subroutine
		 whose  address  is  specified in EXTRAl after the specified
		 interval elapses.   POST  CLKMSG  immediately.   EXTRA2  is
		 ignored.

	  3000 - Execute a RUN ER on the task specified by TASKNO after  the
		 specified  interval elapses, and re-queue this command with
		 the parameters EXTRA1 and EXTRA2 in place  of  TIMEHI   and
		 TIMELO.   This has the effect of running the specified task
		 periodically with a period specified by EXTRA1 and  EXTRA2.
		 POST CLKMSG immediately.

	  4000 - Delete from the clock  queue  all  requests  for  the  task
		 specified  by  TASKNO.   TIMEHI, TIMEL0, EXTRA1, and EXTRA2
		 are ignored.  POST CLKMSG.


	      The clock handler also maintains the current  time-of-day  (in
	      system  ticks  until  midnight) in locations TODH (high-order)
	      and TODL  (low-order)  in  Page  0  of  field  0.   When  this
	      time-of-day  reaches  zero  (i.e.  at midnight) it is reset to
	      the quantity SHERTZ*86400 (24 hours  until  midnight)  and  an
	      OS/8-format  date  word  in location DATE in page 0 of Field 0
	      is incremented by one day.

	      Note that  in  order  for  the  quantity  SHERTZ*86400  to  be
	      contained in 24 bits, SHERTZ must be less than 192.


      SRT-8 User's Manual					     page 22
      SYSTEM TASKS


			 Examples of clock handler calls:


      1)       CAL	      /With a 50Hz system tick rate.		
	       SENDW	      /this causes the current task
	       CLOCK	      /to "go to sleep" for 2 seconds.
	       SLEEPM
	       .
	       .
      SLEEPM,  ZBLOCK 3	      /SRT-8 message overhead
	       0 	      /set event flag after interval
	       0;144	      /interval is 100 (decimal) system ticks

      Note that by changing the 144 to the assembler expression 2^SHERTZ the
      above sequence becomes configuration independent.


      2)       CAL 	      /Run the task REPORT once
	       SEND	      /every hour, indefinitely,
	       CLOCK	      /assuming A 50Hz system tick rate
	       RUNMSG	
	       .
	       .
      RUNMSG,  ZBLOCK 3       /SRT-8 message overhead
	       3000+REPORT    /Run REPORT after specified interval and
			      /periodically thereafter.
	       0;1	      /First run is almost immediately (1/50 second).
	       53;7440	      /period between runs is 180000 (decimal)
			      /system ticks - 3600 seconds = 1 hour.


      SRT-8 User's Manual					     page 23
      SYSTEM TASKS


	   2.  		      Teletype Handler

	       The SRT-8 Teletype  handler  handles  a  single  Teletype  in
	       either  line   or  character  mode.  Input  in  line  mode is
	       terminated by a carriage return or an ALTMODE character,  and
	       may  be edited with the RUBOUT and ^U characters.  The RUBOUT
	       character deletes the last valid character typed and prints a
	       backslash;  the  ^U  character  deletes  the  entire line and
	       returns the carriage.  Character mode input is not echoed and
	       is  terminated by overflow of a specified character count. If
	       multiple Teletypes are to be handled, multiple copies of this
	       Teletype  handler  must be assembled.  Assembly parameters in
	       the body of  the  handler  specify  which  device  codes  the
	       handler  should use to access its Teletype and if the handler
	       is to be a "console" Teletype handler (the  console  Teletype
	       handler  invokes  the  MCR  whenever  a  ^C  is  typed on the
	       keyboard; non-console  Teletype  handlers  treat  ^C  as  any
	       other character).  The parameters edited into the distributed
	       version of the Teletype handler assemble  it  to  handle  the
	       PDP-8 console Teletype as a "console" device.

	       A message to the Teletype handler performs a (possibly  null)
	       output operation followed (optionally) by an input operation.
	       The format of messages to the teletype handler is:

		TTYMSG, ZBLOCK 3
			PACK+CRLF+IND+LINE+ASSIGN+LENGTH
			INBUF
			OUTTXT


      SRT-8 User's Manual					     page 24
      SYSTEM TASKS


			where

		PACK   =0     if output text is in packed ASCII format.
		       =4000  if input text is in unpacked ASCII
			      (one character per word, zero word terminates)
		CRLF   =0     if output message  should  be  followed  by  a
			      carriage return/line feed.
		       =2000  if it should not.
		IND    =0     if OUTTXT is the first word of the output text
		       =1000  if OUTTXT points to  the  first  word  of  the
			      output text
		LINE   =0     if  input  is  in  line  mode  (terminated  by
			      carriage return or ALTMODE)
		       =400   if input  is  in  character  mode  (terminated
			      after  "LENGTH"  input  characters  have  been
			      read)
		ASSIGN =0     for normal I/O operations.
		       =200   "Assigns" the Teletype  handler  to  the  task
			      specified  by  the  LENGTH  field.   This will
			      cause the  Teletype  handler  to  only  accept
			      messages  from the specified task.  If another
			      task tries to SEND a message to  the  Teletype
			      handler while it is assigned, the message will
			      be placed in the  Teletype  handler's  Message
			      Input  Queue  but  will  not  be  removed  for
			      processing by the Teletype handler  until  the
			      assignment is released.  The task to which the
			      Teletype handler is assigned can  release  the
			      assignment  by sending a message assigning the
			      teletype handler to task  number  0.   No  I/O
			      operation   is   performed  by  an  assignment
			      message.
		LENGTH	      is a  seven  bit  field  which  specifies  the
			      maximum  size  of the input buffer if input is
    			      in line mode,  the  number  of  characters  to
			      input  if  input  is  in character mode, and a
			      task number if the  ASSIGN  bit  is  set.   If
			      input  is  in line mode and there are LENGTH-1
			      characters in  the  input  buffer,  characters
    			      other  than  carriage  return, ALTMODE, RUBOUT
    			      and ^U will not be accepted or echoed.
		INBUF	      is a pointer to the input buffer -  if  it  is
    			      zero,  no input is taken.  The input buffer is
			      filled with input characters  packed  one  per
			      word  with the parity bit forced on.  If input
			      is in line mode, the  last  character  of  the
			      line is followed by a zero word (if a carriage
			      return terminated the line) or a negative word
			      (if an ALTMODE character terminated the line).
		OUTTXT	      is either the first word of  the  output  text
			      string  (if  IND=0)  or a pointer to the first
    			      word of the output string (if IND=1000).


      SRT-8 User's Manual					     page 25
      SYSTEM TASKS


				    Examples:

		HIYA, 	ZBLOCK 3      /SRT-8 Message overhead
			0	      /Packed text, end with CR/LF
			0	      /No input
			TEXT /HELLO/  /Text to be output

		Sending the above message to  the  Teletype  handler  prints
		"HELLO" on the Teletype.

		QUEST,	ZBLOCK 3      /SRT-8 Message Overhead
			2060 	      /Packed text, no CR/LF,
				      /48 character input limit,	
			ANSWER 	      /Pointer to input buffer
			TEXT /TYPE THE ANSWER:/

		Sending the above message to  the  Teletype  handler  prints
		"TYPE  THE  ANSWER:"  on  the  Teletype  and  inputs a reply
		without first returning the carriage.  The  answer  obtained
		from  the  above message could be printed on the teletype by
		sending the following message:

		TYPANS, ZBLOCK 3      /The usual overhead
			5000 	      /Unpacked text, indirect, with CR/LF
			0	      /No input
			ANSWER 	      /Pointer to output text





	   3.			Line Printer Handler

		The SRT-8 line printer handler outputs to an  LE8,  LS8E  or
		LV8  line  printer.  The  format  of  messages  to  the line
		printer handler is identical to the format  of  messages  to
		the  Teletype  handler,  but the INBUF word and the LINE bit
		are ignored (the INBUF word must, however, be present).


      SRT-8 User's Manual					     page 26
      SYSTEM TASKS


	   4.		Mass storage handlers

		This group of handlers all accept the same  request  message
		format  to  read  or  write  blocks  on various mass storage
		devices.  Handlers have been written for TC08 Dectape,  DF32
		and  RF08  fixed-head  disks,  and  RK8 and RK8E moving-head
		disks.

		The format of messages to mass storage handlers is:

		MSMESG, ZBLOCK 3
			UNIT
			RW + PAGES + FIELD
			BUFADD
			BLOKNO
			STATUS

			where

		 UNIT	is the number of the unit on which the operation  is
			to be performed.
			DF32 and RF08 disks consist of only one unit.
			TC08 Dectape has units  0-7.  corresponding  to  its
			physical units 0-7.
			RK8 disk has units 0-3 corresponding to its physical
			units 0-3.
			RK8/E disk has unit 0-7, units 0-3 correspond to the
			outer  (lower  track  number) half of physical units
			0-3, and units 4-7 correspond to the  inner  (higher
			track number) half of physical units 0-3.

		RW	is  0  for  a  read  operation,  4000  for  a  write
			operation.

		PAGES	specifies  the  number  of  (128  word)   pages   to
			transfer,  times 100(8), i.e. if PAGES=2000 it means
			transfer 20(8) pages or  2048  words.   If  PAGES=0,
			40(8) pages or 4096 words will be transferred.

		FIELD	if the PDP-8  field  in  which  the  transfer  takes
			place,  times  l0(8),  i.e. if FIELD=30 the transfer
			will take place in field 3.

		BUFADD 	is  the  starting  address  of  the  buffer  to   be
			transferred.


      SRT-8 User's Manual					     page 27
      SYSTEM TASKS


		BLOKNO  is the block number on the  device  from  which  the
			transfer  will  begin.   All  devices are assumed to
			have 256 word blocks.  On  Dectape,  the  first  128
			words  of  each  of  an  even/odd  pair  of 129 word
			Dectape records are considered to be a block.

		STATUS	is a word which is set by the handler on  completion
			of  the  operation.   It  will contain a zero if the
			operation was successful, otherwise it will  contain
			a  non-zero  quantity  which  is  the  device status
			register.  Tasks which use the mass storage handlers
			should  test  this  word after the I/O operation has
			been completed (i.e. after the Event Flag  has  been
			Posted)  to  determine if any errors occurred during
			the transfer.  All SRT-8 mass storage handlers retry
			operations  three  times  if  errors are encountered
			before setting the STATUS word non-zero.

		Note that the middle three words of a message to  the  SRT-8
		mass  storage  handlers are identical to the arguments to an
		OS/8 handler which performs the same operation.



				     Example:


			CAL
			SENDW
			DTA	    /Send a message to the Dectape handler
			DTAMSG	    /and wait for completion.
			TAD STATUS  /Check the status of the operation.
			SZA CLA
			JMP ERR     /Bad - go to error routine.

		DTAMSG, ZBLOCK 3    /SRT-8 message overhead
			4 	    /Dectape unit 4
			4210 	    /Write 256 words from field	1,
			BUFFER 	    /location BUFFER,
			55	    /into block 55 (records 132	& 133).

		STATUS, 0	    /status of operation stored here.


      SRT-8 User's Manual					     page 28
      SYSTEM TASKS


	    5.	  OS/8 File Support Task

		The OS/8 File Support Task (hereafter referred to  as  OS8F)
		allows  other  tasks  to lookup, create, and delete files in
		OS/8 directories.  It is included in the same source file as
		the OS/8 Support Task, but may be assembled independently of
		that task (depending on which   tasks  are  defined  in  the
		system parameter file).  The format of messages to OS8F is:

		OSFMSG,	ZBLOCK 3    /SRT-8 OVERHEAD
			DEVHND+UNIT+FUNCT
			FILPTR
			STATUS
			BLOKNO
			LENGTH

				where

		DEVHND 		is the task number of the  handler  for  the
				desired device.
		UNIT		is the unit number on which the operation is
				to be performed.
		FILPTR		is a pointer to a four-word  filename.   The
				PAL8  pseudo-op  FILENAME  may  be  used  to
				generate these filenames.
		FUNCT		represents the function to be performed.  It
				may have the following values:

			0 	Look up the specified file name  and  return
				its  starting block number in BLOKNO and its
				(positive) length in LENGTH.
			2000 	Enter the specified file name into the first
				empty  space  on  the  device  whose  length
				exceeds the value  in  LENGTH.   Return  the
				starting  block  number  of  the new file in
				BLOKNO.   If  a  file  of  the   same   name
				previously  existed  on  the  device  it  is
				deleted.  The value of LENGTH is unchanged.
			4000	Delete the specified file name.


      SRT-8 User's Manual					     page 29
      SYSTEM TASKS


		STATUS 	Describes the final status of the operation:

			0	Means operation successful.
			1	Means file not found on LOOKUP or Delete.
			2 	Means no room for file on Enter.
			>2	Means I/O error occurred - value is hardware
				error status of device.
			-1	Means invalid directory on device.

    		If both OS8F and the OS/8 Support  Task  are  present  in  a
    		system,  an  interlock  is  set  up  to prevent simultaneous
    		updating of directory blocks by both systems.  Because  OS/8
    		tends  to leave directory blocks in core for long periods of
    		time, this interlock scheme is very restrictive.   Before  a
    		Delete  or  Enter  operation  is performed, OS8F waits until
    		OS/8 is in a state in which:
    		a) 	There is no active temporary file on the OS/8
    			device corresponding to DEVHND and UNIT.
    		b)	OS/8 has just loaded the Keyboard Monitor,
    			Command Decoder  or USR into core.

    		Lookup operations are not  interlocked  since  they  do  not
		modify the directory.


      SRT-8 User's Manual					     page 30
      SYSTEM TASKS


	    6.		Power Fail Task


		The Power Fail Task provides  the  mechanism  by  which  the
		system     recovers    from    power    failure    if    the
		power-fail/auto-restart option is present and if the  system
		parameter  PWRFAL  was  equated to a non-zero value, the SPL
		(skip on power low) instruction is included in the interrupt
		skip  chain.  If a power low condition occurs, the processor
		state is saved and the  processor  is  halted.   When  power
		comes  back,  the  processor  state is restored and an Event
		Flag is POSTed which wakes up  the  Power  Fail  Task.   The
		Power  Fail  Task  restores  the clock, console Teletype and
		OS/8 Teletype if they  are  present  and  also  performs  an
		action  for each task in the system based on the contents of
		an internal table.  Each task has a one word entry  in  this
 		table, which contains:

		0	if nothing should be done  for  this  task  (default
			value)
		-1	if the EFWT (Event Flag wait) bit should be  cleared
			in  the  Task  Flags Table entry for this task (i.e.
			this task should be taken out of Event Flag wait)
		ADDR	if the task should be DERAILed to location  ADDR  in
			addition to having its EFWT bit cleared.

		Each task in the system may alter its  entry  in  the  Power
		Fail  Task's  table  by  sending a message to the Power Fail
		Task.  The format of the message is:

		PWRMSG,	ZBLOCK 3 /SRT-8 OVERHEAD
			WORD

		Where WORD is the new contents  of  the  Power  Fail  Task's
		table entry for the sending task.


      SRT-8 User's Manual					     page 31
      SYSTEM TASKS


	    7.		OS/8 Support Task

		This task supports  the  execution  of  the  OS/8  operating
		system as a task under SRT-8. OS/8 is run in the top two (or
		more) memory fields under control of the KT8/E or TSS-8 time
		sharing   hardware   option.    The  OS/8  Support  task  is
		configured  at  system   Startup   time   to   establish   a
		correspondence between OS/8 devices and SRT-8 handler tasks.
		Teletype input and output  from  OS/8  is  ring-buffered  by
		several  characters to minimize input loss due to usurpation
		of the CPU by higher-priority tasks.  Because of  the  large
		number  of  trapped  CDF instructions in OS/8 and its CUSPS,
		response time is slower than a stand-alone OS/8  system  but
		still quite reasonable.

		Several parameters in the system parameter file control	 the
		assembly of the OS/8 support task.  They are:

		OSFLDS 	Should be defined to be the number of fields  to  be
			dedicated to OS/8, OSFLDS=2 specifies 8K for OS/8.

		OSKBDV	Should be set equal to the keyboard IOT code of  the
			OS/8  Teletype  (OS/8  requires  its  own  dedicated
			teletype).
			Example:  OSKBDV=03 will use  the  console  Teletype
			keyboard for OS/8.

		OSTTDV 	Should be set equal to the teleprinter IOT  code  of
			the OS/8 Teletype.
			Example:    OSTTDV=04   would   use   the    console
			Teleprinter for OS/8.

		OSNULL  specifies how many null  characters  must  follow  a
			line-feed  character  on  the  OS/8  teletype.  This
			allows high-speed VT05 terminals to be used as  OS/8
			Teletypes.  For standard Teletypes and parallel LA30
			terminals this parameter should be set to zero.

		OSSYSD 	should be equated to the task  number  of  the  OS/8
			system device handler.
			Example:  OSSYSD=DTA would specify DTA0 as the  OS/8
			system device.


      SRT-8 User's Manual					     page 32
      SYSTEM TASKS


		The OS/8 system which runs under the OS/8 Support  Task  may
		run  all  OS/8  CUSPs  except BUILD and FRTS, the Fortran IV
		run-time  system.   All  references  to  the  keyboard   and
		teleprinter  are diverted to the specified OS/8 keyboard and
		teleprinter.  References in OS/8 to the  LE8,  LS8E  or  LV8
		line printers are diverted to the SRT-8 line printer handler
		if the system parameter LPT is defined;  otherwise they  are
		executed  directly  by  the Support Task.  References to the
		following  OS/8  device  names  will  be  diverted  to   the
		corresponding SRT-8 handler if one is defined:

		DTA0-DTA7
		RKA0-RKA3
		RKB0-RKB3

		In addition, the OS/8 handlers SYS and DSK are  diverted  to
		the  handler  specified  by  the  parameter  OSSYSD.   Other
		references to I/O under the supported OS/8 system may  cause
		the OS/8 support task to hang in a loop.


      SRT-8 User's Manual					     page 33
      SYSTEM TASKS



			     Monitor Console Routine


      The Monitor Console Routine (MCR) provides functions which   the  user
      can  request  from  the console Teletype in order to control, Inspect.
      and (to some extent) debug his system.

	   The MCR indicates that it is ready to accept  input  by  printing
      the  prompting character ">" on the Teletype.  An MCR command consists
      of  a  command  word  (of  which  only  the  first  2  characters  are
      significant)  followed  by  arguments,  and  terminated  with either a
      Carriage return or an altmode.   Commands  may  be  a  maximum  of  40
      characters  long.   If the command is terminated by a carriage return,
      the MCR will return to the Teletype for another  command  when  it  is
      finished  processing  this  one;  if an altmode terminates the command
      line the MCR will  put  itself  in  a  wait  state  when  it  finishes
      processing  the  command - it can be brought out of this wait state by
      typing ^C (Control/C) on the  console  Teletype.   When  the  MCR  has
      prompted  with  its  ">" and is waiting for input no other SRT-8 tasks
      can use the Teletype;  therefore if the Teletype is used for something
      other  than an exclusive MCR terminal (for instance for error logging)
      the operator should type ^C, type his MCR command,  and  terminate  it
      with  an  altmode  character.   This  way  the MCR will not tie up the
      Teletype.


      SRT-8 User's Manual					     page 34
      SYSTEM TASKS



      Certain syntactic constructions are used as arguments to  several  MCR
      commands;  these are defined below to avoid needless repetition:

	     ,		  A single comma or  a  single  space  may  be  used
			  interchangeably   to  separate  arguments  to  MCR
			  commands.

	     Task-ID	  A Task-ID is either a number or a name.  If it  is
			  a  number  it  represents  the internal SRT-8 Task
			  Number which  is  also  the  task  priority  of  a
			  task.   If it is a name, the first 4 characters of
			  the name are looked up  in  the  MCR'S  Task  Name
			  table to produce a Task Number.

	     Time-of-day  A Time-of-day is  of  the  form  hh:mm,  where  hh
			  represents  hours  past midnight and mm represents
			  minutes past hh:00.

	     Address	  An Address is an octal number from 1 to  5  digits
			  in length which represents a PDP-8 memory address.
			  If the address is less than 5 digits long the high
			  order digits are assumed to be 0.

	     Word	  A word is an octal number from 1 to 4 digits long.


      Starting on the next page is a list  of  the  MCR  commands.   In  the
      header line of the description, the significant portion of the command
      word is  capitalized.   Optional  arguments  are  enclosed  in  square
      brackets  ([])  and  choices  will  be  embedded  in  parentheses  and
      separated by exclamation points (!). Following the header line will be
      a  description  of the action which the command causes and possibly an
      example.

      Commands which are starred are not present  if  the  symbol  CLOCK  is
      not  defined  in the SRT-8 parameter file (indicating that there is no
      clock in the system).


      SRT-8 User's Manual					     page 35
      SYSTEM TASKS


      1.   REquest Task-ID [,( @Time-of-day ! Interval ) [,interval] ]

	     Where "Interval" is of the form:
		    nH	      Meaning n hours.
		    nM	      Meaning n minutes.
		    nS	      Meaning n seconds.
		    nT	      Meaning n system ticks.

	     Requests  a  task  to  run  immediately  (if  only  Task-ID  is
	     specified),  at a given time-of-day, or after a given interval.
	     Requesting a task clears the RUNWT bit in the Task  Flag  Table
	     entry  for  that  task.  If the third argument is specified the
	     task is rerun periodically with the interval given in the third
	     argument  as  the  period.  If the parameter CLOCK in the SRT-8
	     parameter file is not defined, the second and  third  arguments 
	     of this  command  are  ignored and the given task is always run
	     immediately.

			      Examples:

		    >REQUEST X
	     Will run task X immediately.

		    >RE FOO,@2:00
	     Will run task FOO at 2:00 A.M. (if	it is after 2AM, FOO Will be
	     run tomorrow at 2AM).

		    >RE 5,10M,5M
	     Will run task number 5 10 minutes from now and every 5  minutes
	     thereafter.


		    >REQ HIPR,1T,6T
	     On a machine with a 60 Hz clock, this command Will run the task
	     HIPR  immediately (well, almost immediately - .016 seconds from
	     now) and 10 times per second thereafter.

	     Note:  If at the time the REQUEST command is  executed,  (which
	     may  be  several hours after it is typed in) the task specified
	     by Task-ID does not have the RUNWT bit set in  its  Task  Flags
	     Table  entry,  then the REQUEST command is a no-op.  Similarly,
	     if the task had other bits set besides RUNWT it will not be run
	     upon execution of the REQUEST command, but will be run when the
	     other blocking bits are cleared.


      2.   STop Task-ID

	     Suspends execution of the task specified by Task-ID by  turning
	     the  RUNWT  bit on in the Task Flags Table entry for that task.
	     A task which has been stopped may be resumed  via  the  REQUEST
	     MCR  command  (in  this instance it is easier to think of it as
	     the RESUME MCR command).


      SRT-8 User's Manual					     page 36
      SYSTEM TASKS


      3.   NAme Task-ID,Newname

	     The character string "Newname" becomes the new name of the task
	     specified  by  Task-ID.   The old name of that task (if any) is
	     lost. "Newname"  may  be  any  length  but  only  the  first  4
	     characters are stored.  "Newname" should not be the name of any
	     other task or an error message will result.

			      Examples:

		    >NAME 7 REPORT
	     Task number 7 is given the name REPO.

		    >NAME REPORT,FOO
	     Task number 7, which is known as REPO, is now known as FOO.

	     Note:  The MCR name table is initialized at  assembly  time  to
	     contain the names of any DEC-SUPPLIED tasks which are listed in
	     the parameter file - e.g. if the symbol CLOCK is defined in the
	     parameter  file  as  CLOCK=2,  task  number 2 will get the name
	     clock.  The MCR name table may  be  modified  by  the  user  to
	     include  his  own  task  names  permanently by editing the file
	     MCR.PA after the label NMTBL.


      4. * DAte [mm/dd/yyyy [,Time-of-day] ]

	     The date mm/dd/yyyy, if specified,  becomes  the  system  date.
	     only the last digit of the year is significant - all others are
	     ignored  and  "197"  assumed.   The  SRT-8   system   date   is
	     automatically   bumped   at  midnight  to  the  next  day.  but
	     transitions between months are not handled correctly.   If  the
	     second  argument  is  specified  the  system Time-of-day is set
	     equal to it.  If no arguments are specified, the current system
	     date is printed on the console Teletype in the form MM/DD/197Y.


      5. * Time [Time-of-day]

	     If  a  Time-of-day  is  specified,  it   becomes   the   system
	     Time-of-day.   If  no  argument is specified the current system
	     Time-of-day is printed out on the console Teletype in the  form
	     HH:MM.


      6.   Disable Task-ID

	     Disables future execution of the specified task by setting  the
	     ENABWT bit on in the Task Flags Table entry for that task.


      SRT-8 User's Manual					     page 37
      SYSTEM TASKS


      7.   ENable Task-ID

	     Clears the ENABWT bit in the Task Flags  Table  entry  for  the
	     specified task, thus enabling it to run.  If the ENABWT bit was
	     not set, the command is a no-op.


      8. * CAncel Task-ID

	     Cancels any clock queue entries involving the task specified by
	     Task-ID.   This  includes  any  entries  made  by the MCR (from
	     previous  timed  REQUEST  commands),  entries   involving   the
	     specified  task  made  by other tasks (e.g. a timed DERAIL) and
	     entries made by the specified task  involving  itself  (e.g.  a
	     timed POST).  Note that in the case of the timed POST the event
	     flag will not be posted  and  the  task  may  hang  up  forever
	     waiting for it.


      9.   SYstat [Task-ID]

	     If no argument is specified, the SYSTAT command prints a system
	     status  report.   Each line of the report describes an existent
	     task in the system.  The data printed for  each  task  are  its
	     Task  Number/priority,  its  name,  (if  it  has one), and what
	     blocking bits are on in  its  Task  Flags  Table  entry.   Each
	     blocking  bit  is  printed  as a one-letter code, preceded by a
	     space.  The possible one letter codes and their meanings are:

		    E		Waiting for event flag
		    M		Waiting for a message
		    O		Waiting for an event flag or a message
		    R		Waiting to be REQUESTed or RUN
		    S		Waiting to be swapped in (not in Phase 1)
		    D		Disabled
		    U		USERWT bit set

	     In addition, an asterisk is printed at the end of the  line  if
	     the task has any messages waiting in its input queue.

	     A more detailed status report on a single task may be  obtained
	     by  specifying  the  Task-ID of that task as an argument to the
	     SYSTAT  command.  The  detailed   report   contains   all   the
	     information  in  the  general  report,  followed  by five octal
	     words:

		    WORD 1    The location of the TASK state Table
			      entry containing words 2-5.  This word is
			      followed by a colon.
		    WORD 2    task Link in sign	bit, IF	in bits	6-8,
			      DF in bits 9-11.
		    WORD 3	Task PC
		    WORD 4	Task AC
		    WORD 5	Task MQ


      SRT-8 User's Manual					     page 38
      SYSTEM TASKS



			      Examples:

	     A general SYSTAT command might  produce  the  following  sample
	     output line:

	     13  CARD   E *

	     meaning task number 13, named "CARD", is in event flag wait and
	     has input messages pending,  The command:
		
		    >SYSTAT CARD

	     might produce the single line:

	     13  CARD   E *  1320: 0022  1741  0000  2525

	     indicating that CARD is stopped at location 21741 with  its  AC
	     and Link zero and 2525 in its MQ.

	     The SYSTAT command may be left  out  of  the  MCR  assembly  by
	     setting  the system parameter MCRSYS equal to zero in the SRT-8
	     parameter file saving one page of code.


      SRT-8 User's Manual					     page 39
      SYSTEM TASKS


      10.  OPen Address [,Count]

	     If "Count" is not specified it is  assumed  to  be  1,   "Count"
	     locations  starting  at  Address  are displayed in octal on the
	     console Teletype in the form:

	     lllll/ cccc

	     The range of locations displayed may cross a field boundary.


      11.  EXamine Address, [Count}

	     The EXAMINE command is identical to the OPEN command.


      12.  DEposit Address,word [,word] [,word],...

	     The Second through Nth arguments are  deposited  into  core  at
	     consecutive  locations  starting at Address.  As in OPEN, field
	     boundaries may be crossed.

	     Example:  >DEPOSIT 26132,7700,7200,50

	     Deposits 7700 into location 26132, 7220  into  location  26133,
	     and 0050 into location 26134.


      13.  POst Address POSTs the Event Flag at the specified address.  This
	   command  is  useful  when  debugging  a system for simulating the
	   effects of non--existent tasks or devices.



      14.  EXIT

	     The EXIT command causes the MCR to	 terminate  SRT-8  execution
	     (after  pausing  approximately  1  second  for  pending  I/O to
	     complete) and return to the OS/8  monitor  at  location  07600.
	     This  command  must  be  spelled  out  completely or it will be
	     regarded as an EXAMINE command.


	   The MCR checks each command line for errors and, if it finds one,
      issues one of the following messages and reprompts on the Teletype for
      a corrected command:

 	   BAD CHAR	  Character was not expected where it occurred
	   BAD NUMBER	  Number out of legal range or missing
	   BAD DELIM	  No space or comma where one was expected
	   BAD NAME	  Task name not in name table or duplicate


      SRT-8 User's Manual					     page 40
      SYSTEM TASKS


    			  SRT-8 Distributed Source Files

	   The SRT-8 source files included on the distribution tape are;

	FILE	  TASK(S)	    COMMENTS
      PARAM.PA	  -		    System parameter file with all equates
				    blank.  Should never be altered, but
				    should be edited to create specific
				    parameter files.
      SRT8,PA     - (null task)	    SRT-8 Executive.
      MCR.PA	  MCR		    Monitor Console Routine
      OS8SUP.PA	  OS8		    OS/8 Support Task
		  OS8F		    OS/8 File Support Task
      PWRF.PA	  PWRF		    Power Fail Task
      CLOCK.PA	  CLOCK		    Clock handler
      TTY.PA	  TTY		    Teletype driver Task
      LPT PA	  LPT		    Line Printer driver Task
      DTA.PA	  DTA		    TC08 Dectape driver Task
      RK8.PA	  RK8		    RK8 disk driver Task
      RK8E.PA	  RK8		    RK8E disk driver TASK
      RF08.PA	  RF08/DF32	    RF08/DF32 fixed-head disk driver Task
      CSA.PA	  CSA		    Cassette driver Task
      CSAF.PA	  CSAF		    Cassette File Support Task
      UDC.PA	  UDC		    Universal Digital Controller handler


      SRT-8 User's Manual					     page 41
      SYSTEM TASKS


    			      SRT-8 Component sizes

      The following table gives the appropriate size (or projected size)  of
      each component of the SRT-8 system as of January 11, 1974:

	   NTASKS = Number of tasks in system
	   CLKQLN = Number of entries in clock queue
	   MCRSYS = 1 if MCR SYSTAT function desired, else 0

	   Any fractions from divides should be dropped.

			     Number of Pages
      Software Component     required (1 page = 128	  Comments
			     words)

      ----------------------------------------------------------------------

      SRT-8 Executive	     5 + NTASKS/18	    Must  be  in   locations
						    00200-01200.    Requires
						    about    16    page    0
						    locations	   and    an
						    auto-index register.

      Clock handler	     3 + CLKQLN/22	    must be in field 0. Uses
						    an auto-index register.

      Console Teletype	     2
      handler

      Non-Console	     2
      Teletype handler

      Line Printer handler   1

      TC08 DECtape handler   2

      RK8E Disk handler	     2

      DF32/RF08 handler	     1

      RK8 Disk handler       1


      SRT-8 User's Manual					     page 42
      SYSTEM TASKS


			     Number of Pages
      Software Component     required (1 page = 128	  Comments
			     words)

      ----------------------------------------------------------------------

      UDC handler	     7-9 depending on	    uses 16 page 0 locations
			     table space desired.

      Cassette handler	     3

      Cassette label	     3			    Requires	    cassette
      support handler				    handler.

      OS/8 file		     6			    Requires a mass  storage
      support handler				    handler.   Must  run  in
						    field 0.

      OS/8 Support task	     6			    Must run in  field  0  -
						    requires   8K  for  OS/8
						    plus   a    mass-storage
						    handler.  Uses 12 page 0
						    locations.

      Monitor Console	     5 + 3 (if Clock fns    Requires       "console"
      Routine task	     desired) + MCRSYS 	    teletype   handler   and
			     + (NTASKS+40)/64.	    16 page 0 locations.